| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | ---- | 8800A 32 KW 12-BIT MEMORY [0000] |
| 2 | ---- | 4 CHANNEL LECROY TRANSIENT DIGITIZER 8210 +/- 5 VOLTS, 32 KW MEMORY |
| 3 | ---- | 8210 (slot 2 of 3) |
| 4 | ---- | 8210 (slot 3 of 3) |
| 5 | ---- | 8800A 32 KW 12-BIT MEMORY [0000] |
| 6 | ---- | 4 CHANNEL LECROY TRANSIENT DIGITIZER 8210 +/- 5 VOLTS, 32 KW MEMORY |
| 7 | ---- | 8210 (slot 2 of 3) |
| 8 | ---- | 8210 (slot 3 of 3) |
| 9 | ---- | 8800A 32 KW 12-BIT MEMORY [0000] |
| 10 | ---- | 4 CHANNEL LECROY TRANSIENT DIGITIZER 8210 +/- 5 VOLTS, 32 KW MEMORY |
| 11 | ---- | 8210 (slot 2 of 3) |
| 12 | ---- | 8210 (slot 3 of 3) |
| 13 | ---- | 8800A 32 KW 12-BIT MEMORY [0000] |
| 14 | ---- | 4 CHANNEL LECROY TRANSIENT DIGITIZER 8210 +/- 5 VOLTS, 32 KW MEMORY |
| 15 | ---- | 8210 (slot 2 of 3) |
| 16 | ---- | 8210 (slot 3 of 3) |
| 17 | ---- | 8800A 32 KW 12-BIT MEMORY [0000] |
| 18 | ---- | 4 CHANNEL LECROY TRANSIENT DIGITIZER 8210 +/- 5 VOLTS, 32 KW MEMORY |
| 19 | ---- | 8210 (slot 2 of 3) |
| 20 | ---- | 8210 (slot 3 of 3) |
| 21 | ---- | ---- |
| 22 | ---- | 000 TRIGGER BUFFER MODULE (PPPL) |
| 23 | ---- | ---- |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NOs.: 2 - 4 | MODULE TYPE 8210 TRANSIENT DIGITIZER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 1-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
| SLOT 2, CHANNEL 1 | ETX-DGT-2-1 |  |  | +- | CNTR SHLD | 1 |
| SLOT 2, CHANNEL 2 | ETX-DGT-2-2 |  |  | +- | CNTR SHLD | 2 |
| SLOT 2, CHANNEL 3 | ETX-DGT-2-3 |  |  | +- | CNTR SHLD | 3 |
| SLOT 2, CHANNEL 4 | ETX-DGT-2-4 |  |  | +- | CNTR SHLD | 4 |
| FROM TRIGGER BUFFER MODULE, SLOT 22 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
|  |  |  |  | +- | CNTR SHLD | EXT. CLK |

| SLOT NOs.: 6 - 8 | MODULE TYPE 8210 TRANSIENT DIGITIZER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 1-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
| SLOT 6, CHANNEL 1 | ETX-DGT-6-1 |  |  | +- | CNTR SHLD | 1 |
| SLOT 6, CHANNEL 2 | ETX-DGT-6-2 |  |  | +- | CNTR SHLD | 2 |
| SLOT 6, CHANNEL 3 | ETX-DGT-6-3 |  |  | +- | CNTR SHLD | 3 |
| SLOT 6, CHANNEL 4 | ETX-DGT-6-4 |  |  | +- | CNTR SHLD | 4 |
| FROM TRIGGER BUFFER MODULE, SLOT 22 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
|  |  |  |  | +- | CNTR SHLD | EXT. CLK |

| SLOT NOs.: 10 - 12 | MODULE TYPE 8210 TRANSIENT DIGITIZER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 1-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
| SLOT 10, CHANNEL 1 | ETX-DGT-10-1 |  |  | +- | CNTR SHLD | 1 |
| SLOT 10, CHANNEL 2 | ETX-DGT-10-2 |  |  | +- | CNTR SHLD | 2 |
| SLOT 10, CHANNEL 3 | ETX-DGT-10-3 |  |  | +- | CNTR SHLD | 3 |
| SLOT 10, CHANNEL 4 | ETX-DGT-2104 |  |  | +- | CNTR SHLD | 4 |
| FROM TRIGGER BUFFER MODULE, SLOT 22 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
|  |  |  |  | +- | CNTR SHLD | EXT. CLK |

| SLOT NOs.: 14 - 16 | MODULE TYPE 8210 TRANSIENT DIGITIZER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 1-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
| SLOT 14, CHANNEL 1 | ETX-DGT-14-1 |  |  | +- | CNTR SHLD | 1 |
| SLOT 14, CHANNEL 2 | ETX-DGT-14-2 |  |  | +- | CNTR SHLD | 2 |
| SLOT 14, CHANNEL 3 | ETX-DGT-14-3 |  |  | +- | CNTR SHLD | 3 |
| SLOT 14, CHANNEL 4 | ETX-DGT-14-4 |  |  | +- | CNTR SHLD | 4 |
| FROM TRIGGER BUFFER MODULE, SLOT 22 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
|  |  |  |  | +- | CNTR SHLD | EXT. CLK |

| SLOT NOs.: 18 - 20 | MODULE TYPE 81810 TRANSIENT DIGITIZER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 1-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
| SLOT 18, CHANNEL 1 | ETX-DGT-18-1 |  |  | +- | CNTR SHLD | 1 |
| SLOT 18, CHANNEL 18 | ETX-DGT-18-2 |  |  | +- | CNTR SHLD | 2 |
| SLOT 18, CHANNEL 3 | ETX-DGT-18-3 |  |  | +- | CNTR SHLD | 3 |
| SLOT 18, CHANNEL 4 | ETX-DGT-18-4 |  |  | +- | CNTR SHLD | 4 |
| FROM TRIGGER BUFFER MODULE, SLOT 22 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
|  |  |  |  | +- | CNTR SHLD | EXT. CLK |

| SLOT NO.: 22 | MODULE TYPE TRIGGER BUFFER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | CONN | CH |
| --- | --- | --- | --- | --- | --- | --- |
| TRIGGER INPUT |  |  |  | +- |  | 1 |
| TRIGGER OUTPUT #1 |  |  |  | +- | CNTR SHLD | 2 |
| TRIGGER OUTPUT #2 |  |  |  | +- | CNTR SHLD | 3 |
| TRIGGER OUTPUT #3 |  |  |  | +- | CNTR SHLD | 4 |
| TRIGGER OUTPUT #4 |  |  |  | +- | CNTR SHLD | EXT. TRIG |
| TRIGGER OUTPUT #5 |  |  |  | +- | CNTR SHLD | EXT. CLK |