| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 2 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 3 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 4 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 5 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 6 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 7 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 8 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 9 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 10 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 11 | ---- | 8100 LECROY 2 CHANNEL AMPLIFIER |
| 12 | ---- | ---- |
| 13 | ---- | ---- |
| 14 | ---- | ---- |
| 15 | ---- | ---- |
| 16 | ---- | ---- |
| 17 | ---- | ---- |
| 18 | ---- | 322 16-BIT DIGITAL INPUT MODULE - ISOLATED CONTACT |
| 19 | ---- | 16-BIT DIGITAL OUTPUT MODULE - 304A OPTO OUTPUTS, MOMENTARY, NORM OPEN |
| 20 | ---- | 3340 KINETICS SYSTEMS 2-CHANNEL COMMUNICATION MODULE |
| 21 | ---- | 404A 8-CHANNEL TIMING MODULE [ALL E-STOP OFF] |
| 22 | ---- | 404A (slot 2 of 2) |
| 23 | ---- | ---- |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NO.: 1 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 2, CHANNEL 1 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 2, CHANNEL 2 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |  |

| SLOT NO.: 2 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 2, CHANNEL 3 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 2, CHANNEL 4 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 3 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 6, CHANNEL 1 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 6, CHANNEL 2 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 4 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 6, CHANNEL 3 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 6, CHANNEL 4 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 5 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 10, CHANNEL 1 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 10, CHANNEL 2 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 6 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 10, CHANNEL 3 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 10, CHANNEL 4 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 7 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 14, CHANNEL 1 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 14, CHANNEL 2 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 8 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 14, CHANNEL 3 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 14, CHANNEL 4 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 9 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 18, CHANNEL 1 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 18, CHANNEL 2 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 10 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
| FOR 8210, SLOT 18, CHANNEL 3 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
| FOR 8210, SLOT 18, CHANNEL 4 |  | CCC-EE-205, C=14 |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 11 | MODULE TYPE 8100 2-CHANNEL AMPLIFIER |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR |  | 2-PIN LEMO | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | +- | 2 1 | CH 1 IN |
|  |  |  |  | +- | 2 1 | CH 1 OUT |
|  |  |  |  | +- | 2 1 | CH 2 IN |
|  |  |  |  | +- | 2 1 | CH 2 OUT |
| THE FOLLOWING 2-PIN LEMO CONVENTION IS USED : PIN 2) SIGNAL (FEMALE RECEPTACLE ON CABLE PLUG) PIN 1) RETURN (MALE PIN ON CABLE PLUG) |

| SLOT NO.: 18 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | F B | BRN TAN | 1B 1A | 1 |
|  |  |  |  | F B | RED TAN | 2B 2A | 2 |
|  |  |  |  | F B | ORN TAN | 3B 3A | 3 |
|  |  |  |  | F B | YLW TAN | 4B 4A | 4 |
|  |  |  |  | F B | GRN TAN | 5B 5A | 5 |
|  |  |  |  | F B | BLU TAN | 6B 6A | 6 |
|  |  |  |  | F B | VIO TAN | 7B 7A | 7 |
|  |  |  |  | F B | GRY TAN | 8B 8A | 8 |
|  |  |  |  | F B | BRN TAN | 9B 9A | 9 |
|  |  |  |  | F B | RED TAN | 10B 10A | 10 |
|  |  |  |  | F B | ORN TAN | 11B 11A | 11 |
|  |  |  |  | F B | YLW TAN | 12B 12A | 12 |
|  |  |  |  | F B | GRN TAN | 13B 13A | 13 |
|  |  |  |  | F B | BLU TAN | 14B 14A | 14 |
|  |  |  |  | F B | VIO TAN | 15B 15A | 15 |
|  |  |  |  | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 19 | MODULE TYPE 304 DIGITAL OUTPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | F B | BRN TAN | 3B 3A | 1 |
|  |  |  |  | F B | RED TAN | 4B 4A | 9 |
|  |  |  |  | F B | ORN TAN | 5B 5A | 2 |
|  |  |  |  | F B | YLW TAN | 6B 6A | 10 |
|  |  |  |  | F B | GRN TAN | 7B 7A | 3 |
|  |  |  |  | F B | BLU TAN | 8B 8A | 11 |
|  |  |  |  | F B | VIO TAN | 9B 9A | 4 |
|  |  |  |  | F B | GRY TAN | 10B 10A | 12 |
|  |  |  |  | F B | BRN TAN | 11B 11A | 5 |
|  |  |  |  | F B | RED TAN | 12B 12A | 13 |
|  |  |  |  | F B | ORN TAN | 13B 13A | 6 |
|  |  |  |  | F B | YLW TAN | 14B 14A | 14 |
|  |  |  |  | F B | GRN TAN | 15B 15A | 7 |
|  |  |  |  | F B | BLU TAN | 16B 16A | 15 |
|  |  |  |  | F B | VIO TAN | 17B 17A | 8 |
|  |  |  |  | F B | GRY TAN | 18B 18A | 16 |

| SLOT NO.: 20 | MODULE TYPE 3340 COMMUNICATION MODULE |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | COLOR | FCT | PIN | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | TX RX GND |  | CH 1 |
|  |  |  |  | TX RX GND |  | CH 2 |

| SLOT NO.: 21/22 | MODULE TYPE 404A TIMING MODULE |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 1B 1A | CE |
| START TRIGGER FOR CRATE 22, N=5 908 TRANSIENT DIGITIZER | PCTM-22-1 | 908, N=22 TRIG INPUT |  | F B | RED TAN | 2B 2A | 1 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 3B 3A | CE |
|  |  |  |  | F B | YLW TAN | 4B 4A | 2 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 5B 5A | CE |
|  |  |  |  | F B | BLU TAN | 6B 6A | 3 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 7B 7A | CE |
| START TRIGGER FOR CRATE 22, N=20 908 TRANSIENT DIGITIZER | PCTM-22-4 | 908, N=22 TRIG INPUT |  | F B | GRY TAN | 8B 8A | 4 |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 9B 9A | CE |
| START TRIGGER FOR CRATE 14, 8210 TRANSIENT DIGITIZERS | PCTM-14-A | TRIGGER BUFFER, C=14, N=22 |  | F B | RED TAN | 10B 10A | 5 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 11B 11A | CE |
|  |  |  |  | F B | YLW TAN | 12B 12A | 6 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 13B 13A | CE |
|  |  |  |  | F B | BLU TAN | 14B 14A | 7 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 15B 15A | CE |
|  |  |  |  | F B | GRY TAN | 16B 16A | 8 |