| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | A01 - A16 | 322 16-bit ac/dc digital input module [5 volts] |
| 2 | ---- |  |
| 3 | ---- |  |
| 4 | ---- |  |
| 5 | ---- |  |
| 6 | ---- |  |
| 7 | ---- |  |
| 8 | ---- |  |
| 9 | ---- |  |
| 10 | ---- |  |
| 11 | ---- |  |
| 12 | direct wired | 404A 8-CHANNEL TIMING MODULE [ALL E-STOP OFF] |
| 13 | ---- | 404A (slot 2 of 2) |
| 14 | ---- | 3421 Strobed Digital Input Module |
| 15 | ---- | 903 32 KW 12-BIT MEMORY [0001] |
| 16 | ---- | 903 32 KW 12-BIT MEMORY [0000] |
| 17 | ---- | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 64 KW MEMORY, P2 CLOCK SOURCE |
| 18 | ---- | 908 (slot 2 of 3) |
| 19 | ---- | 908 (slot 3 of 3) |
| 20 | A65-A80 | 322 16-bit ac/dc digital input module [5 volts] |
| 21 | direct wired | 409 4-Channel Timed Gate |
| 22 | direct wired | 302 16-bit Digital Output (relay) |
| 23 | ---- | 313 U-PORT/FACILITY CLOCK REPEATER |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NO.: 01 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME (‘0’ TRUE) | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Unit1 Force Fault | pc_pf_FFault1_CALC |  | A01 | F B | BRN TAN | 1B 1A | 1 |
| Unit1 Fault Protection Bypassed | pc_pf_FPByp1_CALC |  | A02 | F B | RED TAN | 2B 2A | 2 |
| Unit1 Internal Fault | pc_pf_IntFault1_CALC |  | A03 | F B | ORN TAN | 3B 3A | 3 |
| Unit1 Test Mode | pc_pf_TestMode1_CALC |  | A04 | F B | YLW TAN | 4B 4A | 4 |
| Unit2 Force Fault | pc_pf_FFault2_CALC |  | A05 | F B | GRN TAN | 5B 5A | 5 |
| Unit2 Fault Protection Bypassed | pc_pf_FPByp2_CALC |  | A06 | F B | BLU TAN | 6B 6A | 6 |
| Unit2 Internal Fault | pc_pf_IntFault2_CALC |  | A07 | F B | VIO TAN | 7B 7A | 7 |
| Unit2Test Mode | pc_pf_TestMode2_CALC |  | A08 | F B | GRY TAN | 8B 8A | 8 |
|  |  |  | A09 | F B | BRN TAN | 9B 9A | 9 |
|  |  |  | A10 | F B | RED TAN | 10B 10A | 10 |
|  |  |  | A11 | F B | ORN TAN | 11B 11A | 11 |
|  |  |  | A12 | F B | YLW TAN | 12B 12A | 12 |
|  |  |  | A13 | F B | GRN TAN | 13B 13A | 13 |
|  |  |  | A14 | F B | BLU TAN | 14B 14A | 14 |
|  |  |  | A15 | F B | VIO TAN | 15B 15A | 15 |
|  |  |  | A16 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 12/13 | MODULE TYPE 404A TIMING MODULE |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 1B 1A | CE |
| Test Trigger(PC32) | pc_404c17n13ch1 |  |  | F B | RED TAN | 2B 2A | 1 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 3B 3A | CE |
|  |  |  |  | F B | YLW TAN | 4B 4A | 2 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 5B 5A | CE |
|  |  |  |  | F B | BLU TAN | 6B 6A | 3 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 7B 7A | CE |
| START TRIGGER C=17/N=17 908 TRANSIENT DIGITIZER | pc_404c17n13ch4 | 908 TRIG INPUT |  | F B | GRY TAN | 8B 8A | 4 |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 9B 9A | CE |
|  |  |  |  | F B | RED TAN | 10B 10A | 5 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 11B 11A | CE |
|  |  |  |  | F B | YLW TAN | 12B 12A | 6 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 13B 13A | CE |
| Trigger for 409 Timed Gate in slot 21. | pc_404c17n13ch7_dly_LO |  |  | F B | BLU TAN | 14B 14A | 7 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 15B 15A | CE |
|  |  |  |  | F B | GRY TAN | 16B 16A | 8 |

| SLOT NO.: 17/19 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| PF5U-1S Force(lbs) = (Vin-2) x 100,000 | pc_UprWeldStrP1 |  |  | + - SH | 2 3 1 | 1 |
| PF5L-1S | pc_LwrWeldStrP1 |  |  | + - SH | 2 3 1 | 2 |
| PF4U-1S | pc_UprWeldStrN1 |  |  | + - SH | 2 3 1 | 3 |
| PF4L-1S | pc_LwrWeldStrN1 |  |  | + - SH | 2 3 1 | 4 |
| PF5U-2S | pc_UprWeldStrP2 |  |  | + - SH | 2 3 1 | 5 |
| PF5L-2S | pc_LwrWeldStrP2 |  |  | + - SH | 2 3 1 | 6 |
| PF4U-2S | pc_UprWeldStrN2 |  |  | + - SH | 2 3 1 | 7 |
| PF4L-2S | pc_LwrWeldStrN2 |  |  | + - SH | 2 3 1 | 8 |
|  |  |  |  | + - SH | 2 3 1 | 9 |
|  |  |  |  | + - SH | 2 3 1 | 10 |
|  |  |  |  | + - SH | 2 3 1 | 11 |
|  |  |  |  | + - SH | 2 3 1 | 12 |
|  |  |  |  | + - SH | 2 3 1 | 13 |
|  |  |  |  | + - SH | 2 3 1 | 14 |
|  |  |  |  | + - SH | 2 3 1 | 15 |
|  |  |  |  | + - SH | 2 3 1 | 16 |

| SLOT NO.: 17/19 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | + - SH | 2 3 1 | 17 |
|  |  |  |  | + - SH | 2 3 1 | 18 |
|  |  |  |  | + - SH | 2 3 1 | 19 |
|  |  |  |  | + - SH | 2 3 1 | 20 |
|  |  |  |  | + - SH | 2 3 1 | 21 |
|  |  |  |  | + - SH | 2 3 1 | 22 |
|  |  |  |  | + - SH | 2 3 1 | 23 |
|  |  |  |  | + - SH | 2 3 1 | 24 |
|  |  |  |  | + - SH | 2 3 1 | 25 |
|  |  |  |  | + - SH | 2 3 1 | 26 |
|  |  |  |  | + - SH | 2 3 1 | 27 |
|  |  |  |  | + - SH | 2 3 1 | 28 |
|  |  |  |  | + - SH | 2 3 1 | 29 |
|  |  |  |  | + - SH | 2 3 1 | 30 |
|  |  |  |  | + - SH | 2 3 1 | 31 |
|  |  |  |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 17/19 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | From Chan 4 Slot 13 404 Timing Module | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER |  | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |

| SLOT NO.: 20 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| OH Repetition Rate Switch 1 = 300 seconds | pc_acpOHrep_MBBI | ACP Chassis | A65 | F B | BRN TAN | 1B 1A | 1 |
| OH Repetition Rate Switch 1 = 450 seconds | pc_acpOHrep_MBBI | ACP Chassis | A66 | F B | RED TAN | 2B 2A | 2 |
| OH Repetition Rate Switch 1 = 600 seconds | pc_acpOHrep_MBBI | ACP Chassis | A67 | F B | ORN TAN | 3B 3A | 3 |
| TF Instantaneous Ground Current Fault 1 = Fault | pc_tfinstgndflt_MBBI |  | A68 | F B | YLW TAN | 4B 4A | 4 |
| OH Instantaneous Ground Current Fault 1 = Fault | pc_ohinstgndflt_MBBI |  | A69 | F B | GRN TAN | 5B 5A | 5 |
| CHI Instantaneous Ground Current Fault 1 = Fault | pc_chiinstgndflt_MBBI |  | A70 | F B | BLU TAN | 6B 6A | 6 |
| PF1 Instantaneous Ground Current Fault 1 = Fault | pc_pf1instgndflt_MBBI |  | A71 | F B | VIO TAN | 7B 7A | 7 |
| PF2 Instantaneous Ground Current Fault 1 = Fault | pc_pf2instgndflt_MBBI |  | A72 | F B | GRY TAN | 8B 8A | 8 |
| SP1 Instantaneous Ground Current Fault 1 = Fault | pc_sp1instgndflt_MBBI |  | A73 | F B | BRN TAN | 9B 9A | 9 |
| SP2 Instantaneous Ground Current Fault 1 = Fault | pc_sp2instgndflt_MBBI |  | A74 | F B | RED TAN | 10B 10A | 10 |
| SP3 Instantaneous Ground Current Fault 1 = Fault | pc_sp3instgndflt_MBBI |  | A75 | F B | ORN TAN | 11B 11A | 11 |
|  |  |  | A76 | F B | YLW TAN | 12B 12A | 12 |
|  |  |  | A77 | F B | GRN TAN | 13B 13A | 13 |
|  |  |  | A78 | F B | BLU TAN | 14B 14A | 14 |
|  |  |  | A79 | F B | VIO TAN | 15B 15A | 15 |
| NCSX ACP Enable Signal 1 = Enabled | pc_ncsxacp_enable_BI |  | A80 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 21 | MODULE TYPE 409 TIMED GATE |
| --- | --- |

| SIGNAL NAME | PRIMARY PV NAME (may be others) | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DIAMAGNETIC INTEGRATOR GATE, START TRIGGER [CHAN 1 XFMR TRIG INPUT] | pc_409c17n21ch1_ dis_LO | direct FROM 404, SLOT 13, CH 7 OF 8 | --- | F B |  | 1B 1A | 1 |
| [CHAN 2 XFMR TRIG INPUT] |  |  | --- | F B | --- | 2B 2A | 2 |
| [CHAN 3 XFMR TRIG INPUT] |  |  | --- | F B | --- | 3B 3A | 3 |
| [CHAN 4 XFMR TRIG INPUT] |  |  | --- | F B | --- | 4B 4A | 4 |
| [CHAN 1 XFMR OUTPUT] |  |  | --- | F B | --- | 5B 5A | 1 |
| [CHAN 2 XFMR OUTPUT] |  |  | --- | F B | --- | 6B 6A | 2 |
| [CHAN 3 XFMR OUTPUT] |  |  | --- | F B | --- | 7B 7A | 3 |
| [CHAN 4 XFMR OUTPUT] |  |  | --- | F B | --- | 8B 8A | 4 |
| DIAMAGNETIC INTEGRATOR GATE OUTPUT [CHAN 1 OPTO OUTPUT] | pc_409c17n21ch1_ dis_LO | direct to destination (by Marsala) | --- | F B | --- | 9B 9A | 1 |
| [CHAN 2 OPTO OUTPUT] |  |  | --- | F B | --- | 10B 10A | 2 |
| [CHAN 3 OPTO OUTPUT] |  |  | --- | F B | --- | 11B 11A | 3 |
| [CHAN 4 OPTO OUTPUT] |  |  | --- | F B | --- | 12B 12A | 4 |
| [CHAN 1 OPEN COLLECTOR OUT.] |  |  | --- | F B | --- | 13B 13A | 1 |
| [CHAN 2 OPEN COLLECTOR OUT.] |  |  | --- | F B | --- | 14B 14A | 2 |
| [CHAN 3 OPEN COLLECTOR OUT.] |  |  | --- | F B | --- | 15B 15A | 3 |
| [CHAN 4 OPEN COLLECTOR OUT.] |  |  | --- | F B | --- | 16B 16A | 4 |
| [STOP SIGNAL XFMR INPUT] |  |  | --- | F B | --- | 17B 17A | ALL |
| NO SIGNAL |  |  | --- | F B | --- | 18B 18A | --- |

| SLOT NO.: 22 | MODULE TYPE 302 DIGITAL OUTPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Fault RESET Unit2 | pc_pf_FReset_BO WriteBits = 1 |  |  | F B |  | 3B 3A | 1 |
| RESET to ACP Fault Detector Chassis | pc_acpReset_BO |  |  | F B |  | 4B 4A | 2 |
| Fault RESET Unit1 | pc_pf_FReset_BO WriteBits = 4 |  |  | F B |  | 5B 5A | 3 |
|  |  |  |  | F B |  | 6B 6A | 4 |
|  |  |  |  | F B |  | 7B 7A | 5 |
|  |  |  |  | F B |  | 8B 8A | 6 |
|  |  |  |  | F B |  | 9B 9A | 7 |
|  |  |  |  | F B |  | 10B 10A | 8 |
|  |  |  |  | F B |  | 11B 11A | 9 |
|  |  |  |  | F B |  | 12B 12A | 10 |
|  |  |  |  | F B |  | 13B 13A | 11 |
|  |  |  |  | F B |  | 14B 14A | 12 |
|  |  |  |  | F B |  | 15B 15A | 13 |
|  |  |  |  | F B |  | 16B 16A | 14 |
|  |  |  |  | F B |  | 17B 17A | 15 |
|  |  |  |  | F B |  | 18B 18A | 16 |