| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | ---- | 903 32 KW 12-BIT MEMORY [00000] |
| 2 | D65 - D80 | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 32 KW MEMORY, P2 CLOCK SOURCE |
| 3 | ---- | ---- |
| 4 | ---- | ---- |
| 5 | ---- | ---- |
| 6 | ---- | ---- |
| 7 | ---- | ---- |
| 8 | ---- | ---- |
| 9 | ---- | ---- |
| 10 | ---- | ---- |
| 11 | ---- | ---- |
| 12 | ---- | ---- |
| 13 | ---- | ---- |
| 14 | ---- | ---- |
| 15 | ---- | ---- |
| 16 | ---- | ---- |
| 17 | ---- | ---- |
| 18 | ---- | ---- |
| 19 | ---- | ---- |
| 20 | ---- | ---- |
| 21 | ---- | ---- |
| 22 | ---- | ---- |
| 23 | ---- | 000 FACILITY CLOCK REPEATER |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| CHI-PSS-1S-1P CURRENT 8 V = 24 KA (4.99 K IN-LINE RESISTORS DIVIDE INPUT VOLTAGE BY 2) | pc_chi_pss_1s_1p_i | B-4F1005 SH. 620,621 | D65 | + - SH | 2 3 1 | 1 |
| CHI-PSS-2S-1P CURRENT | pc_chi_pss_2s_1p_i | B-4F1005 SH. 620,621 | D66 | + - SH | 2 3 1 | 2 |
| CHI-PSS-1S-1P VOLTAGE 10 V = 1500 VOLTS (DITTO 4.99 K) | pc_chi_pss_1s_1p_v | B-4F1005 SH. 620,621 | D67 | + - SH | 2 3 1 | 3 |
| CHI-PSS-2S-1P VOLTAGE | pc_chi_pss_2s_1p_v | B-4F1005 SH. 620,621 | D68 | + - SH | 2 3 1 | 4 |
| CHI-PSS-1S-2P CURRENT | pc_chi_pss_1s_2p_i | B-4F1005 SH. 622,623 | D69 | + - SH | 2 3 1 | 5 |
| CHI-PSS-2S-2P CURRENT | pc_chi_pss_2s_2p_i | B-4F1005 SH. 622,623 | D70 | + - SH | 2 3 1 | 6 |
| CHI-PSS-1S-2P VOLTAGE | pc_chi_pss_1s_2p_v | B-4F1005 SH. 622,623 | D71 | + - SH | 2 3 1 | 7 |
| CHI-PSS-2S-2P VOLTAGE | pc_chi_pss_2s_2p_v | B-4F1005 SH. 622,623 | D72 | + - SH | 2 3 1 | 8 |
| PF3U-PSS-2S-1P CURRENT | pc_pf3u_pss_2s_1p_i | B-4F1005 SH. 624,625 | D73 | + - SH | 2 3 1 | 9 |
| PF3U-PSS-1S-1P CURRENT | pc_pf3u_pss_1s_1p_i | B-4F1005 SH. 624,625 | D74 | + - SH | 2 3 1 | 10 |
| PF3U-PSS-2S-1P VOLTAGE | pc_pf3u_pss_2s_1p_v | B-4F1005 SH. 624,625 | D75 | + - SH | 2 3 1 | 11 |
| PF3U-PSS-1S-1P VOLTAGE | pc_pf3u_pss_1s_1p_v | B-4F1005 SH. 624,625 | D76 | + - SH | 2 3 1 | 12 |
|  |  | B-4F1005 SH. 627 | D77 | + - SH | 2 3 1 | 13 |
|  |  | B-4F1005 SH. 627 | D78 | + - SH | 2 3 1 | 14 |
|  |  |  | D79 | + - SH | 2 3 1 | 15 |
|  |  |  | D80 | + - SH | 2 3 1 | 16 |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | + - SH | 2 3 1 | 17 |
|  |  |  |  | + - SH | 2 3 1 | 18 |
|  |  |  |  | + - SH | 2 3 1 | 19 |
|  |  |  |  | + - SH | 2 3 1 | 20 |
|  |  |  |  | + - SH | 2 3 1 | 21 |
|  |  |  |  | + - SH | 2 3 1 | 22 |
|  |  |  |  | + - SH | 2 3 1 | 23 |
|  |  |  |  | + - SH | 2 3 1 | 24 |
|  |  |  |  | + - SH | 2 3 1 | 25 |
|  |  |  |  | + - SH | 2 3 1 | 26 |
|  |  |  |  | + - SH | 2 3 1 | 27 |
|  |  |  |  | + - SH | 2 3 1 | 28 |
|  |  |  |  | + - SH | 2 3 1 | 29 |
|  |  |  |  | + - SH | 2 3 1 | 30 |
|  |  |  |  | + - SH | 2 3 1 | 31 |
|  |  |  |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | FROM 404A, CH 0 OF 7 TOK1 : C = 9, N = 22 DEVICE : PCTM-19-1 | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER |  | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |