| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | ---- | 903 32 KW 12-BIT MEMORY [0000] |
| 2 | D65 - D80 | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 64 KW MEMORY, P2 CLOCK SOURCE |
| 3 | ---- | 908 (slot 2 of 3) |
| 4 | ---- | 908 (slot 3 of 3) |
| 5 | ---- | 322 16-BIT DIGITAL INPUT MODULE - ISOLATED CONTACT |
| 6 | ---- | 336 PC LINK REPEATER MODULE |
| 7 | ---- | 337X (SPECIAL) POWER SUPPLY CONTROLLER |
| 8 | C01 - C16 | 337X (slot 2 of 2) |
| 9 | ---- | 337X (SPECIAL) POWER SUPPLY CONTROLLER |
| 10 | C33 - C48 (ODD) | 337X (slot 2 of 2) |
| 11 | ---- | 337X (SPECIAL) POWER SUPPLY CONTROLLER |
| 12 | C17 - C32 | 337X (slot 2 of 2) |
| 13 | ---- | 7064 64 KW 12-BIT MEMORY [0000] |
| 14 | ---- | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 64 KW MEMORY, P2 CLOCK SOURCE |
| 15 | ---- | 908 (slot 2 of 3) |
| 16 | ---- | 908 (slot 3 of 3) |
| 17 | E01 - E16 | 322 16-BIT DIGITAL INPUT MODULE - 5V |
| 18 | E17 - E32 | 322 16-BIT DIGITAL INPUT MODULE - 5V |
| 19 | E33 - E48 | 322 16-BIT DIGITAL INPUT MODULE - 5V |
| 20 | E49 - E64 | 322 16-BIT DIGITAL INPUT MODULE - 5V |
| 21 | E65 - E80 | 322 16-BIT DIGITAL INPUT MODULE - 5V |
| 22 | F01 - F16 | 16-BIT DIGITAL OUTPUT MODULE - 302 RELAY OUTPUTS, MOMENTARY, NORM OPEN |
| 23 | ---- | --- FACILITY CLOCK REPEATER |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| PF2L-PSS-2S CURRENT 8 V = 24 KA (4.99 K IN-LINE RESISTORS DIVIDE INPUT VOLTAGE BY 2) | pc_pf2l_pss_2s_i | B-4F1005 SH. 660,661 | D65 | + - SH | 2 3 1 | 1 |
| PF2L-PSS-1S CURRENT | pc_pf2l_pss_1s_i | B-4F1005 SH. 660,661 | D66 | + - SH | 2 3 1 | 2 |
| PF2L-PSS-2S VOLTAGE 10 V = 1500 VOLTS (DITTO 4.99 K) | pc_pf2l_pss_2s_v | B-4F1005 SH. 660,661 | D67 | + - SH | 2 3 1 | 3 |
| PF2L-PSS-1S VOLTAGE | pc_pf2l_pss_1s_v | B-4F1005 SH. 660,661 | D68 | + - SH | 2 3 1 | 4 |
|  |  | B-4F1005 SH. 662,663 | D69 | + - SH | 2 3 1 | 5 |
|  |  | B-4F1005 SH. 662,663 | D70 | + - SH | 2 3 1 | 6 |
|  |  | B-4F1005 SH. 662,663 | D71 | + - SH | 2 3 1 | 7 |
|  |  | B-4F1005 SH. 662,663 | D72 | + - SH | 2 3 1 | 8 |
| PF3L-PSS-2S-1P CURRENT | pc_pf3l_pss_2s_1p_i | B-4F1005 SH. 664,665 | D73 | + - SH | 2 3 1 | 9 |
| PF3L-PSS-1S-1P CURRENT | pc_pf3l_pss_1s_1p_i | B-4F1005 SH. 664,665 | D74 | + - SH | 2 3 1 | 10 |
| PF3L-PSS-2S-1P VOLTAGE | pc_pf3l_pss_2s_1p_v | B-4F1005 SH. 664,665 | D75 | + - SH | 2 3 1 | 11 |
| PF3L-PSS-1S-1P VOLTAGE | pc_pf3l_pss_1s_1p_v | B-4F1005 SH. 664,665 | D76 | + - SH | 2 3 1 | 12 |
|  |  | B-4F1005 SH. 667 | D77 | + - SH | 2 3 1 | 13 |
|  |  | B-4F1005 SH. 667 | D78 | + - SH | 2 3 1 | 14 |
|  |  | B-4F1005 SH. 667 | D79 | + - SH | 2 3 1 | 15 |
|  |  |  | D80 | + - SH | 2 3 1 | 16 |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | + - SH | 2 3 1 | 17 |
|  |  |  |  | + - SH | 2 3 1 | 18 |
|  |  |  |  | + - SH | 2 3 1 | 19 |
|  |  |  |  | + - SH | 2 3 1 | 20 |
|  |  |  |  | + - SH | 2 3 1 | 21 |
|  |  |  |  | + - SH | 2 3 1 | 22 |
|  |  |  |  | + - SH | 2 3 1 | 23 |
|  |  |  |  | + - SH | 2 3 1 | 24 |
|  |  |  |  | + - SH | 2 3 1 | 25 |
|  |  |  |  | + - SH | 2 3 1 | 26 |
|  |  |  |  | + - SH | 2 3 1 | 27 |
|  |  |  |  | + - SH | 2 3 1 | 28 |
|  |  |  |  | + - SH | 2 3 1 | 29 |
|  |  |  |  | + - SH | 2 3 1 | 30 |
|  |  |  |  | + - SH | 2 3 1 | 31 |
|  |  |  |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 2/4 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | FROM 404A, CH 0 OF 7 C = 11, RACK 653 DEVICE : PCTM-20-1 | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER |  | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |

| SLOT NO.: 6 | MODULE TYPE 336 PC_LINK REPEATER |
| --- | --- |

| DESCRIPTION | CONMMENT | CONT'D DWG |
| --- | --- | --- |
| CONTROL FOR POWER SUPPLY : INTERRUPTER/REVERSING SWITCHES |
| HOUSE ADDRESS (HA) = 31 |  | N/A |
| SUBAGGREGATE HOUSE ADDRESS = NONE |  | N/A |
| PC LINK INPUT |  |  |
| PC LINK OUTPUT |  |  |
| I/O TO POWER SUPPLY CONTROLLER |  |  |

| SLOT NO.: 7/8 | MODULE TYPE 337 POWER SUPPLY CONTROLLER |
| --- | --- |

| DESCRIPTION | CONMMENT | CONT'D DWG |
| --- | --- | --- |
| CONTROL FOR POWER SUPPLY : ____INTERRUPTER OPEN/CLOSE CMDS____ |
| POWER SUPPLY ADDRESS (PSA) = _1_ |  | N/A |
| LINK I/O (UPPER CONNECTOR) |  |  |
| LINK I/O (LOWER CONNECTOR) |  |  |
| SIGNAL NAME | CONT. DWG | CROSS |  | CLR | PIN# | BIT |
| FIRING ANGLE 20 - LSB |  | C1 | F B | BRN TAN | 1B 1A | 1 |
| FIRING ANGLE 21 |  | C2 | F B | RED TAN | 2B 2A | 2 |
| FIRING ANGLE 22 |  | C3 | F B | ORN TAN | 3B 3A | 3 |
| FIRING ANGLE 23 |  | C4 | F B | YLW TAN | 4B 4A | 4 |
| FIRING ANGLE 24 |  | C5 | F B | GRN TAN | 5B 5A | 5 |
| FIRING ANGLE 25 |  | C6 | F B | BLU TAN | 6B 6A | 6 |
| FIRING ANGLE 26 |  | C7 | F B | VIO TAN | 7B 7A | 7 |
| FIRING ANGLE 27 - MSB |  | C8 | F B | GRY TAN | 8B 8A | 8 |
| "CONVERT" MODE |  | C9 | F B | BRN TAN | 9B 9A | 9 |
| "CYCLIC BYPASS" MODE |  | C10 | F B | RED TAN | 10B 10A | 10 |
| "BLOCK BYPASS" MODE |  | C11 | F B | ORN TAN | 11B 11A | 11 |
| SPARE - BIT 12 |  | C12 | F B | YLW TAN | 12B 12A | 12 |
| SPARE - BIT 13 |  | C13 | F B | GRN TAN | 13B 13A | 13 |
| SPARE - BIT 14 |  | C14 | F B | BLU TAN | 14B 14A | 14 |
| SPARE |  | C15 | F B | VIO TAN | 15B 15A | 15 |
| READY |  | C16 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 9/10 | MODULE TYPE 337X SPECIAL POWR SUPPLY CONTROLLR |
| --- | --- |

| DESCRIPTION | CONMMENT | CONT'D DWG |
| --- | --- | --- |
| CONTROL FOR POWER SUPPLY : ____INTERRUPTER START CMDS___ |
| POWER SUPPLY ADDRESS (PSA) = _2__ |  | N/A |
| LINK I/O (UPPER CONNECTOR) |  |  |
| LINK I/O (LOWER CONNECTOR) |  |  |
| SIGNAL NAME | CONT. DWG | CROSS |  | CLR | PIN# | BIT |
| FIRING ANGLE 20 - LSB |  | C33 | F B | BRN TAN | 1B 1A | 1 |
| FIRING ANGLE 21 |  | C34 | F B | RED TAN | 2B 2A | 2 |
| FIRING ANGLE 22 |  | C35 | F B | ORN TAN | 3B 3A | 3 |
| FIRING ANGLE 23 |  | C36 | F B | YLW TAN | 4B 4A | 4 |
| FIRING ANGLE 24 |  | C37 | F B | GRN TAN | 5B 5A | 5 |
| FIRING ANGLE 25 |  | C38 | F B | BLU TAN | 6B 6A | 6 |
| FIRING ANGLE 26 |  | C39 | F B | VIO TAN | 7B 7A | 7 |
| FIRING ANGLE 27 - MSB |  | C40 | F B | GRY TAN | 8B 8A | 8 |
| "CONVERT" MODE |  | C41 | F B | BRN TAN | 9B 9A | 9 |
| "CYCLIC BYPASS" MODE |  | C42 | F B | RED TAN | 10B 10A | 10 |
| "BLOCK BYPASS" MODE |  | C43 | F B | ORN TAN | 11B 11A | 11 |
| SPARE - BIT 12 |  | C44 | F B | YLW TAN | 12B 12A | 12 |
| SPARE - BIT 13 |  | C45 | F B | GRN TAN | 13B 13A | 13 |
| SPARE - BIT 14 |  | C46 | F B | BLU TAN | 14B 14A | 14 |
| SPARE |  | C47 | F B | VIO TAN | 15B 15A | 15 |
| READY |  | C48 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 11/12 | MODULE TYPE 337X SPECIAL POWR SUPPLY CONTROLLR |
| --- | --- |

| DESCRIPTION | CONMMENT | CONT'D DWG |
| --- | --- | --- |
| CONTROL FOR POWER SUPPLY : __REVERSING SWITCHES OPEN/CLOSE CMDS_ |
| POWER SUPPLY ADDRESS (PSA) = __3__ |  | N/A |
| LINK I/O (UPPER CONNECTOR) |  |  |
| LINK I/O (LOWER CONNECTOR) |  |  |
| SIGNAL NAME | CONT. DWG | CROSS |  | CLR | PIN# | BIT |
| FIRING ANGLE 20 - LSB |  | C17 | F B | BRN TAN | 1B 1A | 1 |
| FIRING ANGLE 21 |  | C18 | F B | RED TAN | 2B 2A | 2 |
| FIRING ANGLE 22 |  | C19 | F B | ORN TAN | 3B 3A | 3 |
| FIRING ANGLE 23 |  | C20 | F B | YLW TAN | 4B 4A | 4 |
| FIRING ANGLE 24 |  | C21 | F B | GRN TAN | 5B 5A | 5 |
| FIRING ANGLE 25 |  | C22 | F B | BLU TAN | 6B 6A | 6 |
| FIRING ANGLE 26 |  | C23 | F B | VIO TAN | 7B 7A | 7 |
| FIRING ANGLE 27 - MSB |  | C24 | F B | GRY TAN | 8B 8A | 8 |
| "CONVERT" MODE |  | C25 | F B | BRN TAN | 9B 9A | 9 |
| "CYCLIC BYPASS" MODE |  | C26 | F B | RED TAN | 10B 10A | 10 |
| "BLOCK BYPASS" MODE |  | C27 | F B | ORN TAN | 11B 11A | 11 |
| SPARE - BIT 12 |  | C28 | F B | YLW TAN | 12B 12A | 12 |
| SPARE - BIT 13 |  | C29 | F B | GRN TAN | 13B 13A | 13 |
| SPARE - BIT 14 |  | C30 | F B | BLU TAN | 14B 14A | 14 |
| SPARE |  | C31 | F B | VIO TAN | 15B 15A | 15 |
| READY |  | C32 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 14/16 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| EF1 DIODE TEMP. | EFOH-PDP-TR1-01 |  |  | + - SH | 2 3 1 | 1 |
| EF2 DIODE TEMP. | EFOH-PDP-TR1-02 |  |  | + - SH | 2 3 1 | 2 |
| EF3 DIODE TEMP. | EFOH-PDP-TR1-03 |  |  | + - SH | 2 3 1 | 3 |
| EF4 DIODE TEMP. | EFOH-PDP-TR1-04 |  |  | + - SH | 2 3 1 | 4 |
| EF1 DIODE CURRENT | EFOH-PDP-TR1-05 |  |  | + - SH | 2 3 1 | 5 |
| EF2 DIODE CURRENT | EFOH-PDP-TR1-06 |  |  | + - SH | 2 3 1 | 6 |
| EF3 DIODE CURRENT | EFOH-PDP-TR1-07 |  |  | + - SH | 2 3 1 | 7 |
| EF4 DIODE CURRENT | EFOH-PDP-TR1-08 |  |  | + - SH | 2 3 1 | 8 |
| OH11 DIODE TEMP. | EFOH-PDP-TR1-09 |  |  | + - SH | 2 3 1 | 9 |
| OH12 DIODE TEMP. | EFOH-PDP-TR1-10 |  |  | + - SH | 2 3 1 | 10 |
| WATER TEMP. | EFOH-PDP-TR1-11 |  |  | + - SH | 2 3 1 | 11 |
| TRIP LEVEL TEMP. | EFOH-PDP-TR1-12 |  |  | + - SH | 2 3 1 | 12 |
| EF1 POWER SUPPLY CURRENT | EFOH-PDP-TR1-13 |  |  | + - SH | 2 3 1 | 13 |
| EF2 POWER SUPPLY CURRENT | EFOH-PDP-TR1-14 |  |  | + - SH | 2 3 1 | 14 |
| EF3 POWER SUPPLY CURRENT | EFOH-PDP-TR1-15 |  |  | + - SH | 2 3 1 | 15 |
| EF4 POWER SUPPLY CURRENT | EFOH-PDP-TR1-16 |  |  | + - SH | 2 3 1 | 16 |

| SLOT NO.: 14/16 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| OH1 DIODE TEMP. | EFOH-PDP-TR1-17 |  |  | + - SH | 2 3 1 | 17 |
| OH2 DIODE TEMP. | EFOH-PDP-TR1-18 |  |  | + - SH | 2 3 1 | 18 |
| OH3 DIODE TEMP. | EFOH-PDP-TR1-19 |  |  | + - SH | 2 3 1 | 19 |
| OH4 DIODE TEMP. | EFOH-PDP-TR1-20 |  |  | + - SH | 2 3 1 | 20 |
| OH5 DIODE TEMP. | EFOH-PDP-TR1-21 |  |  | + - SH | 2 3 1 | 21 |
| TRIP LEVEL TEMP. | EFOH-PDP-TR1-22 |  |  | + - SH | 2 3 1 | 22 |
| OH7 DIODE TEMP. | EFOH-PDP-TR1-23 |  |  | + - SH | 2 3 1 | 23 |
| OH8 DIODE TEMP. | EFOH-PDP-TR1-24 |  |  | + - SH | 2 3 1 | 24 |
| OH9 DIODE TEMP. | EFOH-PDP-TR1-25 |  |  | + - SH | 2 3 1 | 25 |
| OH10 DIODE TEMP. | EFOH-PDP-TR1-26 |  |  | + - SH | 2 3 1 | 26 |
| WATER TEMP. | EFOH-PDP-TR1-27 |  |  | + - SH | 2 3 1 | 27 |
| TRIP LEVEL TEMP. | EFOH-PDP-TR1-28 |  |  | + - SH | 2 3 1 | 28 |
| OH1 DIODE CURRENT | EFOH-PDP-TR1-29 |  |  | + - SH | 2 3 1 | 29 |
| OH2 DIODE CURRENT | EFOH-PDP-TR1-30 |  |  | + - SH | 2 3 1 | 30 |
| OH3 DIODE CURRENT | EFOH-PDP-TR1-31 |  |  | + - SH | 2 3 1 | 31 |
| OH4 DIODE CURRENT | EFOH-PDP-TR1-32 |  |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 14/16 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | FROM 404A, CH 1 OF 7 C = 11, RACK 653 DEVICE : PCTM-20-14 | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER |  | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |

| SLOT NO.: 17 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PDP INTEGRATOR STATUS 1 BIT 0 | EFOH-PDP-INT-D1 |  | E1 | F B | BRN TAN | 1B 1A | 1 |
| BIT 1 | EFOH-PDP-INT-D1 |  | E2 | F B | RED TAN | 2B 2A | 2 |
| BIT 2 | EFOH-PDP-INT-D1 |  | E3 | F B | ORN TAN | 3B 3A | 3 |
| BIT 3 | EFOH-PDP-INT-D1 |  | E4 | F B | YLW TAN | 4B 4A | 4 |
| BIT 4 | EFOH-PDP-INT-D1 |  | E5 | F B | GRN TAN | 5B 5A | 5 |
| BIT 5 | EFOH-PDP-INT-D1 |  | E6 | F B | BLU TAN | 6B 6A | 6 |
| BIT 6 | EFOH-PDP-INT-D1 |  | E7 | F B | VIO TAN | 7B 7A | 7 |
| BIT 7 | EFOH-PDP-INT-D1 |  | E8 | F B | GRY TAN | 8B 8A | 8 |
| BIT 8 | EFOH-PDP-INT-D1 |  | E9 | F B | BRN TAN | 9B 9A | 9 |
| BIT 9 | EFOH-PDP-INT-D1 |  | E10 | F B | RED TAN | 10B 10A | 10 |
| BIT 10 | EFOH-PDP-INT-D1 |  | E11 | F B | ORN TAN | 11B 11A | 11 |
| BIT 11 | EFOH-PDP-INT-D1 |  | E12 | F B | YLW TAN | 12B 12A | 12 |
| BIT 12 | EFOH-PDP-INT-D1 |  | E13 | F B | GRN TAN | 13B 13A | 13 |
| BIT 13 | EFOH-PDP-INT-D1 |  | E14 | F B | BLU TAN | 14B 14A | 14 |
| BIT 14 | EFOH-PDP-INT-D1 |  | E15 | F B | VIO TAN | 15B 15A | 15 |
| BIT 15 | EFOH-PDP-INT-D1 |  | E16 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 18 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PDP INTEGRATOR STATUS 1 BIT 0 | EFOH-PDP-INT-D2 |  | E17 | F B | BRN TAN | 1B 1A | 1 |
| BIT 1 | EFOH-PDP-INT-D2 |  | E18 | F B | RED TAN | 2B 2A | 2 |
| BIT 2 | EFOH-PDP-INT-D2 |  | E19 | F B | ORN TAN | 3B 3A | 3 |
| BIT 3 | EFOH-PDP-INT-D2 |  | E20 | F B | YLW TAN | 4B 4A | 4 |
| BIT 4 | EFOH-PDP-INT-D2 |  | E21 | F B | GRN TAN | 5B 5A | 5 |
| BIT 5 | EFOH-PDP-INT-D2 |  | E22 | F B | BLU TAN | 6B 6A | 6 |
| BIT 6 | EFOH-PDP-INT-D2 |  | E23 | F B | VIO TAN | 7B 7A | 7 |
| BIT 7 | EFOH-PDP-INT-D2 |  | E24 | F B | GRY TAN | 8B 8A | 8 |
| BIT 8 | EFOH-PDP-INT-D2 |  | E25 | F B | BRN TAN | 9B 9A | 9 |
| BIT 9 | EFOH-PDP-INT-D2 |  | E26 | F B | RED TAN | 10B 10A | 10 |
| BIT 10 | EFOH-PDP-INT-D2 |  | E27 | F B | ORN TAN | 11B 11A | 11 |
| BIT 11 | EFOH-PDP-INT-D2 |  | E28 | F B | YLW TAN | 12B 12A | 12 |
| BIT 12 | EFOH-PDP-INT-D2 |  | E29 | F B | GRN TAN | 13B 13A | 13 |
| BIT 13 | EFOH-PDP-INT-D2 |  | E30 | F B | BLU TAN | 14B 14A | 14 |
| BIT 14 | EFOH-PDP-INT-D2 |  | E31 | F B | VIO TAN | 15B 15A | 15 |
| BIT 15 | EFOH-PDP-INT-D2 |  | E32 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 19 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PDP INTEGRATOR STATUS 1 BIT 0 | EFOH-PDP-INT-D3 |  | E33 | F B | BRN TAN | 1B 1A | 1 |
| BIT 1 | EFOH-PDP-INT-D3 |  | E34 | F B | RED TAN | 2B 2A | 2 |
| BIT 2 | EFOH-PDP-INT-D3 |  | E35 | F B | ORN TAN | 3B 3A | 3 |
| BIT 3 | EFOH-PDP-INT-D3 |  | E36 | F B | YLW TAN | 4B 4A | 4 |
| BIT 4 | EFOH-PDP-INT-D3 |  | E37 | F B | GRN TAN | 5B 5A | 5 |
| BIT 5 | EFOH-PDP-INT-D3 |  | E38 | F B | BLU TAN | 6B 6A | 6 |
| BIT 6 | EFOH-PDP-INT-D3 |  | E39 | F B | VIO TAN | 7B 7A | 7 |
| BIT 7 | EFOH-PDP-INT-D3 |  | E40 | F B | GRY TAN | 8B 8A | 8 |
| BIT 8 | EFOH-PDP-INT-D3 |  | E41 | F B | BRN TAN | 9B 9A | 9 |
| BIT 9 | EFOH-PDP-INT-D3 |  | E42 | F B | RED TAN | 10B 10A | 10 |
| BIT 10 | EFOH-PDP-INT-D3 |  | E43 | F B | ORN TAN | 11B 11A | 11 |
| BIT 11 | EFOH-PDP-INT-D3 |  | E44 | F B | YLW TAN | 12B 12A | 12 |
| BIT 12 | EFOH-PDP-INT-D3 |  | E45 | F B | GRN TAN | 13B 13A | 13 |
| BIT 13 | EFOH-PDP-INT-D3 |  | E46 | F B | BLU TAN | 14B 14A | 14 |
| BIT 14 | EFOH-PDP-INT-D3 |  | E47 | F B | VIO TAN | 15B 15A | 15 |
| BIT 15 | EFOH-PDP-INT-D3 |  | E48 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 20 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PDP EF PROC STATUS BIT 0 | EFOH-PDP-502-D1 |  | E49 | F B | BRN TAN | 1B 1A | 1 |
| BIT 1 | EFOH-PDP-502-D1 |  | E50 | F B | RED TAN | 2B 2A | 2 |
| BIT 2 | EFOH-PDP-502-D1 |  | E51 | F B | ORN TAN | 3B 3A | 3 |
| BIT 3 | EFOH-PDP-502-D1 |  | E52 | F B | YLW TAN | 4B 4A | 4 |
| BIT 4 | EFOH-PDP-502-D1 |  | E53 | F B | GRN TAN | 5B 5A | 5 |
| BIT 5 | EFOH-PDP-502-D1 |  | E54 | F B | BLU TAN | 6B 6A | 6 |
| BIT 6 | EFOH-PDP-502-D1 |  | E55 | F B | VIO TAN | 7B 7A | 7 |
| BIT 7 | EFOH-PDP-502-D1 |  | E56 | F B | GRY TAN | 8B 8A | 8 |
| BIT 8 | EFOH-PDP-502-D1 |  | E57 | F B | BRN TAN | 9B 9A | 9 |
| BIT 9 | EFOH-PDP-502-D1 |  | E58 | F B | RED TAN | 10B 10A | 10 |
| BIT 10 | EFOH-PDP-502-D1 |  | E59 | F B | ORN TAN | 11B 11A | 11 |
| BIT 11 | EFOH-PDP-502-D1 |  | E60 | F B | YLW TAN | 12B 12A | 12 |
| BIT 12 | EFOH-PDP-502-D1 |  | E61 | F B | GRN TAN | 13B 13A | 13 |
| BIT 13 | EFOH-PDP-502-D1 |  | E62 | F B | BLU TAN | 14B 14A | 14 |
| BIT 14 | EFOH-PDP-502-D1 |  | E63 | F B | VIO TAN | 15B 15A | 15 |
| BIT 15 | EFOH-PDP-502-D1 |  | E64 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 21 | MODULE TYPE 322 DIGITAL INPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PDP OH PROC STATUS BIT 0 | EFOH-PDP-502-D1 |  | E65 | F B | BRN TAN | 1B 1A | 1 |
| BIT 1 | EFOH-PDP-502-D1 |  | E66 | F B | RED TAN | 2B 2A | 2 |
| BIT 2 | EFOH-PDP-502-D1 |  | E67 | F B | ORN TAN | 3B 3A | 3 |
| BIT 3 | EFOH-PDP-502-D1 |  | E68 | F B | YLW TAN | 4B 4A | 4 |
| BIT 4 | EFOH-PDP-502-D1 |  | E69 | F B | GRN TAN | 5B 5A | 5 |
| BIT 5 | EFOH-PDP-502-D1 |  | E70 | F B | BLU TAN | 6B 6A | 6 |
| BIT 6 | EFOH-PDP-502-D1 |  | E71 | F B | VIO TAN | 7B 7A | 7 |
| BIT 7 | EFOH-PDP-502-D1 |  | E72 | F B | GRY TAN | 8B 8A | 8 |
| BIT 8 | EFOH-PDP-502-D1 |  | E73 | F B | BRN TAN | 9B 9A | 9 |
| BIT 9 | EFOH-PDP-502-D1 |  | E74 | F B | RED TAN | 10B 10A | 10 |
| BIT 10 | EFOH-PDP-502-D1 |  | E75 | F B | ORN TAN | 11B 11A | 11 |
| BIT 11 | EFOH-PDP-502-D1 |  | E76 | F B | YLW TAN | 12B 12A | 12 |
| BIT 12 | EFOH-PDP-502-D1 |  | E77 | F B | GRN TAN | 13B 13A | 13 |
| BIT 13 | EFOH-PDP-502-D1 |  | E78 | F B | BLU TAN | 14B 14A | 14 |
| BIT 14 | EFOH-PDP-502-D1 |  | E79 | F B | VIO TAN | 15B 15A | 15 |
| BIT 15 | EFOH-PDP-502-D1 |  | E80 | F B | GRY TAN | 16B 16A | 16 |

| SLOT NO.: 22 | MODULE TYPE 302 DIGITAL OUTPUT |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | F1 | F B | BRN TAN | 3B 3A | 1 |
|  |  |  | F2 | F B | RED TAN | 4B 4A | 2 |
|  |  |  | F3 | F B | ORN TAN | 5B 5A | 3 |
|  |  |  | F4 | F B | YLW TAN | 6B 6A | 4 |
|  |  |  | F5 | F B | GRN TAN | 7B 7A | 5 |
|  |  |  | F6 | F B | BLU TAN | 8B 8A | 6 |
|  |  |  | F7 | F B | VIO TAN | 9B 9A | 7 |
|  |  |  | F8 | F B | GRY TAN | 10B 10A | 8 |
|  |  |  | F9 | F B | BRN TAN | 11B 11A | 9 |
|  |  |  | F10 | F B | RED TAN | 12B 12A | 10 |
|  |  |  | F11 | F B | ORN TAN | 13B 13A | 11 |
|  |  |  | F12 | F B | YLW TAN | 14B 14A | 12 |
|  |  |  | F13 | F B | GRN TAN | 15B 15A | 13 |
|  |  |  | F14 | F B | BLU TAN | 16B 16A | 14 |
|  |  |  | F15 | F B | VIO TAN | 17B 17A | 15 |
|  |  |  | F16 | F B | GRY TAN | 18B 18A | 16 |