| CRATE LAYOUT DESCRIPTION |  |
| --- | --- |

| SLOT | CROSS-CX | MODULE DESCRIPTION & STRAPPING |
| --- | --- | --- |
| 1 | ---- | 59256 256 KW 12-BIT MEMORY [01] |
| 2 | ---- | 59256 256 KW 12-BIT MEMORY [00] |
| 3 | ---- | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 64 KW MEMORY, P2 CLOCK SOURCE |
| 4 | ---- | 908 (slot 2 of 3) |
| 5 | ---- | 908 (slot 3 of 3) |
| 6 | ---- | 59256 256 KW 12-BIT MEMORY [01] |
| 7 | ---- | 59256 256 KW 12-BIT MEMORY [00] |
| 8 | ---- | 32 CHANNEL TYPE 1 TRANSIENT DIGITIZER 908 +/- 5 VOLTS, 64 KW MEMORY, P2 CLOCK SOURCE |
| 9 | ---- | 908 (slot 2 of 3) |
| 10 | ---- | 908 (slot 3 of 3) |
| 11 | ---- | ---- |
| 12 | ---- | ---- |
| 13 | ---- | ---- |
| 14 | ---- | ---- |
| 15 | ---- | ---- |
| 16 | ---- | ---- |
| 17 | ---- | ---- |
| 18 | ---- | ---- |
| 19 | ---- | ---- |
| 20 | ---- | ---- |
| 21 | ---- | 404A 8-CHANNEL TIMING MODULE [ALL E-STOP OFF] |
| 22 | ---- | 404A (slot 2 of 2) |
| 23 | ---- | 313 U-PORT/FACILITY CLOCK REPEATER |
| 24/25 | ---- | 3952 L-2 CRATE CONTROLLER |

| SLOT NO.: 3/5 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| Branch Current Signal 5000 A/V | pc_tf_br_1_cur_1 | HSC-1 Out2Ch1 |  | + - SH | 2 3 1 | 1 |
| Branch Current Signal 5000 A/V | pc_tf_br_2_cur_1 | HSC-1 Out2Ch2 |  | + - SH | 2 3 1 | 2 |
| Branch Current Signal 5000 A/V | pc_tf_br_3_cur_1 | HSC-1 Out2Ch3 |  | + - SH | 2 3 1 | 3 |
| Branch Current Signal 5000 A/V | pc_tf_br_4_cur_1 | HSC-1 Out2Ch4 |  | + - SH | 2 3 1 | 4 |
| Branch Current Signal 5000 A/V | pc_oh_br_1_cur_1 | HSC-1 Out2Ch5 |  | + - SH | 2 3 1 | 5 |
| Branch Current Signal 5000 A/V | pc_oh_br_2_cur_1 | HSC-1 Out2Ch6 |  | + - SH | 2 3 1 | 6 |
| Branch Current Signal 10000 A/V | pc_pf1al_cur_1 | HSC-1 Out2Ch7 |  | + - SH | 2 3 1 | 7 |
| Branch Current Signal 5000 A/V | pc_pf1au_cur_1 | HSC-1 Out2Ch8 |  | + - SH | 2 3 1 | 8 |
| Branch Current Signal 5000 A/V | pc_pf1b_cur_1 | HSC-1 Out2Ch9 |  | + - SH | 2 3 1 | 9 |
| Branch Current Signal 5000 A/V | pc_pf2l_cur_2 | HSC-1 Out2Ch10 |  | + - SH | 2 3 1 | 10 |
| Branch Current Signal 5000 A/V | pc_pf2u_cur_2 | HSC-1 Out2Ch11 |  | + - SH | 2 3 1 | 11 |
| Branch Current Signal 5000 A/V | pc_pf3l_cur_2 | HSC-1 Out2Ch12 |  | + - SH | 2 3 1 | 12 |
| Branch Current Signal 5000 A/V | pc_pf3u_cur_2 | HSC-1 Out2Ch13 |  | + - SH | 2 3 1 | 13 |
| Branch Current Signal 5000 A/V | pc_pf5_cur_2 | HSC-1 Out2Ch14 |  | + - SH | 2 3 1 | 14 |
| Branch Current Signal 10000 A/V | pc_chi_tot_cur_1 | HSC-1 Out2Ch15 |  | + - SH | 2 3 1 | 15 |
| Branch Current Signal 6000 A/V | pc_pf4_cur_1 | HSC-1 Out2Ch16 |  | + - SH | 2 3 1 | 16 |

| SLOT NO.: 3/5 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| Branch Current Signal 5000 A/V | pc_tf_br_1_cur_2 | HSC-2 Out2Ch1 |  | + - SH | 2 3 1 | 17 |
| Branch Current Signal 5000 A/V | pc_tf_br_2_cur_2 | HSC-2 Out2Ch2 |  | + - SH | 2 3 1 | 18 |
| Branch Current Signal 5000 A/V | pc_tf_br_3_cur_2 | HSC-2 Out2Ch3 |  | + - SH | 2 3 1 | 19 |
| Branch Current Signal 5000 A/V | pc_tf_br_4_cur_2 | HSC-2 Out2Ch4 |  | + - SH | 2 3 1 | 20 |
| Branch Current Signal 5000 A/V | pc_oh_br_1_cur_2 | HSC-2 Out2Ch5 |  | + - SH | 2 3 1 | 21 |
| Branch Current Signal 5000 A/V | pc_oh_br_2_cur_2 | HSC-2 Out2Ch6 |  | + - SH | 2 3 1 | 22 |
| Branch Current Signal 10000 A/V | pc_pf1al_cur_2 | HSC-2 Out2Ch7 |  | + - SH | 2 3 1 | 23 |
| Branch Current Signal 5000 A/V | pc_pf1au_cur_2 | HSC-2 Out2Ch8 |  | + - SH | 2 3 1 | 24 |
| Branch Current Signal 5000 A/V | pc_pf1b_cur_2 | HSC-2 Out2Ch9 |  | + - SH | 2 3 1 | 25 |
| Branch Current Signal 10000 A/V | pc_pf2l_cur_1 | HSC-2 Out2Ch10 |  | + - SH | 2 3 1 | 26 |
| Branch Current Signal 10000 A/V | pc_pf2u_cur_1 | HSC-2 Out2Ch11 |  | + - SH | 2 3 1 | 27 |
| Branch Current Signal 5000 A/V | pc_pf3l_cur_1 | HSC-2 Out2Ch12 |  | + - SH | 2 3 1 | 28 |
| Branch Current Signal 10000 A/V | pc_pf3u_cur_1 | HSC-2 Out2Ch13 |  | + - SH | 2 3 1 | 29 |
| Branch Current Signal 10000 A/V | pc_pf5_cur_1 | HSC-2 Out2Ch14 |  | + - SH | 2 3 1 | 30 |
| Branch Current Signal 10000 A/V | pc_chi_tot_cur_2 | HSC-2 Out2Ch15 |  | + - SH | 2 3 1 | 31 |
| Branch Current Signal 6000 A/V | pc_pf4_cur_2 | HSC-2 Out2Ch16 |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 3/5 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | FROM 404A, CH 0 OF 7 TOK1 : C = 17, N = 13 DEVICE : pc_404c17n13ch1_SUB | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER | TO 908 IN SLOT 8/10 | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |

| SLOT NO.: 8/10 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 1-16 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| Branch Current Signal 5000 A/V | pc_pf3l_br_2_cur_1 | HSC-3 Out2Ch1 |  | + - SH | 2 3 1 | 1 |
| Branch Current Signal 5000 A/V | pc_pf3u_br_2_cur_1 | HSC-3 Out2Ch2 |  | + - SH | 2 3 1 | 2 |
| Branch Current Signal 5000 A/V | pc_chi_br_2_cur_1 | HSC-3 Out2Ch3 |  | + - SH | 2 3 1 | 3 |
| Branch Current Signal 5000 A/V | pc_chi_br_1_cur_1 | HSC-3 Out2Ch4 |  | + - SH | 2 3 1 | 4 |
| F_FLSPPU3 |  | HSC-3 Out2Ch5 |  | + - SH | 2 3 1 | 5 |
| F_FLSPPL3 |  | HSC-3 Out2Ch6 |  | + - SH | 2 3 1 | 6 |
| F_L1DMSPPGU3 |  | HSC-3 Out2Ch7 |  | + - SH | 2 3 1 | 7 |
| Plasma Current #1 20 KA/V | pc_plasma_cur_1 | HSC-3 Out2Ch8 |  | + - SH | 2 3 1 | 8 |
| Dummy Load Current | pc_dummy_load_cur | HSC-3 Out2Ch9 |  | + - SH | 2 3 1 | 9 |
| Plasma Current #2 240 KA/V | pc_plasma_cur_2 | HSC-3 Out2Ch10 |  | + - SH | 2 3 1 | 10 |
| NB POWER |  | HSC-3 Out2Ch11 |  | + - SH | 2 3 1 | 11 |
| B_L1DMSPPGL3 |  | HSC-3 Out2Ch12 |  | + - SH | 2 3 1 | 12 |
| PF1AU BR2 CUR 1 (-) 1000 A/V |  | HSC-3 Out2Ch13 |  | + - SH | 2 3 1 | 13 |
| PF1AL BR2 CUR 1 (-) 1000 A/V |  | HSC-3 Out2Ch14 |  | + - SH | 2 3 1 | 14 |
| PF1AU BR1 CUR 1 (+) 5000 A/V |  | HSC-3 Out2Ch15 |  | + - SH | 2 3 1 | 15 |
| PF1AL BR2 CUR 3 INV 5000 A/V |  | HSC-3 Out2Ch16 |  | + - SH | 2 3 1 | 16 |

| SLOT NO.: 8/10 | MODULE TYPE 908 TRANSIENT DIGITIZER, CHS 17-32 |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CX | FCT | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- |
| PC TF Sum Current 20 KA/V | pc_tf_tot_cur |  |  | + - SH | 2 3 1 | 17 |
| PC OH Sum Current 20 KA/V | pc_oh_tot_cur |  |  | + - SH | 2 3 1 | 18 |
| TF/OH/PF1 Fault and PDP Status. Encoded data format.See Marsala/Raki | pc_oh_tf_perm | rack 209, B52 |  | + - SH | 2 3 1 | 19 |
| PF2/PF1 Fault and PDP Status. Encoded data format. See Marsala/Raki | pc_pf1_pf2_perm | rack 209, B53 |  | + - SH | 2 3 1 | 20 |
| PF & RF Fault. Encoded data format. See Marsala/Raki | pc_pf_rf_perm |  |  | + - SH | 2 3 1 | 21 |
| Reserved for a Fault signal. | pc_future_perm |  |  | + - SH | 2 3 1 | 22 |
| NB Fault. Encoded data format. See Marsala/Raki | pc_nb_perm |  |  | + - SH | 2 3 1 | 23 |
| CHI Fault. Encoded data format. See Marsala/Raki | pc_chi_perm |  |  | + - SH | 2 3 1 | 24 |
| PSRTC FAST MODE 5V = FAST 0V = SLOW |  | FIMM Status PAN J2 |  | + - SH | 2 3 1 | 25 |
|  |  |  |  | + - SH | 2 3 1 | 26 |
|  |  |  |  | + - SH | 2 3 1 | 27 |
|  |  |  |  | + - SH | 2 3 1 | 28 |
| D(Itf)/dt |  | Diamagnetic Differentiator B-9D1309 |  | + - SH | 2 3 1 | 29 |
| TF Voltage For Diamagnetics |  | Diamagnetic Summing Amp J4 |  | + - SH | 2 3 1 | 30 |
| TF Current |  | Diamagnetic Summing Amp J5 |  | + - SH | 2 3 1 | 31 |
| Diamag flux |  | Diamagnetic Flux Int. Aout C-9D1306 |  | + - SH | 2 3 1 | 32 |

| SLOT NO.: 8/10 | MODULE TYPE 908 TRANSIENT DIGITIZER, CLK/TRIG |
| --- | --- |

| SIGNAL NAME | CONT. DWG | FCT | PIN# |
| --- | --- | --- | --- |
| TRIGGER INPUT - UPPER | FROM 908 IN SLOT 3/5 | + - SH | 2 3 1 |
| TRIGGER INPUT - LOWER |  | + - SH | 2 3 1 |
| CLOCK INPUT - UPPER |  | + - SH | 2 3 1 |
| CLOCK INPUT - LOWER |  | + - SH | 2 3 1 |

| SLOT NO.: 21/22 | MODULE TYPE 404A TIMING MODULE |
| --- | --- |

| SIGNAL NAME | DEVICE ID | CONT. DWG | CROSS |  | CLR | PIN# | CH |
| --- | --- | --- | --- | --- | --- | --- | --- |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 1B 1A | CE |
| START TRIGGER FOR CRATE 16, N=3&8 908 TRANSIENT DIGITIZER |  | 908 TRIG INPUT |  | F B | RED TAN | 2B 2A | 1 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 3B 3A | CE |
|  |  |  |  | F B | YLW TAN | 4B 4A | 2 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 5B 5A | CE |
|  |  |  |  | F B | BLU TAN | 6B 6A | 3 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 7B 7A | CE |
|  |  |  |  | F B | GRY TAN | 8B 8A | 4 |
| CLEAN EARTH |  |  |  | F B | BRN TAN | 9B 9A | CE |
|  |  |  |  | F B | RED TAN | 10B 10A | 5 |
| CLEAN EARTH |  |  |  | F B | ORN TAN | 11B 11A | CE |
|  |  |  |  | F B | YLW TAN | 12B 12A | 6 |
| CLEAN EARTH |  |  |  | F B | GRN TAN | 13B 13A | CE |
|  |  |  |  | F B | BLU TAN | 14B 14A | 7 |
| CLEAN EARTH |  |  |  | F B | VIO TAN | 15B 15A | CE |
|  |  |  |  | F B | GRY TAN | 16B 16A | 8 |