NSTX Boundary Physics 5 year plan outline – 7/13/07

R. Maingi

## H-mode pedestal, ELMs, fueling, and power threshold

- What sets the H-mode pedestal widths, e.g transport, stability or fueling?

- How can the pedestal be optimized in NSTX?

- Does the pedestal limit core performance in NSTX?

- Is there a correlation between pedestal and global performance in NSTX?

- How does the pedestal in an ST compare with models of the pedestal, i.e. fully identify the role of aspect ratio?

- Can Enhanced Pedestal H-mode be extended to long pulse?

- Should identify the role of shape on pedestal and ELMs

- Need additional edge Thomson channels

- Need improved ERD spatial and time resolution

- Additional 3-color USXR capability would give fast, spatially resolved Te by cross-calibration with Thomson

- To attack the fueling problem, neutral density measurements/interpretation at multiple poloidal locations might be needed

- Given the edge fueling source, the edge transport properties can be computed with TRANSP (see transport section)

- Tighter coupling to neoclassical theory desired – find as many connections to XGC calculations – need to develop the ideas here

- What determines the ELM regime, e.g transport, stability or fueling?

- Are there steady small ELM regimes? How to extrapolate?

- Are small ELM regimes common across tokamaks and ST’s?

- In general, NSTX seems to have lower toroidal mode number than tokamaks and even MAST – specifically the Type V ELM has n=1-2 only. What is the underlying instability?

- Attack the problem with M3D?

- Tighter coupling to neoclassical theory desired – XGC recently upgraded with ELITE edge stability code coupling

- What role do error fields play?

- Active control requires additional EFC coils and/or research to develop and verify algorithms across all shapes

- Internal coils being considered for RMP control of ELMs as well as adding to the RWM research

- Optimal placement being modeled with help from GA, i.e. location relative to passive plates or vacuum vessel wall

- Assessment of required currents in progress, and results to be included in document

- May also help to spread out heat flux – must be connected to next section

- What is the role of Scrape-off layer current in determining the ELM stability?

- Need to install a tile current monitoring system (poloidal and toroidal)

- If currents are high and predictable by theory to affect edge stability, then consider addition of localized biasing hardware

- Does the fueling method affect plasma performance in an ST?

- H-mode access seems to be much easier with center stack (HFS) gas puffing than LFS fueling in STs than tokamaks – what is the physics reason behind the difference?

- Quantify fueling efficiency and performance with various gas puffing techniques (including SGI with various nozzles and other upgrades) vs. center stack fueling vs. deuterium pellets

- Should we consider CT fueling research, given the ITER approval?

- CT injector is in storage on-site at PPPL, cost is to retro-fit onto NSTX and then resources to run a program

- Role of neutral density values vs, scale length, etc?

- Need fueling upgrades (SGI, pellets, CTs?), plus improved edge diagnostics above

- Power threshold studies – here we can special items add to existing worldwide effort

- Quantify the role of shape, e.g. triangularity and X-point height

- Compare with recent models (XGC)

- Need to implement algorithm for obtaining a 2-D neutral density profile in X-point region, e.g. collaboration with W. Meyer (LLNL)

- Need to verify Ip and Bt dependencies as that will be important for extrapolation to next step STs

# SOL and divertor physics themes

- Liquid lithium test in diverted machine with hot SOL

- Test to see if better core confinement, reduced Zeff, improved edge stability, reduced recycling and neutral fueling at fixed external rate

- Demonstrate that density can be reduced in the flat top

- Investigation of impurity sources and transport with Li PFC

- Quantify pumping efficiency of Lithium – partly for FY09 milestone

- Density reduction vs. e.g. evaporation rate, number of LiTERs used, temperature of liquid lithium, etc.

- Comparison with simple models, e.g. vs. Lithium surface area, vs. 2-chamber 0-D model

- Comparison with 2-D models, e.g. UEDGE predictions by Stotler

- Study hydrogenic retention by Lithium – partly for FY09 milestone

- Gas balance during discharges – present capability

- Gas balance between discharges, with and without HeGDC

- Identify role and optimum duration of HeGDC

- Wall coupons for long term film thickness composition

- Possible DiMES-like probe for controlled sample exposures

- Shot by shot changes to film thicknesses with Quartz Micro-balance

- Requires upgrade of test Penning gauge near pump port to quantify exhaust during HeGDC

- Study divertor regimes, divertor heat flux handling, and X-point MARFE formation with lithium pumping and strong lithium radiation.

- Compare different Lithium delivery methods: powder, pellets, molten Li

- Lithium tray in ‘09, need new diagnostics and to retro-fit existing diagnostics

- IR cameras with known emissivity problems – need a solution (several ideas: dedicated tile gaps, looking at the back side of a tile spectroscopically, thermocouples, Langmuir probes)

- Desire for large toroidal coverage of tray means that divertor diagnostics will be packed into small toroidal gaps – pushes toward smart tile solutions with many diagnostics integrated into single tile

- May require implementaton of rtEFIT/isoflux strike point control algorithms for power flux control

- Additional, DOLLOP-like Lithium aerosol delivery systems

- Future decision point to determine if advanced Lithium tray or cryopump needed – end FY 11

- What sets the SOL width, i.e. role of turbulence, gyro-motion, flows, and transient events?

- Turbulence studies beginning to make comparisons with analytic theory (Myra) and desire more complex theory comparison

- First step in understanding the turbulence, i.e. comparing with models, and more advanced step is controlling it, e.g. with biasing

- Existing models predict 1-2mm for midplane heat flux SOL width; qmid from divertor IR~ 6-10mm when far from detachment – why do ST’s look so different? Is critical parameter minor radius, not major radius?

- How do the heat flux widths compare with ne, Te, and Gamma widths at the midplane, e.g. from reciprocating probe?

- Can simple models reproduce the trends?

- How does a more complex model predict the SOL width dependencies, e.g. GEM (B. Scott) or BOUT (X. Xu)

- Extrapolation to NHTX requires well-characterized PNBI dependence (6 MW -> 40 MW), Ip (1.2 MA -> 3.5 MA), and Bt (0.5 T -> 1.9 T), e.g. experimental plan

- What is the role of SOL flows in setting the SOL width?

- Need many more diagnostics

- Divertor Thomson (+ 2-D JHU imaging system for ne, Te?)

- Fully implemented divertor bolometry

- more divertor Langmuir probes,

- fast IR camera,

- X-point reciprocating probe,

- densely packed diagnostic “smart” tiles,

- divertor GPI,

- div. Penning gauge,

- div. Imaging spectrometer

- Edge and divertor flow diagnostic continued development, e.g. SWIFT from S. Paul

- ST divertor physics and heat flux amelioration

  - How does an ST divertor extrapolate, e.g. which is the correct parameter: P/R, q||, and/or q(?

- What is role of magnetic balance, divertor volume, private flux region?

- Need 2-D divertor measurements of ne, Te, Prad (divertor Thomson and/or divertor USXR system, divertor imaging spectrometer), and maybe neutral density measurements

- Is a radiative or detached divertor compatible with good E in NSTX? Seems to be so in high triangularity discharges; what about low delta?

- Improved outer divertor detachment may require

- more closed geometry,

- with divertor target shape and passive plate modifications and

- reduction of midplane/divertor vacuum conductance

- How important is the private flux region in determining the SOL? This issue may be important for the ITER dome physics.

- Integration of radiative divertor regimes, obtained with deuterium or impurity injection, with main plasmas (confinement, MHD, ELM, stability).

- Can/should we test the X-divertor concept?

- How much improved control of the heat flux profile does this provide, given that we can generate high flux expansion without them?

Need internal hardware to make X-divertor, plus additional divertor diagnostics as listed above

- How does a lithium-coated plate or a lithium tray handle high heat flux

- What are the divertor regimes obtained with lithium pumping and strong lithium concentration in the divertor region?

- SOL and/or divertor biasing

- Existing biasing electrodec

- May need additional hardware for divertor biasing

- MARFE studies

  - MARFE formation and operational space in various configurations (LSN, DN)

  - MARFE models - presently observe very low Te and high ne which is not explained by “classical” radiative instability” models

  - Develop models for the observed MARFE dynamics

- Where are impurity sources? What is role of sources and transport in setting Zeff? Role of Dust?

- Need impurity injection and testing system, like DIII-D DiMES

  - SOL transport and turbulence

    - Use available SOL and divertor measurements to infer transport using multi-fluid edge transport codes (UEDGE) or kinetic edge transport codes (XGC, TEMPEST) together with neutral transport (DEGAS 2)

    - Use edge turbulence codes (BOUT, Bruce Scott, XGC) to model existing diagnostic measurements (fast cameras, GPI, edge reflectometry, fast UCSD probe)

    - From the modeling, obtain time-averaged transport coefficients and turbulence characteristics related to particle (hydrogenic and impurity) transport

    - Continue with blob transport studies both experimental (fast cameras, GPI) and analytic theories of blob formation and transport (Lodestar)

    - Experimental studies of SOL flows?

  - Need SOL flow diagnostic (SWIFT or divertor imaging spectrometer)