Transport and Turbulence for Five Year Plan

Extended Outline

S. Kaye  7/12/07

- Motivation and Introduction

  - NSTX provides unique opportunities

    - Collisionality similar to conventional R/a, but extended  range

    - Enhanced toroidicity and natural shaping leads to reduced microturbulence

    - Low BT, near Mach flow gives large ExB shear and reduced microturbulence

    - Electromagnetic effects, high trapped particle fraction

    - Ability to measure electron scale turbulence locally

  - NSTX results extend and stress theory

    - Many computational tools will be brought to bear

    - Stress computational resources due to importance of high-k modes

      - pedaflop, multi-processors required

    - Test whether scale separation in gyrokinetic calcs is appropriate

    - Extensive Verification and Validation planned at all levels of the primacy hierarchy

  - Lays foundation for comprehensive understanding and predictive capability to allow discharge scenario development in both NSTX and in future devices (NHTX, ST-CTF, ARIES-ST)

    - Determine regimes in which plasma profiles for current drive and fusion production are optimized

    - Confident extrapolation of transport and turbulence properties to ensure that confinement requirements can be satisfied at high Pin/PLH, P/R

    - Understand and extrapolate momentum transport in order to assure adequate rotation, ExB shear for suppression of microturbulence, MHD modes respectively

- Energy Transport

  - Motivation

    - Critical to the success of high performance plasmas

    - Understand electron vs ion transport and sources

    - Extrapolate to future devices

  - NSTX is an excellent laboratory in which to study electron transport

    - Dominant electron heating, as in ITER, NHTX (?), ST-CTF (?)

    - Electron transport anomalous, ions near neoclassical in H

    - Localized electron scale turbulence measurable (re~0.1 mm)

    - Strong rotational shear that can influence transport

  - Objective is to develop comprehensive picture of energy transport for both electrons and ions

    - Profile diagnostics, transport analysis (TRANSP) yield power fluxes, thermal diffusivities

      - Fluctuation diagnostics across entire range of kperp (ion to electron scale)

    - Linear and non-linear gyrokinetic calculations for determining the unstable microinstabilities and their characterisitics

    - Verification and Validation of models and codes will eventually lead to a high confidence predictive tool for extrapolation to future devices

      - Build synthetic diagnostics into codes to mirror actual diagnostics

      - Comparisons between theory and experiment at all levels of the “primacy hierarchy”

        - Fluctuation spectra

          - Primary: synthetic diagnostics in codes to give T, n, and cross-phase

          - Secondary: Zonal Flow characteristics; k, f spectra

        - Local transport: thermal diffusivities

        - Global trends: confinement scalings

    - Transport and Turbulence inexorably tied to one another

      - Integrate into single coherent plan

  - Global Confinement

    - Results

      - Dedicated confinement studies have revealed global trends in NSTX that differ from those at conventional aspect ratio

        - BT, Ip scalings (Fig. 1)

        - Beta scaling as a function of shape/ELMS (Fig. 2, 3)

          - High-priority ITPA issue

        - Trends have been established; turn to local analysis for understanding source of trends

    - Plans

      - Most of experimental focus will be on local transport and turbulence; global confinement studies as needed

      - FY09-10

        - R/a scaling within NSTX to optimize NHTX design/scenarios

      - FY12-13

        - Verify scaling trends at very high Pinput/PLH when second beam brought on line

  - Ion Transport

    - Results

      - Ions close to neoclassical in H-mode plasmas

      - Do not exhibit scaling with BT, but responsible for Ip scaling – comparison to GTC-NEO results (Fig. 4)

      - Ion transport can be anomalous during L-phase, dropping to neo after transition to H

        - Consistent with linear GS2 results (Fig. 5)

        - Non-linear GTC calcs show neoclassical fluxes greater than ITG induced fluxes (in agreement)

        - Expect further suppression of low-k due to high ExB shear

      - Ion transport reduced in RS plasmas

      - Ion transport barrier physics

        - Strong Ti gradients associated with regions of near zero toroidal and poloidal velocity (Fig. 6)

        - Strong evidence for neoclassical orbit shrinking/squeezing

    - Plans: Objective is to develop predictive capability by end of Five Year Plan

      - FY09-10

        - Continue study of ion energy transport – determine under what conditions ions are governed by neoclassical transport vs electrostatic vs electromagnetic turbulence induced transport

          - Couple RF to NBI to change Ti/Te damping term for ITG in L- and H-mode

          - Fast CHERS (?) to infer ion transport in OH, RF plasmas with Te/Ti>1 using NBI blip to measure Ti

          - Control of ExB shear: use RMP to slow plasma down and decrease ExB suppression of ITG – at what level does the ITG grow and ions become anomalous?

          - Use Doppler reflectometry to assess role of Zonal Flows at plasma edge

          - Couple results to gyrokinetic calculations, using v, v, grad p to determine full Er

        - Continue studies of orbit squeezing/shrinking to determine operating conditions under which this occurs

          - Potential for improved performance with development of ITB

          - Validation of neoclassical theory at low R/a

          - Relation to integer q-values, current profile, Zonal Flows at edge

      - FY11-13

        - Assess relation of inferred ion thermal diffusivity to low-k fluctuations throughout plasma using BES

        - Couple results to gyrokinetic calculations (coupled high-k / low-k simulations)

        - Assess non-local nature of turbulence due to large 

        - Verify ion transport at high beam power (second beam line)

        - Continue studies of transport barrier physics at high beam power

          - Relate to changes in low-k fluctuations

      - FY13

        - Assess ion transport in OH, RF heated plasmas with Ti/Te<1 using non beam based Ti measurement (Imaging X-ray Crystal Spectrometer)

  - Electron Transport

    - Results

      - Electron transport anomalous in both L- and H-mode plasmas

      - Governs BT scaling  (Fig. 7)

      - Gyrokinetic simulations indicate ETG can be important in some cases (Fig. 8)

        - Consistent with high-k measurements (Fig. 9)

      - Theory indicates that microtearing may also be important within some range of collisionality

        - Electron transport reduced with RS

        - Core reduction related to narrowing of k-range unstable to microtearing

        - Predicted non-linear ETG heat flux consistent with TRANSP calculation result outside RS region (Fig. 10)

      - Critical gradient physics experiments just started

        - Make use of HHFW to change grad Te

        - Measure change in high-k	(Fig. 11)

    - Plans

      - Because of relatively large re in NSTX, electron-scale turbulence can be measured

        - NSTX’s particular strength is for testing ETG and short wavelength CTEM turbulence

        - Scannable, highly localized kr measurement

        - SXR arrays can be used to image electron temperature fluctuations

        - Can isolate anomalous electron turbulence from neoclassical ions in H-modes; makes non-linear gyrokinetic ETG simulations with adiabatic ions and scale separation possible

      - Goal is to develop comprehensive picture of electron transport for predictive capability by end of 5 YR Plan

      - FY09-10

        - Continue identification of TEM, ETG using present high-kr system

          - Perform collisionality scans to differentiate modes

          - Determine critical gradient for high-k turbulence experimentally using HHFW to change grad Te in fine steps

          - Address role of RS, low order rational q, in development of electron ITBs

            - Reduction in CTEM dur to precession reversal?

            - Vary driving terms such as magnetic shear, density grad beta, Te/Ti

          - V&V of codes/theory

            - Build synthetic diagnostics into g-k codes

            - Role of microtearing

          - Effect of Zonal Flows at edge w/Doppler reflectometry

      - FY10-11

        - Test electron transport and turbulence modification using local deposition of EBW @ 200 kW level

          - Include early application to modify q-profile and possibly induce ITB formation

          - Test turbulent spreading outside critical gradient region with scannable high-k

            - Relate to ExB shear layer and variation in magnetic shear

          - Use modulated EBW to probe local critical gradient phsyics, with response to pulses measured by SXR and upgraded MPTS

            - Mary need to combine several shots with different MPTS timing to get complete evolution

          - First k measurements from high-k; couple with low-k from BES

          - In conjunction with gyrokinetic calculations

      - FY12-13

        - Studies of electron transport with full kr, kq coverage, higher input power (second beamline)

          - High-kq, BES, Microwave Imaging Reflectometry covers full k-range (Fig. 12)

          - Allows for much more comprehensive V&V across all-k

        - Utilize high power EBW system (2 MW) for localized deposition and heating to probe

          - Critical gradient physics

          - Turbulence spreading

        - Probe mode structure of higher-k fluctuations for identification

          - TEM, ETG strongly ballooning outside (high-B side density fluctuations?)

          - Modes highly dispersive: ky scan of frequency

          - Radial streamers from ETG

        - Experimental identification of microtearing modes

          - E-M modes that are extended along field line

          - Require internal B-field fluctuation measurements

- Particle Transport

  - Motivation

    - Particle transport not well understood at present

    - Fertile area for analysis

      - Aids in understanding of microturbulent vs neoclassical transport of ions (complementary to energy transport studies)

      - Can study Helium transport, relating to He ash issue on ITER

    - Much data already exists

      - Analysis can proceed immediately

      - Diagnostic and facility enhancements will aid studies

    - NSTX unique in terms of high mirror ratio is SOL (high trapped particle fraction), extend collisionality, q, beta ranges

  - Results

    - Limited to studies of impurity transport in beam-heated H-mode plasmas

    - Neon-injection into MHD quiescent plasmas

    - Use tangential SXR with multi-foil capability for energy discrimination

    - MIST simulations of synthetic SXR diagnostic of He, H-like and higher energy Neon	(Fig. 13)

    - Indicates core D~1 m2/s~neoclassical		(Fig. 14)

    - Indicates low level of turbulent ion transport, consistent with power balance inferences

  - Plans

    - FY09-11

      - Assess transport in core, within NBI-fueling regime (r/a<0.55) using TRANSP

        - NBI fueling source dominant in this regime

        - Understand systematic variation of D’s with power, current, BT, etc from pre-existing dataset

        - Relation of Ds to s	(Fig. 15)

          - Are there the same parametric dependences?

        - L- vs H- (particles may be driven by turbulent transport in L, as thermal ion heat flux seems to be)

      - Density peaking study, in conjunction with ITPA

        - Impact for ITER, ST-CTF reactivity

        - Extend range of q, beta, etc in database

        - L- vs H-modes

        - Relation to particle pinch

      - Modulated core fueling with beam blips

        - Will have to build up evolution from numerous discharges

        - Use amplitude/phase analysis to determine taup*

        - Determine D, vpinch from data

          - Compare to particle balance value (TRANSP)

          - Compare to theory

      - Assess transport outside r/a=0.55, which is dominated by wall fueling/recycling

        - Need to determine ionization source using combination of codes

          - Iteration between codes (SOLPS/UEDGE, DEGAS2/EIRENE) to provide 2D ionization source (forward modeling)

          - Input D, c, R, no, etc

          - Match profiles ne, Te,.. at midplane; ne, Te, heat flux, … at target plate, 2D divertor radiation profiles

          - Input parameters to Monte-Carlo codes to determine plasma-neutral source profiles

          - Iterate until convergence, when global particle balance is achieved

        - TRANSP to compute Ds with these source profiles across full plasma radius

          - Assess sensitivities to core fueling

          - Assess sensitivities and variations from SOL flows for core and wall fueling profiles

      - Impurity transport

        - Assess with impurity puffing, pellet injection at edge

          - Done with SXR or CHERS

          - SXR requires extensive modeling (MIST) and assumptions to deduce D, vpinch

          - Difficult to separate D, vpinch in MIST

          - CHERS more straightforward, but would require

            - Faster CHERS would be helpful (~1 ms temporal resolution)

            - Change in grating for measuring different impurities

          - Can separated D, Vpinch in a straightforward manner using known perturbative impurity source

      - Helium transport

        - Needed for assessment of integrated scenarios in future devices

        - Assess with He puffing or in He plasmas

        - Requires change in CHERS grating to measure emission from He transitions

        - He plasmas can give steady-state D

        - He puffing can give D, vpinch near edge

        - Need to determine He edge source fueling rate: use edge plasma and neutrals code, as in above

      - Effect of LLD on particle transport

    - FY11-13

      - Assess role of low-k turbulence in controlling core particle transport

        - Newly implemented BES

        - Variation of density fluctuations with D/Dneo

          - L vs H

          - High vs low density (collisionality effect)

          - RS vs non RS (q-profile effect)

      - Continue modulated core transport studies

        - Take advantage of upgraded MPTS

        - Higher beam power

      - Continue edge particle transport studies

        - Modulated fueling

          - SGI puffs

          - Pellet fueling with  D pellet injector

          - Take advantage of upgraded MPTS

      - Continue impurity transport studies

        - Take advantage of fast CHERS

      - Continue Helium transport studies

        - Assess core effects with change of NBI system

          - Run beams in Helium

      - Verify particle transport characteristics at higher beam power

      - Effect of Lithium wall conditioning on particle, impurity and He transport: how do D, vpinch change?

- Momentum Transport

  - Motivation

    - Rotation in NSTX with NBI is high

      - Leads to strong ExB shearing, which can suppress low-k microturbulence

    - Important for suppression of MHD modes (internal and external), achieving high performance goals in NSTX, future devices

    - Want to understand source of this rotation

      - How momentum diffusivity relates to electron and ion energy (and particle) diffusivities

      - Conventional R/a, i due to ITG modes

      - NSTX not true, do not scale either

        - f neoclassical?

        - Due to ITG suppression?

      - Understand effect of rotation, ExB shear on energy and particle confinement

      - Study intrinsic rotation (no NBI source)

  - Results

    - Steady-state  obtained from TRANSP calcs for H-modes

    - Statistical studies show i are unrelated; do not scale (Fig. 16)

    -  from dedicated scans scales better with electrons than ions	(Fig. 17)

    - Dedicate momentum confinement studies use perturbations of v from RMP blips	(Fig. 18)

    - Infer , vpinch after RMP turn off when NBI is only known torque

      - >>E,  model~ mom. Balance	(Fig. 19)

      - , vpinch also inferred	(Fig. 20)

    - NTV theory torque from RMP consistent with dL/dt      (Fig. 20)

  - Plans

    - FY09-10

      - Continue RMP studies inferring , vpinch at RMP turn off under different discharge conditions

        - Relate to theory

          - Peeters Coriolis effect

          - Hahm B-drift, thermoelectric effect

      - Deduce , vpinch from time of RMP on

        - Estimate RMP torque from NTV theory

        - Consistent with post RMP-values?

        - Does NTV theory provide a consistent picture? Is it extrapolatable to other, future devices?

      - L- vs H- steady-state determination of 

        - Is i recovered in L when ITG not suppressed and neo?

      - Edge Zonal Flows with Doppler Reflectometry

        - L-mode plasmas

        - Dependence on discharge parameters (q, …)

    - FY11-13

      - Continue rotation modulation studies using RMP

        - Fast CHERS allows phase/amplitude analysis with series of RMP blips

      - Relation of low-k fluctuations from BES with momentum transport in L- and H-modes

      - Zonal Flow/GAM studies using BES

        - Coupling to other microinstabilities

        - Bicoherence analysis

        - Effect on transport

      - Begin study of intrinsic rotation using fast CHERS (non-perturbing beam blip into OH, RF plasmas

    - FY13

      - Continue intrinsic rotation studies using imaging X-ray crystal spectrometer (non-beam-based diagnostic)

- Tools and Modeling

  - Present tools

    - TRANSP for transport analysis

    - Embryonic pTRANSP for predictive transport analysis, discharge scenario development (need good, benchmarked transport model relevant to low R/a)

    - Linear and non-linear gyrokinetic analysis

      - GTC-NEO – finite banana width, non-local effects for neoclassical

      - GS2 flux tube – kinetic electron/ions, finite beta, gen. Geo

      - GYRO – global, contains all features

      - GEM – U. of Colorado collaboration, being tested for low-k (microtearing), global code that contains all features

        - High-k, kinetic electron version not yet working

      - GTC – global, still under development for high-k, finite beta to explore electron scale modes (and ion modes without scale separation)

  - Plans: Use all tools at disposal, with eye towards V&V at all levels

    - FY09-10

      - 2D/3D neutrals package implemented in TRANSP to aid in particle transport studies

      - pTRANSP used to validate predictive models such as those given by TGLF

      - GTC-NEO upgraded with multiple species will be utilized to test neoclassical theory with v measurements

      - GYRO simulations with synthetic diagnostics over full range of k

      - GTC simulations with kinetic electrons and synthetic diagnostics for high-k will begin

        - Multi-ion species capability

      - GEM simulations for low-k (microtearing)

        - Develop version with kinetic electrons

      - Couple GTC-NEO with non-linear calcs (GYRO, GTC) to evaluate neoclassical and non-diffusive turbulent flux (pinch and residual stress) or toroidal angular momentum

    - FY11

      - Initial comparisons of gyrokinetic codes with synthetic diagnostics and BES on NSTX

        - Role of Zonal Flows and relation and coupling to low-k turbulence

      - pTRANSP simulations getting more sophisticated as plasma transport properties more fully understood and physics-based

      - Begin tests of turbulence spreading using results from local EBW deposition experiments – comparison with code predictions

    - FY12

      - Predict scalings of ion and electron heat, and particle transport with respect to dimensionless variables at different radii with realistic profiles

        - Use gyrokinetic analysis with full features, collisions, turbulence spreading, etc.

        - TGLF-type codes

        - Compare to expt. Results (part of V&V)

    - FY13

      - Fully predictive simulation capabilities will continue to be developed

        - Combine with other simulations (e.g., MHD) to form fully integrated scenario development package

        - Use as a basis for developing actual expt’l discharge scenarios in NSTX and in future devices

- Facility and Diagnostic Upgrades

  - FY09

    - Additional MPTS edge channels

    - Full poloidal CHERS for poloidal velocity

    - Full FIDA for beam deposition profiles for power balance

    - High-k backscattering

  - FY10

    - Filters for CCD cameras for He recycling profiles

    - Fast CHERS (?)

    - Extra channels for ERD (edge toroidal and poloidal rotation)

    - Low power ECH/EBW system

  - FY11

    - High-kq measurement

    - MPTS upgrade to 45 channels, 100 Hz

    - BES

    - Second neutral beam

  - FY12

    - Initial high power EBW

    - Divertor Thomson Scattering

  - FY13

    - Microwave imaging reflectometer (MIR)

    - Imaging x-ray crystal spectrometer

Internal-B fluctuation measurements (TBD)

MSE

UCLA reflectometry