## Slide 1: Proposed NSTX-U operational goals are to: operate at full forces (IPIP, IPBT, BTBT) in 2 years, full coil heating in 3rd year
Table based on assessment of physics needs for first year of operations.
1st year goal: operating points with forces 1/2 the way between NSTX and NSTX-U, ½ the design-point heating of any coil:
  OH FZ apparently requires full influence matrices for essentially ANY operations.
2nd year goal: full field and current, but still limiting the coil heating.
  Of course, will revisit year 2 parameters once year 1 data has been accumulated.
3rd year goal: full capability
 | NSTX | Year 1 NSTX-U | Year 2 NSTX-U | Year 3 NSTX-U | Ultimate Goal
IP [MA] | 1.4 | 1.6 | 2.0 | 2.0 | 2.0
IPIP [MA2] | 2.0 | 2.5 | 4.0 | 4.0 | 4.0
BT [T] | 0.55 | 0.8 | 1.0 | 1.0 | 1.0
BTBT [T2] | 0.3 | 0.65 | 1.0 | 1.0 | 1.0
IPBT [MA*T] | 0.61 | 1.3 | 2 | 2.0 | 2
Allowed I2t Fraction On Any Coil | 1.0 | 0.5 | 0.75 | 1.0 | 1.0
IP Flat-Top at max. allowed I2t, IP, and BT [s] | ~0.7 | ~3.5 | ~3. | 5 | 5