| Appendix A - Table I. NSTX Measurement Capabilities – May 2011 (black – routine operation, blue – under active development) |
| --- |
| Physics Measurement | Typical range and coverage | Spatial; Temporal Resolution | Typical Precision | Available Diagnostic Techniques | Comment | Contact |
| Coil currents |  | follow pulse shape. | 0.5% | Rogowski coil on buswork; Hall effect transducers at power supplies | For EFIT/LRDFIT equilibrium reconstruction | S. Gerhardt – PPPL |
| Plasma current, Ip, |  | 0.1 ms | 1.0% | 2 Rogowski coils around plasma outside vacuum vessel | For EFIT/LRDFIT reconstruction | S. Gerhardt – PPPL |
| Equilibrium Poloidal Field and Flux |  | Variable spatial resolution 5 kHz sampling rate | 1-3% | 2D and 3D solenoids (Mirnov coils) inside vv, flux loops inside and outside vv | For EFIT/LRDFIT reconstruction | S. P. Gerhardt-PPPL |
| Plasma Equilibrium Reconstruction |  | 10 mm absolute 1 ms | 3 mm with RTEFIT |  | Between shot analysis with the EFIT code; post-experiment analysis with EFIT and LRDFIT | S. Sabbagh – CU, J. Menard-PPPL |
| Plasma kinetic energy | > 10 kJ | 1 ms | 1 kJ | diamagnetic loop | EFIT/LRDFIT constraint, uses TF coil | M. Bell - PPPL |
| Electron density line integrals | >2x1011 cm-2 | 4 MHz | 2x1011 cm-2 | tangential interferometry, polarimetry (FIReTIP) | FIR laser with retro-reflectors in 4 tangential chords (2 additional under dev) | K. C. Lee – UC Davis |
|  |  | TBD (probably ~2 MHz) |  | 1 mm radial polarimeter (configured as an interferometer) | 1 mm, with retroreflection from center stack | S. Kubota - UCLA |
| Electron density profile | 5x1011 - 5x1014 cm-3 | 3.0 cm core, 0.9 cm edge, 2 30 Hz lasers | >3% | Thomson scattering | 60 Hz Nd:YAG, laser nearly radial on horizontal midplane, 42 of 48 channels implemented | B. LeBlanc, A. Diallo – PPPL |
|  | 2x1012– 3.5x1013 cm-3 | Up to 200 kHz, 21398 sweeps | ≤ 1 cm | reflectometry FM/CW | 13 – 53 GHz swept | S. Kubota - UCLA |
|  | 0.02-1.6x1013 cm-3 | 1 kHz |  | reflectometry (SOL) | 6 - 36 Ghz swept system, 1 kHz sweep rate | J. Wilgen - ORNL |
| Real time density for density feedback control | >2x1011 cm-2 | 5kHz | 2x1011 cm-2 | tangential interferometry, polarimetry (FIReTIP) | Two fringe counter signals from mid-radius channel (Ch3: Rt=85 cm) | K. C. Lee – UC Davis |
| Electron temperature profile | 0.003 – 5 keV | 3.0 cm core, 0.9 cm edge, 2 30 Hz lasers | >3% | Thomson Scattering | 2 - 30 Hz Nd:YAG lasers nearly radial on horizontal midplane, 42 of 48 possible spatial channels implemented | B. LeBlanc, A. Diallo – PPPL |
|  | 0.1-5 keV | 1 cm, < 10 kHz | 5% (rel) | tangential multi-color sxr arrays | 5 color/ 20 spatial channels, AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  |  |  |  | imaging horizontal x-ray crystal spectrometer | vertical profile (30 cm, requires Ar injection, spherical crystal, upgraded to PILATUS II solid state detectors | M. Bitter, K. Hill – PPPL |
| Ion temperature profile | 0.02 – 5.0 keV | 3.0 cm core, 0.5 cm edge, 10 ms | ≥ 2% | toroidal CHERS | 51 channels system using C VI with heating beam, dedicated background view | R. Bell, M.Podestà – PPPL |
|  |  | 3.0 cm edge only, 10 ms | ≥ 2% | edge Doppler spectroscopy | 7 channels from tangential view and 6 channels from vertical view of outer midplane edge. Uses intrinsic C III and He II. | R. Bell, M.Podestà – PPPL |
|  | 0.2 – 5.0 keV | 2.5 cm, 5 ms | ≥ 5% | scanning neutral particle analysis | horizontal and vertical scan, profile requires vertical scan, L-mode beam heated discharges only | S. Medley - PPPL |
|  |  | 5 cm, 20 ms |  | imaging horizontal x-ray crystal spectrometer | see above | M. Bitter, K. Hill - PPPL |
| Plasma rotation profile | -100 km/s to +300 km/s | 3.0 cm core, 0.5 cm edge, 10 ms | ≥ 2% | toroidal CHERS | see above | R. Bell, M.Podestà – PPPL |
|  |  | ~ 3.0 cm edge only, 10 ms | ≥ 2% | edge Doppler spectroscopy | see above | R. Bell, M.Podestà – PPPL |
|  |  | 1.6 cm core, 0.6 cm edge, 10 ms |  | poloidal CHERS | up and down views of heating beam and dedicated background views, 75 active channels using C VI with heating beam. | R. Bell, M.Podestà – PPPL |
|  |  | ~ 3.0 cm, 10 ms |  | edge Doppler spectroscopy | see above | R. Bell, M.Podestà – PPPL |
|  | -100 km/s to +300 km/s | 4 radial channels; up to 5kHz sampling rate |  | Real-time toroidal CHERS | 4 channels measuring C VI, active and passive (background) views, fast acquisition and analysis for real-time velocity data | M.Podestà, R. Bell – PPPL |
|  | 1.0-2.0 x1013cm-3 | 2 MHz BW |  | correlation reflectometry | 28.5-40 GHz, 2 channels, configured for poloidal correlation | S. Kubota - UCLA |
| B field pitch (for determination of q(R) using LRDFIT or EFIT) |  | 3 cm core, 2 cm edge, 10 ms (target 5 ms) | ≥ 0.2° | motional Stark effect based on collisionally-induced- fluorescence (MSE/CIF) | 18 channels, presently applies correction for toroidal rotation, requires heating beam source A. | H. Yuh, F. Levinton – Nova Photonics |
|  |  | target - 3 cm core, 2 cm edge, 10 ms | target ≥ 0.2° | motional Stark effect based on laser-induced-fluorescence (MSE/LIF) using DNB | requires compact, radial DNB | J. Foley, F. Levinton – Nova Photonics |
|  |  | TBD (probably ~2 MHz) |  | 1 mm radial polarimeter | provides line integral constraint, in conjunction with electron density profile input | S. Kubota - UCLA |
| Magnetic field pitch angle fluctuations |  | 3 cm core, 2 cm edge, 5 ms | >0.2° | motional Stark effect based on collisionally-induced- fluorescence (MSE/CIF) | 18 channels implemented, presently applies correction for toroidal rotation, requires heating beam source A. | J. Foley, F. Levinton – Nova Photonics |
| B field magnitude, P(R) |  | 5 cm core, 2 cm edge, 10 ms | >5 Gauss | motional Stark effect based on laser-induced-fluorescence (MSE/LIF) using DNB | requires compact, radial DNB | J. Foley, F. Levinton – Nova Photonics |
| Profile of the radial Electric field |  | 5 cm core, 2 cm edge, 10 ms |  | MSE/CIF and MSE/LIF | see above; requires heating source A and DNB | F. Levinton, H. Yuh, J. Foley - Nova Photonics |
|  |  | 3.0 cm core, 0.5 cm edge, 10 ms |  | toroidal and poloidal CHERS | see above; requires heating beam | R. Bell, M.Podestà – PPPL |
|  |  | 3.0 cm, 10 ms |  | edge Doppler spectroscopy | may need helium | R. Bell, M.Podestà – PPPL |
| Radiation profile |  | 8 cm, 0.2 ms |  | toroidal bolometer array | tangential view, 16 channel AXUV diode array | S. Paul - PPPL |
|  | Divertor radiation profile | 8 cm, 5 ms |  | divertor bolometers | 20 gold foil bolometers: 8 viewing divertor radially from outside, 8 viewing divertor from top, and 4 viewing down from midplane | S. Paul - PPPL |
|  | Lower divertor area | 1-2 cm, 10-20 kHz |  | Divertor radiometer (bolometer) array, can be used with Ly-alpha filter | Vertical view, 20 channel AXUV diode array | V. Soukhanovskii - LLNL |
| Zeff |  | line integral | 10% abs. | visible continuum sensor | single filterscope chord, RTAN~60 cm, (= | C. Skinner - PPPL |
|  |  | 3.0 cm core, 0.5 cm edge, 10 ms | ≥ 5% in (Zeff-1) | toroidal CHERS | see above, assumes C only impurity | R. Bell, M.Podestà – PPPL |
| Impurity concentrations | C+5 conc. | 3.0 cm core, 1.0 cm edge, 10 ms | 20% abs. | toroidal CHERS | see above | R. Bell, M.Podestà – PPPL |
|  | H/D ratio, detachment signature, line emission | Integral; 10 ms | 5% (rel) | Visible (VIPS 2) survey spectrometer | 10 sightlines coupled via fiber to 0.5 M Czerny-Turner; 3500-11000Å, CCD detector. NIR capability (8000-22000Å) under development. | V. Soukhanovskii - LLNL |
|  | O/C ratio, impurity influx | Integral; 15 ms | 5% (rel) | VUV (SPRED) survey spectroscopy | 100 – 1100Å with 2 gratings, radial midplane view, microchannel plate with CCD readout | C. Skinner, S. Paul - PPPL |
|  | Z≥3 ions (Li, B, C, O, Cu, Ne, Ar, Fe, Kr, Mo) | 5 cm; 5 ms for impurities | 15% abs | filtered poloidal soft x-ray arrays | 2 horizontal arrays (32 ch); discrete AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  |  | 1 cm, < 10 kHz | 5% (rel) | tangential multi-color sxr arrays | 5 color/ 20 spatial channels, AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  |  | r/a~0.08, 10 ms | 15% abs | TGI spectrometer | 12 chord transmission grating imaging spectrometer; 10Å – 300Å CCD camera | K. Tritz, D. Clayton – JHU |
|  |  | Integral; 12 ms | 5% (rel) | EUV spectrometer (XUES) | Flat field grazing incidence spectrometer covering 10-60 Å | P. Beiersdorfer-LLNL |
|  |  | Integral; 12 ms | 5% (rel) | EUV spectrometer (LoWEUS) | Flat field grazing incidence spectrometer covering 60-220 Å | P. Beiersdorfer-LLNL |
| Low (m,n) MHD modes, sawteeth, locked modes, and disruption precursors | B/B = 10-4 – 10-1, (0,0)<(m,n) < (5,10) | poloidal DC – 250 kHz toroidal DC – 2 MHz |  | low frequency Mirnov coils outside plasma | 12 toroidal | E. Fredrickson, S. P. Gerhardt - PPPL |
|  |  | n=1,2&3 RWM Detection |  | Toroidal arrays of BP and BR sensors inside the vessel. | Used for both n=1 RWM feedback and Dynamic Error Field Correction, and offline analysis | S. P. Gerhardt-PPPL |
|  |  | 5 cm; < 300kHz bw |  | filtered poloidal sxr arrays | 2 horizontal arrays (32 ch); discrete AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  |  | 1 cm, < 10 kHz | 5% (rel) | tangential multi-color sxr arrays | 5 color/ 20 spatial channels, AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  |  | 4 cm, < 200 kHz. 1 cm, < 60 kHz |  | fast tangential soft x-ray pinhole camera | uses various foils and apertures, phosphor and demagnifying image tube with Phantom Camera (typ 96 x 96 pixels) | D. Battaglia – ORNL |
|  | >2x1011 cm-2 | 4MHz | 2x1011 cm-2 | tangential interferometry, polarimetry (FIReTIP) | FIR laser with retroreflectors in 4 tangential chords (2 additional) | K. C. Lee – UC Davis |
|  |  | TBD (probably ~2 MHz) |  | 1 mm radial polarimeter (OR configured as an interferometer) | 1 mm, with retroreflection from center stack | S. Kubota - UCLA |
|  | 1.1-7.0 x1013cm-3 | 2.5 MHz BW |  | quadrature reflectometer | 30-75 GHz, 16 channels | S. Kubota - UCLA |
|  |  | 500 kHz |  | Neutron scintillator array | plastic scintillators with PM tubes 1- ZnS; 3 BC400 | L. Roquemore - PPPL |
| High frequency instabilities (MHD, fast ion modes) | B/B ≥ 10-3 to 10-7, n = 0 – 30 | 5 MHz | Toroidal and poloidal | Mirnov coils outside plasma | 3-BT in toroidal array, and 8-BP in toroidal array, 4-BP in poloidal array | E. Fredrickson – PPPL |
|  |  | 5 cm; < 300kHz bw |  | filtered poloidal sxr arrays | 2 horizontal arrays (32 ch); discrete AXUV diode arrays | K. Tritz, D. Clayton – JHU |
|  | 1.1-7.0 x1013cm-3 | 2.5 MHz BW |  | quadrature reflectometer | 30-75 GHz, 16 channels | S. Kubota - UCLA |
|  | >2x1011 cm-2 | 500 kHz | 2x1011 cm-2 | tangential interferometry, polarimetry (FIReTIP) | FIR laser with retroreflectors in 4 tangential chords (2 additional) | K. C. Lee – UC Davis |
|  |  | TBD (probably ~2 MHz) |  | 1 mm radial polarimeter (OR configured as an interferometer) | 1 mm, with retroreflection from center stack | S. Kubota - UCLA |
| Disruption Halo Currents | 0-200 A | 10x20cm tiles, 0.1 msec resolution |  | Lower Outboard Divertor Shunt Tile Array | 6 tiles in each of row 3 and 4 of the lower outboard divertor, for a total of 12 | S.P. Gerhardt, PPPL |
|  | 0-80 kA | 90 Degrees toroidal, 0.5 msec |  | LLD Ground Strap Rogowskis | Each LLD tray is single point grounded with a flexible copper strap; the rogowski is mounted on that strap. |  |
| Core turbulence | 1.0-2.0 x1013cm-3 | 2 MHz BW |  | correlation reflectometry | 28.5-40 GHz, radial or poloidal correlation | S. Kubota - UCLA |
|  | 2x1012– 3.5x1013 cm-3 | Up to 200 kHz, 21398 sweeps | ≤1 cm | reflectometry FM/CW | 13 – 53 GHz swept; radial correlation length; broad-kr backscattering | S. Kubota - UCLA |
|  |  | -20 cm-1<kr<20 cm-1, (R ~ 5 cm | (n/n >0.1% | high-k scattering | tangential microwave scattering at (= 1 mm, 5 detector channels viewing r/a ~ 0.3-0.8 | Y. Ren, E. Mazzucato - PPPL |
|  | kI <1 | (R ~2 cm; 120 cm < R< 150 cm | (n/n >0.1% | Beam Emission Spectroscopy | 2 arrays viewing heating beams with 2-D (radial and poloidal) array of 32 detector channels | D. Smith, G. McKee - UW |
|  |  | TBD (probably ~2 MHz) |  | 1 mm radial polarimeter (OR configured as an interferometer) | 1 mm, with retroreflection from center stack | S. Kubota - UCLA |
|  | 1.1-7.0 x1013cm-3 | 2.5 MHz BW |  | quadrature reflectometer | 30-75 GHz, 16 channels | S. Kubota - UCLA |
|  |  | ~ 1 cm for r/a> 0.8, <400 kHz |  | gas puff imaging | Supported by gas puff manifold. Various fast cameras used | S. Zweben – PPPL |
| Edge recycling and impurity influx |  | 2 kHz |  | filterscopes | 5 upper divertor, 5 lower divertor, 12 midplane CS. filters include H(,(,( , CII, CIII, LiI, BII | V. Soukhanovskii – LLNL, T. Gray, R. Maingi – ORNL, C. Skinner - PPPL |
|  |  | 0.03-0.2 ms/frame |  | 1D CCD cameras | 2 lower divertor, 1 midplane, 1 upper divertor | V. Soukhanovskii – LLNL |
|  |  | 1 kHz or higher |  | Divertor Imaging Spectrometer - DIMS | 19 sightlines coupled via fiber to 0.61m Czerny-Turner; 3500-11000Å, CCD detector. NIR capability (8000-22000Å) under development. Ion temperature measurements (Doppler spectroscopy) under development. | V. Soukhanovskii - LLNL |
|  | 380-590 nm range 1.0 Ǻ/pixel dispersion | 2.5 cm chord views of LLD, Mo and ATJ tiles. 1 kHz |  | Compact Spectrometer Array (CSA) | Three medium optical resolution (0.43 nm) f/4 Czerny-Turner spectrometers. Absolute intensity calibrated. Simultaneous monitoring of divertor D, He, C, CD, C2, Li and Mo emissions. | A. McLean - ORNL |
|  |  | Up to 100kHz At 256x208 |  | wide angle divertor fast cameras | Top view of lower divertor from Bay E (Phantom 710) and Bay J (Phantom 7.3). Equipped with narrow bandpass filters | F. Scotti, L. Roquemore - PPPL |
|  |  | 6 ms, 128x128 |  | ENDD | Tangential view of outer midplane edge - CII filter | F. Scotti - PPPL |
| Dust monitoring |  | few seconds | sens. 1(g/cm2 | electrostatic grid detector | biased fine pitch PC grid, pulse counting electronics, Bay C bottom | C. Skinner - PPPL |
| First wall deposition |  | 2 sec continuous | few Angstroms | quartz microbalances | four QMBs (Bay H top, Bay H bottom, Bay I midplane, Bay B midplane), 3 shuttered, Inficon XTM/2 | C. Skinner - PPPL |
| Surface chemical state and composition | <1 micron | Outboard lower divertor. Single location intershot |  | Materials Analysis Particle Probe (MAPP) utilizes multiple surface-science measurement techniques to characterize a sample material exposed to NSTX conditions | Thermal Desorption Spectroscopy (TDS), X-ray Photoelectron Spectroscopy (XPS), Low energy Ion Secondary Scattering (LEISS), and Direct Recoil Spectroscopy (DRS) | J. P. Allain - Purdue |
| Target Langmuir probes | 1 – 40 eV 1017 – 1020 m-3 | ~2 mm electrode heads at various locations, 1-10 ms sweep resolution |  | Classical interpretation yields ne, Te, V. Non-local interpretation yields additional Vp and EEDF | Flush-mount probes embedded in carbon or molybdenum tiles (2 inner div and various CS) 99-electrode high-density Langmuir probe array at outer divertor with 5 mm spatial resolution | M. Jaworski - PPPL |
| Fusion source profile |  |  |  | Si diode detectors | 2-channel prototype being tested; 8 channels planned | W. Boeglin – Florida Int’l U |
| Neutron flux monitors |  | 1 ms | 5% rel. 25% abs. | fission chambers | 2 U235 detectors with x26 sensitivity ratio | L. Roquemore - PPPL |
|  |  | 0.2 (s | <5% rel. | scintillator detectors | plastic scintillators with PM tubes 1- ZnS; 3 BC400 | L. Roquemore - PPPL |
| Core RF waves | 2x1012– 3.5x1013 cm-3 | Up to 45 kHz, 4064 sweeps | ≤1 cm | reflectometry FM/CW | 13 – 53 GHz swept, some modifications required from standard profile reflectometry | S. Kubota - UCLA |
| RF driven surface waves |  |  |  | high-frequency Langmuir probe | located between antenna segments, | R. Wilson – PPPL, J. Wilgen - ORNL |
| Gas pressure at several locations |  |  |  | Penning gauges | 1 in lower divertor, 1 in upper divertor, 1 in pumping duct with spectroscopy, 1 below lower divertor with spectroscopy | R. Raman – U. Wash |
|  |  |  |  | micro-ion gauges | Bays E and C-midplane, Bay L-pumping duct, Bay C-top | R. Raman – U. Wash |
| Gas composition in vacuum vessel | typ A = 1-50/100, ∆A=1 | Approx. 1 min./1 sec. mass sweep | 10-11 /10-9 torr typical sens. | 2 Residual gas analyzers (continuous monitoring/after discharge measurements) | In Bay L pumping duct, differentially pumped system | W. Blanchard - PPPL |
| Runaway electrons |  | 10 ms | 30% | hard X-ray detector | at start-up and thermal quench | L. Roquemore, K. Hill - PPPL |
| First wall filtered visible images | Phantom MIRO2 | >256x256 | 10 bit | 5.5 kHz at 32x16 | cameras share various views: top view of lower divertor tangential view of lower divertor fish eye radial view of entire plasma 3 tangential midplane views including one view near pellet port view of gas puff manifold along B field | L. Roquemore,. F. Scotti, S. Zweben - PPPL |
|  | Phantom 7.3-2048 | >32x32 | 14 bit | 190 kHz at 32x32 |  |  |
|  | Phantom V4 | >64x64 | 8 bit | 50kHz at 64x64 |  |  |
|  | Phantom MIRO4 | >64x64 | 8 bit | 60 kHz at 64x64 |  |  |
|  | Phantom V710 | >64x64 | 12 bit | 200 kHz at 128x128 |  |  |
| First wall temperature | 20-700°C | 30 Hz 15° FOV 7 mm/pixel | 5°C abs <1°C rel | Standard frame rate, single-band infrared cameras | Two FLIR Omega 8-12 μm LWIR (bolometer cameras (160x128 pixels) with views of upper and lower divertors. | T. Gray, R. Maingi - ORNL |
|  | 50-800°C | 1.6 kHz 12° FOV 5 mm/pixel | 5% typical | Fast, dual-band infrared camera | SBFP ImagIR HgCdTe camera (128x128 pixels). Bay H top viewing lower divertor at Bay G, H, I (R=0.2 to 1.0 m). Calibrated to 4-6 μm (MWIR) / 7-10 μm (LWIR) intensity ratio. | A. McLean, J.-W. Ahn - ORNL |
|  | 20-800°C | 30 Hz 40° FOV 4 mm/pixel >180° view of strike points | 5% typical | Wide-angle, two-color infrared camera | FLIR Tau 640 (bolometer camera (640x480 pixels). Re-entrant view of lower divertor from Bay H top (R=0.2 to 1.2 m). Calibrated to 8-10 μm (LWIR) / 10.5-13 μm (LWIR) intensity ratio. | A. McLean, R. Maingi - ORNL |
|  | 20-1200°C | 30 Hz 18° FOV 2 mm/pixel | 5°C abs <1°C rel | Standard frame rate, single-band infrared camera | FLIR Tau 640 8-13 μm LWIR (bolometer camera (640x480 pixels). View from Bay B midplane of RF antenna straps at Bay D, E, and F. | P. Ryan, R. Maingi - ORNL |
|  | 0-2300°C | 1 kHz 2 locations, 2 mm isolation | 3% typical | Fast ‘eroding’ thermocouples | Pair of high speed Type C eroding thermocouples at PFC surface. Located at R=0.64 and 0.70 m in the Gap H tile 1. | A. McLean, R. Maingi - ORNL |
| Vacuum Vessel Illumination |  |  |  | 3 in-vessel tungsten filaments, ~ 25x5 mm helical | Provide lighting of the first-wall surfaces, Bays G and K near midplane, Bay K/L above midplane | H. Kugel - PPPL |
| Fast Lost Ions |  |  |  | FLIP | radial array of Faraday cups | D. Darrow - PPPL |
|  |  | 50 kHz | 2° 3 cm | SFLIP | scintillator probe with energy and pitch angle resolution | D. Darrow - PPPL |
| Fast ion dynamics | n < 5x1013 cm-3 | 10ms, 5cm, 10keV |  | s-FIDA - Spectrometer/CCD (energy resolved signal) | Vertical views from bay A/B. Tangential views from bay L/F. Based on active charge-exchange spectroscopy: requires NB injection; MPTS and CHERS data needed for analysis | A. Bortolon, W.W. Heidbrink – UCI |
|  |  | 20us, R=100, 120,140cm |  | f-FIDA - Band-Pass Filter/PMT (energy-integrated signal) |  | A. Bortolon, W.W Heidbrink – UCI |
| Fast ion distribution | 1-100 keV | 2 msec | rel 5% abs. x2 | scanning NPA | horizontal and vertical spatial distribution | S. Medley – PPPL |
|  | 35 – 100 keV | 1 msec counting window |  | solid state NPA | 4 chords RTAN= 60, 90, 100, 120 cm, Si- diodes in current mode, with 0.15( Al foils and apertures, <1MHz sample rate | A. Bortolon, W.W. Heidbrink - UCI |

| Appendix A - Table II. Systems Capable of Supporting Active Diagnostics – May 2011 (black – routine operation, blue – under active development, red – EXAMPLES of potential future diagnostics) |
| --- |
| System | Purpose of system | Characteristics | Used in diagnostic: | Contact |
| Heating Neutral Beam | Provide neutral population to produce beam emission for various diagnostics | D, 90 - 100 keV, ~50cm V x 20cm H, ~ 150mA/cm2 neutrals entering plasma | CHERS, MSE, MSE/LIF, BES (D) | T. Stevenson - PPPL |
| Diagnostic Neutral Beam | Provide excited neutral atoms for intensity and polarimetry measurement | H, 40 keV, 1 - 2 cm dia., 30 mA neutrals entering plasma | MSE/LIF | J. Foley, F. Levinton – Nova Photonics |
| Supersonic Gas Injector | Provides low divergence, high pressure gas jet | Laval nozzle, on midplane probe | thermal atomic beam spectroscopy | V. Soukhanovskii - LLNL |
| Gas Puff Manifold | Provides neutral atoms to highlight edge density turbulence | linear manifold ( to edge B field, multiple 1 mm dia holes, D, He or Ar. | gas puff imaging | S. Zweben - PPPL |
| TAE antenna | Excite stable Alvén waves to measure linear damping | 5-turn radial loop antenna, ≤ 1 kW | Fast Mirnov Coil | E. Fredrickson - PPPL |
| BEaP probes | Measure density, potential and electron temperature at LLD diagnostic tiles | 5 radial probes at Bay E and Bay K, digitized at 200 kHz | evaluates effect of BEaP electrodes on local SOL plasma | S. Zweben - PPPL |