## Slide 1
Diagnostics supporting advanced global mode stabilization studies
NSTX
Supported by
V1.0
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
NFRI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
S.A. Sabbagh1, J.W. Berkery1 J.M. Bialek1, T.E. Evans2, S.P. Gerhardt3, Y.S. Park1, K. Tritz4
1Department of Applied Physics, Columbia University, NY, NY
2General Atomics, San Diego, CA
3Plasma Physics Laboratory, Princeton University, Princeton, NJ
4Johns-Hopkins University, Baltimore, MD
NSTX-U Facility Enhancement Brainstorming Meeting
February 8th, 2012
PPPL

## Slide 2: Some new diagnostics would significantly enhance proposed MHD stability studies
Magnetic
  Low frequency MHD sensors over a wider poloidal range
    Midplane: for global mode/RWM diagnosis – are our eigenfunction expectations from MHD correct, especially during mode growth? WIll internal sensors show key difference compared to external LMD?
    Closer to divertor: diagnose, and perhaps feed back upon the “divertor” mode with the NCC
    Direct use in RWM state space controller: for both physics studies of the observer model, and improved control – defined needs for ITER, etc.
Kinetic
  SXR sensors for global mode feedback
    Magnetic sensors problematic in future high neutron environments
    Typically aimed at RWM – still a major application. Proposed before for NSTX (JHU), but not funded
    Also use in real-time to detect internal (global) kinks - using NBI, plasma rotation as actuators to alter mode stability in feedback; disruption detection

## Slide 3: Multi-mode RWM computation shows 2nd eigenmode component has dominant amplitude at high bN in NSTX stabilizing structure
NSTX RWM not stabilized by wf
  Computed growth time consistent with experiment
  2nd eigenmode (“divertor”) has larger amplitude than ballooning eigenmode
NSTX RWM stabilized by wf
  Ballooning eigenmode amplitude decreases relative to “divertor” mode
  Computed RWM rotation ~ 41 Hz, close to experimental value ~ 30 Hz
ITER scenario IV multi-mode spectrum
  Significant spectrum for n = 1 and 2
dBn from wall, multi-mode response
dBn RWM multi-mode composition
ideal eigenmode number
dBn amplitude (arb)
t = 0.655s
mode 1
mode 2
2.0
1.0
0.0
R(m)
1.0
-1.0
Z(m)
2.0
0.0
-2.0
mode 3
q
133775
mode
1
mode
3
mode
2
Unstable
Stabilized by rotation
BP9.00059 J. Bialek, et al.; see poster for detail
mmVALEN code
bN = 6.1