## Slide 1: Point-Source Helicity Injection Startup
Capabilities are being explored for NSTX-U…
  ~1 MA startup plasma, appropriate for OH, NBI, and/or RF sustainment
  Well-defined startup procedures and plasma development scenarios
  Unobtrusive and retractable injection hardware
Pegasus results are evolving the conceptual design:
  Arc gun needed to generate the “seed” plasma
  Formation of the poloidal field null is sensitive the geometry
  Outer-PF induction provides finite Volt-seconds
  Passive electrodes may be the optimum tool for providing maximum effective Volt-seconds with high Taylor limit for Ip
  Electrodes and guns require different fuelling → active gas control
  Local limiters mitigate impurities (Pegasus Zeff ≤ 2 during HI; ~1 in OH)

## Slide 2: Conceptual design for the NSTX-U startup system
Gun/electrode injector:
  Single 8+ inch port off midplane
  Retractable behind gate valve
  Combines gun with large electrode
  Piezoelectric gas control
  Local limiter structure
Power supplies:
  Bias comparable to Pegasus (1-2 kV; 15 kA; Dt ~ 1 ms)
  Arc plasma uses simple PFN supply
Robust operating scenarios
  Especially null formation and Ip buildup
  Pegasus experiments informing and validating scenario development