## Slide 1
NSTX-U 5 Year Plan for Macroscopic Stability
J. Berkery (Columbia University)
J.-K. Park, A. Boozer,
S.A. Sabbagh, S. Gerhardt, R. Raman,
J.M. Bialek, K. Kim, J. Menard
for the NSTX Research Team
NSTX-U 5 Year Plan Review
LSB B318, PPPL
May 21-23, 2013
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Macroscopic stability group will provide the physics basis for long-pulse sustainment
Poloidal sensors (Bp)
Radial sensors (Br)
Stabilizer
plates
Uniqueness of NSTX/NSTX-U:
  high β above no-wall limit, high rotation with strong NTV braking
Accomplishments in NSTX:
  EF correction; RWM active control
  Comparison of kinetic RWM stabilization theory to experiments
  NTV physics for magnetic braking
  Disruption prediction algorithm and halo current measurements
Midplane control coils
  n = 1 – 3 error field correction
  Magnetic braking of ωφ by NTV
  n = 1 active RWM control with: combined Br and Bp PID control or model-based RWM state-space (RWMSC) active control

## Slide 3: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Demonstrate 100% non-inductive sustainment at performance that extrapolates to ≥ 1MW/m2 neutron wall loading in FNSF
Access reduced n* and high-b combined with ability to vary q and rotation to dramatically extend ST physics understanding
Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas

## Slide 4: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
    Resistive wall mode (RWM) active control
    New non-axisymmetric control coils (NCC) and enhanced magnetic sensors
    MHD mode stability physics
Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas

## Slide 5: Dual-component PID (Br + Bp) and model-based RWM state-space (RWMSC) active control will enable long pulse, high β operation
Year 1 of 5 year plan (2014):
  Expand/analyze RWMSC for 6 coil control and n>1 physics
Years 4 & 5:
  Utilize model-based active control with the new NCC to demonstrate improved global MHD mode stability and very low plasma disruptivity, producing highest-performance, longest-pulse plasmas
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWMSC
Years 2 & 3:
  Establish Br + Bp active control capability in new machine, use with snowflake divertor
  Examine RWMSC with:
    independent actuation of six coils
    multi-mode control with n up to 3
    rotational stabilization in the model
  Advantages:
  potential for use of external coils with less power

## Slide 6: NCC will greatly enhance physics studies and control; Enhanced magnetics near divertor will measure multi-modes
Present sensor locations
Multi-mode n = 1 ideal eigenfunction for fiducial plasma
Proposed new sensor locations
mmVALEN
Years 4 & 5:
  Implement improvements to active feedback of n =1-3 modes via RWMSC control allowed by the partial NCC
  Utilize rotation profile control capabilities allowed by the partial NCC to demonstrate reduced disruptivity by actively avoiding global instability boundaries
Partial NCC
Existing coils
(Next talk by Park will concentrate on NCC)
Mode diagnosis:
  If two modes are near marginal, need to be able to distinguish
  Measure increased amplitude near divertor (3D analysis shows >2x increase over present sensors)
  Similar results in ITER simulations
Significant toroidal phase change would be measured
  Can help constrain the RWMSC

## Slide 7: MHD spectroscopy shows improved stability at high bN/li; kinetic RWM stability may be enhanced at low n
Years 1 - 3:
  Investigate the dependence of stability on reduced n through MHD spectroscopy; compare to kinetic stabilization theory
Years 4 & 5:
  Utilize rotation control, NCC, and cryo-pump (for reduced n) to change proximity to kinetic resonances for RWM control
Theory: RWM γ vs. n and wf
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases up to bN/li = 10 then increases at higher bN/li
  Agrees with larger NSTX disruption database
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
0.0 0.5 1.0 1.5 2.0
Rotation ω/ωexp
0.1
0.0
-0.1
-0.2
-0.3
-0.4
Growth rate gtw
off
resonance
Decreasing
Collisionality
on resonance
bN
li
All NSTX discharges since 2006

## Slide 8: Realizing NSTX-U long-pulse scenarios will require stability of internal MHD modes
Years 2 & 3:
  Use new neutral beam and qmin control to determine increment of qmin above rational values to avoid internal modes
  Detect internal modes with RWMSC and non-magnetically with ME-SXR
Years 4 & 5:
  Examine time-evolution of global mode internalization using newly-installed, additional toroidally-displaced ME-SXR diagnostic
  Combine rotation, q, and βN control to demonstrate improved RWM/internal MHD mode stability
Coupled saturated 1/1 kink and 2/1 tearing modes grow when qmin -> 1
NSTX-U: Combinations of NB sources
(steady-state)
Low frequency mode activity measured with multi-energy soft X-ray

## Slide 9: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
    Error field (EF) correction
    Locking and tearing modes with resonant and non-resonant Efs
    Tearing mode physics vs. rotation and rotation shear
    Neoclassical toroidal viscosity
Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas

## Slide 10: Correction of intrinsic error fields (EFs) is critical for performance; Resonant and non-resonant EFs affect locking and tearing stability
Resonant error field threshold vs. locking density (IPEC) for five devices
Year 1:
  Use IPEC to model EFs
Years 2 & 3:
  Assess intrinsic EFs in new machine
  Optimize dynamic EF correction, including n>1 and using 6 SPAs and RWMSC
  Investigate resonant EF effects on tearing mode onset
Years 4 & 5:
  Utilize NCC to understand locking and tearing modes in the presence of resonant and non-resonant EFs
    develop predictability for ITER
Dynamic error field correction in NSTX
Gain

## Slide 11: NSTX-U will investigate tearing mode physics vs. rotation and rotation shear
Low rotation is bad for the NTM threshold
Year 1:
  Analyze NSTX TM/NTMs, project to NSTX-U with resistive DCON, MARS-K, M3D-C1
Years 2 & 3:
  Investigate the rotation and rotational shear vs. TM/NTM in NSTX-U, compared with NSTX
  Investigate the β limit for TM/NTM onsets with varied rotation and rotation-shear
Years 4 & 5:
  Use the partial NCC and the 2nd NBI beam to study TM/NTM dynamics as a function of (βN,vϕ)
    develop predictability for ITER
Rotation shear may be an even more important parameter
Rotation shear
Onset bootstrap drive

## Slide 12: NSTX-U will investigate neoclassical toroidal viscosity (NTV) at reduced n, which is important for rotation control and ITER
POCA NTV calculations for n=2 and n=3 magnetic braking
Year 1:
  Analyze existing NSTX NTV data on n dependence and offset rotation
  Develop/benchmark leading theory/codes
    NTVTOK, IPEC, POCA, FORTEC-3D
0.0 0.5 1.0 1.5 2.0
ω/ωexp
1.5
1.0
0.5
n/nexp
9
0
Theoretically, torque can be a strong function of rotation and n
Years 2 & 3:
  Assess NTV profile and strength at reduced collisionality, and examine the NTV offset rotation at long pulse
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system
Years 4 & 5:
  Utilize NCC, demonstrate low rotation profile operation (ITER-like) in steady-state with closed-loop rotation control
Analytic
n=1 braking
NSTX

## Slide 13: Overall objective: establish the physics and control capabilities needed for sustained stability of high performance ST plasmas
Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
    Prediction and avoidance
    Mitigation with MGI
    Transient heat loads and halo currents

## Slide 14: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (1)
Plasma Operations
Avoidance Actuators
PF coils
2nd NBI: q, vf, p control
3D fields (upgraded + NCC):
EF, vf control
n=1-3 feedback
Divertor gas injection
Mitigation
Early shutdown
Massive Gas Injection
EPI (tbp)
Control Algorithms: Steer
Towards Stable Operation
Isoflux and vertical position ctl
LM, NTM avoidance
RWM and dynamic EF control
RWMSC (plasma response)
Divertor radiation control
Disruption Warning
System
Predictors (Measurements)
Shape/position
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), vf(r),…..)
Plasma response (n=0-3, RFA, …)
Divertor heat flux
Loss of Control
General framework & algorithms applicable to ITER

## Slide 15: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (2)
RWMSC observer
MHD Spectroscopy
Kinetic Physics
Compare mismatch between the RWMSC observer and sensor measurements, and disruption occurence
Evaluate simple physics criteria for global mode marginal stability in real-time
Use real-time MHD spectroscopy while varying rotation, qmin, and βN to predict disruptions
  ITER gas-loading :
  Injection into private flux region with higher assimilation efficiency?
γ contours
Avoidance Actuators
Control Algorithms
Disruption Warning System
Predictors
Mitigation
q, vf , βN control
3D fields, feedback
Resonant Field
Amplification (G/G)
1

## Slide 16: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (3)
Year 1:
  Evaluate initial simple physics model for marginal stability based on kinetic stability physics
Years 2 & 3:
  Measure plasma stability using MHD spectroscopy vs. key variables and compare to theory
  Compare the mismatch between the RWMSC observer model and sensor measurements, and disruption occurrence
Years 4 & 5:
  Implement real-time evaluations of: kinetic stability model, MHD spectroscopy, and RWMSC observer disruption prediction for input to profile control algorithms
Year 1:
  Model neutral gas penetration of SOL
Years 2 & 3:
  Commission MGI system
  Characterize density assimilation vs. poloidal location
Years 4 & 5:
  Utilize EPI system
  Trigger the MGI system based on warning of an impending disruption
Predictors
Mitigation

## Slide 17: NSTX-U will provide projections of transient heat loads and halo currents for ITER and FNSF
Year 1:
  Examine thermal loading projections for ITER, including assumptions of axisymmetry
Years 2 & 3:
  Investigate halo current toroidal asymmetry and loading on the center column, using newly installed center column shunt tiles
  Upgrade shunt tile diagnostics for complete coverage of divertor
  Study spatial extent and timing of the heat deposition during VDEs
Years 4 & 5:
  Assess halo current scalings using the full field and current capabilities
  Study 3D and non-axisymmetric effects on the divertor heat loading
Halo current diagnostics
Time [s]
0.410 0.412 0.414
f
300
200
100
0
Halo current rotation
ITER high priority item: ITER has vessel resonances at frequencies of rotating halo currents
= Existing
= Baseline plan
(others incremental)
New diagnostic: high-speed IR thermography (ORNL)

## Slide 18: Summary of NSTX-U 5 year plan for Macroscopic Stability
MS research is establishing the physics understanding and control capabilities needed for sustained stability of high performance ST plasmas
  In unexplored ST operational regime: low n, high β, low li, long pulse
NSTX-U will make critical contributions in the areas of:
  Advancement of stability physics and control to sustain macroscopic stability at low collisionality
  Understanding 3D field effects and providing the physics basis for profile control by 3D fields
  Understanding disruption dynamics and developing techniques for disruption prediction, avoidance, and mitigation
MS research in NSTX-U will be greatly enriched, and have significantly greater impact on ITER, by having the NCC coils

## Slide 19: Backup

## Slide 20: NSTX-U macroscopic stability research is directly coupled to ITER through the ITPA
Through the experimental outage, our group:
  Maintains contributions to five joint experiments and two working groups
    leads the MDC-2 joint experiment / analysis on RWM physics
    co-leads the Working Group 7 effort on aspects of active mode control
  Communicated NSTX research bi-annually at each ITPA MHD Stability group meeting for many years
  Led two elements of the recent ITPA Integrated Plasma Control Working Group study, led by Dr. Joseph Snipes of ITER
    also contributed with direct calculations for ITER on RWM and error field control associated with this effort.
 | MHD |  | 
MDC-2 | Joint experiments on resistive wall mode physics | MDC-17 | Active disruption avoidance
MDC-8 | Current drive prevention/stabilization of NTMs | MDC-18 | Evaluation of axisymmetric control aspects
MDC-15 | Disruption database development | MDC-21 | Global mode stabilization for disruption prediction and avoidance (proposed)
NSTX-U stability research plans expand this effort in the coming five year period.

## Slide 21: Dual component (BR, Bp) PID and state space control
t (s)
40
0
80
0.56
0.58
0.60
t (s)
0.56
0.58
0.60
d
B
p
90
Dt (s) (model)
phase = 180o
phase = 90o
phase = 0o
Calculation of Br + Bp control (VALEN)
2.4
2.6
2.8
0.0
0.04
0.08
0.12
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWM State Space Controller
No NBI port
3D wall,
ports,
mode currents
Sensor Differences (G)
Measurement
Controller
Measurement
Controller
With 3D NBI port
Inclusion of 3D mode and wall detail improves control
d
B
p
90
Model validation and predictive capability:
VALEN code feedback predictions
Brn = 1 (G)

## Slide 22: RWM active control capability increases as partial NCC coils are added
Partial 1x12 NCC coil set significantly enhances control
  Present RWM coils: active control to bN/bNno-wall = 1.25
  NCC 1x12 coils: active control to bN/bNno-wall = 1.54
Existing
RWM
coils
NCC upper
1x12 coils
Using present midplane RWM coils
Partial NCC 1x12 (upper), favorable sensors

## Slide 23: RWM active control capability increases further with full NCC
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.61
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.70
Existing
RWM
coils
NCC full
2x12 coils
NCC partial
2x6 coils

## Slide 24: Multi-mode theory shows high amplitude near divertor, enhanced magnetics proposed
Present sensor locations
Multi-mode n = 1 ideal eigenfunction for fiducial plasma
Proposed new sensor locations
mmVALEN
code
Global mode diagnosis: measure theoretically increased amplitude in the divertor at high βN
3D analysis of candidate sensor positions show >2x increase in signal over present sensors
Significant toroidal phase change would be measured
  Constrain RWM state space controller
toroidal angle
poloidal angle
Present sensor positions
outboard midplane
center
column
new sensors
n = 1 mode
new sensors
Multi-mode physics
  Implement in RWMSC
  Validate theory predictions with measurements
  Found similar results in ITER simulations

## Slide 25: 3D analysis of extended MHD sensors show significant mode amplitude off-midplane, approaching divertor region
New sensor locations (includes
one new location above midplane)
n = 1 ideal eigenfunction for high beta plasma
Present sensor locations
Z(m)
R(m)
BR sensors (nominally normal, Bnorm)
Bp sensors (nominally tangential, Btan)
Bnorm(normalized)
q (deg)
Model characteristics
  New 3D model of divertor plate
  3D sensors with finite toroidal extent; n*A of existing sensors
Results summary
  Field amplitude increases >2x with new sensors
  Perturbed field reversals observed with new sensors
  Signals sufficient with plasma shifted off-midplane
q
Bnorm vs. theta (normalized to present Br sensors)
q (deg)
F = 0 deg
F = 0 deg
Present sensors
Zplasma = -10 cm
= -5 cm
= 0 cm

## Slide 26: Stability control improvements significantly reduce unstable RWMs at low li and high bN; improved stability at high bN/li
Resonant Field Amplification (RFA) vs. bN/li
unstable
mode
Unstable RWM
Stable / controlled RWM
Disruption probability reduced by a factor of 3 on controlled experiments
  Reached 2 times computed n = 1 no-wall limit of bN/li = 6.7
Lower probability of unstable RWMs at high bN/li
Mode stability directly measured in experiments using MHD spectroscopy
  Stability decreases up to bN/li = 10
  Stability increases at higher bN/li
  Presently analysis indicates consistency with kinetic resonance stabilization

## Slide 27: Internal modes may limit long-pulse scenarios; kinetic RWM stability may be enhanced at low n
0.0 0.5 1.0 1.5 2.0
Coupled m/n = 1/1+2/1 modes grow when qmin approaches 1
  EPM or ELM triggers cause modes to onset at larger qmin.
  “triggerless” internal kinks as qmin -> 1
Expectations at lower n:
Mode stability directly measured in experiment using MHD spectroscopy
  Decreases with n “on resonance”
  Independent of n “off resonance”
Experiment: RFA vs n
Theory: RWM γ vs. n and wf
on resonance
off resonance
off
resonance
on resonance
  More stability on resonance almost no effect off-resonance
Experiments measuring global stability vs. n support kinetic RWM stability theory
Model validation and predictive capability:
MISK code RWM stability calculations
Collisionality
Unstable
RWMs
n = 1 RFA (G/G)
1.5
1.0
0
.5
0.0
n
ii
[kHz]
0
1
3
2
ω/ωexp
0.1
0.0
-0.1
-0.2
-0.3
-0.4
gtw
NBCD can determine the required increment of qmin above rational values to avoid internal modes
Various combinations of neutral beam sources

## Slide 28: Internal kink/ballooning modes must be measured via non-magnetic means
Non-magnetic measurement is also important for mode control systems to be used in future devices with high neutron fluence
The RWMSC can determine how incorrect the observer is in reproducing the measured magnetic flux
  Can be used as a criterion as input to a disruption warning system.
Multi-energy soft X-ray can measure low frequency mode activity
  used to determine mode amplitude and in conjunction with the external magnetic sensors to determine the degree to which the mode is internal

## Slide 29: Understanding neoclassical toroidal viscosity (NTV) is crucial for rotation control
NTVTOK code:
  Shaing theory NTV computation including ion and electron effects
  Comparison to experiment of NTV in all collisionality regimes
A new δf guiding-center particle code, POCA, was developed to investigate neoclassical transport in perturbed tokamaks.
  solves the Fokker-Planck equation with non-axisymmetric magnetic field perturbations
“Investigate magnetic braking physics to develop toroidal rotation control at low n”
Model validation and predictive capability: NTV calculations with multiple codes, comparison to experiments
R(12-1)
POCA NTV calculations for n=2 and n=3 magnetic braking in NSTX
Analytic NTV calculations for (a) n=1 and (b) n=3 magnetic braking in NSTX, as a function of collisionality and rotation
0.0 0.5 1.0 1.5 2.0
ω/ωexp
0.0 0.5 1.0 1.5 2.0
ω/ωexp
1.5
1.0
0.5
n/nexp
1.5
1.0
0.5
n/nexp
(a) n=1
(b) n=3
9
0
2
0

## Slide 30: Correction of intrinsic error fields is critical for studies of 3D field physics and for performance
The perturbed n=1 field (IPEC) from intrinsic error fields in NSTX
Various successful error field correction schemes in NSTX
Dynamic error field correction (green)
  sustains βN above the no-wall limit
  sustains substantial toroidal rotation
NSTX-U will have a different error field
  Identification of error field in first year of operation
  measure vacuum fields; revise models
  Perform n=1,2 compass scans with 6 independent SPAs.
  RWMSC for dynamic error field correction
Predictive capability:
IPEC model of error fields

## Slide 31: Disruption mitigation technologies that will benefit the ITER design are being prepared
MGI research will assess gas penetration efficiency by injection at different poloidal locations
NSTX-U can offer new insight by
  Reducing the amount of gas
  Injecting gas into the private flux and lower x-point regions of divertor to determine if these are more desirable locations for MGI.
Predictive capability: Modeling using DEGAS-2 is quantifying the gas penetration past the SOL for NSTX-U
The EPI is capable of delivering:
  A large particle inventory
  All particles at nearly the same time
  Particles tailored to contain multiple elements in different fractions and sizes
  Tailored particles fully ionized only in higher current discharges (to control current quench rates)
Well suited for long stand-by mode operation
A novel mitigation technology, an electromagnetic particle injector (EPI), will be used to terminate plasmas
Rail gun electrodes
Particulate container projectile
Cone for shattering

## Slide 32: Understanding of thermal quench physics and transient heat loads is critical for projections
Examining assumptions:
  How much stored energy?
Typically only 15-20% of the stored energy remains in a late flat top disruption in NSTX
Example of rapid disruption with high stored energy
 | NSTX-U | ITER | ST-Pilot | Power Reactor
Thermal Loading [MJ m2 s-1/2] | 15 | 540 | 768 | 2061
0.408 0.410 0.412 0.414
f
300
200
100
0
Time [s]
  Halo currents are non-axisymmetric, but are heat fluxes?
rapid thermal quench
neutron emission [arb.]
Soft X-ray
Proposed expansion of the NSTX-U shunt tile diagnostic set

## Slide 33: Disruptivity studies and warning analysis of NSTX database are being conducted for disruption avoidance in NSTX-U
Disruption warning algorithm shows high probability of success
  Based on combinations of single threshold based tests
Results
  ~ 98% disruptions flagged with at least 10ms warning, ~ 6% false positives
  False positive count dominated by near-disruptive events
Disruptivity
Physics results
  Low disruptivity at relatively high bN ~ 6; bN / bNno-wall(n=1) ~ 1.3-1.5
    Consistent with specific disruption control experiments, RFA analysis
  Strong disruptivity increase for q* < 2.5
  Strong disruptivity increase for very low rotation
Warning Algorithms
All discharges since 2006
bN
li
q*

## Slide 34
KSTAR: equilibrium operating space 2009 –11
(evolution of > 130 discharges) + new results
New MP2012-04-23-021
session 1 session 2+
Plasmas have passed the predicted “closest approach” to the n = 1 ideal no-wall stability limit: li = 0.7, bN = 2.5
DIII-D: RFA of ~ 20Hz n = 1 increase to very high levels while βN increases and rotation decreases
Rapidly rotating n = 1 appears (TM?), clamps RFA amplitude
MS group continues strong collaborations with other devices such as KSTAR, DIII-D, and ITER team
ITER: RWM passive growth rates by CarMa and VALEN

## Slide 35: Many important computational codes are used for theory-experiment comparison on NSTX-U
Code | Description | Scope | Improvements
VALEN | Models currents in structures with thin shell finite elements | RWM active feedback simulation, growth rate prediction with 3D walls | Multi-mode effects, study extra time delay in plasma model
RWMSC | Resistive wall mode state-space controller computations | Generate control matrices for real-time controller, and offline physics studies | Generalization for partial actuator availability, n > 1 and multi-mode spectrum
NTVTOK | Shaing theory NTV computation including ion and electron effects | Calculation for comparison to experiment of NTV in all collisionality regimes | Continued implementation of NTV models, guided by experiment
DCON | Ideal MHD stability code | Ideal Kink stability analysis with and without the wall up to n=6 | Resistive layer physics across rational surfaces (Resistive DCON)
MISK | Modifications to ideal stability by kinetic effects | Calculation of resistive wall mode stability | Improved model of energetic particle, anisotropy effects
DEGAS-2 | Monte Carlo code to compute transport of neutral atoms | Calculation of neutral gas penetration through SOL | Include multiple gas species Use exact NSTX-U SOL conditions from UEDGE
EFIT | Equilibrium reconstruction code | Between-shots equilibrium reconstruction | Higher resolution, auto best level, new diagnostics
IPEC/GPEC | Ideal and general perturbed equilibrium with 3D fields | Plasma response, locking, and NTV studies with 3D fields | General force balance equation including general jump conditions
MARS-K | Self-consistent kinetic stability calculation | Calculation of RWM stability and plasma response to perturbation | Inclusion of energy dependent collisionality for NTV calculation
M3D-C1 | Implicit resistive and 2-fluid MHD code | Linear and nonlinear MHD stability | Neoclassical terms, resistive wall being added
FORTEC-3D | Monte-Carlo drift-kinetic physics simulation code | Non-ambipolar transport and NTV physics in general geometry | Continued integration with IPEC and application to NSTX-U
POCA | δf guiding-center orbit code | Calculation of neoclassical transport, perturbed pressures and NTV | Improved numerical scheme to enhance computation speed

## Slide 36: Many important computational codes are used for theory-experiment comparison on NSTX-U
Code
VALEN
RWMSC
NTVTOK
DCON
MISK
DEGAS-2
EFIT
IPEC/GPEC
MARS-K
M3D-C1
FORTEC-3D
POCA

## Slide 37
FY13
14
15
16
17
18
Physics
Optimize shaping, RWM/TM control (n≥1 using the second SPA), validate internal mode physics and RMW kinetic physics
Optimize error field correction (n≥1), dynamic correction, and understand NTV physics in reduced v* and controlled rotation
5 year plan period
Study halo currents, disruption loads, and precursors, and test MGI or other mitigation techniques
Optimize and combine rotation profile and β-feedback control using NCC, to improve stability and for fully non-inductive operation
Understand non-resonant error field effects using NCC, NTV effects vs. rotation profile on transport, utilize 3D field to improve stability
      Provide FSNF/Pilot projection,
      Integrate MS control to improve RWM/TM/ELM/ internal mode stability, disruption avoidance, with disruption mitigation protection
Tools
Real-time velocity measurement and MSE, toroidally displaced ME-SXR
Utilize 3D field for rotation (profile) and β-feedback control, to improve RWM/TM/internal mode stability
5 year goal
Diagnostics
Theory
Facility
Plasma Control
Integrate and validate 3D equilibrium, stability, and transport codes
5 year plan period
Investigate avoidance scenarios and couple to mitigation techniques
Integrate MS control with disruption avoidance and mitigation
Utilize equilibrium reconstruction, and transport and stability codes
RWM state-space control (n≥1), error field control, snowflake divertor control
Non-axisymmetric Control Coil (NCC), enhanced magnetics, cryopump for low v*
Thrust #1
Thrust #2
Thrust #3
Real-time MPTS, X-ray imaging spectrometer,
Internal dB measurement from MSE,
enhanced magnetic sensors
Expanded shunt tile measurements, disruption load diagnostics
Gas penetration dynamics
Disruption simulation
Second switching power amplifier (SPA),
MGI disruption mitigation system
2014-18 Macroscopic Stability Research Timeline