## Slide 1
In collaboration with
M.J. Choi, M. Kim, J. Lee, W. Lee, G.S. Yun (POSTECH), C.W. Domier, N.C. Luhmann, Jr.
(UC Davis), Y.M. Jeon, S.G. Lee (NFRI), I. Joseph, W. Meyer, X.Q. Xu (LLNL),
Hyeon K. Park
POSTECH,
Pohang, Korea
A3 Seminar
Jan. 22-25 , 2013
Hokkaido, Japan
Simulated
image
Measured
image
Validation/Verification of MHD physics via 2D/3D ECEI in KSTAR (ELM dynamics)
Dual flux tubes (dual m/n=1/1)
Edge Localized Modes
m/n=2/1 Tearing Modes
Notes: Satoru on MHD stability and Houyang’s talks on current drive, ELM control (instability in general) is essential for SS operation in Tokamaks and Stellarators. Do we have models to challenge the future (SS on high beta and long pulse?? Answer is “No” Then are we continue on “empirical physics?? Answer is “No”

## Slide 2: Outline
2D/3D ECEI system for visualization
  Improvement of the predictive capability of complex dynamics of MHDs, Waves and Turbulence
  Verification/validation of the ELMs in KSTAR
    Validation: synthetic image of the ELMs via BOUT++ simulation
    Verification: ELM dynamics/responses to the external perturbations (e.g. MP and SMBI)
    Fundamental of the role of magnetic perturbation ?
The beginning of 3D imaging in KSTAR
  Sawtooth, Tearing mode, and ELMs, etc.

## Slide 3
Alfvén waves (DIII-D)
B. Tobias et al., PRL (2010)
Sawtooth crashes (TEXTOR)
H.K. Park et al., PRL (2006)
Tearing modes (TEXTOR)
I. Classen et al., PRL (2007)
ELMs (KSTAR)
G.S. Yun et al., PRL (2011)
Improve predictive capability of MHD and wave physics
(e.g. Sawtooth, NTM, Alfvén waves, and ELMs)
Analogous to evolution of
diagnostic capabilities from
Stethoscope to MRI/CT
Why 2D/3D visualization (ECEI)?
Dual m/n=1/1
Mode
G.S. Yun et al.,
PRL (2012)
“SEEING IS BELIEVING”
for complex system

## Slide 4
ECE measurement is an established tool for electron temperature measurement in high temperature plasmas
Sensitive 1-D array detector, imaging optics, and wide-band mm wave antenna, and IF electronics are required for 2-D imaging system
Te fluctuation measurement
  Real time fluctuations can be studied down to ~2% level (lower w/ SVD, etc……)
  Fluctuation studies down to 0.1 % level have been performed using long time integration
Conventional 1-D ECE system
2-D ECE imaging system
ECE imaging for Te fluctuation measurement

## Slide 5
G
H
~1m
shot 4362
B0 ~ 2 T
Te0 ~ 2 keV
ne0 ~ m-3
First simultaneous
2D visualization of the internal kink (m=1)
and
Edge-Localized Modes
(ELMs)
H
G
KSTAR (2012)
Comibined
with MIR
KSTAR 2D/3D ECE imaging systems

## Slide 6
G.S. Yun et al.,
PRL 107 (2011)
1
2
3
100 ms
200 ms
0 ms
Initial growth to saturation
Shot=4431
ECEI (V)
1
2
3
Time (ms)
crash phase
4
855 ms
4
ELM dynamics in KSTAR plasmas
Time evolution of a single ELM

## Slide 7
215
220
225
230
R [cm]
KSTAR shot #6123 @ t~3.4s
Validation of the stationary ELM
2D image of an ELM
Toroidal mode number (n=5) is identified by the magnetics
q- and pressure profiles from EFIT are used to get the 2D image of the n=5 mode w/ the max. growth rate
BOUT++ Simulation (linear) of
the n=5 ELM
Outcomes
Poloidal mode spacing is
incorrect !
Radial thickness is too thin !

## Slide 8
Parametric dependence of the mode structure
A) Poloidal mode spacing is sensitive to the local q-value
#1
#2
#3
B) Radial thickness and growth rates sensitive to P’
#1
#2
#4
Identification of the bootstrap current (Jb) due to P’ and n* changes w/ 3D system !!
Notes: q and P are not self-consistent here

## Slide 9
BOUT++
Simulation
Synthetic
Image
Synthetic image
with system noise
Measured Image
Finite radial resolution of the system broadens the image
A phantom image appears outside the separatrix due to ECE
downshift from inside (known phenomenon) -- finite system
noise and wall reflections may complicates the interpretation
Ignore images contaminated by downshifts.
Synthetic image with the system noise

## Slide 10
Optimum pressure profile for KSTAR ELMs
Measured
image
Synthetic
image
Simulated
image
ELMs in KSTAR H-modes
Discrete n numbers were observed (n~5 and n~10)
Pressure scale length is proportional to n number (consistent w/ observation)
Optimum pressure profiles
for n=5 and n=10 modes
n=5
n=10
n=5
mode
n=10
mode
Notes: Effective radius of curvature at the mid plane
𝑥(𝑡)=𝑎 cos⁡(𝑡+𝛿 sin⁡𝑡 )
𝑧(𝑡)=𝜅 𝑎 sin⁡(𝑡)
𝑟𝑎𝑑𝑖𝑢𝑠 𝑜𝑓 𝑐𝑢𝑟𝑣𝑎𝑡𝑢𝑟𝑒, 𝑎′= (𝑥^′2+𝑧^′2 )^(3/2)/|𝑥^′ 𝑧^′′−𝑧^′ 𝑥^′′ | =(𝑎 𝜅)/(1+𝛿)^2
Other method to estimate the field line pitch angle
𝑥(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} cos⁡𝜙
𝑦(𝜃,𝜙)={𝑅_0+𝑎 cos(𝜃+𝛿 𝑠𝑖𝑛𝜃)} sin⁡𝜙
𝑧(𝜃, 𝜙)=𝜅𝑎 sin⁡𝜃
𝑝𝑖𝑡𝑐ℎ 𝑎𝑛𝑔𝑙𝑒:tan⁡〖𝛼=〗 ├ Δ𝑧/(Δ𝑥 )]_(𝜃=0, 𝜙=0)=

## Slide 11
Response of the ELMs to perturbations
Peeling/Ballooning
mode model (T. Osborne)
RMP case
unstable n~10 to marginally
unstable n~5,10) may require a
reduction of Jb & P’ (observed
reductions in P’ & n*)
No signature of the applied
stochastic magnetic island (i.e.
interference in magnetic
diffusion time scale)
Resonant Magnetic Perturbation (n=1)
A
B
SMBI case
L1 – L2 is correlated w/ the [increasedn* (decreased P’)]
L2 – L3 is correlated w/ the [decreased n* (increased P’)]
L1~L3 > L2
No change in n number?
Jb change – local q change?
C
A
B
C
No steady filaments
Well defined mode numbers
Supersonic Molecular Beam Injection
Notes: Low (High) collisionality regimes
n mode change is wrong direction based on P’
m(q) mode change is also in wrong direction

## Slide 12
Response of the ELMs from RMP (n=1)
3.1 3.2 3.3 3.4 3.5
ELM frequency increases (6 to 8 kHz)
No change in poloidal spacing
of the mode (n~10)
Te gradient increases
Time (s)
Da(AU)
Pedestal
Te (AU)
Line
density
Da(AU)
Te (AU)
Te (AU)
Freq.
(KHz))
Pedestal
ch#5
LCFS ch #3
RMP
~35 ms
Unstable n~10 ELM
Marginally stable n~5 and n~10 ELM
Time
Transition from stable to marginally stable

## Slide 13
Basic physics and role of RMP (e.g. n=1)
Ip, BT
+Br
+
+
+
+
+
+
, phase
Top
Middle
bottom
Synthetic (+noise) image of islands
Stochastic islands
from n=1 RMP
(Vacuum fields)
Configuration of the n=1 RMP
in KSTAR
Also other configuration such
as n=2 (even and odd parity)

## Slide 14
ㅡ LFS ch.3
ㅡ LFS ch.4
ㅡ LFS ch.5
ㅡ LFS ch.7
Base H-mode pedestal (n~10 ELM) → Steepness of the pedestal (n=5 ELM) → Further steepness of the pedestal (ELM-free: no room for ELM to grow)
The observation is consistent w/ the optimum growth rate of the ELMs (from n=10 to n=5)
Temperature profile evolution during RMP
Time history of LFS ECEI raw data
Filament(pedestal)
Ch.5
Ch.4
Ch.7
Ch.3
Time [s]
Temperature profile evolution during RMP

## Slide 15
Marginally unstable n~5,10 modes during RMP
ELM crash
ELM crash
After crash of the n~5 ELM, n~10 mode appears.
Peeling dominated regime (low n ) – role of Jb is important for marginally unstable n~5, ~10
n~5
n~5
n~10
Te(A.U.)
Freq. (kHz)
Frequency change is due to the change in plasma rotation not toroidal/ poloidal mode number change
Rotation changes from Er ?
Er from charge imbalance ?
Charge imbalance from loss of density (primarily electrons)
Single n=5 ELM

## Slide 16
(shot#7328, t=7,.917s)
ELMs*
16
2nd ECEI
1st ECEI
  A useful constraint for equilibrium reconstruction
Toroidal asymmetry of ELM dynamics under investigation.
NOT A SIMULATION
3D measurement of the n=10 ELM
Apparent rotation direction of the 2012 ELM
is opposite to that of the 2010 & 2011 ELM

## Slide 17
Modulation and toroidal asymmetry of the ELMs

## Slide 18
(shot#7131, t=3.7s)
m/n=2/1 tearing
Internal kink (sawtooth)
(shot#7446, t=2.873s)
NOT A SIMULATION
NOT A SIMULATION
3D measurement of other instabilities in progress

## Slide 19
Summary of “Seeing is believing”
Visualization is a powerful tool for complex physics
  More than a decade of work on real time ECEI in various toroidal devices (TEXTOR, AUG, DIII-D, KSTAR, EAST, Tore-Supra, SST)
Verification and validation of MHD physics in KSTAR
  Observed ELMs are verified by synthetic images
    Poloidal mode number is a sensitive to the local q value for a fixed n number [m=nq]: P’ is for growth rates - radial thickness.
    Instrumental and emissivity broadenings must be considered !
  Responses to the external perturbations used for validation of ELM physics
    RMP(n=1) changes the unstable n~10 ELM into marginally unstable n~ 5,10 ELMs and then stabilize (?) all.
    No clear signature of stochastic magnetic islands from RMP
    Mode number changes are qualitatively consistent with the peeling/ballooning mode model (in Jb and P’ space)
    Further study of the role of Jb in high/low n* plasma
New progress toward 3D imaging and 2D turbulence (2012 KSTAR campaign) !

## Slide 20: POSTECH Center for Fusion Plasma Diagnostics and Steady State Operation
Univ. of York, UK
AUG Germany
IPP, China
General Atomics
Univ. Colorado
MIT
LLNL
KNU
SNU
Sogang Univ.
UNIST
Tore Supra
France
Kyushu Univ.
KFKI Hungary
Positions for Prof. (tenure track), Visiting researchers, Postdoc, and PhD Students available at POSTECH center

## Slide 21
Interpretation of Edge ECE imaging
Near the pedestal foot and outside, ECE signals come mostly from inside, a well-known phenomenon called downshift.
ECE downshift
(not localized)
Localized ECE
E. de la Luna et al., 34th EPS (2007)
JET H-mode pedestal
ne
Te
R (cm)

## Slide 22
ASDEX-Upgrade
KSTAR
215
220
225
230
R [cm]
Classen et al., Rev. Sci. Instrum. 81 (2010)
DIII-D
A clear ELM filament structure has not been observed.
Steeper pedestal
Because the radial size of filament < ECEI resolution ?
ne
Te
P (arb.)