## Slide 1
NSTX-U / KSTAR Collaboration Opportunities
Jonathan Menard (PPPL)
NSTX-U Program Director
NFRI – PPPL Collaboration Meeting
PPPL
October 21, 2013
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Thanks to our KSTAR/NFRI visitors for coming to PPPL!
A few goals for this meeting:
Identify research areas of common interest for possible collaboration w/ NSTX-U (this talk) and PPPL more broadly
Identify research contacts to facilitate future collaboration
Enhance KSTAR/NFRI researcher participation on NSTX-U, possibly through extended stays at Princeton/PPPL

## Slide 3: NSTX Upgrade mission elements
ITER
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
Lithium
“Snowflake”
ST-FNSF

## Slide 4: NSTX Upgrade incorporates 2 new capabilities:
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
Normalized e-collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
Reduces n*  ST-FNSF values to understand ST confinement
  Expect 2x higher T by doubling BT, IP, and NBI heating power
  5x longer pulse-length
  q(r,t) profile equilibration
  Test non-inductive ramp-up
New
center-stack
  2x higher CD efficiency from larger tangency radius RTAN
100% non-inductive CD with core q(r) profile controllable by:
  NBI tangency radius
  Plasma density, position (not shown)
New 2nd NBI
Present NBI
RTAN [cm]
__________________
50, 60, 70, 130
60, 70,120,130
70,110,120,130
n
e
/
n
Greenwald
0.95
0.72
IP=0.95MA, H98y2=1.2, bN=5, bT = 10%, BT = 1T, PNBI = 10MW, PRF = 4MW
NSTX

## Slide 5
NSTX Upgrade project on schedule and cost
Good progress on 2nd NBI, device structural enhancements
New tangential NBI injection port installed
2 new outer TF coils installed
2nd NBI installed
High Voltage Enclosures in-place

## Slide 6: Centerstack is the critical path and highest risk
Components & Hardware
  Flex connectors – delivered
  PF 1b,a,c coils – awarded
  PFC Tiles - delivered and being machined
  Casing - delivered
Inner TF Bundle
  VPI 4 Quadrants - Completed
  VPI Full Bundle - Completed
OH Solenoid
  OH Conductor delivered
  Aqua-pour process – underway
  Begin winding OH solenoid – November
  VPI OH – Jan-Feb 2014
Centerstack Assembly
  Delivery to NSTX Test Cell - May 2014

## Slide 7: NSTX-U operations schedule / plan
New centerstack installation planned for spring / summer 2014 - less than 1 year away
First plasma: late fall 2014
Start research program:
late 2014 - early 2015

## Slide 8: Highest priority research goals for NSTX-U:
Longer-term (5-10 year) goal:
Integrate 100% non-inductive + high b and tE + divertor solution + metal walls
Demonstrate 100% non-inductive sustainment
Access reduced n* and high-b combined with ability to vary q and rotation
Develop/understand non-inductive start-up, ramp-up (overdrive) for ST-FNSF with small/no solenoid
4. Develop high-flux-expansion “snowflake” divertor + radiative detachment to mitigate high heat fluxes
5. Assess high-Z + liquid Li plasma facing components

## Slide 9: Advanced Scenarios and Control 5 Year Goals:
100% non-inductive operation
Lower n*: high-current, partial-inductive scenarios, extend to long-pulse
Implement axisymmetric control algorithms and tools
  Current and rotation profile control
  Improved shape and vertical position control
  Heat flux control for high-power scenarios
Develop disruption avoidance by controlled plasma shutdown
Torque Profiles From
6 Different NB Sources
Rotation Profile Actuators
Neutral
Beams
(TRANSP)
Largest Rtan
Smallest Rtan
Also torques from 3D fields

## Slide 10: Collaboration opportunity: KSTAR also using 3D fields for NTV/rotation control, ELM/EF control
KSTAR Data:

## Slide 11: Macroscopic Stability 5 Year Goals:
Study effects of reduced n*, q and rotation on LM, RWM, NTM
Test state-space control for EF, RWM for ITER, next-steps
Assess 3D field effects to provide basis for optimizing stability through rotation profile control by 3D fields
  EF penetration, rotation damping, ELM triggering and suppression
Understand disruption dynamics, develop prediction and detection, avoidance, mitigation
  Enhance measurements of disruption heat loads, halos
  Develop novel particle delivery techniques for mitigation:
    MGI in private-flux-region (PFR), electromagnetic particle injector

## Slide 12: Collaboration opportunity: KSTAR operating near no-wall stability limit, testing massive gas injection
KSTAR Data:

## Slide 13: Energetic Particle 5 Year Goals:
Assess requirements for fast-ion phase-space engineering
  AE spectroscopy, also stability control using NBI, q, rotation, 3D fields
Develop predictive tools for projections of *AE-induced fast ion transport in FNSF and ITER
  Compare data to simulation, develop reduced models
    ORBIT, NOVA-K, M3D-K, HYM to understand mode-induced transport
Vary fast-ion instability drive using NBI, q, rotation, 3D fields
Measure *AE mode structure
  Magnetics, BES, reflectometry
Characterize fast ion transport vs. *AE type

## Slide 14: Collaboration opportunity: KSTAR also observes Alfvén eigenmodes from NBI, fast-ion loss from MHD
KSTAR Data:

## Slide 15: Transport and Turbulence 5 Year Goals:
Characterize H-mode global energy confinement scaling in the lower collisionality regime of NSTX-U
  Builds on identification of ETG w/ novel high-kr scattering in NSTX
Establish and validate reduced transport models
Identify modes causing anomalous electron thermal, momentum, particle/impurity transport
  Exploit scaling dependencies of modes
    Example: m-tearing ce ~ n1, ETG ce ~ n0
  Relate predicted turbulence to data:
    Low-k (BES), dB (polarimetry), high kr & kq (m-wave)

## Slide 16: Collaboration opportunity: KSTAR beginning to measure low-k turbulence with BES (also MIR, ECEI)
KSTAR Data:

## Slide 17: Boundary Physics, SOL/Divertor, PMI 5 Year Goals:
Assess, optimize, control pedestal structure, transport, stability
Assess and control divertor heat fluxes
  Measure SOL widths at lower , higher BT, IP, PSOL
    Compare data to fluid and gyro-kinetic models
  Assess, control, optimize snowflake/X-divertor
  Develop highly-radiating divertor w/ feedback control
  Assess impact of high-Z tile row(s) on core impurities
Establish, compare particle control methods
  Validate cryo-pump physics design, assess density control
  Compare cryo to lithium coatings for ne, impurity, n* control
Explore Li/liquid-metal plasma material interactions
  Li surface-science, continuous vapor-shielding, material migration and evolution, lab R&D: flowing Li loops, capillary-restrained Li surfaces

## Slide 18: Collaboration opportunity: KSTAR studying castellated W, W surface effects & dust, far-SOL transport
KSTAR Data:

## Slide 19: Summary
NSTX-U and KSTAR research programs have many common goals
Many collaboration opportunities when NSTX-U begins operation in 2015

## Slide 20
Backup

## Slide 21: Proposed longer-term facility enhancements: (2014-2018)
Improved particle control tools
  Control deuterium inventory and trigger rapid ELMs to expel impurities
  Access low n*, understand role of Li
Disruption avoidance, mitigation
  3D sensors & coils, massive gas injection
ECH to raise start-up plasma Te to enable FW+NBI+BS IP ramp-up
  Also EBW-CD start-up, sustainment
Begin transition to high-Z PFCs, assess flowing liquid metals
  Plus divertor Thomson, spectroscopy
Midplane + off-midplane non-axisymmetric control coils (NCC)
Extended low-f MHD sensor set
1-2MW
28 GHz
gyrotron
Divertor cryo-pump
Upward Li evaporator
Li granule injector (LGI)
High-Z tiles
Actively-supplied, capillary-restrained, gas-cooled LM-PFC

## Slide 22: NSTX Upgrade will access next factor of two increase in performance to bridge gaps to next-step STs
Non-inductive start-up, ramp-up, sustainment
Confinement scaling (esp. electron transport)
Stability and steady-state control
Divertor solutions for mitigating high heat flux
* Includes 4MW of high-harmonic fast-wave (HHFW) heating power
VECTOR (A=2.3)
JUST (A=1.8)
ARIES-ST (A=1.6)
Low-A
Power Plants
Key issues to resolve for next-step STs
Parameter | NSTX | NSTX Upgrade | Fusion Nuclear Science Facility | Pilot Plant
Major Radius R0 [m] | 0.86 | 0.94 | 1.3 | 1.6 – 2.2
Aspect Ratio R0 / a |  1.3 |  1.5 |  1.5 |  1.7
Plasma Current [MA] | 1 | 2 | 4 – 10 | 11 – 18
Toroidal Field [T] | 0.5 | 1 | 2 – 3 | 2.4 – 3
Auxiliary Power [MW] | ≤ 8 | ≤ 19* | 22 – 45 | 50 – 85
P/R [MW/m] | 10 | 20 | 30 – 60 | 70 – 90
P/S [MW/m2] | 0.2 | 0.4-0.6 | 0.6 – 1.2 | 0.7 – 0.9
Fusion Gain Q |  |  | 1 – 2 | 2 – 10

## Slide 23: TRANSP simulations support goal of accessing and controlling 100% non-inductive plasma operation
Contours of Non-Inductive Fraction
H98y2
Maximum sustained non-inductive fractions of 65% w/NBI at IP = 0.7 MA
70-100% non-inductive transiently with HHFW current-drive + bootstrap
Total non-inductive current fraction
Ip (MA)
NSTX Results
NSTX-U projections
via high harmonic FW
NSTX achieved:
NSTX-U projections (TRANSP):
100% non-inductive at IP = 0.6-1.3MA for range of power, density, confinement
IP=1 MA, BT=1.0 T, PNBI=12.6 MW

## Slide 24: Rapid TAE avalanches could impact NBI current-drive in advanced scenarios for NSTX-U, FNSF, ITER AT
Discrepancy between reconstruction and total assuming
classical JNBCD
Minor radius
700kA high-bP plasma with rapid
TAE avalanches has time-average DFI = 2-4m2/s
NSTX: rapid avalanches can lead to redistribution/loss of NBI current drive
NSTX-U TRANSP simulations
1 MA, 1T, H98=1, near non-inductive
1.6 MA, 1T, partial inductive
1.2 MA, 0.55T, high bT
All: fGW=0.7, H98=1

## Slide 25: NSTX/NSTX-U is making leading contributions to high-bN stability physics, and assessing possible 3D coil upgrades
Identified several off-midplane 3D coil sets favorable for profile and mode control
  ~40% increase in n=1 RWM bactive / bno-wall
  ~5x reduction in n=1 EF resonant torque
  ~10-100x variation in ratio of non-resonant to resonant n=3 torque in edge
    Important for control, understanding of RMP ELM control, NTV rotation profile control
Resonant Field
Amplification (G/G)
n=1 MHD spectroscopy: high bN can be more stable
  Combination of rotation and current profile effects at high beta
  Important for advanced scenarios
NCC options:

## Slide 26: Beginning to test/utilize transport models to predict NSTX temperature profiles, identify possible missing physics
Over-prediction of core Te in NSTX may be due to transport from GAE/CAE modes not included in gyro-Landau-fluid model
Te (keV)
Ti (keV)
Utilizing neoclassical + drift wave models to simulate NSTX Ti and Te profiles (collaboration with GA)
  Need model for c in edge region
  Discrepancy in core Te prediction for beam-heated H-modes
r/a
Te (keV)
NSTX H-modes showed broadening of Te profile as BT was increased
  Similar broadening trend observed with increased lithium deposition
  BTtE scales as ~1/n* in both datasets

## Slide 27: Simulations support non-inductive start-up/ramp-up strategy
TRANSP: NSTX-U more tangential NBI  3-4x higher CD at low IP (0.4MA)
TSC: non-inductive ramp-up from 0.4MA to 1MA possible w/ BS + NBI
TSC code (2D) successfully simulates CHI IP ~200kA achieved in NSTX
TSC + tools included in 5 year plan support CHI IP  400kA in NSTX-U
0
1.0 ms
1.6 ms
2.7 ms
1
2
0
1
2
0
1
2
R (m)
R (m)
R (m)
0
-2
1
2
-1
Z (m)
  Higher injector flux, toroidal field, CHI voltage
  1MW 28GHz ECH (increases Te)
But, RF heating (ECH and/or HHFW) of CHI likely required to couple to NBI

## Slide 28: Snowflake divertor effective for heat flux mitigation
NSTX: can reduce heat flux by 2-4× via partial detachment
Snowflake  additional x-point near primary x-point
  NSTX: High flux expansion = 40-60 lowers incident q
  Longer field-line-length promotes temperature drop, detachment
Snowflake Divertor
Standard Divertor

## Slide 29: Start-up/Ramp-up + RF Heating/Current Drive Goals:
Test higher-current CHI start-up (~400kA)
Test NBI + bootstrap current overdrive/ramp-up
Develop HHFW and EC heating for fully non-inductive plasma current start-up and ramp-up
  Extend HHFW to higher power (3-4MW), demonstrate HHFW-driven 100% non-inductive at 300-400kA
    Goal: maintain IP to confine 2nd NBI fast-ions
Validate advanced RF codes for NSTX-U, predict RF performance in ITER and FNSF
  Use ECH (~1MW, 28GHz), then HHFW to increase Te of CHI plasmas for NBI
  Test high-power EBW to generate start-up current - builds on MAST results

## Slide 30: Collaboration opportunity: KSTAR using ECH, developing ICRF, testing non-solenoidal start-up (Kyoto)
KSTAR Data: