## Slide 1
Research Topics on Pedestal Physics at KSTAR
Si-Woo Yoon
on behalf of Boundary Physics Division
National Fusion Research Institute (NFRI), Daejeon, Korea
Domestic & International Collaborators

## Slide 2: Contents
Characteristics of H-mode discharges
  L-H transition, confinement, typical H-mode discharges, stimulated transition
Status of pedestal diagnostics
  Validation of profile & fluctuation
  profiles : Thomson Scattering, Charge Exchange Spectroscopy, Reflectometry,
  fluctuations :Beam emission spectroscopy, Imaging of Electron cyclotron emission
Research topics on pedestal physics
  ELM mitigation / control
  (Resonant magnetic perturbation, edge ECRH, supersonic molecular beam injection)
  Pedestal evolution during ELM cycle
  (dynamics, mode structure)
  Searching for small ELM regimes
Near term research plan
  Fast pedestal profile measurements including j║ , Er , & Vpol with cross-check
  (Li-Zeeman, poloidal CES, MSE, DBS)
  ELM physics/control in ITER relevant condition
  Transport in pedestal region (particle pinch, turbulence, ZF)

## Slide 3
Characteristics of H-mode discharges

## Slide 4: KSTAR Pedestal & ELM characteristics
NBI power scan shows type-I character
2x PNBI -> ~2x fELM
Shot 7242

## Slide 5: Pedestal evolution in-between ELMs
Dα Div [a.u.]
Different time scales during ELM cycle
(For large infrequent ELMs)
- Thermal (Te,ped & Ti,ped)
Fast bulidup & saturation
Faster saturation of Te
Rotation
steady increase in entire phase
Rotation (& shear) is the main driver?
(need pedestal density measurement)
Fluctuation analysis is on-going
(using Edge BES)
WMHD [kJ]
Ne [1e19/m3]
Te,ped [eV]
Vt,ped [km/s]
Ti,ped [eV]
ECE
CES
CES
Time [s]
#7552

## Slide 6: With SMBI, Stimulated transitions found with 30% reduced absorbed power
L-mode
SMBI (8 ms)
Back transition
(vertical oscillations)
ne ~2.3e19
Stimulated
Transition
(~300 ms)
Triggering of L-H & small ELM is observed by 8 ms of SMBI
- Transition occurred for less absorbed power
Pabs= Pinj – dW/dt - Prad
(cyan line)
#9078
BT = 2.5 T
#9077
BT = 2.0 T
Known
density
turnover
Pabs

## Slide 7: Edge profile changes are accompanied for the stimulated dynamics
Lower ne branch case (#7865)
The induced density profile steepening is maintained more than ~200 ms until the H-mode onset at 2.65s
  Longer than particle confinement time
Possible mechanism:
SMBI deposit on pedestal local profile changes  changes on
K. Miki, PRL 2013
cf. DIII-D 1.3 mm smaller pellet scan did not report any stimulated transition with no change on pedestal (2013)
ne
Time [s]
SMBI injection
at 2.4 s, #7865
Edge reflectometry
@ 7865
Before
SMBI
After
SMBI
H-mode
Ped.

## Slide 8
Status of pedestal diagnostics

## Slide 9: Profile Reflectometry which covers full radial range
D-port
Reflectometry Specifications | 
# of channel | 3 bands (Q, V, and W)
frequency | 33.6-54 GHz (Q band) 48-72 GHz (V band) 72-108 GHz (W band)
time resolution | 25 ms
spatial resolution | 0.5 mm
maximum storage | 160 ms (32 Mbytes memory)
antenna | pyramidal long horn antenna (40 mm x 32 mm x 300 mm)
antenna position | antenna entrance @ R = 2.624 m
#9422

## Slide 10
Specification of KSTAR Thomson scattering system
KSTAR Thomson scattering system(2013)
Te : 10eV~1.5keV (edge), 500eV~20keV (core)
ne : 3Х1012~2 Х1014 ㎝-3
17spatial points (core 5, edge 12 points)
Spatial Resolution : <10cm (core), <10mm (edge)
Polychromator 17ea (core 5ea by NFRI, edge 12ea by NIFS)
Laser : ~5J, 100Hz Nd:YAG Laser, 1064nm
5J, 100Hz, 1064nm Double laser line
A-line
B-line
2.5J, 100Hz
2.5J, 100Hz
* LASER system rented from JAEA
=1064nm, pulse width ~20nsec
A
B
18mm
Edge
Core
Plasma center
Measuring Position
Calibrated by
Rayleigh scattering with N2
Spectral calibration with W (tungsten) light

## Slide 11
Charge Exchange Spectroscopy on KSTAR
Name | CES specification in 2013
Time resolution | 10 msec (100 Hz)
Spatial resolution | 20 ~ 50 mm (Core), 5 mm (Edge)
Ti & Vf range | > 100 eV & > ~ km/sec
System location | Active CES – M port
No. of Channels | 32 points (Max.51points available)
NBI modulation | 5Hz 95% duty rate (requirement)
Impurity | CVI (529.05 nm)
Spectrometer | DS-spectrometer (DU897), K-spe.

## Slide 12: Li/D Beam Emission Spectroscopy System
BES Optics
D Beam
(Heating)
Li Beam
(Diagnostics)
1st
2nd
3rd
Ion Source
Edge
Core
Measurement
Positions
Radial & Vertical
Positioning
BES Specifications | 
Local (Resolution) | 1 cm
2D (Pixel) | 4x8 (will be upgraded to 4x16)
Fast (Sampling) | 2 MHz
Fluctuation (SNR) | ~ 150 (~ 3% background)
Meas. Position | Radial & Vertical Scan (shot by shot)
Filter | Heatable (for fine tuning) Rotatable (for background cal.) Changeable (for Li/D)
Cameras | APD (fast) / CMOS (high res.)
Time Range | up to 100 sec
Li Beam Parameter | 
Diameter | 2 cm (in the plasma) 10 cm (defocused)
Current | ~ 2 mA
Energy | < 60 keV
Pulse Length | 20 s
Species | Lithium (neutralized by Sodium)

## Slide 13: Typical KSTAR Pedestal profiles
Pedestal structure both in Thomson & CES for H-mode
(further comparison is on-going)
t=2.1 s : L-mode
t=2.3 s: transition
t=2.5 s: H-mode
Issue of TS calibration
Only relative change must be considered

## Slide 14
Value of Te,ped are in good agreement
Position of separatices < ~ 1 cm
ECE could be used for fast pedestal Te measurements with BT>2.6 T
Density need better laser calibration
(also with Li-BES)
Initial comparison showa good correlation between ECE & TS

## Slide 15
Research topics on pedestal physics

## Slide 16: Optimal RMP configurations for KSTAR
Top-FEC
Mid-FEC
Bot-FEC
FEC coils used for RMP = 3 (poloidal) x 4 (toroidal)
+
-
+
-
+
-
+
-
-
+
-
+
+
+
-
-
-
-
+
+
-
+
+
-
Optimal n=1 RMP
: +90 deg. phase
Optimal n=2 RMP
: +90 deg. phase

## Slide 17: In 2012, ELM-suppressions have been successfully demonstrated using both n=1 or n=2 RMP
#8060
n=2 RMP (mid-FEC only) at q95~4.1
#7821
n=1 (+90 phase) RMP at q95~6.0
Y. M. Jeon, PRL2012

## Slide 18: A generalized criterion suggested for ELM-suppression
ELM-suppression requires
B*R95BR(N=0.95)/BT
B*R95  610-4
+
+
-
-
-
-
+
+
-
+
+
-
#7821
q95~6.0
BR(N=0.95)
~13.7G
n=1 +90 deg
q95~4.1
BR(N=0.95)
~10.97G
#8060
-
+
-
+
n=2 mid-FEC
#7821 (n=1, +90 deg)
BR(N=0.95)/BT =13.7x10-4/1.8
~7.71x10-4
#8060 (n=2, mid-FEC only)
BR(N=0.95)/BT =10.97x10-4/1.5
~7.31x10-4
Similar ELM-suppression by ‘+90 phased n=2 RMP’ is expected with less FEC currents if the generalized criterion is valid, since ‘+90 phased RMP’ is more resonant by a factor of 1.7.

## Slide 19: ELMs suppressed using +90 phased n=2 RMP
#9286: Ip=0.65MA, BT=1.8T  q95~4.0
ELM suppression under 6.0kAt n=2 RMP at q95~4.0
Initially ELMs mitigated by n=2 even (top/bot) RMP
As mid-FEC currents added (n=2,+90 RMP), ELMs further mitigated and then suppressed
Note that ELM-suppressed phase showed better confinements than that in ELM-mitigated phase
- See changes on <ne>, Wtot, and p
#9286
n=2 even (top/bot)
n=2 (+90, top/mid/bot)

## Slide 20: ELM responses to n=2 RMP field strength
Blue points: ELM mitigation by different n=2 FEC currents in identical discharges (q95~4.0)
Strong linear correlation between ELM freq. change and FEC currents
Red point: mitigated ELM at just outside ELM-suppression window of q95 (during q95 scan)
fELM change reached up to a factor of ~10
((Bifurcation))
With 6.0kA n=2 RMP fields, ELM-mitigation was bifurcated to ELM-suppression state
No response
IFEC,threshold
ELM-mitigation
ELM-suppression
Transport bifurcation occurred
(Q) Can we get to the point marked with , by applying IFEC=8.0kAt at q95 outside suppression window ?

## Slide 21: Distinctive fast time scale phenomena that are directly linked to the transition to ELM-suppressed state
Distinctive features observed …
Increased base-level of D
Saturated growth of Te,edge
Increased fluctuation of Isat on divertor
Broadband increase of EM fluctuations
All of these “fast time-scale phenomena” were “precisely synchronized”
How we can understand all of these consistently ?
At the moment of transition to ELM-suppression in KSTAR #7820. RMP was applied in whole period here

## Slide 22: How the uniform broadband increase of EM fluctuations can be produced ?
Features of observed EM fluctuation change
Broadband (actually full range up to ~250kHz) frequency
Uniform spectrum power
At the moment of transition to ELM-suppression in KSTAR #7820. RMP was applied in whole period here
Only possible with a bursty event such as shown in ELM-crashes
cannot be explained with coherent MHD activities
A persistent bursty event may be activated in the plasma edge, which produces broadband EM fluctuations

## Slide 23: Rapidly increased, steady fluctuations on Ion saturation current suggests a persistent bursty event as well
At the moment of transition to ELM-suppression in KSTAR #7820. RMP was applied in whole period here
Rapid increase of Isat fluctuation in the inter-ELM period
Rapid decrease of Isat fluctuation prior to the next ELM crash
Precise synchronization with EM fluctuation
Spiky fluctuation on Isat  bursting event
 A persistent, rapidly repeating bursting event produces a steady spiky fluctuations on Isat

## Slide 24: The persistent bursty event occurred in the plasma edge : Increased D emission near the plasma boundary
Emission from CCD  D
No clear change on topology at the transition
Only emission intensity was increased strongly
The persistent bursting event in the plasma edge leads increased neutral recycling near the plasma boundary, thus increasing D emission

## Slide 25: Scan of position of ECH deposition
ρpol ~ 0.86
ρpol ~ 0.90
ρpol ~ 0.94
ρpol ~ 0.98
TORAY-GA
ρpol ~ 0.86
ρpol ~ 0.94
2nd Harmonics deposition at LFS
Poloidal angle scan
Mitigation stronger at larger ρpol
fELM ~30 [Hz]
∆WELM ~20 [kJ]
∆ neL ~0.16 [1019/m3]
∆Te,ped ~0.4 [keV]
fELM ~60 [Hz]
∆WELM ~ 4 [kJ]
∆ neL 0.05 [1019/m3]
∆Te,ped 0.3 [keV]
fELM ~90 [Hz]
∆WELM ~2 [kJ]
∆neL 0.06 [1019/m3]
∆Te,ped 0.15 [keV]
No ECH
ρpol
~ 0.86
ρpol
~ 0.98
Profiles & fluctuations are
under investigation

## Slide 26
Similar ELM crash but more fluctuation during ELM cycle (J. H. Lee, POSTECH)
w/o ECH
w ECH
Judging from ECEI, there is no significant change in mode structure
Slightly higher m with ECH
Larger fluctuations

## Slide 27
Similar ELM crash but more fluctuation during ELM cycle (J. H. Lee, POSTECH)
Low freq fluctuations
(10 kHz)
Localized in pedestal
Similar modes also in density fluctuation
(by D-BES)
10% drop of density
Strong pump-out
at midplane injection

## Slide 28
Issue of TS calibration
Only relative change must be considered
Large scatter in TS Te at SOL region
Change of pedestal profile during ECH injection
ELM averaged difference of pedestal profiles
w/o ECH
w ECH
t=7.095 s (w/o ECH)
t=8.095 s (w ECH)
t=7.095 s (w/o ECH)
t=8.095 s (w ECH)

## Slide 29: Temporary transition to grassy ELMs by Supersonic Molecular Beam Injection
8ms pulse
10ms pulse
Type-I like
Type-III like
Grassy ELMs
Marginal drop of stored energy

## Slide 30
A simple cellular automata model predicts best mitigation case with shallow deposition of SMBI
f / f0 : ELM frequency ratio
(f0 = w/o AGI)
<A>/<A0> : ELM amplitude ratio (A0 = w/o AGI)
(%)
(%)
Scanning SMBI deposition size and injection location
Region for effective mitigation
deposition point (0 = pedestal top, 1 = pedestal edge)
amount of deposition (δn) divided by line averaged pedestal density (n)
x
y
Pedestal base injection effectively mitigates ELM with deposition size greater than a critical level.
Critical deposition size is minimum number of grains which can drive a pedestal cell over hard limit.

## Slide 31
Near term research plan in pedestal physics
Fast pedestal profile measurements
ELM-resolved full sets of pedestal profiles for detailed stability analysis
Detailed cross-validation of all the dynamic parameters
pped : TS(2012), profile reflectometry(2013), r-ECE(2010), Li-BES (2013), t-CES(2010)
j|| + Er + Vp,t : MSE(2015), Li-Zeeman(2015), p-CES (2015), ECEI (2010)
ELM physics/control in ITER relevant condition
  Extension of ELM control technique to ITER based on physics understanding
  Validation of long-pulse RMP suppression in ITER Similar Shape
  Detailed measurements of profile & fluctuation change during ELM control
  Searching for small/no ELM regimes (drsep, I-mode, QH-mode, …)
Transport in pedestal region
  ELM dynamics and identification of background turbulence in the pedestal region
  Validated local measurements of k||, k┴ & v┴ : DBS, MIR and D-BES
  Identification of background transport (Micro-tearing, Flow-shear ITG, k-Ballooning, …)
  Relation between fluctuations and transport : radial particle & thermal pinches
L-H transition Physics
  Mechanism for L-H & H-L transition
  Effect on L-H transition by SMBI & RMP : minimizing power threshold in ITER
  I-phase during H-L back transition : slow back-transition

## Slide 32: KSTAR Doppler Reflectometry (2014)
V-band X-mode Doppler Back-Scattering (DBS) System
Heterodyne system using a single side band modulator (SSBM)
Frequency regime in the plasma edge : V-band (50-75 GHz)
Antenna tilt angle Θo : 10°-12°
max. k⊥= 5.5-6.5 cm-1 @ 75 GHz
fD ~ 1.7-2.6 MHz @ u⊥~20-30 km/s (H-mode)
k⊥ ≈ 2kosinΘo
ωD ≈ u⊥k⊥
u⊥ = vE×B +vph
Er ≈ -vE×B B
pedestal regime

## Slide 33: Lithium-beam Zeeman polarimetry (2015)
KSTAR Li-beam system was successfully commissioned in 2013.
Parameter | 
Diameter | 2 cm (FWHM / fully focused in the plasma), 10 cm (defocused)
Current | 2-4 mA
Energy | 60 keV
Pulse Length | 20 s
Species | Lithium (possible upgrade to Sodium)
The Li-Zeeman emission is at its maximum around the pedestal region (R=2.22–2.25 m).
The Zeeman split greater than the instrumental broadening was observed with Bt > 2.8T. Li-beam emission.
9426
9239
9427
LOS*
NBI
LiBeam
For the Zeeman polarimetry to measure the edge J(r), vertical views are more preferred.
*Lines of sight in 2013 are
horizontal at the midplane.
calculation
measurement