## Slide 1
Turbulence in MAST through the eye of BES
Michael Fox1,2,3, Anthony Field2, Young-chul Ghim4, Alex Schekochihin1,3 and Ferdinand van Wyk1,2
1Rudolf Peierls Centre for Theoretical Physics, University of Oxford
2Culham Centre for Fusion Energy, UK
3Merton College, Oxford, UK
4KAIST, Daejeon, Republic of Korea
25/11/2015 PPPL
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Show eye then title when beginning

## Slide 2
Motivation: Flow shear and turbulence
Part 1: Measuring Turbulence in MAST
  Introduction to the BES system on MAST
  BES instrument functions and why they are important
  How to deal with the instrument effects
  An example
Part 2: Effect of flow shear on the turbulent correlation time
  Theoretical constraints on the correlation time
  Experimental verification
Outline

## Slide 3
Flow shear and turbulence
We know from non-linear gyrokinetic simulations of MAST that flow shear is important in determining heat transport [1].
[1] courtesy of Ferdinand van Wyk. APS 2015 contributed JP12.00123. Paper in preparation.

## Slide 4
Flow shear and turbulence
Ultimately we want to know how the experimental turbulent diffusivity* depends on the shearing rate:
We can measure all the turbulent terms on the right hand side with the Beam Emission Spectroscopy (BES) system.
I will focus on how the correlation time depends on shear.
*Derived assuming: And Boltzmann electron response.
Notes: The normal method of measuring the correlation time is using a cross-correlation time delay technique. However, this is very sensitive to small effects, such as fluctuating radial velocities.

## Slide 5
Flow shear and turbulence
By considering the diffusion of a turbulent eddy in the presence of a sheared flow, the ratio of characteristic wavenumbers parallel to the gradient of the shear (x) and perpendicular (y) is given by [2]:
Where we have used the correlation time of the turbulence to give a statistical measure of the tilt of the turbulence.
Therefore, by measuring the ratio of wavenumbers, we can determine the correlation time of the turbulence.
[2] P. Davidson. ‘Turbulence: an introduction for scientists and engineers’. Oxford University Press, USA, 2015.
Notes: On the left hand side here what are we saying is being measured. The LHS is the final ratio of wavenumbers, does this correspond to the maximum amplitude? Is this what we expect to be measuring? Or are we measuring an average quantity?

## Slide 6
Motivation: Flow shear and turbulence
Part 1: Measuring Turbulence in MAST
  Introduction to the BES system on MAST
  BES instrument functions and why they are important
  How to deal with the instrument effects
  An example
Part 2: Effect of flow shear on the turbulent correlation time
  Theoretical constraints on the correlation time
  Experimental verification
Outline

## Slide 7
32 channels with ~2cm separation on 8x4 radial-poloidal grid.
Time resolution of 0.5 ms
Correlation analysis is used to measure:
  Radial correlation length
  Poloidal correlation length
  Radial wavenumber
  Poloidal wavenumber
  Correlation time
  Apparent poloidal velocity
  Fluctuation amplitude
MAST BES
Mid-plane
BES view location
r
Minor radius
Separatrix
Notes: The BES system relies on the neutral beam enters from the right hand side with an injection energy of 70keV (2.6x10^6m/s – for D).
The beam atoms are excited by the plasma ions, with the emission of interest being the n=3 n=2 Deuterium Alpha line. This excitation rate is proportional to the local plasma density.
This line is Doppler shifted by 2-3nm because of the high beam velocity.
The emission is filtered and measured by an Avalanche Photo Diode detector with 32 channels in a 2D grid with 2cm spacing, as shown in the diagram.
The temporal resolution is required as the turbulence correlation time is ~ 10 us.
I will focus only on the spatial parameters in this talk, but I have also determined the effect on the temporal correlation properties.

## Slide 8
We fit the following function to the correlation function:
And define the tilt of the correlation function as
Measuring turbulence
Notes: The correlation function is shown in the top figure. In order to make this figure we have to assume that the turbulence is spatially homogeneous, because we are averaging over space too.
To extract the parameters of the turbulence from this measured data we fit the function given by the equation
  This equation is a combination of a Gaussian and cosine. We can fit 4 parameters, the radial and poloidal correlation lengths and the radial and poloidal wavenumbers.
  As can be seen in the bottom figure this function is a reasonable fit to the data.
As you can see, the radial correlation length in this example is around 2-3 cm. The poloidal length is harder to see because of the wave structure, but is about 10cm. The wavenumber, or simply the tilt can be seen in the shape of the wave structure. This is small here.
Now, without any other considerations, how does this raw correlation function change during a shot?
Note that the fit function isn’t actually this but has offsets for MHD. Also we use the Mirnov Hunter. And we fix kZ and lZ because we only have 4 poloidal channels.

## Slide 9
Some terminology
BES measures a field of intensity fluctuations
We really want to know the density fluctuation field:
And for comparisons with theory need to know these in the plasma frame (rotating with the plasma and field aligned)
BES measurement
Lab frame
Lab frame
Plasma frame
Instrument Function

## Slide 10
BES Instrument Functions
Point-Spread Functions (PSFs) quantify the instrument effects.
Shape given by finite lifetime of atomic state and integration along the lines of sight.
Spatially and temporally dependent on equilibrium parameters.
Notes: We also know the instrument functions of the system, quantified by the PSFs, which effectively describe the area over which each detector channel can receive light from.
The shape of the PSFs is determined by:
  The finite lifetime of the excited state of the beam atom (3 – 10ns), which gives a width of ~1cm.
  The finite width of the neutral beam, which means that, we have to integrate along the line of sight through the beam. This gives the tilted shape of the PSFs seen in the figure, which is mainly due to the field line curvature.
Note that the PSFs change during a shot, mainly due to the change in the pitch angle of the field.
The PSFs are different for each channel, because of the change in the pitch angle of the field into the plasma.
We characterise each PSF by using a principal component analysis that measures the two lengths and the tilt of the PSF.
Need to discuss that the irregular shape
We note here that the typical sizes of the PSFs are L1~3cm and L2 ~ 1.5cm, while the value of alpha ranges from -90 to -30 degrees in DND plasmas and for LSND plasmas can go to -150 degrees.

## Slide 11
Generate a fluctuating density field from a model that guarantees the lab frame correlation function is of the same functional form as the experimental correlation function.
Apply PSFs numerically using
Can make an analytic prediction assuming:
  All PSFs have the same amplitude;
  All PSFs have the same shape (L1, L2, aPSF); and
  The PSFs can be approximated as 2D Gaussians.
Quantifying the effect of PSFs

## Slide 12
Radial correlation length
Analytic and numerical results agree well.
PSFs cause major difference between BES and lab frame measurements of small radial correlation length.
Typical BES measurement range
Real PSFs
Analytic PSFs
No PSFs
Notes: Need to explain that on the x axis is the plasma frame radial correlation length, and that this matches the lab frame well when measured numerically.
Need to explain what the different cases are.
Need to explain that the solid lines are analytic calculations.
Discuss that for radial correlation lengths that are ~ 3cm there can be large ambiguity between the lab and BES frames.
----- Meeting Notes (05/11/15 13:39) -----
Too much time labouring that Gaussian approximation works. If anyone questions it to work then belabour it.

## Slide 13
Tilt angle
Analytic and numerical results agree within 5 degrees.
Suggests it is reasonable to approximate PSFs as Gaussians.
aPSF = -33o
aPSF = -45o
aPSF = -59o
aPSF = -70o
aPSF = -144o
Real PSFs
Analytic PSFs
No PSFs
Different PSF cases
Notes: Mention agreement between analytic and numerical
Mention good approximation to Gaussian from real
Mention that PSFs can change the tilt angle by up to 50 degrees from what they actually are and change sign
Mention that the difference between the cases is the tilt of the PSF with the ones in the top having –ve tilt and the one in the bottom having +ve tilt, so the measured value depends on the alignment or misalignment between PSFs and correlation function tilts.
----- Meeting Notes (05/11/15 13:39) -----
Emphasise on slide: it is possible to see changes in tilt angle that change the sign of the measured quantities.
Clear up the plot - maybe just plot two example cases.
Highlight two points and do the plot of them to make it clear.

## Slide 14
Inversion
Analytically we can express the lab frame parameters as functions of the PSF and BES parameters.

## Slide 15
Inversion
Requiring real solutions allows the definition of resolution boundaries:
Typical BES measurement range
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Shade region of actual measurements.
Change colour scheme, include only two lines.

## Slide 16
Correcting for PSF effects
GS2 simulation of MAST generates a fluctuating density field
Synthetic BES data
Lab frame
Lab frame
Apply Real PSFs
Apply correction
Simulations performed by Ferdinand van Wyk
Included: Kinetic electrons and ions, experimental ExB shearing rate, full mass ratio.
Notes: We need to test whether the form of the fluctuating field (i.e. the assumptions we’ve made in our model) affects the results. Therefore use GS2 as this has physics.
Need to big up the simulations – mention this has been modified as a test, but that the comparison with experiment matches very well.
----- Meeting Notes (05/11/15 13:39) -----
"BES frame" needs to change. To BES flitered data.
Need to show that I've done some work: Slide with analytical conversion formula given PSFs and measured quantities then analytically convert into real thing. Then flash slide with lots of equations to show them off.
Before moving to physics: enumerate results so far: we have an app that takes what we've measured and what it gives out.
Say the features, i.e. have a new way of measuring tau and new way of measuring ky.
On GS2 slide mention Ferdinand's results and promote his papers.

## Slide 17
Example shot 28155
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Vertical lines and then click through examples showing where they are

## Slide 18
Example shot 28155
Tilt angle vs. time
BES meas.

## Slide 19
Example shot 28155
PSFs also change during the shot
BES meas.

## Slide 20
Example shot 28155
Need to look at the radial correlation length to determine if resolved.
BES meas.
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Label with raw measure values.
Worth saying earlier that the PSF tilt is mainly due to the poloidal magnetic field.

## Slide 21
Example shot 28155
Need to look at the radial correlation length to determine if resolved.
BES meas.
Res. boundary

## Slide 22
Example shot 28155
Need to look at the radial correlation length to determine if resolved.
BES meas.
PSF corrected
BES meas.
Res. boundary
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Change criterion to just one so that it doesn't add confusion. Put plot of lrB vs lrP to show where it is at the end.

## Slide 23
Example shot 28155
Need to look at the radial correlation length to determine if resolved.
Well resolved
BES meas.
PSF corrected
BES meas.
Res. boundary

## Slide 24
Example shot 28155
The corrected tilt angles are then
Well resolved
BES meas.
PSF corrected
BES meas.
Res. boundary

## Slide 25
Example shot 28155
The corrected tilt angles are then
Well resolved
BES meas.
PSF corrected
BES meas.
Res. boundary
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Change green to something else.

## Slide 26
Summary of Part 1
Shown that accounting for PSFs is important when making measurements of the radial wavenumber with BES.
We have developed a method for correcting the measured parameters for the PSF effects:
Plasma frame parameters
BES measurement
Radial correlation length
Perpendicular correlation length
Radial wavenumber
Perpendicular wavenumber
Fluctuation amplitude
Correlation time
Toroidal velocity
Inversion equations
Radial correlation length
Poloidal correlation length*
Radial wavenumber
Poloidal wavenumber*
Fluctuation amplitude
Correlation time*
Apparent poloidal velocity
And mean principal components of PSFs: L1, L2, aPSF
*New methods of measurement

## Slide 27
Outline
Motivation: Flow shear and turbulence
Part 1: Measuring Turbulence in MAST
  Introduction to the BES system on MAST
  BES instrument functions and why they are important
  How to deal with the instrument effects
  An example
Part 2: Effect of flow shear on the turbulent correlation time
  Theoretical constraints on the correlation time
  Experimental verification

## Slide 28
Flow shear and turbulence
Let us assume the correlation time of the turbulence is related to the shearing rate via
We consider the flow shear weak when
And hence the smallest value occurs when
Which agrees with physical intuition, that the correlation time should not be affected by weak flow shear.

## Slide 29
Flow shear and turbulence
In the strong flow shear regime
Which can only be satisfied if
Therefore, we have the constraint that

## Slide 30
Flow shear and turbulence
Plotting tilt angle against shear we expect:
Intermediate?
Weak shear
Maximum possible value in strong shear regime.
Notes: The obvious questions are then:
  Can we see this transition?
  If this does occur, at what value of gammaE does this occur?
  And what value of kx/ky does this occur?

## Slide 31
BES database
We can apply the PSF correction to all the measured BES data in our database of turbulent and equilibrium parameters.
Currently only contains 20 shots with PSFs processed. Consider:
  L-mode
  Double-null divertor
  Core turbulence: 0.4 < r/a < 0.65
Using the “well resolved” criterion removes a large proportion of the measured data points.

## Slide 32
Tilt variation with Flow Shear
Lines are theoretical curves, is taken from Biglari 1990.
Insufficient data to determine the value of in each shear regime
Probable outliers
Notes: Need to explain axes of plot. That y=1 corresponds to a tilt of 45 degrees.
Then say that these are the remaining data points from the database.
The curves are theoretical curves NOT fits.
We see that the data points have alpha between 0 and 1 – see the straight lines.
Cannot say what the value of alpha is. But I have plotted the prediction of alpha=2/3 from Biglari. This is suggestive but obviously not concrete.
----- Meeting Notes (05/11/15 13:39) -----
Tell them what tau_st is - qR/vth.
Change omega to gamma.

## Slide 33
Comparison of methods of measuring the correlation time shows order of magnitude agreement
CCTD method gives correlation times with much larger errors
Tilt variation with Flow Shear
Using tilt angle method
Using CCTD method
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Tell them what tau_st is - qR/vth.
Change omega to gamma.

## Slide 34
Radial correlation length
No measureable change with shear.
Notes: Note that this does not change with shear. BUT it might be a result of our selection of resolved data!

## Slide 35
Perp. (y) correlation length
Increases with shear
Notes: The lower data points might be below the resolution limit but can still see a trend in the resolved regime at the top of the line.

## Slide 36
Wavenumber dependence
See that both wavenumbers change with flow shear
At high flow shear:
Notes: Mention that the reduction in ky is consistent with what McKee sees in DIII-D.

## Slide 37
Conclusions
PSFs can dramatically change the measured turbulent parameters, impacting the interpretation of physics results.
Constructed a method to correct for PSF effects and applied to MAST BES data.
Radial correlation length shows no variation with flow shear.
Poloidal correlation length increases with flow shear.
Can use the tilt angle of the correlation function to gain insight into the behaviour of the correlation time.
Tilt angles are consistent with constraints on how the correlation time can vary with flow shear.
The highest tilt observed is approx. 45o at high flow shear.
This occurs when
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Also how does ly change with shear.

## Slide 38
What I haven’t mentioned
Effect of PSFs on measurements of
  Fluctuation amplitude
  Correlation time
  Apparent poloidal velocity
Effect of flow shear on the other measured parameters (above).

## Slide 39
Temperature Gradients
Both temperature gradients increase with shear
At high shear electron > ion temperature gradient.
Ion temperature gradient
Electron temperature gradient
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Tell them what tau_st is - qR/vth.
Change omega to gamma.

## Slide 40
PSFs and fluctuation amplitude
PSFs decrease fluctuation amplitude (as expected).
Analytic calculation of effect matches real PSFs well in most cases.

## Slide 41
Fluctuation amplitude
Fluctuation amplitude shows little variation with flow shear.
But PSF effects change the value of the fluctuation amplitude of some points significantly.
Uncorrected
Corrected

## Slide 42
Variation with flow shear is hard to identify.
Turbulent diffusivity
Notes: ----- Meeting Notes (05/11/15 13:39) -----
Tell them what tau_st is - qR/vth.
Change omega to gamma.

## Slide 43
Turbulent diffusivity
Large errors on data points! Cannot draw conclusions.

## Slide 44
Exponent of Flow Shear

## Slide 45
The CCTD technique
Fit Gaussian to locations of peak amplitudes to extract measure of correlation time.
Poloidally separated channel pairs:
26-26, 26-18, 26-10, 26-2

## Slide 46
The CCTD technique
PSFs have no effect on correlation time, if assume only toroidal velocity.

## Slide 47
The CCTD technique
If the flow is purely toroidal then the measured correlation time will be given by (not accounting for PSF effects*):
However, if we include a fluctuating radial flow that has a magnitude rho* smaller than the toroidal flow and correlation time equivalent to the turbulent correlation time then:
*In this case PSFs have no effect on the measured correlation time. However, including a radial flow with PSFs there is a difference.

## Slide 48
The CCTD technique
Cross-correlation function with radial velocity.

## Slide 49
The CCTD technique

## Slide 50
The CCTD technique
Heat diffusivity using correlation time from CCTD on points from Tilt method.

## Slide 51
Equilibrium data ranges
Means and standard deviations for parameters of interest over all data points in experimental plots.
 | Mean | Std. dev. | Fractional variation
R/LTe | 5.79 | 2.14 | 0.37
R/LTi | 6.29 | 1.97 | 0.31
R/Lne | 3.40 | 1.07 | 0.31
r/a | 0.53 | 0.077 | 0.14
q/eps | 8.27 | 1.53 | 0.18
dn/n [%] | 0.51 | 0.16 | 0.32
gammaE tau_st | 0.46 | 0.24 | 0.51

## Slide 52
Equilibrium data ranges 2
Means and standard deviations for parameters of interest over all data points, excluding outliers*, in experimental plots.
 | Mean | Std. dev. | Fractional variation
R/LTe | 5.96 | 2.21 | 0.37
R/LTi | 5.74 | 1.44 | 0.25
R/Lne | 3.69 | 0.81 | 0.22
r/a | 0.54 | 0.073 | 0.14
q/eps | 8.58 | 1.41 | 0.16
dn/n [%] | 0.52 | 0.16 | 0.31
gammaE tau_st | 0.48 | 0.25 | 0.52
* Outliers are taken to be those with tilts < 0, which occur late in the shots and the 27276 data at ~ ¾ of the way through the shot, that show significant difference in R/Lne, q/eps, and R/LTi compared to the other data points. (R/LTi > R/LTe)

## Slide 53
Selection Criteria
To identify reliable data from our database we have the following requirements:
  Well resolved – from PSF definitions.
  L-mode.
  No RMPs.
  DND discharges.
  Mean measured intensity >= 0.3 V.
  Time < 0.95 max(time) – removes points near end of shots i.e. when the plasma collapses.
  0 < Normalised shear < 1.5, error of normalised shear < 1.2. (only consider +ve shear as –ve shear is indicative of plasma breaking).
  1 <= q <= 5.
  All 0.0 <= R/Lx <= 25.0, x=(Ti, Te, ne).
  0.4 <= r/a <= 0.8 (actually all in range 0.4 < r/a < 0.65).
  All data inside LCFS.
  Homogeneity measure <= 0.5 (based on spatial variation of fluc. amps.).

## Slide 54
Example shot 28155