## Slide 1: Status of H-mode Discharge Development on NSTX-U
Devon Battaglia
On behalf of the entire NSTX-U team
NSTX-U Monday Science Meeting
April 25, 2016

## Slide 2: Outline
Three unique H-mode scenarios have been observed during NSTX-U commissioning
  Differentiated by the nature of MHD activity and operational limits
H-mode scenario development has benefited from continued improvements in EFC
Scenario that produced the best discharges to date was difficult to repeat in the final week of operations
  Appears discharges were running with low q shear
Working toward establishing target ELMy H-mode scenarios over a range Ip and Bt to support XPs
  Preference is scenarios with periods of minimal MHD activity

## Slide 3: Best H-mode discharges at each maintenance break
Typical shape for
204118
204112
203679
Typical shape for
202946
202946 Feb – no EFC
203679 March – EFC v1
202112 April – EFC v2
202118 April – EFC v2

## Slide 4: Three notable H-mode scenarios have been achieved with different MHD & “limits”
High li (> 0.8)
  Bursty modes keep βN < pressure peaking limit
  Max βN ~ 5 at li ~ 1.15, βN/li ~ 4.4 (EFC v1)
Mid li (~ 0.7)
  Early mode limits rise in βN with qmin < 2
  Mode disappears, followed by desired period of reduced MHD until βN/li ~ 4.4 (EFC v1)
Low li (~ 0.6)
  Elevated qmin, minimal early mode
    βN/li > 4.4 is ok with qmin > 2
  Entrance of qmin = 2 with βN/li > 4.4 was a problem until 2nd version of EFC
  Minimal MHD, shots can approach no-wall limit
  Difficult to repeat, sensitive to details of L-H transition
204112
203679
q0 ≤ 2
q0 ≤ 2
204011
q0 ≤ 2
L-H
L-H
L-H
βN/li ~ 4.4

## Slide 5: Three operational limits observed (Dataset using first version of Low-β EFC)
Green points near Fp limit
Blue points exceed βN/li limit
Orange points exceed
q*/qmin limit
Database of EFIT02 equilibriums, PNBI > 2 MW, ne,edge > 1013 cm-3
Limit depends on qmin

## Slide 6: High-li scenario moves along Fp limit until it gets to βN/li ~ 4.4 with qmin < 2
Fp = p0/<p> EFIT02
Record βN at li = 1.08
L-H

## Slide 7: High-li scenario moves along Fp limit until it gets to βN/li ~ 4.4 with qmin < 2
L-H

## Slide 8: Mid-li and low-li appear to have qmin > 2 for a period following L-H transition
βN/li < 4.4 with qmin < 2
  Limit with EFC v1
  Mid li has early mode that keeps βN/li < 4.4 at entry of qmin = 2
Low li: βN/li > 4.4 at qmin > 2
  No βN/li limit with qmin > 3
  βN/li < 4.8 when 2 < qmin < 3
  Entry of qmin = 2 with βN/li > 4.4 ends the shot
High li
Mid li
Low li

## Slide 9: Entry of qmin = 2 surface when βN/li > 4.4 ends “low-li” shots (with EFC v1)
“Low-li”
“Mid-li”

## Slide 10: βN/li limits increase with next version of EFC
New phase of EFC for last week of ops
  EFC v2 from compass scan with 1MW heated L-mode
    Previous version: shot length metric in ohmic L-mode
Discharges now survive entry of qmin = 2, βN/li > 4.4
  Late beam (450ms) raises βN/li toward 6
    βN/li ~ 6 NSTX no-wall limit
High li
Mid li
Low li

## Slide 11: Best shots also approach Fp limit
High li
Mid li
Low li
Light green:
Blue & green conditions

## Slide 12: Best shot (204112) has long phase with minimal MHD with qmin < 2

## Slide 13: DCON confirms NSTX-U above the no-wall limit; NSTX-based model gives good estimate
NSTX-U H-mode discharges: 204112
204118 (April 2016)
DCON
Above no-wall limit
Below
Composite no-wall limit model
DCON
Above no-wall limit
Below
Composite no-wall limit model
NSTX no-wall limit model ([J.W. Berkery et al., Nucl. Fusion 55, 123007 (2015)]) includes internal inductance, pressure peaking, and aspect ratio, predicts NSTX-U DCON no-wall limit
J.W. Berkery, S.A. Sabbagh (Columbia University)

## Slide 14: Low-li scenario exhibited low repeatability
A number of low-li scenario shots end ~0.3s with q*/qmin < 1
  q* = ε(1+κ2)πaBT0/μ0Ip
  Ratio less than one indicates very little q shear
  Almost all low-li scenarios use NBI: 1C, 1B and 2A
  Evolution very sensitive to L-H timing, density
Future: increase κ to raise edge q in rampup

## Slide 15: Wall conditioning & control development
H-mode development XMPs were run immediately following full-bottle boronizations
  First 1-3 shots following boronization had Type-III ELMs
  Oxygen steadily rises with each full-power discharge
  First two times this was done: the L-H transition became less dependable by the end of the day (~ 20 full power shots)
  Final time, the L-H transition was reliable at the end of the day
    Increased PNBI prior to transition from 4 to 5 MW
  Final week, started ¼ bottle evening boronizations
    Looks viable to support ½ day H-mode experiments
X-point and drsep control integrated into a mid-li H-mode scenario
  Valuable tool for easier shape changes, dependable timing of diverting and L-H transition

## Slide 16: Summary
Over the three weeks of operations in March-April:
  Demonstrated repeatability of “mid-li” scenario
    Used this scenario to integrate improved shape control
  Developed “low-li” scenario
    Reduced early MHD and lower li is attractive
    Required improved EFC to get past ~ 0.5s
    Shot was difficult to repeat … source of operational limit is now established and motivates path for future shot development
  Established boronization scheme for the near-term while conditioning the inner divertor plate
H-mode scenario development will next focus on operations over a range of Ip, BT
  Demonstrate robust operation with mid-li scenario and improved control at BT = 0.65T over a range of IP
  Develop target H-mode scenarios at BT < 0.65T
  Continue development of low-li scenario at BT = 0.65T

## Slide 17: Backup

## Slide 18: Three operational limits observed (Dataset using first version of Low-β EFC)
High li
Mid li
Low li
Green points near Fp limit
Blue points exceed βN/li limit
Orange points exceed
q*/qmin limit
Database of EFIT02 equilibriums, PNBI > 2 MW, ne,edge > 1013 cm-3

## Slide 19: Modes appear when βN/li ~ 4.5
203655
203679
203653
(example of an ELM-free shot that transiently gets to large βN/li)
βN/li = 6 5 4
L-H timing

## Slide 20: Crossing q0=2 at βN/li > 4.5 leads to a disruption
203989 no data
204049
203971
Shots before 204061

## Slide 21: XMP-142 Goals and progress …
Develop a repeatable ELMy H-mode discharge
  Done, in a sense, with operations on Monday, March 28
  Shots repeated well until timing of switch in shape control
  However, we want a fiducial that incorporates these later developments …
Introduce drsep and X-point control
  Completed on Thursday-Friday of final week, but not integrated with preferred front end
  Still needs some tuning of diverting shape and inner gap evolution
Increase ELM frequency via higher NBI heating
  This was good, produced our best shots
Lengthen period of reduced MHD using changes to the front end evolution
  Progress: low-li scenario developed (but exploration will never be really done)
Assess impact of fueling sources, beam order
  Progress: established minimum fueling requirements, optimum HFS gas timing
Develop H-mode fiducial over range of Ip
Develop H-mode fiducial for lower Bt
  Not done, although we have a few good shots that span Ip = 0.8 – 1 MA
  Breakdown and rampup viable for IOH = 8kA precharge down to 0.35T

## Slide 22: Operations following 203679 indicated inner divertor needed conditioning
Shot 203679 was the first shot to put considerable power on the inner divertor
  The next five shots failed to get an H-mode transition
  Blamed on elevated oxygen, radiated power signals
One element of
XMP-142 is to
condition lower inner
divertor target to
achieve repeatable
discharges