## Slide 1
Measurement of the NTV offset rotation profile in KSTAR
S.A. Sabbagh1, Y.-S. Park1, J.Y. Kim2, W. Ko2, K.C. Shaing3, Y.S. Bae2, J.G. Bak2, J. Chung2, S.H. Hahn2, Y. In2, Y. Jeon2, J.H. Kim2, J. Ko2, J.G. Kwak2, S.G. Lee2, Y.K. Oh2, H.K. Park4, J.K. Park5, S.W. Yoon2
1Department of Applied Physics, Columbia University, New York, NY, USA
2National Fusion Research Institute, Daejeon, Korea
3National Cheng Kung University, Tainan, Taiwan
4UNIST, Ulsan, Korea
5Princeton Plasma Physics Laboratory, Princeton, NJ, USA
presented at the
NSTX-U Physics Meeting
PPPL
September 12th, 2016
Princeton, NJ
V1.4
(Supported by U.S. DOE grant DE-FG02-99ER54524)

## Slide 2: Overview Outline of this Talk
Two parts to this talk
  Main part: (Very) recent measurement of NTV offset rotation profile in KSTAR
  Second separate result: NTV rotation braking with global n = 1, non-pitch-aligned 3D field

## Slide 3: The NTV Offset Rotation Profile was recently directly measured in KSTAR
Motivation
  Plasma rotation highly important for tokamak stability and confinement
  Future fusion devices are envisioned to have far less momentum input
   If sufficiently strong, this rotation could provide stabilization and improved performance in ITER and future devices
Outline
  Goal 1: Use an innovative technique to measure the NTV offset rotation profile on KSTAR for the first time - COMPLETED
    NTV offset Vf profile directly measured
  Goal 2: Use new counter-Ip target plasma to measure the NTV offset rotation profile on KSTAR – TO BE DONE
    Reverse-Ip target plasma under development by Jay Kim

## Slide 4: Present experiment directly measured the V0-NTV profile with no NBI momentum
What did we do?
  Used ECH for plasma heating, avoided issues of strong NBI torque
  Measured intrinsic rotation using NBI as a diagnostic beam for CES
Issues related to experiments with NBI torque
  TNBI term in torque balance
    Is computed, not directly measured
    Is typically much larger than the TNTV component due to offset rotation analysis is prone to error
    The profile of TNBI matters – not just zero net input torque from NBI
Companion experiment to proposed NSTX-U experiment
  Original, approved proposal XP1062 for NSTX using HHFW (2010 !)
  Proposal “NTV steady-state offset velocity at reduced torque with HHFW” submitted to NSTX-U Research Forum (2015)

## Slide 5: Intrinsic Torque due to Neoclassical Toroidal Viscosity (NTV) – a controllable momentum source
Full Theory
  The non-ambipolar difference of ion and electron flux due to the application 3D fields yields a so-called “offset rotation profile”, V0-NTV
  Generally, the local rotation speed can be either in the co- or counter-Ip direction if dominated by electron/ion flux, respectively
    The electron effect is ignored in most papers on the topic
Highly Simplified Theory
  Consider a highly simplified theory to help understand characteristics
  Simplified NTV torque profile: TNTV = C1 dB2 (Vf – V0-NTV)
  Simplified V0-NTV profile: V0-NTV = C2 dTi/dr – C3 dTe/dr (for future analysis)
    Electron effects can dominate at low collisionality – important for ITER
  Unlike “intrinsic rotation”, the TNTV can be controlled by the applied 3D field spectrum and strength
(K.C. Shaing, K. Ida, S.A. Sabbagh, Nucl. Fusion 55 (2015) 125001)
(Y. Sun, K. Liang, K.C. Shaing, et al. Nucl. Fusion 51 (2011) 053015)

## Slide 6: Consider simple torque balance equation to further understand expected dynamics (I)
Simple torque balance
Consider equations with/without 3D field (in steady-state)
Use simple NTV model to express offset rotation
(e.g. W. Solomon, et al., Phys. Plasmas 17 (2010) 056108, Equation 8)
(without 3D field  L(0)  IVI/R)
(with 3D field  L  IV/R)

## Slide 7: Consider simple torque balance equation to further understand expected dynamics (II)
Combine equations
  Assume (TRF + Tintrinsic) not function of 3D field; use simple TNTV model
Expected dynamics
    dB = 0: Vf = VI
    low dB: measured Vf profile close to VI
    increased dB and (|Vf| >> |V0-NTV|): Vf  V0-NTV
    sufficiently high dB: Vf saturates to V0-NTV
- (VI is the toroidal velocity measured without 3D field applied)
- I  moment of inertia
dB
VI
Vf
V0-NTV
a)
b)
c)
d)
(on each y surface)

## Slide 8: Technique to measure NTV offset Vf profile
Brief summary of success (~ 10s long pulses)
  NBI used as diagnostic worked well – CES has good data – Vf profile measured
  n = 2 field varied – scans with and without density feedback
    Without density feedback: 2.0, 2.8, 3.2, 4.0 kA/turn
    With density feedback: (at least) 1.0, 2.0, 2.4, 2.8, 3.2, 4.0 (dB2 factor of 16 change)
  Clear changes to CES measured Vf evolution due to varied n = 2 field strength
t(s)
Ip (MA)
t(s)
Ip (MA)
3D
field
ECH
4.0 kA
ECH
NBI A
NBI B (and add C if needed by CES)
140 GHz ECH
(core deposition)
2.8 kA
Measure here
2.8s
6.3s

## Slide 9: Results from first time point measured (2.8s)

## Slide 10: Two techniques were used to measure the rotation profile approaching V0-NTV
CES rotation profile extrapolated back to start of NBI
  Involves an extrapolation 10 - 20 ms earlier in time
  similar to technique used by Podesta on NSTX (2009) to measure intrinsic rotation in HHFW plasmas
CES rotation profile analysis re-analyzed to the earliest possible time after the start of NBI
The best technique to use is still being evaluated
  CES was re-analyzed just a few days ago
  Results are qualitatively similar, exact rotation values change a bit
  Will show results from both techniques

## Slide 11: Analysis of CES data and NBI diagnostic technique measures intrinsic Vf from ECH
The excellent (low error) KSTAR CES diagnostic required for this analysis
Vf (km/s)
R (m)
t = 2.805s (extrapolated)
t = 2.815s (extrapolated)
t = 2.825s
t = 2.835s
t = 2.845s
t = 2.855s
Intrinsic rotation profile at tNBI = 0
Co-NBI spinup
16317

## Slide 12: Condition a): the intrinsic Vf from ECH establishes our dB = 0 reference Vf profile
Note: core rotation speed is FAR slower than with NBI (by ~ factor 5 - 10)
Vf (km/s)
R (m)
Intrinsic rotation profile dB = 0
16317
t = 2.805s (extrapolated)

## Slide 13: Condition b): at 1.0 kA/turn, dB is small and Vf is close to the Vf with no 3D field
Vf (km/s)
R (m)
16317 (0.0)
16313 (1.0)
t = 2.805s
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0

## Slide 14: Condition c): at 2.4 kA/turn, dB is sufficiently large to make Vf approach V0-NTV
Vf (km/s)
R (m)
16317 (0.0)
16314 (2.4)
t = 2.805s
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0
    Clear change in rotation profile
    Velocity increases on outer surfaces

## Slide 15: Condition d): at 3.2 kA/turn, dB is sufficiently large to make Vf saturate to V0-NTV in the core
Vf (km/s)
R (m)
16317 (0.0)
16314 (2.4)
t = 2.805s
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0
16315 (3.2)

## Slide 16: Condition d): at 4.0 kA/turn, dB sufficiently large to make Vf saturate to V0-NTV in core+outer region
The saturated rotation profile  V0-NTV
Vf (km/s)
R (m)
16317 (0.0)
16315 (3.2)
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0
16316 (4.0)
t = 2.805s

## Slide 17: Unique result: resulting saturated V0-NTV profile is in the co-Ip direction – electron NTV dominates
Consistent w/theory: The ratio of ion to electron NTV torque is (Ti/Te)3.5(Mi/Me)0.5=0.15
  electron NTV offset should dominate
  theory expects V0-NTV in the CO-Ip direction
First time that
  NTV offset profile directly measured
  NTV measured in the co-Ip direction
Notably strong velocity shear in outer region
Vf (km/s)
R (m)
Co-Ip direction
Measured V0-NTV profile
16315, t = 2.805s

## Slide 18: Comparison of V0-NTV profile to gradient in T profile shows a correlation: Ti profile
Weaker Ti gradient in the core  weak V0-NTV
Stronger Ti gradient further out  stronger V0-NTV
Vf (km/s)
R (m)
Ti (eV)
Measured V0-NTV profile
Measured Ti profile (CES)
Strong ÑTi
16315, t = 2.805s
16316, t = 2.825s

## Slide 19: Comparison of V0-NTV profile to gradient in Te profile requires further analysis
Te is about 5 times larger than than Ti
Stronger Te gradient seems to be inside stronger V0-NTV region
  Need to check the ECE mapping to R
Vf (km/s)
R (m)
T (keV)
16315, t = 2.805s
Measured V0-NTV profile
Te profile (ECE)
16316, t = 2.825s
Ti profile (CES)
16316, t = 2.80s

## Slide 20: Results from second time point measured (6.3s)

## Slide 21: Condition a): the intrinsic Vf from ECH establishes our dB = 0 reference Vf profile
Vf (km/s)
R (m)
t = 6.305s
(CES re-analysis)
Intrinsic rotation profile dB = 0
16317

## Slide 22: Condition b): at 1.0 kA/turn, dB accelerates the core a small amount, slows further out
Vf (km/s)
R (m)
16317 (0.0)
16315 (1.0)
t = 6.305s
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0

## Slide 23: Condition c): at 1.6 kA/turn, core continues to accelerate, while plasma further out slows
Vf (km/s)
R (m)
16317 (0.0)
16314 (1.6)
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0
t = 6.305s

## Slide 24: Condition d): at 2.4 kA/turn, profile is largely saturated, stronger Vf shear forms at large R
Vf (km/s)
R (m)
16317 (0.0)
16314 (1.6)
16313 (2.4)
Shot (IVCC current (kA/turn))
Intrinsic rotation profile dB = 0
t = 6.305s

## Slide 25: Condition d): at 3.2 kA/turn, much stronger Vf shear at large R is confirmed
    V-1(dV/dr) (ECH) = 1.1 m-1
    V-1(dV/dr) (V0-NTV) = 15.4m-1
Vf (km/s)
R (m)
16317 (0.0)
16313 (2.4)
16312 (3.2)
Shot (IVCC current (kA/turn))
t = 6.305s
Intrinsic rotation profile dB = 0
Average shear (R > 2.14m)
15 times greater shear !

## Slide 26: Why are the present results unique and important?
Why unique?
  First time that V0-NTV profile has been directly measured w/ TNBI = 0
  First time V0-NTV has been measured dominated by electron effects
    V0-NTV profile measured in the co-Ip direction for the first time
Why important?
  Co-Ip directed V0-NTV can be higher than ECH-induced co-Ip rotation in edge region
  Rotation shear in the outer plasma region is 15 times stronger than rotation shear due to ECH
ITER relevant: |V0-NTV| is strong compared to ITER modeling
  ITER 15 MA simulations: Wf ~ 2 krad/s in edge region
  Recent KSTAR experiment: Wf > 12 krad/s in edge region (scaling?)
  Potential to greatly increase rotation shear in outer plasma region

## Slide 27: Several next-steps to address regarding V0-NTV understanding
Perform non-linear least squares fit of Vf vs. dB2 (at each R)
  This will quantitatively determine how close measured Vf is to V0-NTV
V0-NTV profile scaling with plasma parameters
  Data from present experiment may provide some answers
V0-NTV profile comparison to theory – including electron effects
  All known experimental publications only consider V0-NTV ~ d(Ti)/dr
Comparison of present results to ohmic intrinsic rotation
  Results published by S.G. Lee, et al.
Run second part of experiment using reversed-Ip plasma

## Slide 28: STEP 2: Use Counter-Ip to measure NTV offset V profile
Set-up Target Plasma Shots
  For counter-Ip shot (2016) 15884: Bt = 2.3T, Ip = 0.51 MA, q95 = 6, Ip flattop = 1s - 7s; ECH set for BEST OUTER HEATING
Setup for IVCC 3D fields
  Step 2B: Start with IVCC = 4.0 kA (n = 2 midplane coils ONLY - like FIRST STEP of shots 13433 or 13446 )
  Step 2D: Start with IVCC = 4.0 kA (n = 2 midplane + n = 1 non-pitch-aligned (0 deg) - like FIRST STEP of shot 13436 )
t(s)
Ip (MA)
NBI
NBI dropouts for CES (as needed)
t(s)
Ip (MA)
3D
field
0.75s steps
0.75s steps
0.75s steps
NBI source A
NBI source B
NBI source C
ECH
4.0 kA
Step 1 (Completed)
Measurement here

## Slide 29: Second separate result: NTV rotation braking with global n = 1, non-pitch-aligned 3D field

## Slide 30: STEP 3: Isolate NTV torque profile using fast IPS (I)
Set-up Shots
  (2016) Target 15778 (Bt = 1.8T); (2015) Target plasmas 13302 (Bt = 2.0T), 13433 (Bt = 2.6T), 13446 (Bt = 1.8T)
Setup shots for IVCC timing
  Vary applied field magnitude and spectrum (2 or three steps using n = 2 midplane; n = 1 non-pitch-aligned; n = 1 pitch-aligned  shots 13433 , 13446
  Take second shot, changing the order of the IVCC current steps  shots 13434
t(s)
Ip (MA)
NBI
Attempt two or three IVCC levels per spectrum; attempt three spectra / shot if pulse allows
NBI dropouts for CES (~ 0.66 Hz)
A
B
B
A
0.75s steps
n = 2 mid
(4.5s duration)
0.75s steps
n = 1: 0 deg
(4.5s duration)
0.75s steps
n = 1: 180 deg
(4.5s duration)
t(s)
Ip (MA)
NBI
NBI dropouts for CES (~ 0.66 Hz)
n = 1: 0 deg
(4.5s duration)
n = 1: 180 deg
(4.5s duration)
n = 2 mid
(4.5s duration)

## Slide 31: STEP 3: Isolate NTV torque profile using fast IPS (II)
Shots with COMBINED non-resonant field spectra (n = 2 + n =1 non-pitch-aligned)
  Vary applied field magnitude fixed combined spectrum (n = 2 midplane; n = 1 non-pitch-aligned:  shots 13437, 13447
  Take second shot, changing the order of the IVCC current steps  shots 13436
t(s)
Ip (MA)
NBI
Attempt two or three IVCC levels per spectrum; attempt three spectra / shot if pulse allows
NBI dropouts for CES (~ 0.66 Hz)
Ac
Bc
0.75s steps
n = 2 mid, n = 1, 0 deg (non-pitch-align)
(4.5s duration)
0.75s steps
0.75s steps
t(s)
Ip (MA)
NBI
NBI dropouts for CES (~ 0.66 Hz)
Bc
Ac
n = 2 mid, n = 1, 0 deg (non-pitch-align)
(4.5s duration)
n = 2 mid, n = 1, 180 deg (pitch align)
(4.5s duration)

## Slide 32: Important new results were ALSO found in “Step 3” of the experiment (7 shots)
Significantly stronger non-resonant n = 2 NTV braking was found compared to our 2015 experiment, apparently due to high plasma performance (Ti)
The n = 1 non-pitch-aligned field spectrum – concluded last year to allow non-resonant braking – was found to disrupt the plasma this year
  Apparently due to higher Ti this year
  Hypothesis is that stronger non-resonant n = 1 breaking gives way to resonant 3D field penetration and locking
  Reduces confidence that n = 1 non-resonant field can be reliably used for core plasma rotation control

## Slide 33: Stronger n = 2 non-resonant NTV in Monday’s experiment than in 2015
NTV n = 2 braking (2016)
NTV n = 2 braking (2015)
Note: scale change

## Slide 34: Stronger n = 2 non-resonant NTV during 2016 run apparently due to increased Ti
(2016)
(2015)
NTV torque in “1/n” regime scales as Ti2.5

## Slide 35: n = 1 non-pitch-aligned 3D field spectrum now apparently leads to resonant field penetration/locking
NTV braking appears non-resonant to start, but Vf eventually bifurcates
Before 3D field
Non-resonant
period
Profile locked

## Slide 36: n = 1 non-pitch-aligned 3D field spectrum now apparently leads to resonant field penetration/locking
NTV braking appears non-resonant to start, but Vf eventually bifurcates
Non-resonant
period
Resonant field
Penetration/bifurcation

## Slide 37: Supporting slides follow

## Slide 38: STEP 3: Long-pulse shots that need to be taken
  IVCC setup 13434 (type (B)), 13436 (type (Bc))
  IVCC setup 13443 (constant current steps)
  Divertor gas puffing – setup from shots: 13443 (0.6v), 13442 (0.7V)
Bt = 1.8 T
  Suggested 2016 target is 15778; reduce Ip to 0.5 from 0.6 MA and match Ip rise time of a shot like 13433, 13434
  Shots to take:
    type (B) (IVCC setup 13434), type (Bc) (IVCC setup 13436) (2 shots)
    NO divertor gas puff (constant IVCC steps like 13443) (1 shot)
    with divertor gas puff 0.6V (constant IVCC steps like 13443) (1 shot)
Bt = 2.0 T
  Shots to take: (Increase Bt = 2.0T from above)
    NO divertor gas puff (constant IVCC steps like 13443) (1 shot)
    with divertor gas puff 0.6V (constant IVCC steps like 13443) (1 shot)

## Slide 39: MP2015-05-23-001 “Isolation of NTV torque profile” on KSTAR established isolated NTV profile using IPS capability
Results show non-resonant NTV characteristics; broad NTV torque profile
  Dwf does not change sign across profile (non-resonant); Dwf ~ 0 near plasma edge
  3D field spectrum varied: similar Dwf profiles, n = 1 pitch non-aligned has largest NTV
(Y.S. Park, S.A. Sabbagh, Y. Jeon., et al., (approved by U.S. Committee for IAEA FEC 2016)
 Present experiment aims to create distinct NTV profiles  NOT enough time given for this
IVCC n = 2 configuration
n = 1 pitch non-aligned
n = 1 pitch aligned
Plasma rotation
Change in plasma rotation