## Slide 1: Prediction of the nonlinear character of Alfvénic instabilities and their induced fast ion losses
Vinícius Duarte1,
in collaboration with
Nikolai Gorelenkov1, Herb Berk2, Roscoe White1, Eric Fredrickson1, Mario Podestà1,
Mike Van Zeeland3, David Pace3 and Bill Heidbrink4
1Princeton Plasma Physics Laboratory
2University of Texas, Austin
3General Atomics
4University of California, Irvine
Work funded by DOE under contracts DE-AC02-09CH11466 and DE-FC02-04ER54698 and through the SciDAC project “Integrated Simulation of Energetic Particles in Burning Plasmas”
NSTX-U / Magnetic Fusion Science Meeting - March 16th 2020
Notes: V&V exercises, Motivated 2 DIII-D dedicated experiments, Read 5Y plan; talk about CGM (refresh what it is); predictive modeling, transp;
Refresh what was covered at the MIT School
predicting energetic particle transport in Advanced Tokamak scenarios, which is a major Challenge described by the current DIII- D 5-year Plan.

## Slide 2: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 3: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 4: Alfvén waves can exhibit a range of bifurcations upon their interaction with fast ions
Major question: why is chirping common in spherical tokamaks and rare in conventional tokamaks?
Podestà et al, Nucl. Fusion 51 063035 (2011)
Heidbrink, Plasma Phys. Control. Fusion 37 937 (1995)
Each chirp induces fast ion losses
Chirping is a gateway to avalanches
N
NSTX
DIII-D

## Slide 5: Chirping is supported by phase-space holes and clumps
Two typical scenarios for fast ion losses:
Diffusive transport (typical for fixed-frequency modes)
can be modeled using reduced theories
  e.g., quasilinear theory
Convective transport (typical for chirping frequency modes)
Requires capturing full phase-space dynamics
  expensive nonlinear simulations
Stochasticity hinders the formation of holes and clumps, preventing chirping
hole
clump
Lilley and Nyqvist, Phys. Rev. Lett. 102, 195003 (2014)

## Slide 6: Chirping is supported by phase-space holes and clumps
Two typical scenarios for fast ion losses:
Diffusive transport (typical for fixed-frequency modes)
can be modeled using reduced theories
  e.g., quasilinear theory
Convective transport (typical for chirping frequency modes)
Requires capturing full phase-space dynamics
  expensive nonlinear simulations
Stochasticity hinders the formation of holes and clumps, preventing chirping
Resonance Broadening Quasilinear (RBQ) code
(later in this talk)
hole
clump
Lilley and Nyqvist, Phys. Rev. Lett. 102, 195003 (2014)

## Slide 7: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 8: A criterion for the likelihood of chirping onset in tokamaks
Starting point: the evolution equation for mode amplitude A near marginal stability:
Berk, Breizman and Pekker, PRL 1996
Lilley, Breizman and Sharapov, PRL 2009

## Slide 9: A criterion for the likelihood of chirping onset in tokamaks
Starting point: the evolution equation for mode amplitude A near marginal stability:
destabilizing (makes integral sign flip)
Berk, Breizman and Pekker, PRL 1996
Lilley, Breizman and Sharapov, PRL 2009
Blow up of A in a finite time-> system enters a strong nonlinear phase (chirping likely)
stabilizing

## Slide 10: A criterion for the likelihood of chirping onset in tokamaks
>0: fixed-frequency solution likely
<0: chirping likely to occur
Starting point: the evolution equation for mode amplitude A near marginal stability:
destabilizing (makes integral sign flip)
Berk, Breizman and Pekker, PRL 1996
Lilley, Breizman and Sharapov, PRL 2009
Chirping criterion:
Blow up of A in a finite time-> system enters a strong nonlinear phase (chirping likely)
(nonlinear prediction from linear physics elements->incorporated into the linear NOVA-K code )
Duarte et al, Nucl. Fusion 57 054001 (2017)
stabilizing

## Slide 11: A criterion for the likelihood of chirping onset in tokamaks
>0: fixed-frequency solution likely
<0: chirping likely to occur
Starting point: the evolution equation for mode amplitude A near marginal stability:
stabilizing
destabilizing (makes integral sign flip)
Berk, Breizman and Pekker, PRL 1996
Lilley, Breizman and Sharapov, PRL 2009
Chirping criterion:
Blow up of A in a finite time-> system enters a strong nonlinear phase (chirping likely)
(nonlinear prediction from linear physics elements->incorporated into the linear NOVA-K code )
Duarte et al, Nucl. Fusion 57 054001 (2017)
The criterion ( ) predicts that micro-turbulence should be key in determining the likely nonlinear character of a mode, e.g., fixed-frequency or chirping

## Slide 12: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 13: Correlation between chirping onset and a marked reduction of the turbulent activity in DIII-D
Duarte et al, Nucl. Fusion 57 054001 (2017)
Diffusivity drop due to L→H mode transition
Strong rotation shear was observed
This observation motivated DIII-D experiments to be designed to further test the hypothesis of low turbulence associated with chirping

## Slide 14: Dedicated experiments showed that chirping is more prevalent in negative triangularity DIII-D shots
Transport coefficients calculated in TRANSP are 2-3 times lower in negative triangularity, as compared to the the usual positive/oval triangularity
Van Zeeland et al, Nucl. Fusion 59 086028 (2019)
Notes: The TCV results showed that the eigenmodes are more sheared and that contributes to reduce turbulence
zoom the chirping and the fixed-freq

## Slide 15: Dedicated experiments showed that chirping is more prevalent in negative triangularity DIII-D shots
Transport coefficients calculated in TRANSP are 2-3 times lower in negative triangularity, as compared to the the usual positive/oval triangularity
>0: fixed-frequency
<0: chirping
Van Zeeland et al, Nucl. Fusion 59 086028 (2019)
Notes: The TCV results showed that the eigenmodes are more sheared and that contributes to reduce turbulence
zoom the chirping and the fixed-freq

## Slide 16: Dedicated experiments showed that chirping is more prevalent in negative triangularity DIII-D shots
Transport coefficients calculated in TRANSP are 2-3 times lower in negative triangularity, as compared to the the usual positive/oval triangularity
>0: fixed-frequency
<0: chirping
Van Zeeland et al, Nucl. Fusion 59 086028 (2019)
Notes: The TCV results showed that the eigenmodes are more sheared and that contributes to reduce turbulence
zoom the chirping and the fixed-freq

## Slide 17: GTS global gyrokinetic analyses show turbulence reduction for rare NSTX Alfvénic transitions from fixed-frequency to chirping
Before chirping, 265ms
During chirping, 290ms
Electrostatic turbulence fluctuation
Electrostatic turbulence fluctuation
Before chirping, 265ms
During chirping, 300ms
Peak of the most intense mode
Peak of the most intense mode
Duarte et al, Nucl. Fusion 58 082013 (2018)

## Slide 18: Chirping criterion explains different spectral behavior in spherical vs conventional tokamaks
chirping, NSTX
fixed-frequencies, DIII-D and TFTR
Chirping is ubiquitous in NSTX but rare in DIII-D, which is consistent with the inferred fast ion micro-turbulent levels
Similar agreement was later found in ASDEX-U [Lauber et al, IAEA inv. talk 2018]
Arrows represent how much turbulent diffusion changes the prediction with respect to collisions alone
Transport in NSTX in mostly neoclassical at the ion scale
Duarte et al, Nucl. Fusion 57 054001 (2017)

## Slide 19: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 20: Alfvénic chirping is unlikely but cannot be ruled out in ITER
Predictions for the most unstable (n=7-11) TAEs in ITER are near threshold between fixed frequency and chirping, based on TRANSP analysis, requiring Q>10
Duarte et al, Nucl. Fusion 58 082013 (2018)
Notes: Ratio

## Slide 21: Validated chirping criterion predicts when fast ion transport can be modeled with reduced models
Reduced transport models are only applicable when details of phase-space dynamics are unimportant (no chirping modes)
Nonlinear theory has been used to develop a criterion for when chirping is likely to occur
Stochasticity destroys phase space coherence necessary for chirping
  less turbulence favors chirping  confirmed in negative triangularity experiments
  Chirping criterion explains why chirping is ubiquitous in NSTX and rare in DIII-D
    predicts that chirping is possible but unlikely in ITER

## Slide 22: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 23: Critical gradient behavior in DIII-D suggests that quasilinear modeling is a viable tool for fast ion relaxation
Fully nonlinear modeling of fast ion interaction with Alfvénic modes in a realistic tokamak is numerically expensive
Reduced (but still realistic) modeling can be exploited if linear mode properties do not change faster than the equilibrium, e. g.,
  eigenstructure
  resonance condition
Simulations need to cope with the simultaneous excitation of multiple unstable Alfvénic instabilities
Critical gradient is often observed in DIII-D - stiff, resilient fast ion profiles as beam power varies
-stochastic fast ion transport (mediated by overlapping resonances) gives credence in using a quasilinear approach
Collins et al, Phys. Rev. Lett. 116, 095001 (2016)
Notes: fast-ion transport suddenly becomes stiff above a critical threshold in the presence of many overlapping small-amplitude Alfvén eigenmodes

## Slide 24: Resonance-broadened quasilinear (RBQ) diffusion model -a reduced but yet a realistic framework-
-_
Broadened delta
eigenstucture
information
Formulation in action and angle variables
Diffusion equation:
Mode amplitude evolution:
Broadening is the platform that allows for momentum and energy exchange between particles and waves.
  Heuristic broadening recipes historically used
  Physics-based determination of the resonance broadening function was only very recently achieved
The model is applicable for both single/isolated resonances and also multiple and overlapping ones.
Berk et al, Nucl. Fusion 35 1661 (1995); Duarte, PhD thesis (2017); Gorelenkov, Duarte, Podestà and Berk, Nucl. Fusion 58 082016 (2018)

## Slide 25: First-principles analytical determination of the collisional resonance broadening
Duarte et al, Phys. Plasmas 26, 120701 (2019)
The use of the obtained resonance broadening functions implies that essential features of nonlinear theory, such as the growth rate and the saturation level, are automatically built into a reduced QL theory
Broadening functions
Distribution modification
Blue curve: pitch-angle scattering
Red curve: Krook collisions
Starting with the kinetic equation:
(from collisions, turbulence,…)
Near marginal stability, perturbation theory can be employed to show that a quasilinear transport equation naturally emerges, with the resonance functions given by

## Slide 26: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 27: Verification of the analytical predictions against ORBIT simulations of Alfvénic resonances
White, Duarte et al, Phys. Plasmas 26, 032508 (2019)
Red and black: guiding-center ORBIT simulation results for two different levels of collisionality
Green: analytic fit
Modification of the distribution function vs canonical toroidal momentum

## Slide 28
Close to marginal stability2:
Far from marginal stability3:
Undamped case1
Collisionless case
Collisional cases
Expected saturation levels from analytic theory are shown by
1Fried et al, Report No. PPG-93 (UCLA,1972); 2Berk et al. Plasma Phys. Rep, 23(9), 1997; 3Berk and Breizman. Phys. Fluids B, 2(9), 1990
Quasilinear simulations replicate analytical predictions for the mode saturation amplitude from nonlinear theory
Definitions: initial linear growth rate , mode damping rate and trapping (bounce) frequency (proportional to square root of mode amplitude)

## Slide 29: Outline
Part I: Prediction of the nonlinear spectral character of Alfvén waves
Chirping vs quasi-steady frequency responses and the applicability of reduced models
A criterion for the chirping onset
Analysis of NSTX and DIII-D data
Predictions for ITER scenarios
Part II: Reduced quasilinear modeling of fast ion losses
Development of the broadened quasilinear framework
Verification and validation exercises
Integration of the Resonance Broadened Quasilinear (RBQ) code into TRANSP
  modeling of DIII-D critical gradient experiments

## Slide 30: Verification of RBQ runs for the collisional evolution of an Alfvénic wave
Resonance
broadening
Mode
structure
DIII-D discharge 153072
Gorelenkov, Duarte et al, Phys. Plasmas 26, 072507 (2019)
Idealized bump-on-tail scaling (obtained using Dirichlet boundary conditions on both ends of the domain):

## Slide 31: RBQ is interfaced with TRANSP: multi-mode case
Distribution at 805ms - DIII-D shot 159243
11 unstable Alfvénic modes at 805ms
Gorelenkov, Duarte et al, Phys. Plasmas 26, 072507 (2019)

## Slide 32: RBQ is interfaced with TRANSP: multi-mode case
Distribution at 805ms - DIII-D shot 159243
11 unstable Alfvénic modes at 805ms
Gorelenkov, Duarte et al, Phys. Plasmas 26, 072507 (2019)
Collins et al, Phys. Rev. Lett. 116, 095001 (2016)

## Slide 33: Summary
Prediction of Alfvénic spectral character
Chirping criterion determines when reduced models, such as quasilinear, can be applied
  also explains why chirping is more common in spherical tokamaks
DIII-D negative triangularity experiments confirm prediction that chirping is more prevalent when turbulence is reduced
The criterion ITER scenarios are predicted to be near boundary between chirping and fixed-frequency behavior
Quasilinear modeling
The Resonance Broadened Quasilinear (RBQ) model exactly preserves key properties of the full nonlinear system
  Extensively verified and validated
Integration in TRANSP enables predictions in realistic scenarios
  Captures hollow fast ion profiles observed in DIII-D discharges

## Slide 34: Ongoing study on the evolution of toroidal Alfvén modes in DIII-D, with a changing drive due to beam blips
The INPA signal is being used as a proxy for the mode drive
[Duarte and Van Zeeland, in progress]
Amplitude A vs time t for nonlinear simulation (green) and the analytic formula (black)
Duarte et al, Nucl. Fusion 59 044003 (2019)
DIII-D shot 176523
Amplitude evolution for a single mode near marginal stability:

## Slide 35
Thank you

## Slide 36: Backup slides

## Slide 37: First-principle analytical determination of the collisional resonance broadening – part I
Start with the kinetic equation:
Periodicity over the canonical angle allows the distribution to be written as a Fourier series:
(from collisions, turbulence,…)
Near marginal stability, a perturbation theory can be developed in orders of
which leads to the ordering . When memory effects are weak, i.e., ,

## Slide 38: Self-consistent formulation of collisional quasilinear transport theory near threshold
A QL theory naturally emerges when considering kinetic theory near threshold when collisions occur at a time scale faster than the phase mixing time scale.
The QL plasma system automatically replicates the nonlinear growth rate and the wave saturation levels calculated from full kinetic theory near marginality, with a rather complex time-delayed integro-differential equation (Berk, Breizman and Pekker, Phys. Rev. Lett. 1996)

## Slide 39: Determining the parametric dependencies of the broadening from single mode saturation levels
The broadening is assumed with the parametric form where the coefficients and are determined in order to enforce QL theory to replicate known nonlinear saturation levels:
Limit near marginal stability3
→
Limit far from marginal stability4
→
Resonance-broadened quasilinear formalism can cope with both situations of isolated and overlapping modes
3H. L. Berk et al. Plasma Phys. Rep, 23(9), 1997 4H. L. Berk and B. N. Breizman. Phys. Fluids B, 2(9), 1990
Top-hat, square resonance function heuristically assumed

## Slide 40: Characterization of a rarely observed chirping mode in DIII-D
Before chirping, at 900ms: D~1m2/s
During chirping, at 960ms: D~0.2m2/s
TRANSP run
Diffusivity
vs
time
Diffusivity drop due to L→H mode transition
Strong rotation shear was observed
Duarte et al, Phys. Plasmas 24, 122508 (2017)

## Slide 41: A criterion for the likelihood of chirping onset in tokamaks
>0: fixed-frequency solution likely
<0: chirping likely to occur
The criterion ( ) predicts that micro-turbulence should be key in determining the likely nonlinear character of a mode, e.g., fixed-frequency or chirping
Starting point: lowest-order nonlinear correction to the evolution of mode amplitude A:
-_
stabilizing
destabilizing (makes integral sign flip)
Berk, Breizman and Pekker, PRL 1996
Lilley, Breizman and Sharapov, PRL 2009
-_
Chirping criterion:
(nonlinear prediction from linear physics elements->incorporated into NOVA-K code )
Blow up of A in a finite time-> system enters a strong nonlinear phase (chirping likely)
Duarte et al, Nucl. Fusion 57 054001 (2017).

## Slide 43: The overlapping of resonances lead to losses due to global diffusion
Broadened QL theory is designed to address both regimes of isolated and overlapping resonances
  the fast ion distribution function relaxes while self-consistently evolving the amplitude of modes
      H. Berk, B. Breizman, J. Fitzpatrick, and H. Wong, Nucl. Fusion 35, 1661 (1995).

## Slide 44: Correction to the diffusion coefficient: the inclusion of electrostatic microturbulence
Microturbulence can well exceed pitch-angle scattering at the resonance1
From GTC gyrokinetic simulations for passing particles:2
As pitch-angle scattering, microturbulence acts to destroy phase-space holes and clumps
Unlike DIII-D and TFTR, transport in NSTX in mostly neoclassical
Complex interplay between gyroaveraging, field anisotropy and poloidal drift effects leads to non-zero EP diffusivity3
1Lang and Fu, PoP 2011
2Zhang, Lin and Chen, PRL 2008
3Estrada-Mila et al, PoP 2005
Ratio of fast ion diffusivity to thermal ion diffusivity2
Pueschel et al, NF 2012 gives similar microturbulence levels

## Slide 45
Frequency chirping
frequency shift due to trapped particles
does not exist without resonant particles
timescale: ~1ms
Frequency sweeping
frequency shift due to time-dependent background equilibrium
MHD eigenmode
timescale: ~100ms
Two types of frequency shift observed experimentally
Sharapov et al, PoP 2006
Pinches et al, NF 2004

## Slide 46: Nonlinear vs Quasilinear approach
Requires particles to remember their phases from one trapping bounce to another;
Full kinetic approach necessary;
Entropy is conserved in the absence of collisions;
Convective transport.
Requires particles to forget their phase (via collisions, turbulence or mode overlap);
Assumes that the modes remain linear (therefore NOVA is suited) while the distribution function is allowed to slowly evolve nonlinearly in time;
Entropy increases due to particle memory loss (due to phase averaging).
Diffusive transport.