## Slide 1
Effect of 3-D fields on edge power/particle fluxes between and during ELMs (XP1026)
A. Loarte, J-W. Ahn, J. M. Canik, R. Maingi, and J.-K. Park
and the NSTX Research Team
NSTX Team Review
B252, PPPL
July 23, 2010
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Motivation
XP 1046 (Ahn): Effect of 3-D fields below ELM triggering threshold
XP 1048 (Park): Effect of 3-D fields on ELM characteristics with q95 scan
  ELM control in ITER is required for a large range of plasma conditions, not only for flat top of 15 MA QDT =10 scenario
   Dependences of the applied 3-D field effects on divertor power/particle fluxes on plasma parameters need to be determined to understand consequences for ITER stationary conditions and controlled ELM power fluxes
   Compatibility with scenario requirements to be checked: acceptable stationary power flux (high ne divertor), erosion,
Characterization of 3-D field effect above the ELM triggering threshold with parameter scan (I3-D, ν*e, q95, etc)

## Slide 3: Best aligned 3-D magnetic perturbation from XP1048
VAC3D modeling for NSTX expects different ratio of non-resonant to resonant components for different q95
 Smaller ratio for lower q95 is expected. Use the result of XP1048 to figure out best aligned 3-D field perturbation
 Parameter scan at this alignment
NSTX
q95~10
NSTX
q95~6
J.-K. Park

## Slide 4: Parameter scan at best alignment
Ip scan at constant q95
 Higher Ip tends to make the ELM size bigger and likely increase radial transport during ELMs
 Will need to vary Bt to keep q95 constant
Pedestal collisionality scan
 Apply 3-D field at different density levels  Effects on power deposition between ELMs and at ELMs
 Change of PNBI can further change the pedestal collisionality
SOL plasma collisionality scan/divertor density scan
 Apply divertor D2 gas puffing to change SOL/divertor plasma conditions
3-D field coil current scan above the ELM threshold
 Higher coil current tends to produce more frequent ELMs. Need to investigate impact on divertor profiles of smaller ELMs at similar Pped and divertor conditions

## Slide 5: Shot plan
Establish lowest q95 (~6) discharge (140000) to obtain best aligned 3-D field spectrum with ELM triggering. Scan 3 coil current levels (eg, 1, 1.5, and 2kA)  Total of 3 shots
Perform Ip scan at constant q95 (~6). Try three Ip values, 700, 900, 1100kA  Total of 3 shots
SOL plasma collisionality scan. Try two divertor D2 gas levels (3000 and 1500Torr of Bay E GIS), 2 shots for each plasma condition
 Total of 4 shots
Pedestal collisionality scan. Apply 3-D field blips at three time slices during the density ramp-up in the H-mode. Try 2 NBI power levels (PNBI=2, 5-6MW), Ip  Total of 2 shots
Misalign 3-D field coil spectrum by changing q95, i.e. Dq95 = 2, by the means of Bt change (0.45T and 0.55T) at fixed Ip (700kA)
 Total of 3 shots