## Slide 1: Overview of Initial NSTX-U Plasma Operations
Devon Battaglia
On Behalf of the NSTX-U team
NSTX-U PAC 37
January 26 - 28, 2016

## Slide 2: Summary of NSTX-U Plasma Operations
CD-4 milestone (Ip > 50kA) completed August, 2015
  Ip ~ 150 kA with GDC and CS bake
2.5 days of operation following full vessel bake, before boronization (December, 2015)
  Ip = 500 kA flattop with inner-wall limited L-mode
  Progress enabled by Ip, gap and Z feedback control
2.5 weeks of operations in January, 2016
  Neutral beam heating: up to 4MW total from four sources
  Diverted L-mode and H-mode operations at Ip = 600 kA
    Good progress toward goal: 1.4 MA, 2s ELMy H-mode by week 8
  Three boronizations completed

## Slide 3: Significant progress over the first few weeks in commissioning NSTX-U
Boronization
First NBI
H-mode
Boronization
Boronization
Maximum Stored Energy (kJ)
Diverting

## Slide 4: Reliable H-mode access has been achieved on NSTX-U
H-mode with NBI > 1.5 MW at Ip > 500 kA, BT = 0.65T
  H-mode achieved with only 0.9 MW NBI in a few cases
  BT exceeds maximum in NSTX
202946
Odd n MHD (G)
Stored energy (kJ)
MHD efit01
Inner gap
(cm) efit01
Lower divertor

## Slide 5: Excellent diagnostic availability has enabled rapid progress
Ip | 0.58 MA
BT0 | 0.61 T
PNBI | 3 MW
POH | 0.2 MW
A | 1.6
κ | 1.53
li | 0.97
δlower | 0.55
W | 151 kJ
βT | 7.86%
βP | 1.22%
βN | 4.66
τe | 50 ms
ψN
202946
L-mode 0.30s
H-mode 0.48s
Lower div Dα
Mid Dα
LFS gas
HFS gas
Divert
L-H transition
ELMs

## Slide 6: Stationary diverted L-mode operations has also been achieved
26 kA swing
1 MW NBI
202814
These discharges have already been used to support research operations

## Slide 7: Significant progress has been made on a number of commissioning activities
XMP-101: Inductive startup on NSTX-U
XMP-106: Magnetics calibration
XMP-126: Initial Ip and R control
XMP-105: Initial n=0 control
XMP-118: Boronization characterization
XMP-127: Neutral beam checkout
XMP-132: Automated rampdown development
XMP-107: Neutron calibration transfer
XMP-133: Increase elongation in L-mode
XMP-116: Initial H-mode access in NSTX-U
XMP-121: Six SPA and RWM coil checkout
XP-1506: Low-beta locked mode studies

## Slide 8: Inductive startup scenario informed by vacuum field modeling
Solenoid provides confining BZ
  Bipolar PF3 coils null this field
  Vloop via ramping OH and PF3 fields
Null properties sensitive to fields from induced wall currents
  LRDFIT wall model used to prepare scenarios in advance
  About 200 kA total wall current at breakdown
PF3 and PF5 coils provide additional Bp following breakdown
  Must maintain passive R and Z stability
Simulated Bp fields at breakdown
PF3

## Slide 9: Startup scenario identified via calculations enabled rapid progress in achieving CD-4
Shot #5
Shot #11
50 kA CD-4 requirement

## Slide 10: Loop voltage required for breakdown in good agreement with calculations
Vloop = 2.0 V
Vloop = 2.4 V
Vloop = 2.5 V
Vloop = 3.3V
Vloop = 3.7 V
Model:
Experiment:
Lloyd parameter:
NSTX
ITF = 65 kA
IOH = 24 kA
NSTX-U
ITF = 80 kA
IOH = 8 kA
NSTX-U
ITF = 80 kA
IOH = 20 kA

## Slide 11: Routine startup at two OH precharge levels has been demonstrated
Goal: scalable scenario for arbitrary OH precharge
  Some experiments desire flexible precharge to optimize constraints from coil heating and coil current limits
Limited L-mode Helium
202567
202573

## Slide 12: New capability: automated rampdown used in routine operations
Plasma control system detects loss of control
  OH solenoid near maximum current
  Vertical oscillations exceed threshold
  Abs( Ip - Ip request ) too large
Feedback control switches to new “states” that attempt to gently end the discharge
See S. Gerhardt’s talk
IP
IP Request
(including asynchronous transition to rampdown)
  ZP(dZP/dt)
  ZP(dZP/dt) threshold
Normal
Fast IP Rampdown
Insufficient IP
  ZP from EFIT
“State”

## Slide 13: Digital coil protection system successful in preventing unacceptable coil operation
Vertical force on PF1A
+ IPF1A
- IOH
Example of a hard shutdown in response to a force limit
More details in Facility Status talk (M. Ono)

## Slide 14: First boronization had positive impact on discharge performance
Flux consumption and oxygen content reduced
Measurements of boron deposition and impurity migration have been completed (see M. Jaworski’s talk)
202439
202532
Limited L-mode Helium

## Slide 15: Operations will restart with continued goal of developing fiducial ELMy H-mode discharge
H-mode operations open path to lower li
  Permits larger κ and Ip range
  Target li ~ 0.5 via an earlier L-H transition, larger NBI power and improved wall conditions
Target fiducial for FY2016 is an ELMy H-mode discharge at Ip = 1.4 MA
Average stored energy over flattop
140
120
100
80
60
40
20
0
<W>FT (kJ)
1.5
1.0
0.5
0
<li>FT
Average li over flattop
First 66 shots: L-mode He

## Slide 16: Operations will restart with continued goal of developing fiducial ELMy H-mode discharge
H-mode operations open path to lower li
  Permits larger κ and Ip range
  Target li ~ 0.5 via an earlier L-H transition, larger NBI power and improved wall conditions
Target fiducial for FY2016 is an ELMy H-mode discharge at Ip = 1.4 MA
Average stored energy over flattop
First H-mode
First H-mode
140
120
100
80
60
40
20
0
<W>FT (kJ)
1.5
1.0
0.5
0
<li>FT
Average li over flattop
First 66 shots: L-mode He
Next 66 shots: L-mode D, NBI

## Slide 17: Operations will restart with continued goal of developing fiducial ELMy H-mode discharge
H-mode operations open path to lower li
  Permits larger κ and Ip range
  Target li ~ 0.5 via an earlier L-H transition, larger NBI power and improved wall conditions
Target fiducial for FY2016 is an ELMy H-mode discharge at Ip = 1.4 MA
Average li over flattop
Average stored energy over flattop
140
120
100
80
60
40
20
0
<W>FT (kJ)
1.5
1.0
0.5
0
<li>FT
First 66 shots: L-mode He
Next 66 shots: L-mode D, NBI
Last 66 shots: Diverted

## Slide 18: Ongoing commissioning activities will prepare NSTX-U for research program
Near-term activities include …
  Optimization of vertical control (see S. Gerhardt’s talk)
  ISOFLUX shape control
    rtEFIT has been successfully running and is ready to support operations
  Error field identification and correction
    Low-beta error field measurements have been completed
  Diagnostic commissioning and calibration
    MPTS, CHERS, MSE, NPAs, FIDA
  NBI power modulation for β control from PCS
    PCS control of beam termination has been used
  MHD spectroscopy and RWM control
    Real-time mode detection in PCS is nearly complete
Covered in detail in Jon Menard’s talk

## Slide 19: Plasma operations on NSTX-U is off to a great start!
First days of NSTX-U have produced H-mode and stationary diverted L-mode discharges
Control and diagnostic capabilities established quickly
Research program starting in parallel with commissioning activities