## Slide 1: Plasma control algorithm development on NSTX-U using TRANSP
Dan Boyer
for the Integrated Scenarios science group
NSTX-U Program Advisory Committee Meeting (PAC-37)
January 26, 2016

## Slide 2: NSTX-U Mission Elements 5 Highest Research Priorities
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
  Understand confinement and stability at high beta and low collisionality
  Study energetic particle physics prototypical of burning plasmas
Develop solutions for PMI challenge
3.Dissipate high edge heat loads using expanded magnetic fields + radiation 4.Compare performance of solid vs. liquid metal plasma facing components
Advance ST as possible FNSF / Pilot Plant
5.Form and sustain plasma current without transformer for steady-state ST

## Slide 3: TRANSP routinely used in interpretive mode, increasingly in predictive mode
Interpretive TRANSP
Injected power
Equilibrium
ne, Te profiles, Zeff
Transport parameters
Predictive TRANSP
Injected power
Coil currents or desired boundary
Transport model
Te, ne profiles, Zeff
Notes: Revise title, less passive

## Slide 4: High-fidelity control simulations needed for model-based control design and validation
Control design typically relies on reduced modeling to make the design problem easier
  Simplified analytical or empirical expression used to capture dominant phenomena
  Linearization, time-scale separation, or other means are often used to further simplify the model used for design
When tested experimentally, the nonlinearities and coupling of the actual system may degrade performance
  Dedicated experimental time needed for commissioning
Testing controllers using the integrated modeling code TRANSP prior to implementation may:
  Improve controller performance and reduce time for commissioning and fine tuning
  Enable demonstration of new control techniques to justify implementation and experimental time
Testing
Design
Actual system
First-principles model
Simplified model
(empirical/analytical scalings)
Model for control design
Control design
TRANSP
Notes: Put TRANSP on figure. More active voice in title, ‘high-fidelity control simulations…’

## Slide 5: NSTX-U TRANSP feedback control simulations based on scenario development
MHD equilibrium
ISOLVER
Heating/current drive
NUBEAM
Sauter
Transport
Ti: Chang-Hinton
Te: prescribed
ne: prescribed
ni: based on Zeff
Zeff: prescribed
Injected power
Desired boundary
ne, Te profiles, Zeff
S. Gerhardt, NF 2012

## Slide 6: Now using TRANSP as a virtual tokamak for control design
MHD equilibrium
ISOLVER
Heating/current drive
NUBEAM
Sauter
Transport
Ti: Chang-Hinton
Te: prescribed
ne: prescribed
ni: based on Zeff
Zeff: prescribed
Injected power
Desired boundary
ne, Te profiles, Zeff
Electron temperature and density no longer a priori inputs
Ability to change actuators in `real-time’, i.e., based on feedback control
An analog to the plasma control system (PCS)
H98, HST
fGW
Notes: Explicit constraints, equations, next to bubbles, change order

## Slide 7: Now using TRANSP as a virtual tokamak for control design
MHD equilibrium
ISOLVER
Heating/current drive
NUBEAM
Sauter
Transport
Ti: Chang-Hinton
Te: prescribed
ne: prescribed
ni: based on Zeff
Zeff: prescribed
Injected power
Desired boundary
ne, Te profiles, Zeff
Electron temperature and density no longer a priori inputs
Ability to change actuators in `TRANSP real-time’, i.e., based on feedback control
An analog to the plasma control system (PCS)
Notes: ‘TRANSP as virtual tokamak’

## Slide 8: Now using TRANSP as a virtual tokamak for control design
MHD equilibrium
ISOLVER
Heating/current drive
NUBEAM
Sauter
Transport
Ti: Chang-Hinton
Te: prescribed
ne: prescribed
ni: based on Zeff
Zeff: prescribed
Injected power
Desired boundary
ne, Te profiles, Zeff
Electron temperature and density no longer a priori inputs
Ability to change actuators in `real-time’, i.e., based on feedback control
An analog to the plasma control system (PCS)
PCS

## Slide 9: Ability to change actuators in `TRANSP real-time’, i.e., based on feedback control
Density
Plasma current
Plasma boundary
NTV torque
Toroidal field
Heating/CD
Confinement factor
Physics layer
Engineering layer
Hardware layer
Implemented
Implementing
Not yet implemented

## Slide 10: Ability to change actuators in `TRANSP real-time’, i.e., based on feedback control
NBI power
Density
Plasma current
Plasma boundary
NTV torque
Gas puff
PF coil currents
OH coil current
RWM coil currents
Toroidal field
Heating/CD
Confinement factor
RF sources
Pellets
OH coil voltage
PF coil voltages
Physics layer
Engineering layer
Hardware layer
TF current
TF voltage
RWM coil voltages
Implemented
Implementing
Not yet implemented

## Slide 11: Ability to change actuators in `TRANSP real-time’, i.e., based on feedback control
NBI power
Density
Plasma current
Plasma boundary
NTV torque
Gas puff
PF coil currents
OH coil current
RWM coil currents
Toroidal field
Heating/CD
Confinement factor
RF sources
Pellets
OH coil voltage
PF coil voltages
Physics layer
Engineering layer
Hardware layer
TF current
TF voltage
NBI modulation
RWM coil voltages
RWM power supplies
TF power supplies
PF power supplies
PF power supplies
Implemented
Implementing
Not yet implemented

## Slide 12: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 13: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 14: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 15: Using TRANSP to test q0 and βN control via beam power and outer gap size actuation
Small outer gap
Large outer gap
Boundary can have strong effect on q profile through
  Effect on beam deposition profile
  Effect on bootstrap current through change in elongation
Two reference boundaries with different outer gap sizes were chosen, and interpolated between based on the feedback controller request
M.D. Boyer, NF 2015

## Slide 16: State-space system identification used for designing simultaneous q0 and βN controller
Open loop signals applied to each actuator in several TRANSP runs
Linear dynamic model optimized to predict outputs
Notes: Denote validation region

## Slide 17: Optimal controller achieves good target tracking in TRANSP simulations
Evolution tracks step change in requested values
Controller increases outer gap and decreases beam power to track change in request
Controller has important implications for MHD stability – ability to avoid q=1, or to move radius of the q=2 surface to avoid 2/1 NTMs.
Notes: Qmin vs q0, scenario optimization (change q0 without large change in beta)

## Slide 18: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 19: βN and q0 control with beam line 1 and outer gap improves response and tracks targets
Reference
Closed loop Target
Power reduced for first βN target, increased for second
Outer gap decreased to speed q0 response, increased to maintain elevated target
Plasma current (not controlled) response varies from reference
  q0 approaches 1 after target change (could adjust target trajectories or control gains)
Notes: X74

## Slide 20: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 21: Simplified model used for rotation profile control design in NSTX-U [I. Goumiri]
Using simplified form of toroidal momentum equation for design, profiles derived from TRANSP
Rotation
Notes: \sum_i n_i m_i \langle R^2\rangle\frac{\partial \omega}{\partial t} = \left(\frac{\partial V}{\partial \rho}\right)^{-1}\frac{\partial}{\partial\rho}\left[\frac{\partial V}{\partial \rho}\sum_i n_i m_i \chi_\phi\langle R^2(\nabla\rho)^2\rangle\frac{\partial\omega}{\partial\rho}\right]+T_{NBI}+T_{NTV}

## Slide 22: Simplified model used for rotation profile control design in NSTX-U [I. Goumiri]
Using simplified form of toroidal momentum equation for design, profiles derived from TRANSP
Rotation
Notes: \sum_i n_i m_i \langle R^2\rangle\frac{\partial \omega}{\partial t} = \left(\frac{\partial V}{\partial \rho}\right)^{-1}\frac{\partial}{\partial\rho}\left[\frac{\partial V}{\partial \rho}\sum_i n_i m_i \chi_\phi\langle R^2(\nabla\rho)^2\rangle\frac{\partial\omega}{\partial\rho}\right]+T_{NBI}+T_{NTV}

## Slide 23: Simplified model used for rotation profile control design in NSTX-U [I. Goumiri]
Using simplified form of toroidal momentum equation for design, profiles derived from TRANSP
New NBI
(central torque)
3D Field Coil
(edge torque)
Rotation
Notes: \sum_i n_i m_i \langle R^2\rangle\frac{\partial \omega}{\partial t} = \left(\frac{\partial V}{\partial \rho}\right)^{-1}\frac{\partial}{\partial\rho}\left[\frac{\partial V}{\partial \rho}\sum_i n_i m_i \chi_\phi\langle R^2(\nabla\rho)^2\rangle\frac{\partial\omega}{\partial\rho}\right]+T_{NBI}+T_{NTV}

## Slide 24: State-space controller achieves good tracking in TRANSP simulations [I. Goumiri]
Rotation (rad/s)
Beam Power (MW)
Coil current [A]
Coil current
Time (s)
Energy (MJ)
Time (s)
Beam power
Stored energy
Rotation
First
target
Second
target
First
target
Second
target
Beam 1
Beam 2A
Beam 2B
Beam 2C

## Slide 25: Several on-going projects using TRANSP feedback control framework
Stored energy and q0 control on NSTX-U
  M. D. Boyer, PPPL, Experiment: XP-1509
Stored energy, q0, and Ip control on NSTX-U (non-inductive scenarios)
  M. D. Boyer, PPPL, Experiment: future XP, possibly XP-1507
Rotation profile control on NSTX-U
  I. Goumiri, Princeton U., Experiment: XP-1564
Current profile control on NSTX-U
  Z. Ilhan, Lehigh U., Experiment: part of XP-1532
Rotation profile control on DIII-D
  W. Wehner, Lehigh U.
Shape control on NSTX-U
  M. D. Boyer, PPPL
NTM control on ITER
  F. Poli, PPPL

## Slide 26: Simplified current profile model used for feedback and feedforward control design
Magnetic diffusion equation
  Similar form to momentum diffusion equation
  Enables similar modeling approach
Multiple actuators considered:
  Loop voltage
  Individual beam heating
  Density
Feedback controller for tracking and disturbance rejection designed and tested in TRANSP
Feedforward control optimization based on reduced model
Z. Ilhan, W. Wehner, E. Schuster

## Slide 27: Feedforward actuator trajectory optimization to match target q profile
Optimizing for target matching
Optimizing for stationarity
Optimizing for both
Time (s)
Time (s)
Time (s)
Z. Ilhan, W. Wehner, E. Schuster

## Slide 28: Summary and future work
Complexity of the control requirements for NSTX-U motivates use of model-based control
A TRANSP framework for testing feedback controllers prior to experiments has been developed:
  Generate and test control-oriented models
  Test/tune feedback control algorithms
  Test new algorithms, demonstrate new control approaches
Future work
  Test on NSTX-U!

## Slide 29: Backup Slides

## Slide 30: Feedback control of NSTX-U is a complex task but model-based design can help
Real-time measurements
Actuators
Performance requirements
Dynamics
By incorporating dynamic models in the design process, control algorithms can be made to handle all of these issues
Nonlinearities
Coupling
Multiple actuators
Spatially distributed
Actuator limitations
Competing goals
Constraints (MHD stability)
Limited
Noisy
Control design problem

## Slide 31: Modifications have been implemented using external code: the Expert file
Expert subroutine called at many places throughout TRANSP production code
An identifier is passed along with the call
  different snippets of code can be run at different points during the simulation
Custom run-specific code can be run at each call to manipulate certain variables (which would typically be input ahead of time) based on the state of the simulation

## Slide 32: Profiles and coil currents during optimal controller simulation
7s: change in outer gap shifts q0 up
  Less peaked NBCD
  Increased bootstrap cur.
Coil currents appear physically achievable

## Slide 33: Reference simulation w/ fixed OH current: slow response, sensitivity to disturbances
NB sources: 1B, 1C, 2A, and 2B
Outer gap: 14cm
Broad ne, Te profiles from NSTX 142301
Particle inventory held fixed during simulation
Slow evolution to 100% non-inductive
  Can feedback control speed up response or track different targets?
Perturbations in density, confinement, and profile shapes can affect response
  Can feedback recover performance?
Reference
Perturbed density
q0 < 1
earlier
with lower density

## Slide 34: βN and q0 feedback using beam line 1 and outer gap control during confinement pert.
Beam line 1 power increased to track reference βN
Increasing beam power and βN leads to increased current
  Reference current nearly recovered despite no feedback control on current
Outer gap adjusted to maintain q0
Reference
Perturbed Closed loop
Notes: X80

## Slide 35: Left: βN control w/ beam line 1 Right: q0 control w/ outer gap
Reference
Closed loop Target
q0 drops below 1 since it is not controlled
Targets tracked in both cases
Target
tracking
Notes: X66, X69

## Slide 36: Feedforward actuatory trajectory optimization