## Slide 1: Overview of the Core Science Group Status and Plans
S.M. Kaye (SG Leader)
S.A. Sabbagh (SG Deputy Leader)
for the Core Science Group
37th NSTX-U PAC
PPPL, Princeton University
26-27 January 2016

## Slide 2: Outline of talk
Core Science Group and its components
Core SG mission elements and TSG research thrusts and their relation to NSTX-U high-level goals
Planned research
  Multi-TSG XPs
  TSG-specific
Benefit of future facility enhancements to TSG goals
Work directed towards FES panels’ recommendations
Summary

## Slide 3: Outline of talk
Core Science Group and its components
Core SG mission elements and TSG research thrusts and their relation to NSTX-U high-level goals
Planned research
  Multi-TSG XPs
  TSG-specific
Benefit of future facility enhancements to TSG goals
Work directed towards FES panels’ recommendations
Summary

## Slide 4: This talk will address all of the PAC charges
  Assess the research planned to be carried out for the NSTX-U FY2016 experimental campaign - are there any major missing elements, or new opportunities?
  Assess the alignment between the NSTX-U research plans and goals and the FESAC / FES initiatives, research opportunities, and ITER urgent research needs
  Comment on the progress and plans for the NSTX-U / PPPL theory partnership, and how well this partnership and the broader NSTX-U research activities support “integrated predictive capability” (see talk by A. Bhattacharjee)
  Please comment on the present team prioritization of planned facility enhancements including: divertor cryo-pump, non-axisymmetric control coils (NCC), 28GHz ECH/EBW gyrotron, and conversion to all high-Z PFCs and liquid metals research

## Slide 5: Core Science Group role is to foster communication/connectivity among TSGs studying confinement and stability (and among other SGs)
Experiment, theory and university reps constitute SG+TSG leadership
Core Science Group consists of three Topical Science Subgroups
SG successful in optimizing run time for XPs that span multiple TSGs

## Slide 6: Core SG addresses high-level research goals and priorities of NSTX-U
Explore unique ST parameter regimes to advance prediction capability
  Understand confinement at high normalized pressure and at low collisionality*
  Study energetic particle physics prototypical of burning plasmas*
Develop solutions for PMI under high heat flux conditions
Advance concept for Fusion Nuclear Science Facility (FNSF) by demonstrating 100% non-inductive ops at high performance
  Form and sustain plasma current without transformer for steady-state ST*
* Directly ITER relevant

## Slide 7: Major upgrades allow the Core SG to accomplish its major research goals
Extended Ip, BT range
  Allows for reduction in ν*
    Confinement scaling (T&T)
    Stability optimization (Macro)
  Allows for leverage on varying q, vfast/vAlfvén, βfast/βtot for fast ion instability studies (EP)
2nd NB
  Modifies q, flow profiles
    Transport, NTV, stability, fast ion confinement (T&T, Macro, EP)
  Affects fast ion distribution function directly for AE studies (EP)
ν*-0.79
Kinetic effects important
for RWM stability
NSTX-U
Increasing BT

## Slide 8: Core SG contributes to many of the 2016-2018 Yearly Milestones

## Slide 9: Early NSTX-U results show promise for physics experiments that address Core SG goals
Long-lived, good performing H-mode achieved after boronization

## Slide 10: Outline of talk
Core Science Group and its components
Core SG mission elements and TSG research thrusts and their relation to NSTX-U high-level goals
Planned research
  Multi-TSG XPs
  TSG-specific
Benefit of future facility enhancements to TSG goals
Work directed towards FES panels’ recommendations
Summary

## Slide 11: TSG objectives and research thrusts define research for 2016-2018
Transport and Turbulence: Establish predictive capability for the performance of FNSF and future devices
  Characterize H-mode global energy confinement in lower collisionality regimes in NSTX-U
  Identify mechanisms responsible for χ, D: explore parametric dependences with q, vφ using 2nd NB and 3D coils
  Establish and validate reduced transport models for establishing predictive capability
Macrostability: Establish the physics objectives and control capabilities needed for sustained stability of high performance plasmas
  Understand and advance passive and active control to sustain macroscopic stability
  Understand 3D effects for optimizing stability through profile control
  Understand disruption dynamics and techniques for avoidance and mitigation

## Slide 12: TSG objectives and research thrusts for 2016-2018 (cont’d)
Energetic particles: Enable predictions of fast ion behavior and associated instabilities in high-β super-Alfvénic regimes (ITER/FNSF)
  Assess effects of NB injection parameters on fast ion distribution function, NB-driven current profile
  Develop predictive tools for *AE-induced fast ion transport
  Develop phase space engineering tools/techniques for fast ion distribution and mode control
Transport and Turbulence
Macrostability
Energetic Particles
Color Coding

## Slide 13: T&T research thrusts map directly to NSTX-U research priorities; recent results support future work
  Understand confinement at high normalized pressure and at low collisionality
    Characterize H-mode global energy confinement in lower ν* regimes
    Identify mechanisms responsible for χ, D: explore parametric dependences with q, vφ using 2nd NB and 3D coils
    Establish and validate reduced transport models for establishing predictive capability
Non-linear GTS indicate low-k ion fluxes
within a factor of two of experimentally
inferred ones
Electrons
Ions
Kelvin-Helmholtz (flow shear driven)+ITG
e- transport cannot be
explained by low-k
Shear-flow modification by 2nd NB, NTV from 3D coils
Low-k turbulence will be diagnosed with expanded, 48-channel, BES array
Wang PRL & PoP (2015)

## Slide 14: Macro research thrusts map directly to NSTX-U research priorities; recent results support future work
  Understand confinement at high normalized pressure and at low collisionality
    Understand and advance passive and active control to sustain macroscopic stability
    Understand 3D effects through profile control
    Understand disruption dynamics and techniques for avoidance and mitigation
      S. Sabbagh talk on disruption PAM
NTV depends on both collisionality and rotation (IPEC-PENT)
Shear-flow modification by 2nd NB, NTV from 3D coils
Rotation, current profile control algorithms
Joint NSTX-U/Theory study of halo currents using tile current measurements
MGI for disruption mitigation
Log(Tφ[Nm])
TRANSP
Superbanana Plateau
(ν*/ν0*)2/5
1/ν
Plateau
1/ωE
NTV by n=3 core-optimized
NCC in NSTX-U
JK Park

## Slide 15: EP research thrusts map directly to NSTX-U research priorities; recent results support future work
  Study energetic particle physics prototypical of burning plasmas
    Develop predictive tools for *AE-induced fast ion transport
    Develop phase-space engineering tools/techniques for ffi, mode control
Suppression of TAE/GAE with HHFW
Developing self-consistent NB+RF code to understand
Shear-flow modification by 2nd NB, NTV from 3D coils tp study effect on CAE/KAW coupling
HHFW + 3D fields for *AE suppression
Expanded FIDA views, ssNPA for measuring energetic particle distribution
Applied 3D fields modify drive and damping of *AE modes
Fredrickson NF (2015)

## Slide 16: EP research thrusts map directly to NSTX-U research priorities; recent results support future work
  Form and sustain plasma current without transformer for steady-state ST
    Assess effects of NB injection parameters on fast ion distribution function, NB-current profile
    Develop predictive tools for *AE-induced fast ion transport
Critical Gradient and “Kick” models successful in reproducing effects of TAE on fast ions (Kick model implemented in TRANSP)
2nd NB for adjusting NB-driven j(r)
Expanded FIDA views, ssNPA for measuring energetic particle distribution
Gorelenkov, Podesta

## Slide 17: Outline of talk
Core Science Group and its components
Core SG mission elements and TSG research thrusts and their relation to NSTX-U high-level goals
Planned research
  Multi-TSG XPs
  TSG-specific
Benefit of future facility enhancements to TSG goals
Work directed towards FES panels’ recommendations
Summary

## Slide 18: SG framework beneficial in synthesizing needs and optimizing run time among TSGs for development of major XPs
  Ip/BT scaling (T&T) – Multi-TSG (XP1520-Kaye) [start with B, later w Li] directly addresses two Yearly Milestones
    R16-1: Assess H-mode (and beam) confinement, pedestal and SOL characteristics at higher Ip, BT, PNBI
    R17-3: Assess confinement and T&T at low ν* with full confinement and diagnostic capabilities (full Ip, BT, high-k scattering in 2017)
    In addition, apply perturbations
    at end of discharge to study
      Impurity transport neon puffs (T&T)
      Particle transport with SGI (T&T)
      NTV studies with 3D fields (Macro)
    Overlap with Boundary SG: Scaling of pedestal structure and transport, SOL widths, transport and turbulence, L-H, H-L threshold studies
Non-linear GTS indicate low-k DTEM leads
to ν* dependence, in addition to μtearing
R16-1, 17-3, 18-1, IR17-1, ITER
Wang PRL & PoP (2015)

## Slide 19: SG framework beneficial in synthesizing needs and optimizing run time among TSGs for development of major XPs
  2nd NB characterization (EP) – Multi-TSG (XP1523-Podesta) [start with B, later w Li] R16-2, 3, 17-1, 4, 18-2, IR18-2, ITER
NSTX #139048
classical
ad-hoc Db
kick model
Profiles of NB-driven current
    R16-2: Assess effects of NBI injection on fast ion f(v) and NBI-CD profile
    Vary beam source (Rtan) injection, power to understand beam ion confinement to modify current, pressure and flow profiles for optimizing plasma confinement, stability and non-inductive current drive
      Energy transport and confinement power scan (T&T)
      NTV studies with varying PNBI and profile (Macro)
    Pedestal structure, L-H threshold dependence on PNBI and heating profile (Boundary SG)
    SOL widths and associated transport and turbulence (Boundary SG)
    βN, li, rotation control (Integrated Scenarios SG)
Critical to use proper model for calculating
NB-driven j(r) (ad-hoc is radial diffusion only)
Podesta JRT15, NF (2015)

## Slide 20: T&T research thrusts and plans 2016
Characterize H-mode global energy confinement in lower collisionality regimes in NSTX-U
  Ip/BT scaling – Multi-TSG (XP 1520-Kaye) [B now, later Li]
Identify mechanisms responsible for χ, D: explore parametric dependences with q, vφ
  Characterize transport and microturbulence from (1): couple to g-k sims
  Perturbative particle transport using SGI (XMP-Ren)
  Perturbative momentum transport (XP1549-Guttenfelder)
  3D effects on momentum transport (XP1585-JK Park)
  Impurity transport
    Ne puff (XP1551-Munoz-Burgos), vs torque (XP1550-Delgado-Aparicio), intrinsic (Scotti)
  Turbulence studies
    Effect of reverse shear (XP1575-Yuh), q-profile (Ren)
    AE bursting and effects on electron transport (XP1574-Tritz)
    2D GAMs and ZFs with extended BES (XP1584-Smith)
Priority 1 XPs
R16-1, 17-3, 18-1, ITER

## Slide 21: T&T research thrusts and plans 2016
Establish and validate reduced transport models for establishing predictive capability
  Validation of gyrokinetic codes in L-mode (XP1521-Ren)
  Develop and test reduced microtearing based electron transport model
  Develop χe,EP using ORBIT and measured CAE/GAE structures (w/EP); move toward coupling with non-linear HYM simulations
R16-1, 16-2, 17-3, ITER
Non-linear HYM calculations indicate an up to 0.5 MW power channeling from the center of the plasma to the CAE-KAW conversion radius (about 2/3 of the way out
Consistent with lack of central electron heating and broadening of the Te profile with higher CAE activity
Priority 1 XPs
Belova PRL (2015)

## Slide 22: Macrostability research thrusts and plans 2016
Understand and advance passive and active control to sustain macroscopic stability
  PID and state-space control (XP1518,1545-Sabbagh)
  RWM stability dependence on NB (XP1546-Berkery)
  Effect of reduced collisionality on NTV (XP1517-Sabbagh)
  TM/NTM physics
    n=1 stability (XP1544-LaHaye), radiation-induced islands (XP1547-Delgado-Aparicio)
Understand 3D effects for optimizing stability through profile control
  EF thresholds and control (XP1506,1515,1516-Myers, XP1543-JK Park, XP1570-Sabbagh)
  3D plasma response (XP1548-Evans, XP1571-Z Wang)
  3D effects on TM/NTMs (XP1572-Okabayashi, XP1573-YS Park)
  Low rotation effects on RWM stability (XP1582-YS Park) and NTV (XP1583-Sabbagh)
Priority 1 XPs
R16-2, 16-3, 18-2, ITER
R16-2, 16-3, 18-2, ITER

## Slide 23: Macrostability research thrusts and plans 2016
Understand disruption dynamics and techniques for avoidance and mitigation
  Explore poloidal angle dependence and private flux region injection of MGI (XP1519-Raman)
  Validation of M3D-C1 for VDE and disruption modeling (Jardin)
  Halo current asymmetries, rotation (Joint NSTX-U/Theory task)
  Implement real-time physics models for disruption forecasting and avoidance (S. Sabbagh talk)
Priority 1 XPs
JRT16, ITER

## Slide 24: EP research thrusts and plans 2016
Assess effects of NB injection parameters on fast ion distribution function, NB-driven current profile
  2nd NB characterization – Multi-TSG (XP1523-Podesta)
  Beam ion confinement (XP1522-Liu)
Develop predictive tools for *AE-induced fast ion transport
  AE critical gradient (XP1524-Heidbrink)
  Use Upgrade capabilities to vary mode properties (frequency, spectrum, structure, regime) for development and validation studies
    NOVA-K, ORBIT, SPIRAL, M3D-K, HYM
Develop phase space engineering tools/techniques for ffi, mode control
  Rotation effects
    Effect on CAE/GAE modes (XP1525-Crocker), TAE modes and gap structure (XP1552-Fredrickson, XP1528-Podesta)
  HHFW (XP1553-Fredrickson)
  3D fields (XP1577-Liu)
Priority 1 XPs
R16-2,3, 17-4, IR17-1, R18-2, IR18-2, ITER
R16-2, IR17-1, R18-2, IR18-2, ITER
R16-3, IR17-1, R18-2, IR18-2, ITER

## Slide 25: Outline of talk
Core Science Group and its components
Core SG mission elements and TSG research thrusts and their relation to NSTX-U high-level goals
Planned research
  Multi-TSG XPs
  TSG-specific
Benefit of future facility enhancements to TSG goals
Work directed towards FES panels’ recommendations
Summary

## Slide 26: Future facility enhancements will benefit Core SG research
Cryopump will allow for reduced collisionality and ne control
  T&T: Decouple ν* and ρ* dependences with ne control, isolate transport changes due to j-profile evolution at constant ne
  Macro: Modify effect of kinetic resonances for RWM control
  EP: Improved flexibility to manipulate fast ion distribution through density control
NCC: Flow profile modification, modification of ffi
  T&T: Effect of flow shear on turbulence suppression
  Macro: EF/Locked mode thresholds and control, plasma response model validation, effect of flow shear on mode stability, NTV physics, use for active mode control
  EP: Impact on mode drive (ffi, flow shear) and mode damping (3D field modification of continuum/gap structure)
ECH/EBW
  T&T: Effect of RF vs NBI on plasma and impurity transport
High-Z tiles and flowing metal divertors
  T&T: Effect of different PFC (C vs High-Z) on plasma and impurity transport, core-edge coupling

## Slide 27: Core SG activities support the priorities identified by the Whole Device Modeling panel
PRD-1: Increase development and support for modular WDM frameworks
  Modularization of TRANSP, including development and implementation of EP transport, NTM island and impurity transport modules
  Fast WDM capability: BEtween and Among Shots Transp (BEAST): NSTX-U ops
PRD-2: Understand and distill physics of gap areas
  Improved kinetic-fluid formulations for both drift-wave turbulence and extended MHD
    T&T: XGC-1, GTS, GYRO with multi-scale physics (exascale computing applications)
    Macro: M3D-C1, MISK, NTVTOK, GPEC, MARS (M3D-C1 exascale application)
  Fast particle interactions with thermal (Alfvén) waves and instabilities
    CGM/Kick, HYM, self-consistent treatment of fast ions and RF (TORIC/CQL3D+NUBEAM)
  Couple core & edge: EPED1 lookup table coupling to TRANSP

## Slide 28: Core SG activities support the priorities identified by the Whole Device Modeling panel
PRD-3: Code/model validation at all fidelity levels through coupling with experiment
  T&T
    Reduced model testing: RLW, TGLF, MMM T(r,t)
    GYRO, XGC, GTS T(r,t), ne,i(r,t), BES, high-k scattering, polarimetry
  Macro: M3D-C1, MISK, NTVTOK, GPEC, MARS 3D MP, vφ, magnetics. etc.
  EP: Kick/CGM, HYM, 3D halos (NUBEAM) FIDA, ssNPA, sFLIP, magnetics, reflectometers

## Slide 29: Research and development on Disruption studies and modeling addresses key FES panel recommendations
Prediction
  RWM global stability model
    Develop predictive understanding of kinetic effects
    State-space controller implementation
    MHD spectroscopy
Avoidance
  Develop passively stable plasmas
    Close-fitting conducting plates
  Extend operation range through active control
    State-space controller
    EF/NTM/RWM control using NBI, 3D fields for control of p, j, vφ
Mitigation
  Measure effect of MGI poloidal position: testing MGI capabilities
  Current quench forces and halo current asymmetries: toroidally/poloidally resolved current monitors (Joint NSTX-U/Theory task)
Modeling
  M3D-C1 for integrated simulations throughout duration of disruption
  Automated plasma state reconstruction and stability assessment for PAM
    Gerhardt disruption warning algorithm
    DECAF (See talk by Sabbagh on DECAF)

## Slide 30: Core Science research is well-positioned to take advantage of the major device upgrades
  2016 research activities address key programmatic goals and TSG research thrusts
  Code development and validation against experimental data with expanded diagnostic set align with FESAC/FES recommendations from the WDM and Transients panels. Core SG research also addresses needs for ITER research preparation
  Much of the accompanying model development and physics understanding of Core SG research is being carried out within the NSTX-U/Theory partnership (see talk by A. Bhattacharjee)
  The planned facility enhancements, especially the cryopump and NCC, will enable more flexibility in addressing the SG and TSG research objectives

## Slide 31: Backup

## Slide 32: T&T highlights since PAC-35 (2014)
Progress on validating core drift wave transport mechanisms
  Identification of possible low-k-turbulence-induced transport mechanisms using global gyrokinetic codes
  Density gradient stabilization of ETG modes and understanding through gyrokinetic simulations
  “Stiff” electron transport cannot be explained by gradient-driven effects
  Investigation of roto-diffusion and centrifugal effects on impurity and momentum transport (Bucholtz et al., PoP (2015), Guttenfelder)
Progress on understanding the role of GAE/CAE on core electron transport
  GAE-KAW coupling and power channeling
  Techniques under development to simulate electron thermal transport caused by measured CAEs/GAEs with ORBIT (Crocker)

## Slide 33: Linear and non-linear gyrokinetic simulations have shown the role of grad ne in stabilizing ETG modes
Decrease in ETG turbulence amplitude with increasing grad ne
grad Te ~constant
ETG
μwave
scattering
Measured δn/n, linear growth rates, non-linear Qe behave similarly with grad ne
(δn/n)2
γlin/(cs/a)
~Qe/QGB
kθ/ρs
kθ/ρs
kθ/ρs
Low grad ne
High grad ne
Ruiz-Ruiz et al.
(MIT grad student),
PoP (2015)
GYRO
GS2

## Slide 34: Non-linear gyrokinetic simulations used to study large changes in e- transport in RF discharges
Gradient driven global g-k simulations do not
predict high enough stiffness to explain transport
Non-local flux-driven transport may
be important
Factor of 4 decrease in high-k turbulence
with no change in local gradients when
RF shuts off
Factor of 2 decrease in
electron transport with no change in local gradients
Ren et al., PoP (2015)
Qe,sim matches expt after RF-turnoff,
but not before
Sims (GTS)
Expt (before)
Expt (after)
a/Lne
a/LTe
a/LTi

## Slide 35: Global non-linear GTS gyrokinetic simulations have identified multiple low-k turbulence transport mechanisms
Recent GTS simulations have shown possible role of DTEM in contributing to observed favorable collisionality scaling (Bτth~ν*e-0.8)
  In addition to microtearing
  Synergy with DIII-D work
W. Wang et al., NF Letters, PoP (2015)
Energy Flux MW/m2
Strong flow shear can destabilize Kelvin-Helmholtz instability
  Non-linear global GTS simulations
  K-H+ITG+Neo ion transport within factor of 2 of expt’l level
  Cannot account for electron transport
Ions
Electrons

## Slide 36: Non-linear HYM simulations of CAE/KAW coupling address power channeling and effect on Te profile
Full non-linear simulations including multiple (n≥4) unstable modes have been performed
n=4 (largest mode) saturation amplitude (δB/B~6.6e-3) comparable to that inferred from reflectometer displacement measurements (δB/B≤3.4e-3)
HYM calculates channeling of 0.3 to 0.5 MW for n=4
Can result in several hundred eV modification of Te profile (Te broadening observed during periods of high CAE activity, with no δTe0)
Belova et al., PRL (2015)
Radial component of Poynting vector

## Slide 37: Macrostability highlights since PAC-35 (2014)
Progress in passive and active control to sustain macroscopic stability
  Joint NSTX/DIII-D experiments to unify kinetic RWM theory
  DCON ideal limits and implications for NSTX-U (Berkery)
Understanding 3D field effects and optimizing stability through profile control
  State-space algorithm for rotation control
  GPEC development for more self-consistent NTV optimization
  Use of stellarator optimization tools+VALEN for RWM control with NCC (Lazerson, Bialek)
Understanding disruption dynamics, prediction, avoidance and mitigation
  3D non-linear simulations of VDEs in NSTX with M3D-C1
  MGI valves for injection in different poloidal locations tested
  DECAF being developed for PAM (see S. Sabbagh talk)
  Multi-machine analysis of non-axisymmetric and rotating halo currents [ITPA] (Myers)

## Slide 38: Joint NSTX/DIII-D experiments have led to a unified picture of kinetic RWM physics
Kinetic RWM stabilization occurs from resonances between ωplasma and ωprecession, ωbounce/circ, ν*
Plasmas free of other MHD modes can reach/exceed linear kinetic RWM stability
Bursting MHD modes can lead to
non-linear stabilization before linear stability limits are reached
S. Sabbagh, APS Invited 2014
When RWM stable, rotation and
kinetic effects important for
stabilizing plasmas near the
Ideal Wall Limit
J. Menard et al., PRL (2014)

## Slide 39: A state-space algorithm for rotation control with NBI and NTV actuators was developed
I. Goumiri (grad student, PU), S. Sabbagh, D. Gates, et al.
Algorithm evolves rotation profile
toward global mode stability
γτwall

## Slide 40: M3D-C1 modeling of Vertical Displacement Events has been extended to 3D
Implemented arbitrary thickness resistive wall
  3 region computational space (vacuum, RW, plasma)
3D modeling of NSTX VDE with realistic wall resistivity
  Growth of n=1 mode
  Halo currents begin to form when plasma makes contact with vessel
Disruption phase: 2700 < t < 2950
Contours of RBT show halo currents
RBT t = 2850
RBT t = 2875
RBT t = 2900
RBT t = 2918
NSTX Discharge 132859
Plasma current
Wall halo current

## Slide 41: Plasma response to 3D fields has significant impact on calculated NTV profiles
The General Perturbed Equilibrium Code incorporates plasma response in calculation of NTV (kinetic effects included)
  3D equilibrium modified by plasma currents induced by 3D fields
Torque creates toroidal phase shift in plasma response
With increasing phase shift, coupling between
external field and plasma becomes inefficient,
resulting in self-shielding process
J.K. Park, APS Invited (2015)

## Slide 42: Disruption studies
MGI will assess injection at various poloidal locations, quantify and model gas assimilation
Joint NSTX-U/Theory study on halo current asymmetries, rotation and forces

## Slide 43: EP highlights since PAC-35 (2014)
Further developed and validated reduced EP transport models
  CGM/Kick models validated for NSTX & DIII-D
  Kick model implemented in TRANSP
Study of low-frequency EP-driven MHD
  Found to depend on q-profile, rotation
  Experimental results compared to M3D-K, MARS-K predictions
Assessed roles of high-frequency AEs in thermal electron transport
  CAE/KAW coupling (w/T&T)
  Compared HYM code predictions with NSTX data (Crocker/Belova)
Studied mitigation/suppression of AEs, fishbones with HHFW and 3D fields

## Slide 44: Models for fast ion profile relaxation in presence of AEs are being validated
“Kick” model (Podesta et al., NF 2015)
  PDF computed by ORBIT & NOVA
  Kicks ~ mode amplitude
Critical Gradient Model (Gorelenkov)
  Compute critical due to AE
  Mode growth/damping computed by NOVA-K
CG used to relax EP profile. It is broadened from the initially unstable one between r± → r1,2
Critical gradient
Classical profile
r-
r+
r-
r+
r2
r1
Both CGM and Kick models reproduce neutron deficit in an NSTX discharge with multiple unstable TAEs
ΔP
ΔE
Time (ms)
Neutron Deficit %
Podesta
Gorelenkov

## Slide 45: Correct treatment of fast ion phase space evolution is relevant for consistent integrated simulations
Two models tested for fast ion transport in integrated simulations in TRANSP
  Ad-hoc diffusion model (radial diffusion only) & kick model
  Ad-hoc model OK for global quantities (e.g. neutrons, stored energy)
Substantial differences observed for profiles, time evolution of
  Fast ion density, NB-driven current, power to thermal plasma
  Fast ion distribution function
NSTX #139048
classical
ad-hoc Db
kick model
Profiles of NB-driven current from TRANSP
Podesta, JRT 2015, Nuc. Fusion (2015)

## Slide 46: Techniques have been employed to mitigate Alfvén Eigenmodes
TAE and GAE modes suppressed by application of HHFW
Self-consistent description of
HHFW/EP under development
using TORIC/CQL3D- NUBEAM
E. Fredrickson et al, NF (2015)
TAE & GAE have been mitigated by application of 3D fields (Bortolon et al, PRL (2013)
  Fast ion drive for GAE reduced due to fast ion losses (Bortolon)
  Continuum damping of TAE increased due to reduced gap
G. Kramer et al, under prep. (2016)

## Slide 47: Extensive simulations investigate role of EP in determining stability and character of low-f MHD modes
Linear & non-linear study of fishbones using M3D-K (Fu, Wang):
  Rotation is destabilizing, favors fishbone over kink
  Mode structure evolves with qmin, non-linear effects cause broadening
  Both passing & trapped EPs contribute to drive
    Trapped particles’ contribution dominant as mode evolves non-linearly
Fishbones and NRKs cause significant flattening of EP profile
Complements studies of Non-Resonant Kink (NRK) with M3D-K, MARS-F (Hao)
  MARS-F: NRK destabilized at high rotation, mode structure broadened by finite resistivity
qmin~1.1
qmin~1.6