## Slide 1: Overview of the Integrated Scenarios Science Group Status and Plans
Stefan Gerhardt, PPPL, SG Leader
R. Raman, U. of Washington, SG Deputy Leader
NSTX-U PAC 37
PPPL B-318
1/27/2015

## Slide 2: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E (cross cutting and enabling)
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 3: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 4: Recall: NSTX-U Mission Elements And How the Integrated Scenarios SG Fits In
Explore unique ST parameter regimes to advance predictive capability – for ITER and Beyond
  WH&CD: Advanced ICRH modeling and code validation
  SFSU: Modeling of reconnection during CHI
Develop Solutions for PMI Challenge
  ASC: Closed loop control of advanced divertor geometry, divertor radiation
Advance ST as a possible FNSF/ Pilot Plant
  HW&CD, SFSU: Non-inductive startup and rampup
  ASC: Fully non-inductive scenarios, profile control

## Slide 5: Integrated Scenarios Leadership Team
Deputy SG Leader: Roger Raman (U. of Washington)
Advanced Scenarios and Control
  TSG Leader: Devon Battaglia (PPPL)
  Deputy TSG Leader: Stefan Gerhardt (PPPL)
  Theory/Modeling Rep.: Francesca Poli (PPPL)
  University Rep.: Egemen Kolemen (Princeton University)
RF Heating and Current Drive
  TSG Leader: Rory Perkins (PPPL)
  Deputy TSG Leader: Joel Hosea (PPPL)
  Theory/Modeling Rep.: Nicola Bertelli (PPPL)
  University Rep.: Paul Bonoli (MIT)
Solenoid Free Start-up and Ramp-up
  TSG Leader: Dennis Mueller (PPPL)
  Deputy TSG Leader: Roger Raman (U. of Washington)
  University Rep. + Theory/Modeling Rep.: Fatima Ebrahimi (Princeton University)

## Slide 6: Integrated Scenarios Members are Highly Supportive of Physics Operations
Deputy SG Leader: Roger Raman (U. of Washington)
Advanced Scenarios and Control
  TSG Leader: Devon Battaglia (PPPL)
  Deputy TSG Leader: Stefan Gerhardt (PPPL)
  Theory/Modeling Rep.: Francesca Poli (PPPL)
  University Rep.: Egemen Kolemen (Princeton University)
RF Heating and Current Drive
  TSG Leader: Rory Perkins (PPPL)
  Deputy TSG Leader: Joel Hosea (PPPL)
  Theory/Modeling Rep.: Nicola Bertelli (PPPL)
  University Rep.: Paul Bonoli (MIT)
Solenoid Free Start-up and Ramp-up
  TSG Leader: Dennis Mueller (PPPL)
  Deputy TSG Leader: Roger Raman (U. of Washington)
  University Rep. + Theory/Modeling Rep.: Fatima Ebrahimi (Princeton University)
Past, Present, and Future NSTX(-U) Physics Operators

## Slide 7: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 8: IS SG Supports Many NSTX-U Research Milestones
FY2017
FY2016
18
16
Develop physics + operational tools for high-performance: k, d, b, EF/RWM
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
Assess disruption mitigation, initial
tests of real-time warning, prediction
Develop high-non-inductive fraction NBI H-modes for sustainment and ramp-up
Assess fast-wave SOL losses, core thermal and fast ion interactions at increased field and current
Run Weeks:
FES 3 Facility Joint Research Target (JRT)
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
C-Mod leads JRT
Assess effects of NBI injection on fast-ion f(v) and NBI-CD profile
Assess scaling, mitigation of steady-state, transient heat-fluxes w/ advanced divertor operation at high power density
R17-1
Assess high-Z divertor PFC performance and impact on operating scenarios
R17-2
Assess impurity sources and edge and core impurity transport
R18-1
Assess role of fast-ion driven instabilities versus micro-turbulence in plasma thermal energy transport
IR18-2
Control of current and rotation profiles to improve global stability limits and extend high performance operation
R18-2
Assess transient CHI current start-up potential in NSTX-U
R18-3
Investigation of power and momentum balance for high density and impurity fraction divertor operation
IR18-1
FY2018
16
12
IR17-1
R17-4
R16-1
R16-2
R16-3
Incremental
Examine effect of configuration on operating space for dissipative divertors
DIII-D leads JRT
18
Assess E and local transport and turbulence at low * with full confinement and diagnostic capabilities
R17-3
TBD
NSTX-U leads JRT
Begin ~1 year outage for
major facility enhancement(s) sometime during FY2018

## Slide 9: IS SG Supports Many NSTX-U Research Milestones
FY2017
FY2016
18
16
Develop physics + operational tools for high-performance: k, d, b, EF/RWM
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
Assess disruption mitigation, initial
tests of real-time warning, prediction
Develop high-non-inductive fraction NBI H-modes for sustainment and ramp-up
Assess fast-wave SOL losses, core thermal and fast ion interactions at increased field and current
Run Weeks:
FES 3 Facility Joint Research Target (JRT)
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
C-Mod leads JRT
Assess effects of NBI injection on fast-ion f(v) and NBI-CD profile
Assess scaling, mitigation of steady-state, transient heat-fluxes w/ advanced divertor operation at high power density
R17-1
Assess high-Z divertor PFC performance and impact on operating scenarios
R17-2
Assess impurity sources and edge and core impurity transport
R18-1
Assess role of fast-ion driven instabilities versus micro-turbulence in plasma thermal energy transport
IR18-2
Control of current and rotation profiles to improve global stability limits and extend high performance operation
R18-2
Assess transient CHI current start-up potential in NSTX-U
R18-3
Investigation of power and momentum balance for high density and impurity fraction divertor operation
IR18-1
FY2018
16
12
IR17-1
R17-4
R16-1
R16-2
R16-3
Incremental
Examine effect of configuration on operating space for dissipative divertors
DIII-D leads JRT
18
Assess E and local transport and turbulence at low * with full confinement and diagnostic capabilities
R17-3
TBD
NSTX-U leads JRT
Begin ~1 year outage for
major facility enhancement(s) sometime during FY2018

## Slide 10: IS SG Supports Many NSTX-U Research Milestones
FY2017
FY2016
18
16
Develop physics + operational tools for high-performance: k, d, b, EF/RWM
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
Assess disruption mitigation, initial
tests of real-time warning, prediction
Develop high-non-inductive fraction NBI H-modes for sustainment and ramp-up
Assess fast-wave SOL losses, core thermal and fast ion interactions at increased field and current
Run Weeks:
FES 3 Facility Joint Research Target (JRT)
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
C-Mod leads JRT
Assess effects of NBI injection on fast-ion f(v) and NBI-CD profile
Assess scaling, mitigation of steady-state, transient heat-fluxes w/ advanced divertor operation at high power density
R17-1
Assess high-Z divertor PFC performance and impact on operating scenarios
R17-2
Assess impurity sources and edge and core impurity transport
R18-1
Assess role of fast-ion driven instabilities versus micro-turbulence in plasma thermal energy transport
IR18-2
Control of current and rotation profiles to improve global stability limits and extend high performance operation
R18-2
Assess transient CHI current start-up potential in NSTX-U
R18-3
Investigation of power and momentum balance for high density and impurity fraction divertor operation
IR18-1
FY2018
16
12
IR17-1
R17-4
R16-1
R16-2
R16-3
Incremental
Examine effect of configuration on operating space for dissipative divertors
DIII-D leads JRT
18
Assess E and local transport and turbulence at low * with full confinement and diagnostic capabilities
R17-3
TBD
NSTX-U leads JRT
Begin ~1 year outage for
major facility enhancement(s) sometime during FY2018

## Slide 11: The Research Forum Determined the Run Plan
Topic | Total Allocation
High-Beta Scenario Development | 3.5
Low Current Ramp-Up | 2 (1 WH&CD + 0.5 SFSU + 0.5 ASC)
Control | 4
CHI | 2.5
HHFW in the Flat-Top | 3
Total | 15
ASC+RF+SFSU | 8+3.5+3.5 = 15
TSG | Requested Days | Allocated Days
ASC | 33 | 8
SFSU | 14.5 | 3.5
WH&CD | 9 | 3.5
Run time allocation set to large extent by the milestones
Significantly more days requested than allocated.
Much discussion produced a tight research plan.
SG structure was very valuable in setting these priorities.

## Slide 12: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 13: ASC Research Thrusts Focus on Plasma Control and Scenario Development
#1– Scenario Develop for NSTX-U and Next-Steps
#2 - Axisymmetric Control Development
#3 - Disruption Avoidance By Controlled Discharge Shutdown
#4 - Understand Scenario Physics for Next Step Devices
Defined in the 5 Year Research Plan
For thrust sub-elements, see:
http://nstx-u.pppl.gov/program/science-groups/integrated-scenarios/advanced-scenarios-and-control

## Slide 14: Significant Modeling Supports the ASC Research Program
Fully relaxed non-inductive operating points have been explored with free-boundary TRANSP calculations
BT=1.0 T, IP=1 MA, Pinj=12.6 MW
Contours of Non-Inductive Fraction
Contours of qmin
Operation Year | BT [T] | Current Goal [kA] | Duration Goal
2016 | <=0.75 | ~600-800 | A few tE
2017 | 0.75-1.0 | ~600-1000 | 1-2 tR
Out-Years | 1 | 800-1300 | Up to 4.5 s at lower IP
Research Timeline for 100% Non-Inductive Scenarios
S.P. Gerhardt, et al, Nuclear Fusion 52 083020 (2012)
R16-3
These scenarios, obtained at first with an inductive ramp-up, will provide a target for non-inductive ramp-up studies
See talk by F. Poli and M. Boyer for more recent modeling results.
fNI=1
qmin=1

## Slide 15: Scenario Studies Will Focus on 100% NI and High-Current Long-Pulse
Non-Inductive Scenario Development (XP-1507, Gerhardt, et al.)
  Goal: Develop 100% non-inductive scenarios with IP~ 600 kA.
  Key Issues: Thermal transport, vertical stability at high-k, n=1 stability
  Modeling/Analysis: TRANSP
Long Pulse Development (XP-1554, Battaglia et al.)
  Goal: Utilize 80 kV beams, optimized OH waveform, to achieve longest possible pulse
  Key Issues: fuelling optimization, preventing q0 evolving too far, impurity control.
  Modeling/Analysis: TRANSP
Sustained Reverser Shear (XP-1575 H. Yuh, et al.)
  Goal: Utilize off-axis NBI to sustain reversed shear
  Key Issues: MHD leading to current redistribution, too-high pressure peaking.
  Modeling/Analysis: TRANSP, GS2, other microstability codes pending results
These support milestones R16-2, R17-4, R18-2, & ASC thrusts #1 and #4
S.P. Gerhardt, et al, Nuclear Fusion 52 083020 (2012)

## Slide 16: NSTX-U Experiments Are Already Using a Significantly Expanded Plasma Shutdown Scheme
SS=0:
Ramp-Up & Flat-Top
SS=4: Insufficient IP
SS=3:
IOH Loss of Control
SS=2:
Fast IP Rampdown
SS=1:
Slow IP Rampdown
NSTX PCS: No means of detecting a disruption, or ramping down the plasma current based on events.
NSTX-U PCS: State machine orchestrates the shutdown.
Disruptions detected by:
  Too large IP error
  Too large ZP(dZP/dt)
  Large locked n=1 modes
Presently using “Fast IP Rampdown” on every shot
  waiting to use “Slow-IP Rampdown”.
  Have not yet turned on n=1 disruption triggering.
Supports ASC thrust #3
Diagram of the State Machine Presently Implemented in PCS
Disruption Imminent
Disruption Imminent
“SS” = “Shutdown State”

## Slide 17: NSTX-U Experiments Are Already Using a Significantly Expanded Plasma Shutdown Scheme
NSTX PCS: No means of detecting a disruption, or ramping down the plasma current based on events.
NSTX-U PCS: State machine orchestrates the shutdown.
Disruptions detected by:
  Too large IP error
  Too large ZP(dZP/dt)
  Large locked n=1 modes
Presently using “Fast IP Rampdown” on every shot
  waiting to use “Slow-IP Rampdown”.
  Have not yet turned on n=1 disruption triggering.
Slow Drift Up, But No VDE or Disruption
IP
Example: This shot would have been a strong VDE in NSTX
IP Request
(including asynchronous transition to rampdown)
  ZP(dZP/dt)
  ZP(dZP/dt) threshold
Normal
Fast IP Rampdown
Insufficient IP
  ZP from EFIT
t=0.705
t=0.793
t=0.849
t=0.897
Supports ASC thrust #3
“State”

## Slide 18: Control Experiments Support NSTX-U Program and Next Step Devices
Snowflake Divertor Control [XP-1508, Kolemen and Vail]
  Goal: Demonstrate control of the unique dual X-point geometry.
  Method: New PCS algorithm with dual X-point tracking based on rtEFIT flux map, PID mechanism for adjusting divertor coil currents.
  Key Issues: rtEFIT quality, coil forces during control oscillations, interaction with other shape controllers
These support milestone R18-2, & ASC thrusts 1, 2, and 4
bN and li Control Study (XP-1509, Boyer et al)
  Goal: Demonstrate closed loop combined control of bN and li.
  Method: Realtime measurements with rtEFIT, control via beam, shape, maybe n=3 actuation.
  Key Issues: rtEFIT quality, beam modulation effects on plasma, limited range of li actuation
Current Profile Controllability Study (XP-1532, Boyer et al, 0.75 days)
  Goal: Demonstrate closed loop control of the current profile
  Method: Dedicated modulation shots for system identification type purposes, attempts at closed loop control if technically possible.
  Key Issues: rtMSE availability, beam modulation effects on plasma
Rotation Control [XP-1564, I. Goumiri, et al]
  Goal: Demonstrate closed loop control of the rotation profile and bN.
  Method: Beam for torque and heating, NTV for breaking. State-Space control algorithm
  Key Issues: rtVf availability, beam modulation effects on plasma

## Slide 19: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 20: Wave H&CD TSG Thrusts Dedicated to HHFW & EC Applications and Code Validation
For thrust sub-elements, see:
http://nstx-u.pppl.gov/program/science-groups/integrated-scenarios/wave-heating-and-current-drive
#1 Develop FW/EC heating for fully NI plasma current start-up and ramp-up
  Joint XP with Solenoid-Free Start-Up TSG…will describe dedicated experiment later in the talk.
#2 Validate state-of-the-art RF codes for NSTX-U and predict RF performance in future burning plasma devices.

## Slide 21: Modeling Is Confirming The Importance of RH Cutoff in Determining SOL Losses
NSTX showed a large loss of RF power in the SOL
Modeling shows large RF field amplitude in SOL under certain conditions
  Seen in full-wave code AORSA
    N. Bertelli et al., Nucl. Fusion 54 (2014) 083004.
    N. Bertelli et al., Nucl. Fusion 56 (2016) 016019.
  Also seen in cylindrical cold-plasma model
    Wave power (axial Poynting flux) confined to periphery, only gradually penetrating the core
    R. J. Perkins et al., 41th EPS Conference on Plasma Physics P-1.011.
RF fields in divertor cause RF sheath; potentially large enough to account for SOL losses
  Increased sheath voltage and electron current predicted to substantially increase heat flux to tiles
    R. J. Perkins et al., Phys. Plasma 22 (2015) 042506.
Cutoff layer
Lower SOL density (nant = 1x1012 cm-3)
Higher SOL density (nant = 2x1012 cm-3)
kφ = 13 m-1
Heating phasing

## Slide 22: Modeling Is Confirming The Importance of RH Cutoff in Determining SOL Losses
NSTX showed a large loss of RF power in the SOL
Modeling shows large RF field amplitude in SOL under certain conditions
  Seen in full-wave code AORSA
    N. Bertelli et al., Nucl. Fusion 54 (2014) 083004.
    N. Bertelli et al., Nucl. Fusion 56 (2016) 016019.
  Also seen in cylindrical cold-plasma model
    R. J. Perkins et al., 41th EPS Conference on Plasma Physics (2015) P-1.011.
Model antenna
adjustable phase
Dense core
nc ~ 5e19 m-3
Diffuse
Annulus (‘SOL’)
na ~ 1-3e18 m-3
Conducting vessel
wall
Axial poynting flux
only gradually penetrates core
Distance along field lines
0.25 m
0.75 m
1.25 m
1.75 m
y
x

## Slide 23: Modeling Is Confirming The Importance of RH Cutoff in Determining SOL Losses
NSTX showed a large loss of RF power in the SOL
Modeling shows large RF field amplitude in SOL under certain conditions
  Seen in full-wave code AORSA
    N. Bertelli et al., Nucl. Fusion 54 (2014) 083004.
    N. Bertelli et al., Nucl. Fusion 56 (2016) 016019.
  Also seen in cylindrical cold-plasma model
    R. J. Perkins et al., 41th EPS Conference on Plasma Physics (2015) P-1.011.
RF fields in divertor cause RF sheath; potentially large enough to account for SOL losses
  Rectified sheath voltage and e- current predicted to substantially increase heat flux to tiles
    R. J. Perkins et al., Phys. Plasma 22 (2015) 042506.
Axial poynting flux
only gradually penetrates core
Distance along field lines
0.25 m
0.75 m
1.25 m
1.75 m
y
x

## Slide 24: NSTX-U Prospect: Higher Toroidal Field May Reduce These SoL Losses
Right-hand cutoff density proportional to B:
  Larger cutoff density may reduce losses.
AORSA modeling confirms this expectation.
  Using NSTX discharge data and NSTX-U TRANSP scenarios.
nf=-21
nf=-12
nf=-21
nf=-12

## Slide 25: NSTX-U Prospect: Wide Range of Possible Partitions for HHFW Power Absorption
Increased BT may increase the thermal and fast ion absorption
  Decreased ion cyclotron harmonic number, increased cyclotron absorption
AORSA predictions for NSTX-U :
  greater deuterium heating when Ti > Te
  Ion heating increases and electron heating decreases as kφ decreases
N. Bertelli, et al AIP Conference Proceedings 2014
This work will benefit from including non-Maxwellian effects in TORIC v.5
  Bertelli et al. APS 2015
Ti/Te~2.3
Ti/Te~1.2
Ti/Te~0.6

## Slide 26: SoL Propagation and Core Absorption Physics Will be Addressed in Two XPs
Characterize SoL Losses of HHFW Power in H-Mode (XP-1510, Perkins, et al.)
  Goal: Assess scaling of SoL losses as a function of edge parameters, BT
  Diagnostics:
    fraction of HHFW power lost & spiral intensity along length of spiral
    RF voltage at the most intense portion of the spiral,
    SOL density profiles in front of antenna.
  Modeling/Analysis: TRANSP, AORSA
HHFW Absorption in NB Heated Plasmas (XP-1533, Bertelli, et al)
  Goal: Characterize RF absorption as a function of RF phase, toroidal field
  Analysis/Modeling
    GENRAY/CQL3D, TORIC, AORSA, AORSA+CQL3D, ORBIT-RF
    Continue validation of CQL3D with fast ion diagnostic (FIDA) data.
These support milestone IR17-2 , WH&CD Thrusts #2
R. Harvey et al., 56th APS-DPP 2014

## Slide 27: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two multi-TSG experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES Priorities and Summary

## Slide 28: SFSU Research Thrusts Are Synergistic with Other IS TSGs, Address Key Issues for a low-A FNSF
#1 – Establish and Extend Solenoid-Free Plasma Start-up
#2 - Test NBI Current Ramp-Up
#3 - Ramp-up CHI plasma discharges using ECH, HHFW and NBI and test plasma gun start-up
For thrust sub-elements, see:
http://nstx-u.pppl.gov/program/science-groups/integrated-scenarios/solenoid-free-start-up-and-ramp-up

## Slide 29: NSTX & NSTX-U Design Incorporates Features for Coaxial Helicity Injection
CHI in NSTX/NSTX-U
Inner and outer vacuum vessels
Injector and absorber regions
Injector coils & TF
Capacitor bank
  2kV, 50 mF
JxB force drives the plasma into the main chamber.
Closed surfaces form when the injector (bank) current dies away or is crowbarred.

## Slide 30: NSTX-U Upgrades that Facilitate CHI Start-up
NSTX-U Machine Enhancements for CHI
  > 2.5 x Injector Flux (proportional to Ip )
  About 2 x higher toroidal field (reduces injector current requirements)
CHI in NSTX/NSTX-U

## Slide 31: TSC Simulations in the NSTX-U Geometry support up to 400kA Current Start-up Capability in NSTX-U
Raman, et al., IEEE Trans. Plasma Sci. (2014)

## Slide 32: At High Lundquist Number, Plasmoid Mediated Reconnection Identified as Assisting in Flux Closure
Sweet Parker (S-P) reconnection in the injector region at low Lundquist number
At high Lundquist number the S-P current sheet is plasmoid unstable
Plasmoids seen in NSTX CHI
F. Ebrahimi, et al., PRL (2015)
NIMROD Simulations

## Slide 33: Two FY-16 Experiments Will Exploit the New Upgrade Capabilities, Target Coupling to Induction
Transient CHI Startup in NSTX-U (XP-1432. R. Raman).
  Motivation: New geometry of CHI gap, PF coils, PFCs mandate experiments to establish transient CHI.
  Goal: Establish reliable flux closure in the NSTX-U geometry.
  Method: Start at NSTX-level fields and currents, then increase BT and injector flux once reliable discharges have been formed.
  Key Issues: Breakdown with new narrow gap, tailoring the flux-footprint with new coils, electrode conditioning.
  Modeling/Analysis: NIMROD + Utilize the extensive suite of cameras to assess plasmoid formation and effects.
Inductive Flux Savings of Inductively-driven Transient CHI Plasmas (XP-1535, B. Nelson)
  Motivation: Coupling transient CHI to induction is a step towards demonstrating compatibility of CHI with subsequent ramp-up schemes.
  Goal: Establish transient CHI discharge and ramp it up with induction
  Key Issues: Persistent enough CHI plasma for good coupling, hand-off to position and IP control.
These support milestone R18-3 , SFSU goal #1

## Slide 34: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES priorities and Summary
See talk by F. Poli for modeling/theory motivation for these two joint XPs

## Slide 35: Effective Heating of Low-IP Plasmas Will Be Further Developed
300 kA inductive NSTX target heated to 3keV using ~1 MW HHFW
Motivation:
Critical to heat low-IP plasmas to the levels needed for NBI CD.
Very efficient heating of a low current plasma was demonstrated on NSTX
  Bootstrap current dominant when ITB forms
Goal
Re-establish ~300 kA, high-fNI, HHFW heated scenarios in NSTX-U
Attempt overdrive.
Key Issues:
  Shape control and ELMs impact on the RF coupling.
  ITB formation
Analysis/Modeling
TRANSP, TRANSP+TORIC
AORSA
These support SFSU thrust #3, WH&CD thrusts #1 & 2
See talk by Poli for how this type of heating fits into the full ramp-up scheme
Low Plasma Current, Fully Non-Inductive, HHFW H-Mode Plasmas
(XP-1534, Taylor)
G. Taylor et al., Phys. Plasmas 19 (2012) 042501

## Slide 36: Ability of Large Tangency Radius Beam to Couple Power/Current at Low Current Will Be Assessed
Motivation
  Calculations predict high current drive efficiency at low IP for large tangency radius sources
Goal:
  Assess lowest IP (& therefor ne, Te) for NB coupling as a function of tangency radius
Key Issues:
  Shine through losses vs. bad orbit losses
  FI pressure peaking
  Confinement & plasma control at low IP
Method
  High BT, 300<IP<500 kA, 80-90 kV beams.
  FI diagnostics and comparison to TRANSP predictions
  HHFW may be used to increase Te
Analysis/Modeling
  TRANSP/NUBEAM
These support milestone SFSU thrust #2, ASC thrust #1
J. Menard, et al., Nuclear Fusion 42, 083015 (2012)
NB Ramp-Up Studies (XP-1567, F. Poli)

## Slide 37: IS SG Also Supports Cross-Cutting and Enabling XPs & XMPs
Optimization of the Vertical Control Algorithm (XP-1501, Boyer)
  Goal: Optimize control observer parameters, feedback gains, and then push to higher elongation.
  Analysis: TOKSYS, TRANSP-ISOLVER
Tuning of Automated Rampdown Software (XP-1502, Gerhardt)
  Goal: Tune shutdown algorithm for the more challenging H-mode rampdown.
  Key Issues: Shape handoff using ISOFLUX, position transients during H->L.
HHFW Antenna Conditioning (XMP-026, Hosea)
  Goal: Antenna conditioning under plasma conditions, after successful antenna conditioning
Commissioning CHI System (XMP-126, Raman)
  Goal: Commission CHI capacitor bank and dedicated instrumentation, make first CHI discharges.
  Key Issues: Noise reduction on new instrumentation, DCPS configuration during CHI, noise on magnetic diagnostics.
LGI Control (XMP-130, Lunsford)
  Goal: Commission Lithium Granule Injector, including PCS algorithms

## Slide 38: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES priorities and Summary

## Slide 39: Proposed Facility Enhancements Will Be a Dramatic Step Forwards for SFSU and WH&CD Research
28 GHz gyrotron system is largely motivated by the need to connect CHI to HHFW and NB heating.
  See talk by F. Poli for details on how SFSU research will be fundamentally enhanced.
28 GHz gyrotron will also allow EBW heating studies to move forward, following a launcher upgrade.
High-Z PFC upgrade will provide metal electrode surfaces, which will likely prove advantageous for CHI once properly conditioned (reduced low-Z impurities, radiation).

## Slide 40: Exciting Opportunities for ASC Research Will Come out of the Facility Enhancements
Cryo-pump should resolve a long-standing, legitimate criticism of NSTX scenario research…lack of density control.
  Will likely be a key capability in exploiting the full NSTX-U magnet and heating systems.
  Will facilitate targeted scenario and physics studies.
  Refer to talks by R. Maingi, M. Ono for more details.
High-Z PFC enhancement will introduce critical, exciting challenges to scenario and control development.
  May make active heat flux management as critical as other control loops, as will be the case in ITER and other next steps.
  See talk by M. Jaworski for details.
NCC will provide an additional key actuator for profile control.
  Closed loop pedestal height control will be assessed as an ELM mitigation strategy.
  More flexible rotation control strategies will be developed, which may be important for scenario optimization

## Slide 41: Outline
Goals & Organization
Milestones and the Research Forum
Research Results, Status, and Plans
  Advanced Scenarios and Control
  RF Heating and Current Drive
  Solenoid Free Start-Up
  Two Multi-TSG Experiments + CC&E
Key Research Enabled by the Proposed Facility Enhancements
Connection to FES priorities and Summary

## Slide 42: IS SG Research Supports FES Priorities
Advancing predictive capability, model validation
  Control oriented modeling, start-up modeling, RF code validation
    See also talks by Boyer, Poli, in addition to these slides.
Mitigating / avoiding transients
  Disruption avoidance via i) advanced profile control and ii) discharge shutdown studies
Taming the PMI
  Closed-loop control of advanced divertors (magnetic geometry and radiation)
Establishing physics basis for FNSF
  Non-inductive start-up, ramp-up, and sustainment
  RF Physics
Supporting discovery science, basic plasma physics
  Reconnection physics during CHI

## Slide 43: This SG Works to Solve Scenario Physics Problems for the NSTX-U Program, ITER, and Next-Step Devices
Strong support for the non-inductive startup, ramp-up, and sustainment across the three TSGs.
Active modeling efforts in all areas support the NSTX-U programmatic goals and FES priorities
Developing the H&CD actuator physics and closed loop control techniques for next step devices.
We have an exciting research program planned for the FY16 run and are ready to go!

## Slide 44
Backup

## Slide 45: Ion Absorption of HHFW Power Has Potential Benefits and Disadvantages
In NSTX, a significant fraction of (core) HHFW power absorbed by fast ions.
  Seen in neutrons, NPA spectrum, FIDA.
Ion acceleration to loss orbits can be a strong loss mechanism
  detrimental heat loads to the PFCs.
FW interactions with beam ions could be useful for influencing energetic particle modes [EP TSG]
  Modification of fast-ion distribution
    D. Liu et al., Plasma Phys. Control. Fusion 52 (2010) 025006.
  Suppression of energetic-particle driven modes
    E. D. Frederickson et al., Nucl. Fusion 55 (2015) 013012.

## Slide 46: High fraction of open flux conversion to closed flux seen in simulations with narrow injector flux footprint
CHI in NSTX-U configuration naturally has a narrower injector flux foot-print due to improved Injector coil positioning
Due to higher Lundquist number in NSTX-U CHI simulations, closed flux surfaces form even during the actively injected phase
F. Ebrahimi, et al., submitted to NF-Lett.
NIMROD Simulations

## Slide 47
Hardware Upgrades Support HHFW Operations and Physics Studies
Twelve-strap antenna re-installed
  New compliant, bellowed feedthrough used to withstand disruptions at IP=2 MA
  Additional grounding points added to raise voltage standoff
Six RF sources recommissioned; conditioning started
  Recent breaker failure being investigated; replacement parts are ready to go
New color fast camera and infrared camera will monitor antenna
New sets of divertor Langmuir probes
  RF-suitable electronics have been designed, reviewed, and tested
Additional grounding to between antenna box and vessel
Poloidal Cut of
Antenna Strap
Compliant Feedthroughs

## Slide 48: Distribution of First Authors (not including CC&E, XMPs) ~12 First Authors
Author | XP | Run Days | Area
Gerhardt | 100% non-inductive | 2 (ASC) | Scenario Development (3.5 Days)
Battaglia | Longest Possible Pulse | 1 (ASC) | 
Yuh | Reversed Shear | 0.5 (ASC+0.5 T&T) | 
Kolemen | SFD Control | 1.5 (ASC) | Control Development (4 Days)
TBD | Rotation Control | 0.5 (ASC) | 
Boyer | Current profile control, bN + li control | 2.0 (ASC) | 
Bertelli | Absorption in NB plasmas | 1.0 (RF) | HHFW at Higher Current (3 Days)
Perkins | SOL Losses in H-mode | 1.75 (RF) | 
D. Smith | Measure Density Perturbation with BES | 0.25 (RF) | 
Poli | NBI Coupling to Low-Current Plasmas | 1 (0.5 ASC+ 0.5 SFSU) | Ramp-Up (2.0 Days)
Taylor/Poli | Low Current, high fNI, HHFW | 1 (0.5 RF+ 0.5 SFSU) | 
Raman | Transient CHI startup | 2.0 (SFSU) | CHI (2.5 Days)
Nelson | Inductive Rampup | 0.5 (SFSU) | 

## Slide 49: AORSA show different behavior of SOL power losses between HHFW and IC minority heating regimes
NO cut-off
Alcator C-Mod & EAST results show a decreasing of E field amplitude outside LCFS with increasing nant
No transition to higher SOL power losses
Results perhaps more intuitive w.r.t. the NSTX/NSTX-U/DIII-D increase SOL density enhances antenna-plasma coupling lower fraction of power lost to the SOL region
Consistent with the C-Mod/ASDEX-U exp.
SOL RF field amplitude increases when FW can propagate in the SOL
Direct correlation between SOL RF field amplitude , FW cut-off location , and SOL power losses behavior
Agreement with DIII-D sim./exp.
Larger evanescent region predicted at higher fields achievable in NSTX-U, favorable for future experiments
Possible aspects: cavity modes & magnetic pitch angle
HHFW
IC minority
VS.
N. Bertelli et al., Nucl. Fusion 56 (2016) 1
C-mod
nf = 10
f = 80 MHz
n/w = 0.01
NSTX-U scenario
BT = 1 T
f = 30 MHz
n/w = 0.01
NO cut-off
NO cut-off
SOL power losses [%]
nant [1018 m-3]
SOL power losses [%]
nant [1018 m-3]
nf = -12
nf = -21

## Slide 50: Extended TORIC v.5 to include non-Maxwellian effects both in HHFW and IC minority heating regimes
implementation of the bi-Maxw. and slowing down analytical distributions
Capability to read a numerical fast ion distr. func. from NUBEAM is underway
Non-Maxwellian effects, generally, result in finite changes in the amount and
spatial location of absorption.
Fast ion absorption
assuming a bi-Maxw
distr. func. in NSTX
Bertelli et al. APS 2015

## Slide 51: Modeling Is Confirming The Importance of RH Cutoff in Determining SOL Losses
NSTX showed a large loss of RF power in the SOL
Modeling shows large RF field amplitude in SOL under certain conditions
  Seen in full-wave code AORSA
    N. Bertelli et al., Nucl. Fusion 54 (2014) 083004.
    N. Bertelli et al., Nucl. Fusion 56 (2016) 016019.
  Also seen in cylindrical cold-plasma model
    Wave power (axial Poynting flux) confined to periphery, only gradually penetrating the core
    R. J. Perkins et al., 41th EPS Conference on Plasma Physics P-1.011.
RF fields in divertor cause RF sheath; potentially large enough to account for SOL losses
  Rectified sheath voltage and e- current predicted to substantially increase heat flux to tiles
    R. J. Perkins et al., Phys. Plasma 22 (2015) 042506.

## Slide 52: ASC (and Broader NSTX-U) Research Facilitated by Numerous Upgrades to the Plasma Control System
Hardware:
  New control computers, reduced latency links to the power supplies
  realtime Vphi in final testing, realtime MSE measurement in development.
Methods:
  Complete prose documentation of all physics algorithms within PCS.
  Control design with full-physics models in TRANSP
    See talk by Dan Boyer
Algorithms:
  Reviewed every line of code in every control algorithm
  New shape control capabilities during the ramp-up and ramp-down
  New automatic discharge shutdown system
  More modular beam control, vertical control, ISOFLUX shape control algorithms.
  In final development:
    Snowflake divertor control
    Rotation/Current profile control