## Slide 1: Macroscopic Stability Research - NSTX-U
NSTX-U PAC-39 Meeting
PPPL
January 9th, 2018
V2.0
S.A. Sabbagh, for the NSTX-U Team

## Slide 2: NSTX-U restart will provide critical macrostability research of compact, high b plasmas with world-leading capabilities
Overview:
  NSTX-U research is critical to the U.S. DOE FES priorities, needs to continue ASAP
  Significant investment in NSTX/-U data leverages unique, high b compact tokamak physics data and research for key theory validation, confident extrapolation of models
Outline:
  U.S. Program high priority needs defined by DOE and NSTX-U essential role
  Unique aspects/findings of NSTX research stimulating world-leading NSTX-U research
  Capabilities for disruption prediction and avoidance research at high beta
  Recent NSTXU researcher efforts to support ITER through ITPA
  Results from NSTX-U initial operation supporting more rapid progress on restart

## Slide 3: Avoidance/control of transient events are one of two highest DOE FES priorities in macrostability research
Workshop on Transients Report
  Broad community process addressing critical disruption and ELM challenges; identified as critical ITER needs
FES Program 10 Year Perspective (NSTX-U uniqueness)
  “Exploration of the impact of (device aspect ratio) can inform much of fundamental science pertaining to magnetic confinement.”
  Disruption prediction / avoidance / mitigation Thrusts/Pursuits include:
    Experimentally validated theoretical understanding of disruption chain events
    Predicted thresholds and control for disruption avoidance and mitigation
    Leverage national/international multi-device data for best extrapolability
Charge 2,3

## Slide 4: NSTX reaches uniquely high bN, low li range of operation, and the highest bN/li is not the least stable
Unique high bN > 7, bN/li > 14 reached!
  In dedicated experiment (shown), disruptivity was higher at “intermediate” values of bN/li
  In larger database, disruptivity decreases at higher levels of bN/li
Research leverages NSTX-U capabilities
  Compact ST field geometry (incl. high shaping)
  Stabilizing conducting wall (copper)
  Reduced collisionality (Ip, BT increase)
  Plasma rotation and current profile control
  Adv. control of high bN ST eigenmodes
   Combined to produce highest sustained bN with broad, self-consistent non-inductive current profile (low li)
bN
8
6
4
2
0
bN/li
13
12
11
14
10
li
0.0
0.2
0.6
0.8
0.4
Unstable RWM
Stable/Controlled RWM
βN/li = 6.7 : computed
NSTX n = 1 no-wall limit
Active control
Passive control
S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)
Charge 2,3
 Key MAST-U complementarity: stability physics without stabilizing wall
(see backup)

## Slide 5
unstable
RWM
Resonant Field Amplification (RFA) vs. bN/li
Stability vs. bN/li
  decreases up to bN/li = 10, increases at higher bN/li
  Consistent with kinetic stabilization
RFA Amp. (G/G)
Less stable
S. Sabbagh,et al., 2016 EPS Landau-Spitzer Award lecture
Most
stable
RFA vs. rotation (wE)
Stability vs. rotation
  Largest stabilizing effect from ion precession drift resonance with wf
RFA Amp. (G/G)
Experiments directly measuring global stability using MHD spectroscopy (RFA) understood by kinetic RWM theory
Charge 1
J. Berkery, et al., PoP 21 (2014) 156112
Rotation
Less stable

## Slide 6: Kinetic modifications completely change the understanding and scaling of mode stability at reduced collisionality
J.W. Berkery, et al., Phys. Rev. Lett. 106 (2011) 075004
Ion precession drift resonance
stabilization
stable
unstable
2.0
weak resonance
unstable
stable
Past models/ideas
  Collisions provide stabilization
  stability decreased with decreasing n
  Unfavorable for ITER
Present model
  Collisions spoil broad stabilizing resonances
  Mode stabilization vs. n depends on rotation profile wf
    At strong resonance: mode stability increases with decreasing n
Scans from NSTX equilibrium
MISK code
 Key next step: verify extrapolation to low n in NSTX-U
S. Sabbagh,et al., 2016 EPS Landau-Spitzer Award lecture
Charge 1,3,4

## Slide 7: NSTX shows dominant precession drift resonance stabilization vs. bounce resonance for DIII-D in joint XP at similar, high rotation
|δWK| for trapped resonant ions vs. scaled experimental rotation (MISK code)
DIII-D experimental rotation profile
NSTX experimental rotation profile
133103 @ 3.330 s
stable plasma
133776 @ 0.861 s
stable plasma
precession
resonance
bounce / circulating
resonance
precession
resonance
bounce / circulating
resonance
DIII-D
NSTX
- J. Berkery et al., PRL 104, 035003 (2010)
- S. Sabbagh, et al., NF 50, 025020 (2010)
- J. Berkery et al., PRL 106, 075004 (2011)
- S. Sabbagh et al., NF 53, 104007 (2013)
- J. Berkery et al., PoP 21, 056112 (2014)
- J. Berkery et al., PoP 21, 052505 (2014)
- J. Berkery et al., NF 55, 123007 (2015)
Some NSTX / MISK analysis references
Charge 1
Also, computed kinetic RWM stability matches disruption onset in both machines over wide rotation range (using same analysis tools)
  (see backup slide)

## Slide 8: State space rotation controller designed for NSTX-U using non-resonant NTV (3D field) and NBI to maintain stable profiles
MISK
unstable
stable
increasing time
gtwall
I. Goumiri, C. Rowley, S.A. Sabbagh, et al, PoP 24 (2017) 056101
wf evolution in NSTX (disruption)
Plasma rotation (kHz)
0
15
20
10
5
yN
0.0
0.2
0.4
0.6
0.8
1.0
NSTX-U (6 NBI sources and n = 3 NTV)
Steady-state reached in ~ 3tm
Marginally stable profile
Broader stable
profile
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
NBI
NTV
Charge 2,3

## Slide 9: Automated Disruption Event Characterization and Forecasting innovation to enable disruption avoidance
DECAF code
Automated disruption event chain analysis
RWM
VSC
WPC
LON
IPR
LOQ
DIS
(0.717s)
(0.736s)
(0.724s)
(0.729s)
(0.731s)
(0.747s)
NSTX
Disruption forecasting
Global kinetic MHD mode growth
gtw
Increasing time
Collisionality (kHz)
Rotation
J.W. Berkery, S.A. Sabbagh, et al., Phys. Plasmas 24 (2017) 056103
Predicted instability statistics
NSTX (high bN)
NSTX
Cue disruption avoidance systems
Physics-based disruption forecasting, compared to experiment
Recent automated rotating MHD module for TM analysis (see backup)
Portable code for collaborative (inter)national multi-device studies (including NSTX/-U, KSTAR, DIII-D, TCV); supports NSTX-U r/t event handler
Charge 1,2,3,4

## Slide 10: In aggregate, NSTX-U provides key capability for disruption avoidance research of unique high beta, compact ST plasmas
Predictor/Sensor (CY available) | Control/Actuator (CY available) | Physics Research
- Rotating and low freq. MHD (n=1,2,3) 2003 | - Dual field -component RWM sensor control (closed loop 2008) | NTM, RWM
- Low freq. MHD spectroscopy (open loop 2005); - Kinetic RWM modeling (2008) | - Control of high βN ST plasmas (closed loop 2007) | Kink/ballooning, RWM
- Real-time physics-based RWM state-space controller observer (2010) | - Physics model-based RWM state-space control of ST modes (2010) | NTM, RWM (ballooning), VDE
- Real-time Vf measurement (2016 NSTX-U) | - Plasma Vf control (by NTV 2004) - NTV + NBI rotation control (closed loop) | NTM, Kink/ballooning, RWM
- Reduced Kinetic RWM stabilization model (2016) - Automated MHD identification (2017) - Real-time MHD spectroscopy (5 Year Plan) - Real-time kinetic stabilization model (new) - Real-time rotating MHD identification (new) | - Safety factor, li control (closed loop) - NTV + NBI rotation control (closed loop) - Upgraded 3D coils (NCC): improved Vf and mode control (in 5 Year Plan) | NTM, RWM Kink/ballooning, VDE
Charge 2,3,4
Existing
Recent
Upcoming
Capability
Routine use of existing systems (reliability shown)

## Slide 11: NSTX-U researchers are leading international efforts to support ITER in macrostability analysis
Error fields (ITPA MDC-19)
  On-going effort to predict ITER error field (EF) tolerance using 3D MHD response metrics
  Resonant n = 1 EF criterion (2017)
  (dB/BT)pen=0.0006(ne)1.3BT-1.7R0.7βN-0.78
3D field coil effectiveness (ITPA MDC-19)
  Top / bottom ex-vessel coils are found to be 10 times less efficient to control n=1, 2 resonant fields than other coils
Halo currents (ITPA MHD WG-6)
  Multi-machine database (NSTX, DIII-D, C-Mod, JET, AUG) examining halo current magnitudes, asymmetries, rotation
Global mode stability/control (MDC-21)
  Extensive kinetic RWM analysis code benchmarking effort
  Alpha particles, and/or active control required for RWM stabilization at all wf in advanced scenario bN = 2.9
J.-K. Park et al.
J.-K. Park et al.
C. Myers, et al.
S. Sabbagh, J. Berkery, et al.
Charge 1,2,3

## Slide 12: Macrostability research from initial NSTX-U operation provides key insight for rapid progress upon restart
Error field rapidly characterized
  EF partly corrected using 3D field coils
  IPEC, M3D-C1 plasma response modeling implicated TF misalignment as likely primary source of locking
    TF misalignment identified, will be corrected
  Codes now being used to set alignment tolerances for all coils
Charge 1,2,3
Observation of direct 1/1 mode locking
(C. Myers et al., submitted to PRL (2017))
(J.-K. Park, N. Ferraro)
Condition: resonant 2/1 Field < RMP coil at 1 kA-t
Larger bars are better

## Slide 13: Summary (I): NSTX-U recovery paves the way back to world-leading research on unique, compact high b plasmas
Charge 1: Quality/importance of recent NSTX/NSTX-U research results
  Kinetic RWM stabilization research fundamentally changed physics understanding of experimental stability, importance of rotation profile, extrapolation to reduced collisionality (2016 Landau-Spitzer Award)
  Direct measurement of plasma stability through RFA verified key understanding of greater stability at uniquely high bN/li
  Physics-based disruption prediction/avoidance research (DOE high priority) established
Charge 2: Uniqueness / timeliness for the world program
  Unique (in the world) high bN, bN/li operational regime provides critical theory validation
  Global MHD stability, error field/plasma response, applied 3D field research directly serve ITER, KSTAR, et al. now; will continue
  Disruption prediction/avoidance research expanded to collaborations on world tokamaks

## Slide 14: Summary (II): NSTX-U recovery paves the way back to world-leading research on unique, compact high b plasmas
Charge 3: How/whether NSTX-U will be world-leading after restart
  Disruption prediction and avoidance research is world-leading, highest priority, remains active – plan to be significantly advanced by restart
  Advanced control technique plan for disruption avoidance will remain world-leading on restart, collaborations to keep effort active
  Unique low A, high bN joint experiments w/ tokamaks can resume in timely fashion on restart
Charge 4: How recent findings influence the future NSTX-U program
  NSTX-U 5 Year Plan remains largely intact (e.g. study of kinetic RWM stabilization paradigm at low n, w/ greatly varied / controlled rotation profile remains strongly relevant)
  Advanced control techniques are planned; if recommended, recovery period provides opportunity for early development / implementation - restart research ASAP
  Disruption prediction research plan can be even more aggressive (e.g. real-time MHD ID)
  3D field coil upgrade remains important for NTV rotation, adv. mode control, ELM studies

## Slide 15: Backup Slides Follow

## Slide 16: High priority research elements of recent Strategic Planning Meetings align strongly with NSTX-U Macro research
Madison meeting:
  Uniquely high level of consensus in critical Macrostability research areas including
    Compact tokamak design (high field utilization)
    Disruption-free (very low disruption rate)
    Fully/highly non-inductive stable operation
Austin meeting:
  Innovations stated (Working Group-SA3) align with NSTX-U research, including
    Physics understanding of low A advantages
    Disruption event characterization and forecasting
    Disruption avoidance through profile, active mode control
    Stability physics of self-consistent, fully/highly non-inductive operation

## Slide 17: NSTX reaches uniquely high bN, low li range of operation, and the highest bN/li is not the least stable
Unique high bN > 7, bN/li > 14 reached!
  In dedicated experiment (shown), disruptivity was higher at “intermediate” values of bN/li
bN
8
6
4
2
0
bN
li
0.0
0.2
0.4
0.6
0.8
bN/li
13
12
11
14
10
bN/li
13
12
11
14
10
li
0.0
0.2
0.6
0.8
0.4
Unstable RWM
Stable/Controlled RWM
βN/li = 6.7 : computed
NSTX n = 1 no-wall limit
0
8
6
4
2
Disruptivity
Active control
Passive control
S. Sabbagh et al., Nucl. Fusion 53, 104007 (2013)
S. Gerhardt et al., Nucl. Fusion 53, 043020 (2013)
In the larger database, disruptivity decreases at higher levels of bN/li
Charge 2,3
 Key MAST-U complementarity: physics of stability without stabilizing wall

## Slide 18: Global mode stability forecasting: build from success of drift kinetic theory modification to MHD as a model
Kinetic modification to ideal MHD
Stability depends on
  Trapped / circulating ions, electrons
  Collisionality; Energetic particles
  Integrated wf profile matters!!! : broad rotation resonances in dWK
ion gyro-orbit
and trajectory
(Fig. adapted from R. Pitts et al., Physics World (Mar 2006))
Trapped particle orbit precession drift
Trapped particle
orbit
Trapped orbit 2D
projections
plasma integral over particle energy
collisionality
wf profile (enters in wE)
precession drift
bounce
Just some references:
B. Hu, R. Betti, et al., PoP 12 (2005) 057301
J. Berkery et al., PRL 104 (2010) 035003
S. Sabbagh, et al., NF 50 (2010) 025020
J. Berkery et al., PRL 106 (2011) 075004
J. Berkery et al., NF 55 (2015) 123007

## Slide 19: Kinetic RWM stability evaluated for DIII-D and NSTX plasmas, reproduces dedicated experiments over wide rotation range
Kinetic RWM stability analysis for experiments (MISK)
S. Sabbagh et al., APS Invited talk 2014
Summary of results
  Plasmas free of other MHD modes can reach or exceed linear kinetic RWM marginal stability
  Bursting MHD modes can lead to non-linear destabilization before linear stability limits are reached
  Extrapolations of DIII-D plasmas to different Vf show marginal stability is bounded by 1.6 < qmin < 2.8
Charge 1

## Slide 20: Joint NSTX / DIII-D experiments and analysis gives unified kinetic RWM physics understanding for disruption avoidance
RWM Dynamics
  RWM rotation and mode growth observed
  No strong NTM activity
  Some weak bursting MHD in DIII-D plasma
    Alters RWM phase
  No bursting MHD in NSTX plasma
DIII-D (bN = 3.5)
NSTX (bN = 4.4)
DBpn=1(G)
fBpn=1(deg)
(arb)
Frequency (kHz)
t (s)
t (s)
amplitude
phase
Da
toroidal magnetics
rotation
growth
rotation
growth
amplitude
phase
Da
toroidal magnetics
S. Sabbagh et al., APS Invited talk 2014
Charge 1

## Slide 21: Evolution of plasma rotation profile leads to linear kinetic RWM instability as disruption is approached
DIII-D (minor disruption)
NSTX (major disruption)
MISK
unstable
stable
increasing time
gtwall
MISK
unstable
stable
increasing time
gtwall
Kinetic RWM stabilization occurs from broad resonances between plasma rotation and particle precession drift, bounce/circulating and collision frequencies
S. Sabbagh et al., APS Invited talk 2014
Charge 1

## Slide 22: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
(non-linear)
yN
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
-NTV
Torque
NBI
Torque
(NSTX)
Charge 2,3

## Slide 23: State space rotation controller designed for NSTX-U using non-resonant NTV and NBI to maintain stable profiles
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
(non-linear)
yN
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
0.0
0.2
0.4
0.6
0.8
1.0
NBI and NTV torque profiles for NSTX-U
Momentum Actuators
New NBI
(broaden rotation)
3D Field Coil
(shape wf profile)
NBI
Torque
(NSTX)
-NTV
Torque
NBI Torque
(NSTX-U)
Charge 2,3

## Slide 24: With planned NCC coil upgrade, rotation controller can reach desired rotation profile faster, with greater fidelity
NSTX-U wf control with
  6 NBI sources
  Greater core NTV from planned NCC upgrade
Better performance
  Faster to target t ~ 0.5tm
  Matches target wf better
Marginally stable profile
Broader stable
profile
NBI
NTV
Plasma rotation (kHz)
0
15
20
10
5
NBI, -NTV torque density (N/m2)
0.0
0.5
1.0
1.5
2.0
0.0
0.2
0.4
0.6
0.8
1.0
yN
Planned NCC upgrade
Also, calculations show that NCC can allow RWM control up to ideal MHD wall limit
Charge 2,3

## Slide 25: DECAF replicates the triggers found in new real-time plasma shutdown / event handler capability of NSTX-U
Important capability of DECAF: compare analysis using offline vs. real-time data
Plasma Shutdown Handler conditions are analogous to DECAF events
  Control system loss of vertical control  DECAF
DECAF comparison: VDE event
  Matches Plasma Control System when r/t signal is used (1 criterion)
  VDE event 13 ms earlier using offline EFIT signals (3 criteria: Z0, dZ0/dt, Z0 x dZ0/dt)
VDE
PCS state
Z0 (m)
Ip (MA)

## Slide 26: Automated identification of MHD mode bifurcation and locking recently developed for the DECAF code
NSTX 138854
bifurcation
lock
Zoomed-in View
Required capability to automatically analyze ubiquitous rotating MHD
Code is completely portable, kept fairly simple, potential future real-time processing
Charge 3,4

## Slide 27: Physics-based RWM state-space controller sustains high bN, low li plasma; NSTX-U with allow independent coil control
Controller model compensates wall currents
  Includes plasma mode-induced current model (DCON)
  Potential to allow control coils to be moved further from plasma and be shielded (e.g. ITER)
  Straightforward inclusion of multiple modes in controller
Balancing transformation
~3000+ states
Full 3-D model
…
RWM eigenfunction(2 phases, 2 states)
State reduction (< 20 states)
+
+
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
 USED on NSTX to sustain high bN > 6 operation
Charge 2,3

## Slide 28: High bN ST global eigenmodes have unique shape, multi-mode character; computed 2nd eigenmode component has dominant amplitude
mmVALEN code
t = 0.655s
mode 1
mode 2
2.0
1.0
0.0
R(m)
1.0
-1.0
Z(m)
2.0
0.0
-2.0
DCON dBN
mode 3
q
NSTX 133775
Computed n = 1 eigenmodes (bN = 6.1)
dBn RWM multi-mode composition
ideal eigenmode number
dBn amplitude (arb)
mode
1
mode
3
mode
2
Unstable
Stabilized by rotation
Charge 2,3

## Slide 29: In addition to active mode control, the NSTX-U RWM state space controller will be used for real-time disruption warning
RWM state space controller used for RWM control in NSTX - long pulse plasmas reached high stability parameters bN = 6.4, bN /li = 13
S. Sabbagh et al., Nucl. Fusion 53 (2013) 104007
RWM Sensor Differences (G)
dBp180
100
200
0
-100
t (s)
0.56
0.58
0.60
0.62
RWM
Measurement
Controller
(observer)
The controller “observer” produces a physics model-based calculation of the expected sensor measurements – a real-time synthetic diagnostic
If the real-time synthetic diagnostic poorly matches the measured sensor data, a real-time disruption warning signal can be triggered
  Technique will be assessed using the DECAF code
RWM sensors
Charge 2,3

## Slide 30: Active RWM control design study for proposed NSTX-U 3D coil upgrade (NCC coils) shows superior capability up to ideal wall limit
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.58
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.67
NCC (plasma facing side)

## Slide 31: Successful predicition of RMP optimization with partial coil sets and for new targets in 2017 KSTAR campaign
[J.K. Park, KSTAR 2017]
Charge 1, 3

## Slide 32: Generalized Neoclassical Toroidal Viscosity (NTV) Offset rotation profile V0NTV measured in KSTAR
(S.A. Sabbagh, Y.S. Park, J. Kim, W. Ko, et al.)
 Initially proposed on NSTX-U, potential for joint experiment/analysis with KSTAR
Charge 1, 3