## Slide 1: EP-TSG: impact of potential “polar region” modifications on research and scenarios
M. Podestà
for the EP-TSG
PPPL
May 24th, 2017

## Slide 2: Magnetic equilibrium, pulse duration, injected NB power
Required scenarios include LSN, IWL, USN
Configuration | Flat-top [s] | Max NB power | Notes
LSN | 2 | 8 | Default option for H-mode discharges. Need 2sec for current equilibration, average data over NB modulation pulses or RMPs in stationary conditions.
IWL | 1 | 4 | Excellent scenario for theory/experiment comparison. Good for diagnostics (reduced background from divertor). Well reproducible. Need 1sec for CHERS, MSE data with NB modulation.
USN | 2 | 8 | High-performance alternative to IWL plasmas. Good for diagnostics (reduced background from lower divertor, e.g. vert. FIDA)
EP-related experiments mostly insensitive to details of in/out gap, X-point radius
Reproducibility and reliability (e.g. of NB sources) more important
Possible exception: AE damping rate measurements vs k, d
  But: will start with ohmic discharges (no AE drive), then add <4MW Pnb
Scenarios with rev-Bt and rev-Ip are highly desirable
  Characterize NB ion confinement for counter-NB injection
  Validate diagnostics/theory/models, e.g. FIDA, AE destabilization by cntr NB ions

## Slide 3: Toroidal field, current and heating systems
Required Bt is 0.5-1T
  Highly desirable: decrease Bt to 0.35T to connect with NSTX
  Rev-Bt desirable if rev-Ip is also possible
Required Ip=0.6-1.5MA
  Lower limit: high/fully non-inductive scenarios at moderate Pnb<6MW
  Rev-Ip operations desirable
Require reliable NBI, need all 6 source
  Include NB modulation capability, min. on/off 10ms
  Include adjustable injection voltage 60-90kV
Highly desirable: up to 4MW of HHFW power for 0.5sec
  Study interaction of NB ions with RF
  Validate codes, e.g. “RF kick operator” in TRANSP
  NSTX-U is the only US device with RF

## Slide 4: Summary of required parameters