## Slide 1: Materials and Plasma-Facing Components TSG Discussion of Recovery Project impacts
MA Jaworski on behalf of the M&P TSG
NSTX-U Materials and PFCs Topical Science Group
B318 – PPPL – May 24, 2017
*Work supported by DOE contract DE-AC02-09CH11466

## Slide 2: Topical overview
Brief summary of TSG shape/scenario requirements based on FY16/17 and 5/7 year plan
  Review of 5/7 year research thrusts for M&P
  Review of experimental capabilities for FY16/17 plans
TSG summary of impact of polar regions modifications
  Impact on PFC-testing shape requests
  Impact of Recovery and polar regions on research thrusts

## Slide 3: M&P research will develop understanding of material migration and heat-flux handling of high-Z and liquid Li PFCs
MP-1: Understand lithium surface-science for long-pulse
  Assess impact of more complete Li coverage
  Use the Material Analysis and Particle Probe (MAPP) and laboratory studies to link tokamak performance to PFC surface composition
MP-2: Unravel the physics of tokamak-induced material migration and evolution
  Confirm erosion scalings and evaluate extrapolations
  Determine migration patterns to optimize technical solutions
MP-3: Establish the science of continuous vapor-shielding
  Determine the existence and viability of stable, vapor-shielded divertor configurations
  Determine core compatibility and extrapolations for extended durations and next-step device parameters
5-Year Plan Research Thrusts

## Slide 4: Staged conversion mitigates risk and enables comparative assessment of both high-Z and liquid Li
Open divertor and flexible magnetic configuration enables multiple studies and material selection
Single-variable experiment in single campaign enabled by conversion (i.e. high-Z vs. lithium PFCs)

## Slide 5: Reference shape requests enable exposure of novel PFC materials and utilizes MAPP diagnostic
High-performance discharge
PFC test reference discharge
Shape developed to perform dedicated tests on outboard PFCs
  Heat-flux figure of merit indicates 2/3 of high-performance heat flux on row 2
  Does not reverse helicity on IBDH
FY16 plans limited to 1s discharge at 10 MW/m2
  Can make MAPP measurements with discharges similar to 2016
  Science aided by long pulse capability
Reference shape request:
  0.73<RSP,out<0.84 (i.e row 2)
  Qinc = 10 MW/m2 for 1s, & <max qualified for 5s>
MAPP exposure shape request:
  OSP close to/on MAPP R~1.04m
  Qinc = <max qualified for 5s>

## Slide 6: Reference shape requests enable exposure of novel PFC materials and utilizes MAPP diagnostic
Shape developed to perform dedicated tests on outboard PFCs
  Heat-flux figure of merit indicates 2/3 of high-performance heat flux on row 2
  Does not reverse helicity on IBDH
FY16 plans limited to 1s discharge at 10 MW/m2
  Can make MAPP measurements with discharges similar to 2016
  Science aided by long pulse capability
Reference shape request:
  0.73<RSP,out<0.84 (i.e row 2)
  Qinc = 10 MW/m2 for 1s, & <max qualified for 5s>
MAPP exposure shape request:
  OSP close to/on MAPP R~1.04m
  Qinc = <max qualified for 5s>
FOM ~ 60 MW/m2
High-performance discharge
High-Z reference discharge
Shape already achieved in 2016 (203879)

## Slide 7: Topical overview
Brief summary of TSG shape/scenario requirements based on FY16/17 and 5/7 year plan
  Review of 5/7 year research thrusts for M&P
  Review of experimental capabilities for FY16/17 plans
TSG summary of impact of polar regions modifications
  Impact on PFC-testing shape requests
  Impact of Recovery and polar regions on research thrusts

## Slide 8: Research thrusts MP-1 and MP-2 not significantly impacted*
M&P TSG meeting held May 11 to gather input
  *Assuming diagnostic interpretation and implementation can be addressed
  *Assumes B and Li conditioning will continue
Diagnostic impacts
  MAPP not affected (Kaita)
  IR thermography and spectroscopic: needs analysis of spatial resolution (Vlad, Gray)
  Witness plates & QCMs not affected (Skinner)
  Langmuir probes; need redesign (Jaworski – included in PFC requirements draft document)
C. Skinner
J. Nichols
R. Kaita

## Slide 9: Research thrust MP-3 can continue on general ablative materials
Research plan modified by delay in high-Z and liquid Li
  Expect restart with graphite PFCs
  Accessible PFC temperatures far exceed NSTX
Redeposited material can create reservoir for decomposition into plasma
  Li2CO3 decomposition releases CO2 and should cool plasma
  Represents general case of self-limiting material by ablative shielding
  Motivates evaluation in revised milestone 18-2 (text tomorrow)
Potential reservoir

## Slide 10: Summary
Materials and PFCs TSG group has identified impacts of the recovery activity
  Diagnostic impacts brought forth by group
  Research plans only require some specific shapes
  Shapes for PFC testing already expected to be determined by material performance limits
M&P TSG research thrusts partially impacted by polar-region changes
  MP-1 and MP-2 can be conducted with attention to diagnostic impacts
  Consideration of general material ablation can make MP-3 more applicable to a wider range of materials