## Slide 1: Parametric dependencies of low-k pedestal turbulence in NSTX H-mode plasmas
David R. Smith1
with R. Fonck1, G. McKee1, D. Thompson1, I. Uzun-Kaymak1, A. Diallo2, and B. Stratton2
1University of Wisconsin-Madison 2Princeton Plasma Physics Lab
Plasma Physics Seminar
UW-Madison
April 23, 2012

## Slide 2: What are the characteristics and parametric dependencies of pedestal turbulence in NSTX?
ITER and next-step devices need accurate models of pedestal dynamics
  Global confinement predictions
  Diverter heat flux and first-wall lifetime predictions
  ST edge parameters are among the most challenging regimes for turbulence simulations (steep gradients, high b, large ri/a, strong shaping)
Here, we measure pedestal turbulence parameters in NSTX H-mode plasmas during ELM-free, MHD quiescent periods
  Poloidal correlation length, wavenumber, and decorrelation time
  Identify parametric dependencies (∇ne, ∇Ti, etc)
NSTX: BES
measurements
from multiple discharges in steep gradient region
C-Mod: stored energy increases with pedestal height
Hughes, PoP, 2002

## Slide 3: Outline
Beam emission spectroscopy (BES) diagnostic overview
Pedestal turbulence measurements
  LH transition
  ELM-free, MHD quiescent periods
  Parametric scalings
Correlation length during the ELM cycle
  Initial theory/experiment comparison
Other BES observations
  Post-ELM harmonic features
  TAE and GAE mode structures
Future work and summary

## Slide 4: Beam emission spectroscopy (BES) is a diagnostic technique for measuring ion gyroscale (kρi < 1) density fluctuations
Measured & derived quantities
  Fluctuation amplitudes
  Frequency spectra
  Radial and poloidal correlation lengths
  Decorrelation times
  Poloidal flow, flow fluctuations, flow shear, and 2D flow fields
  2D fluctuation imaging
  3-wave bispectral analysis
  Particle flux
Figures courtesy of
DIII-D BES group

## Slide 5: BES measures Doppler-shifted Da emission (l0=656 nm) from neutral beam particles
neutral beam Da emission
density
fluctuation
C ≈ 1/2

## Slide 6: NSTX BES system includes 56 sightlines in radial and poloidal arrays spanning core to SOL
32 detection channels; expansion planned for NSTX-U
2 MHz sampling with digital anti-alias filter
2-3 cm image size and sensitive to ñ with k┴ri ≤ 1.5
Field-aligned optics with high throughput (etendue = 2.3 mm2-ster)

## Slide 7: Point spread functions
Model | Ideal fiber | Focusing optics | Optical+NB decay | Optical+NB intensity | Optical+fieldline excursion | All effects
Y 1/e2 width (cm) | 3.2 | 4.0 | 4.4 | 3.2 | 4.4 | 4.4
Y displacement (cm) | 0.0 | 0.0 | 0.5 | 0.0 | -0.5 | 0.3
X (au) image int.
Y (cm) ~ radial
Z (cm) ~ binormal

## Slide 8: NSTX BES system commissioned in 2010

## Slide 9: BES measurements show radially-localized response to NB emission and high signal-to-noise ratio

## Slide 10: BES measurements provide poloidal correlation lengths (Lc), poloidal wavenumbers (kq), and decorrelation times (td) in the pedestal
Filtered data shows eddy propagation
Turbulence quantities calculated from time-lag cross-correlations

## Slide 11: Decrease in fluctuations at LH transition observed from edge to core regions
Similar increase in fluctuations observed at HL back-transitions

## Slide 12: BES shows complex turbulence activity in pedestal during quiescent H-mode periods

## Slide 13: Questions about pedestal turbulence to ask and answer with BES measurements
What are typical Lc, kq, and td values in the H-mode pedestal during ELM-free, MHD quiescent periods?
How do Lc, kq, and td change with plasma parameters?
  ∇ne, ∇Ti, q/ŝ, ne, be, nped, etc.
Can we connect observations to edge turbulence simulations?
  XGC1 or BOUT++?

## Slide 14: Pedestal turbulence measurements and plasma parameters from ELM-free, MHD quiescent H-modes were gathered in a database
Database details
129 entries from 29 discharges
  BT0 = 4.5 kG
  Ip = 700-900 kA
  15-45 ms averaging
Turbulence parameters
  Lc/ri ~ 12
  kqri ~ 0.2
  td/(a/cs) ~ 5
  tdw*pi ~ 0.15
Plasma parameters
  generally 50%-300% variation
  ne, ∇ne, Te, ∇Te, Ti, ∇Ti, vt, ∇vt, q, ŝ, ne, ni, b, be, nped, DRped, drsep

## Slide 15: A search algorithm identified linear regression models that show similar scalings despite different parameter compositions
Search algorithm minimizes regression model’s squared sum of errors (SSE) by adding or removing xk in model
Many SSE local minima exist in high dimensional xk space
Objective: find many models and screen for statistical quality
  Statistical significance (ak t-statistics)
  Multicollinearity (variance inflation factor)
  Error normality (Studentized residuals)
plasma
parameters
scaling
coefficient
turbulence
parameters
Linear regression models exhibit similar scalings despite different parameter compositions

## Slide 16: Lc increases at higher ∇ne, 1/LTe, n, and nped; decreases at higher Ti, ∇Ti, and ∇vt
Consistent scalings
emerge from different regression models

## Slide 17: kq scalings consistent with Lc scalings; td scalings provide additional insight

## Slide 18: Scalings point to a variety of turbulence mechanisms
Parametric scalings point to enhanced turbulence structures (larger Lc and td) at higher ∇ne and 1/LTe
  Possibly TEM turbulence
∇vt scalings for Lc and kq point to turbulence suppression
  Equilibrium E×B flow shear
ne and ni scalings for Lc and kq are consistent with zonal flows
  td decreases with ne
Pedestal height (nped) increases at larger Lc and td
  Consistent with larger structures and wider pedestals

## Slide 19: Poloidal correlation lengths during inter-ELM cycle are consistent with XGC1 simulation
~ 4 cm
~ 10 cm
Sampled BES region
Radial Lc analysis is in progress (BES & refl.)

## Slide 20: Post-ELM harmonic features at 50-100 kHz are localized at the top of the pedestal
Harmonic features are either absent from or weakly present in magnetic spectra

## Slide 21: TAE and GAE mode structures have been observed in extended radial regions
GAE mode
TAE burst

## Slide 22: Directions for future work
Quantify fluctuation amplitudes
Quantify radial correlation length
Study pre- and post-LH transition
Measure flow fluctuations and flow shear
  Study flow fluctuations and shear across LH transition
Identify post-ELM harmonic oscillations
  Captured by peeling-ballooning model?
  Connect to DIII-D observations

## Slide 23: Summary: We measured pedestal turbulence quantities and identified parametric dependencies in ELM-free, MHD quiescent H-mode plasmas
ST edge parameters are among the most challenging regimes for simulations
The BES system on NSTX can measure poloidal correlation length, wavenumber, and decorrelation time of pedestal turbulence
Regression models identify parametric scalings that point to a variety of turbulence mechanisms
  Enhanced turbulence structures at higher ∇ne and 1/LTe
  ∇vt scalings point to E×B turbulence suppression
  Collisionality scalings for Lc and kq are consistent with zonal flows
  Pedestal height increases at longer Lc and td
Other observations
  Initial experiment/theory comparison for inter-ELM measurements
  Reduced turbulence at LH transition
  Post-ELM harmonic oscillations
  TAE and GAE mode structure