## Slide 1
Scientific Opportunities and Challenges on the
National Spherical Torus eXperiment Upgrade (NSTX-U)
Jon Menard
NSTX-U Program Director
Graduate Student Seminar
PPPL theory conference room
February 2, 2015
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Talk Outline
Introduction to Spherical Tokamaks/Tori (STs)
Description of NSTX Upgrade
Unique physics characteristics of ST and research opportunities
  Macroscopic Stability
  Transport and Turbulence
  Boundary Physics
  Energetic Particles
  Non-inductive start-up, ramp-up, sustainment
Summary

## Slide 3
ST is a low aspect ratio tokamak with A < 2
Natural elongation makes its spherical appearance
Y-K.M. Peng, D.J. Strickler, NF (1986)
A. Sykes, et al., Nucl. Fusion (1999).
Camera image from START
Aspect Ratio A = R /a
Elongation k = b/a
“natural” = “without active shaping”
ITF
ITF
BTF ∝ ITF/R
Ip
Ip
Ip
x
Ip
x
x
Ip
Ip
Note: ST differs from FRC, spheromak due to BTF

## Slide 4
A ~ 3,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
A ~ 1.5,
k = 2-3,
q95 = 8-12,
bT = 10-40%
Tokamak
ST
A spherical tokamak (ST) is a high beta tokamak
Favorable average curvature improves stability at high beta
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 5
ST can be compact, high beta, and high confinement
Higher elongation k and low A lead to higher Ip, bT and tE
Ip ~ ITF (1 + k2) / (2 A2 q*)
bT [%] º bN Ip / (aBT0)
S. Jardin et al., FS&T (2003)
D.A. Gates et al., NF (2007).
High κ ∼ 3.0 equilibrium in NSTX.
tE ∝ Ip
Ip ~ ITF for ST due to low A and high k
• ST has high Ip due to high κ and low A
• Ip increases tokamak performance
• ST can achieve high performance cost effectively
$
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 6
  Lower A  increased toroidicity  higher b, strong shaping
  Higher b  electromagnetic effects in turbulence, energetic-particle modes, RF heating and CD (over-dense plasmas)
  Higher fraction of trapped particles (low A), increased normalized orbit size (high b), and flow shear (due to low B, low A) broad range of effects on transport and stability
  Increased normalized fast-ion speed (high b)  simulate fast-ion transport/losses of ITER
  Compact geometry (small R)  high power/particle/neutron flux relevant to ITER, reactors
New physics regimes are accessed at low aspect ratio, enhancing the understanding of toroidal confinement physics
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 7
Extend Predictive Capability for ITER and Toroidal Science
  High b physics, rotation, shaping for MHD, transport
  Non-linear Alfvén modes, fast-ion dynamics, Electron gyro-scale turbulence at low n*
Unique ST properties support and accelerate a range of development paths toward fusion energy
Burning Plasma Physics - ITER

## Slide 8
If the cost of volume neutron source (FNSF) facility is “modest” << ITER, DEMO, it becomes highly attractive development step in fusion energy research. M.A. Abdou, et al., FTS (1996)
Fusion needs FNSF(s) (modest cost, low T, and reliable) to Test and Qualify Fusion Components
FNSFs
Without R&D, fusion components could fail prematurely which often requires long repair/down time. This would cripple the DEMO operation.
FNSF can help develop reliable fusion components.
Such FNSF facilities must be modest cost, low T, and reliable.
Fusion needs to develop reliable/qualified components which are unique to fusion:
Divertor / PFC
Blanket and Integral First Wall
Vacuum Vessel and Shield
Tritium Fuel Cycle
Remote Maintenance Components
FNSF-ST
FNSF-AT

## Slide 9
There have been several studies of ST-FNSF showing the potential attractiveness of this approach
Projected to access high neutron wall loading at moderate R0, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R0 ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R0, careful design
R&D Needs for an ST-FNSF
  Non-inductive start-up, ramp-up, sustainment
    Low-A  minimal inboard shield  no/small transformer
  Confinement scaling (especially electrons)
  Stability and steady-state control
  Divertor solutions for high heat flux
  Radiation-tolerant magnets, design
Culham (UK)
UT Austin
ORNL
PPPL
Example ST-FNSF concepts

## Slide 10
NSTX-U to provide data base to support ST-FNSF design, ITER operations, boundary solutions
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
~ 5-10x increase in nTt from NSTX
NSTX-U average plasma pressure ~ Tokamaks
Key NSTX-U research topics for FNSF and ITER
Stability and steady-state control at high b
Confinement scaling (esp. electron transport)
Non-inductive start-up, ramp-up, sustainment
Divertor solutions for mitigating high heat flux
J. Menard, et al., NF (2012)
New CS provides higher 2x TF (improves stability), 3-5s needed for J(r) equilibration
More tangential injection provides 3-4x higher CD at low IP:
  2x higher absorption (4080%) at low IP
  1.5-2x higher current drive efficiency

## Slide 11
11
New 2nd NBI
1st NBI
NSTX Upgrade Project nearing completion
First plasma expected Mar/Apr 2015, research in May/June

## Slide 12: New Center-Stack Installed In NSTX-U Vacuum pump-down achieved last month (January)

## Slide 13: Talk Outline
Introduction to Spherical Tokamaks/Tori (STs)
Description of NSTX Upgrade
Unique physics characteristics of ST and research opportunities
  Macroscopic Stability
  Transport and Turbulence
  Boundary Physics
  Energetic Particles
  Non-inductive start-up, ramp-up, sustainment
Summary

## Slide 14
Higher bT enables higher fusion power and compact FNSF for required neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Data base from START, MAST, PEGASUS and NSTX
Pfusion ∝ p 2 x Vol
Pfusion ∝ bT2 BT04 x Vol
$
Physics Knob
Product
Investment
Wn ∝ Pfusion / Area
High neutron wall loading Wn possible in a compact ST
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1 MW/m2 with R ~ 1 m FNSF feasible!

## Slide 15
S.A. Sabbagh PRL(2006)
Record bN and bN / li accessed in NSTX
using resistive wall mode stabilization
J. W. Berkery, PRL (2011)
W. Zhu, PRL (2006)
S.A. Sabbagh at this APS
High bN regime is important for bootstrap current generation.
High bN/li regime important since high fBS regime has low li.
Major mission of NSTX-U is to achieve fully non-inductive operations at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM

## Slide 16: Research opportunities
How do RWM stability and rotation damping from neoclassical toroidal viscosity (NTV) change at the lower (ultimately up to 10x lower) collisionality values of NSTX-U?
  Enhanced kinetic damping for RWM?
  Enhanced rotation damping in 1/n regimes?
What are leading causes of disruptions in ST? and what are implications for next steps?
  NSTX-U will implement advanced profile and instability controls – how much does this reduce disruptivity?
  NSTX-U will perform in-depth study/diagnosis of “halo/hiro” currents, i.e. edge plasma and wall currents and forces induced by disruptions

## Slide 17
Favorable Confinement Trend with Collisionality and b found
Important implications for future STs and Demo with much lower n*
M. Valovic et al., NF (2011)
Fig. 70. (a) Normalized confinement time as a function of collisionality at mid-radius in NSTX. Blue points are from discharges that used HeGDC+B wall conditioning, while red points are from discharges that used Li. Reprinted with permission from S.M. Kaye et al., Nucl. Fusion 53 063005 (2013). Copyright (2013). Institute of Physics.
(b) Collisionality scan of thermal energy confinement time in MAST. Reprinted with permission from M. Valovic et al., Nucl. Fusion 51 073045 (2011). Copyright (2011) Institute of Physics.
NSTX
Very promising ST scaling to reactor condition, if continues on NSTX-U/MAST-U
NSTX
tE, th µ n*e-0.1 b-0.9 tokamak empirical scaling (ITER98y,2)
tE, th µ n*e-0.8 b-0.0 ST scaling
S.M. Kaye et al., NF (2007) (2013)
MAST
B tE,th [ T s]
~ n*e -0.82
n*e

## Slide 18
Microtearing-driven (MT) transport may explain ST collisionality scaling
Microtearing-driven ce vs. nei using the GYRO code.
W. Guttenfelder, et al., PoP(2012)
MT growth rate decreases with reduced collisionality in qualitative agreement with the NSTX experiment.
Further electron confinement improvement expected due to reduced collisionality.
NSTX-U

## Slide 19
ETGs measured for the first time with high-k scattering
High be or larger re ∝ be0.5 of ST plasma enabled measurement of ETGs.
E. Mazzucato et al., NF (2009)
H.Y. Yuh et al., PoP (2009)
J.L. Peterson, et al., PoP(2011).
ETG Suppression in Reversed Shear
Electron Temperature Gradient Mode (ETG) Excitation with Core Electron Heating
Shear stabilization of ETGs D. R. Smith, et al., PRL (2009)
Density gradient stabilization of ETGs Y. Ren, et al., PRL (2011)
Note: Here we call electron gyro-scale turbulence as ETGs
Calculated ETG ce by GTS code agrees with experiment
S. Ethier et al., IAEA (2010)
ce (m2/sec)
ce (m2/sec)
time (Vth/LTe)
ce (GTS)

## Slide 20
What are the leading causes of anomalous electron transport in the ST, and tokamaks generally?
  Will electrostatic turbulence (ETG, TEM) dominate over micro-tearing (ce ~ n) at lower collisionality values of NSTX-U?
Will ion thermal and impurity transport remain predominantly neoclassical?
  Neoclassical diffusivities also scale ~ n
Research opportunities
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 21
H-mode / ELM physics: High Priority Research Goal
Unmitigated ELMs could cause PFC damage in reactors
ST is in strongly shaped ELM regimes
P.B. Snyder et al., PoP (2002).
NSTX, PEGASUS
(Type I)
MAST
(Type I)
Video images of MAST plasmas showing a filamentary ELM structure.
  N. Ben Ayed et al., PPCF (2009).
K.E. Thome et al., EPR (2014)
FNSF
L-H power threshold scaling extended for low A
• NSTX/MAST/PEGASUS accessed H-mode at very low heating power < 1 MW and also in ohmic plasmas
• NSTX-U and MAST-U will provide H-mode access scaling for FNSF

## Slide 22
ELM Stabilization and Mitigation
Through application of lithium and 3-D fields
D.K. Mansfield, et al., JNM (2009)
ELMs stabilized with edge pressure modification with Li in NSTX
R. Maingi, et al., PRL (2009).
ELM mitigation with n=3
3-D fields (ELM Coils) in MAST
Increasing Type I ELM freq. by x 8 (900 Hz) has reduced heat flux
A. Kirk et al., NF (2013)

## Slide 23: Research opportunities
At higher aspect ratio and lower collisionality of NSTX-U, will ELMs remain predominantly J||-driven?
H-mode pedestal profiles determine overall fusion performance…. But what are dominant transport mechanism(s) in the H-mode pedestal region?
  Neoclassical, kinetic ballooning, electron T (ETG), other?
  Ahmed Diallo’s Early Career Award with “burst” Thomson Scattering will help determine fast time evolution, transport
Lithium coatings substantially increased NSTX global confinement (1.4x ITER H) – important for next-steps
  How high can we make energy confinement in NSTX-U?
  2x ITER H-mode scaling? What sets the limit?

## Slide 24
Divertor heat flux in Low-A regime
ST power flux width clearly shows 1/Bpoloidal variation
Most divertor power arrives at outboard side in MAST and NSTX!
Ratio of outboard power flux vs. inboard in MAST
STs data breaks A degeneracy of power flux width study.
* Unfavorable for large size, Ip devices such as ITER and Demo
"P B / R" as the new heat flux metric which is favorable for STs
Outboad heat flux
POB >> PIB
Inboad heat flux
PIB (kW)
POB (kW)
POB/PIB
Time (s)
G.F. Counsell et al., PPCF (2002)
Heuristic model by R.J. Goldston, NF (2012).
~ 40 kW
~ 2 MW
~ 50
T. Eich et al., NF (2013).

## Slide 25
Divertor flux expansion of ~ 50 achieved with
Snow Flake Divertor with large heat flux reduction in NSTX
NSTX-U will investigate novel divertor heat flux mitigation concepts needed for FNSF and Demo.
• Up-and-down symmetric Snow Flake / X-divertors
• Lithium + high-Z metal PFCs
Divertor heat flux (MW/m2)
Snowflake divertor in NSTX
OSP
V. A. Soukhanovskii et al., PoP (2012)

## Slide 26: Research opportunities
What sets the heat flux width in the open field line region?
  Mostly drifts + collisions (i.e. neoclassical) or does turbulence play a role?
How does divertor geometry (such as snowflake) influence the plasma edge properties?
How do Li and high-Z PFCs modify the edge region, and also the core performance?
  NSTX-U will study “vapor shielding” regime to improve understanding of Li evaporation + radiation and impact on power exhaust / heat-flux mitigation / core performance

## Slide 27
NBI heated ST plasmas provide an excellent testbed for a-particle physics
Alfvenic modes readily accessed due to high Va > VAlf
EP parameter space
a-particles couples to Alfven-type mode strongly when Va > VAlf ~ b-0.5 Cs
Va > VAlf in ITER and reactors
In STs, the condition is easily satisfied due to high beta
A prominent instabilities driven by fast particles are global and called toroidal Alfven eigenmodes (TAE).
NSTX-U will also explore Va < VAlf regime giving more flexibility
  M.P. Gryaznevich et al. PPCF (2004)
Stabilization of TAEs at high β in MAST
TAEs significantly modified at high b as VAlf Cs
  E. D. Fredrickson et al., NF (2013)

## Slide 28
“TAE avalanche” shown to cause energetic particle loss
Uncontrolled a-particle loss could cause reactor first wall damage
Time (ms)
(a)
Multi-mode TAE avalanche can cause significant EP losses as in “sea”of TAEs expected in ITER
D.S. Darrow et al., NF (2013).
  E. D. Fredrickson et al., NF (2013)
Progress in simulation of neutron rate drop
due to TAE avalanche
Time (ms)
Neutron rate (a.u.)
Fast ion loss rate (a.u.)
Frequency (kHz)

## Slide 29: Research opportunities
Will reduced drive for fast-ion instabilities in NSTX-U reduce anomalous fast-ion transport?
How will NSTX-U plasmas respond to more tangential neutral-beam / fast-ion injection?
  Are current and momentum drive consistent with theory?
What is role of high-f fast-ion instabilities (GAE/CAE) in core electron transport?
  Is this physics unique to high-beta/ST?

## Slide 30
Compact ST-FNSF has no/small central solenoid
IP Start-up/Ramp-up Critical Issue for ST-FNSF/Demo
ST-FNSF Scenarios
IP [MA]
NBI
Time
HHFW
EC/EBW, HI, PF
Solenoid-free
Start-up
high bT, bN, k, disruption avoidance, high H, heat flux mitigation
Current ramp-up and profile control
• Two novel techniques for solenoid-free start-up and ramp-up will be investigated
  RF: ECH/EBW and HHFW
  Helicity Injection
~ 1-2 MA of solenoid-free start-up current needed for FNSF
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 31
Helicity Injection Is an Efficient Method for Current Initiation
Coaxial Helicity Injection (CHI) Concepts Being Developed
CHI developed on HIT and HIT-II and transferred to NSTX
Discharge evolution of 160 kA closed flux current produced by CHI alone in NSTX
R. Raman et al., PRL (2006)

## Slide 32
Current Ramp-Up and Profile Control Crucial for FNSF
Major Research Topics for NSTX-U
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
Near sustained discharges obtained with modest HHFW power
NSTX

## Slide 33
NSTX has accessed A, bN, k needed for ST-based FNSF
Requires fBS ≥ 50% for plasma sustainment
fBS º IBS / Ip = CBS bp / A0.5 = (CBS/20) A0.5 q* bN µ A-0.5 (1+k2) bN2 / bT
SC-ST
NSTX achieved fBS ~ 50% and fNI ~ 65-70% with beams
NSTX-U expects to achieve fNI ~100% with the more tangential NBI (~ 1.5- 2x higher current drive efficiency)
S.P. Gerhardt et al., NF (2011)

## Slide 34: Research opportunities
Can NSTX-U really sustain all of its current without a transformer? If so, at what performance level?
If NSTX-U succeeds at non-inductive sustainment, what level of non-inductive start-up and ramp-up is achievable?
  Is it really possible to have a tokamak with NO solenoid?
Can we develop simple yet powerful enough models to simulate all this accurately?
  Complex combination of current drive, transport, stability (TRANSP, TSC, + other models)

## Slide 35
NSTX-U will provide many opportunities to study toroidal confinement physics in new regimes:
  Low aspect ratio, strong shaping, high b, low collisionality
  Access to strong fast-ion instability drive, high rotation
  Advanced divertors, lithium walls, high-Z PFCs
The opportunities described here are just a small fraction of the research possibilities available!
Please see next slide for people to contact for more
Summary
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 36
Contacts for 1st/2nd year projects, thesis ideas
Notes: Here is the outline of this review to give you an overview of the world ST research.