## Slide 1: Confinement and stability discoveries from high-beta spherical tori
Jonathan Menard (PPPL)
Program Director for NSTX Upgrade
With contributions from the NSTX, MAST
Pegasus, and other ST research teams
Norman Rostoker Memorial Symposium
The Fairmont Newport Beach Hotel
August 24-25, 2015

## Slide 2: Outline
ST overview
Global MHD Stability
Energy Confinement
Energetic Particles
ST Upgrade Status
Summary

## Slide 3
A ~ 3-4,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
A ~ 1,
k = 0.5-10,
q ~ 0,
b ~ 100%
Tokamak
ST
“Spherical” tokamak (ST) has aspect ratio A < 2
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Natural elongation makes its spherical appearance
Favorable average curvature improves stability at high beta
FRC
A ~ 1.2-2,
k = 2-3,
q95 = 6-20,
bT = 10-40%
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 4
High bT enables compact Fusion Nuclear Science Facility (FNSF) with high neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Database from START, MAST, PEGASUS, NSTX
Pfusion ∝ p 2 x Vol
Pfusion ∝ bT2 BT04 x Vol
$
Physics limited
Investment & engineering limited
Wn ∝ Pfusion / Area
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1-2 MW/m2 with R ~ 1-2m FNSF feasible!

## Slide 5
MA-Class ST Research Started ~2000
Complementary Physics Capabilities of NSTX and MAST
NSTX
MAST
A. Sykes, IAEA 2000, NF 2001
M. Ono, IAEA 2000, NF 2001
NSTX
R = 85 cm
A ≥ 1.3
= 1.7 - 3.0
BT = 5.5 kG
Ip ≤ 1.5 MA
Vp ≤ 14 m3
PNBI = 7.4 MW
Similar Capabilities
MAST
R = 80 cm
A ≥ 1.3
= 1.7 – 2.5
BT ~ 5.0 kG
Ip ≤ 1.5 MA
Vp ≤ 10 m3
PNBI = 4.0 MW
Comprehensive diagnostics
Physics integration
Scenario development
Passive Plates
Helicity Injection
Fast wave heating
1 x 6 RWM Coils
Large divertor volume
Merging/Compression
Electron Cyclotron
2 x 12 ELM coils
Complementary Capabilities

## Slide 6: Mega-ampere-class STs rely heavily on co-injected neutral beams for heating, current drive
New 2nd NBI
(RTAN=110, 120, 130cm)
5MW, 5s, 80keV
Original NBI
(RTAN = 50, 60, 70cm)
5MW, 5s, 80keV
NSTX-U

## Slide 7: New physics accessed in ST  enhanced understanding of toroidal confinement physics
Lower A  higher b, strong shaping
Higher b 
  Electromagnetic effects in turbulence
  More potential drive for fast-ion-driven instabilities
    Simulate fast-ion transport of ITER / burning plasmas
  Over-dense plasmas: RF heating, current drive
Low-A / high-b broadly impact transport, stability:
  Higher fraction of trapped particles (low A)
  Increased normalized orbit size (high b)
  Increase flow shear (due to low B, low A)
  Compact geometry (small R)  higher power and particle fluxes relevant to ITER, reactors

## Slide 8: Outline
ST overview
Global MHD Stability
Energy Confinement
Energetic Particles
ST Upgrade Status
Summary

## Slide 9: Simulations find bN is more aspect ratio invariant than bN – both with & without wall stabilization
bT  2m0p / BT02
b  2m0p / B2
IN  IP / aBT0 [MA/mT]
bN  bT (%) / IN
bN  b (%) / IN
J. Menard, PoP 2004, PPPL-3779
Para / diamagnetic effects and BP / B ratio important at low-A
fBootstrap ~ 50%
fBS ~ 100%

## Slide 10
Record bN and bN / li accessed in NSTX using passive + active resistive wall mode stabilization
High bN regime is important for bootstrap current generation.
High bN / li regime important since high fBS regime has low li.
Major NSTX-U mission is to achieve fully non-inductive operation at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM
S. Sabbagh, PRL 2006
J. Berkery, PRL 2011
W. Zhu, PRL 2006

## Slide 11: Rotation / centrifugal effects important and measureable in equilibrium
J. Menard, NF 2005

## Slide 12: Kelvin-Helmholtz (KH) instabilities predicted when central sound-speed Mach number Ms ≈ 0.7-0.8
Rotation profile
n=1 K-H
Eigenfunction
I. Chapman, NF 2012

## Slide 13: Hybrid MHD-drift-kinetic stability calculations find rotation + fast-ions can weaken wall-stabilization of p-driven kink
Low-rotation fluid with-wall limit is very high  marginal bN ~ 7-8
Increasing rotation lowers max bN to ~5.5 at mode onset time
Full kinetic treatment including fast-ions  marginal bN ~3.5  most consistent with experiment
MARS-K code needed / used to explain NSTX instability onset at highest rotation, bfast fractions
J. Menard, PRL 2014
Experimental bN

## Slide 14: Outline
ST overview
Global MHD Stability
Energy Confinement
Energetic Particles
ST Upgrade Status
Summary

## Slide 15
High confinement multiplier H needed for compact ST
Fusion gain Q depends strongly on “H”, Q µ H 5-7
H = 1.2 – 1.3 enables compact FNSF, design flexibility/margin
• Ion energy transport in H-mode ST plasmas near neoclassical level due to high shear flow and favorable curvature
• Electron energy transport anomalous (as for all tokamaks)
EPH
H-mode
NSTX
ST-FNSF
Y. Ren (PPPL)
NSTX
R. Maingi, PRL 2010
S. Gerhardt NF 2014
Enhanced pedestal H-mode (EPH) has H up to 1.5-2  attractive for ST-FNSF

## Slide 16: Electron and ion tE scale differently in ST, and different than at higher aspect ratio
Ions: tE  Ip
Neoclassical
(r/a=0.5-0.8)
Ion tE  IP, consistent with neoclassical ion transport
  Implies ion turb. suppressed by high E×B shear  possibility of isolating causes of e-transport
Electron tE  BT
  Could imply Electron Temperature Gradient (ETG) modes, and/or electromagnetic turbulence
Electrons: tE  BT
3.5 kG
5.5 kG
S.M. Kaye, PRL 2007

## Slide 17
Favorable confinement trend with collisionality, b found
Important implications for future ST FNSF, Demo with lower n*
Fig. 70. (a) Normalized confinement time as a function of collisionality at mid-radius in NSTX. Blue points are from discharges that used HeGDC+B wall conditioning, while red points are from discharges that used Li. Reprinted with permission from S.M. Kaye et al., Nucl. Fusion 53 063005 (2013). Copyright (2013). Institute of Physics.
(b) Collisionality scan of thermal energy confinement time in MAST. Reprinted with permission from M. Valovic et al., Nucl. Fusion 51 073045 (2011). Copyright (2011) Institute of Physics.
NSTX
Very promising ST scaling to reactor condition, if continues on NSTX-U/MAST-U
NSTX
tE, th µ n*e-0.1 b-0.9 tokamak empirical scaling (ITER 98y,2)
tE, th µ n*e-0.8 b-0.0 ST scaling
S.M. Kaye, NF 2007, 2013
MAST
B tE,th [ T s]
~ n*e -0.82
n*e
M. Valovic, NF (2011)

## Slide 18
Micro-tearing-driven (MT) transport
may explain ST tE collisionality scaling
MT-driven ce vs. nei using the GYRO code
W. Guttenfelder, PoP 2013, PoP 2012, PRL 2011
MT growth rate decreases with reduced collisionality in qualitative agreement with the NSTX experiment.
Further electron confinement improvement expected due to reduced collisionality.
NSTX-U
NSTX

## Slide 19: Outline
ST overview
Global MHD Stability
Energy Confinement
Energetic Particles
ST Upgrade Status
Summary

## Slide 20
NBI-heated STs excellent testbed for a-particle physics
Alfvenic modes readily accessible due to high Vfast > VAlfvén
a-particles couple to Alfvénic modes strongly when Va > VA ~ b-0.5 Cs
Va > VA in ITER and reactors: condition easily satisfied in ST due to high b
Fast-particle-driven Alfvén Eigenmodes: Toroidal, Global, Compressional
NSTX-U will also explore Vfast < VA regime giving more flexibility
  M.P. Gryaznevich, PPCF 2004
Stabilization of TAEs at high b in MAST
TAEs significantly modified at high b as VA  Cs
  E. Fredrickson, NF 2013
EP parameter space
NSTX data:

## Slide 21
“TAE avalanche” shown to cause energetic particle loss
Uncontrolled a-particle loss could cause reactor first wall damage
Time (ms)
(a)
Multi-mode TAE avalanche can cause significant EP losses as in “sea”of TAEs expected in ITER
D.S. Darrow, NF (2013)
  E. Fredrickson, NF 2013
Time (ms)
Neutron rate (a.u.)
Fast ion loss rate (a.u.)
Frequency (kHz)
Progress in simulation of neutron rate drop
due to TAE avalanche

## Slide 22: Rapid TAE avalanches could impact NBI current-drive in advanced scenarios for NSTX-U, FNSF, ITER AT
Discrepancy between reconstruction and total assuming
classical JNBCD
Minor radius
700kA high-bP plasma with rapid
TAE avalanches has time-average DFI = 2-4m2/s
NSTX: rapid avalanches can lead to redistribution/loss of NBI current drive
NSTX-U TRANSP simulations
1 MA, 1T, H98=1, near non-inductive
1.6 MA, 1T, partial inductive
1.2 MA, 0.55T, high bT
All: fGW=0.7, H98=1
S. Gerhardt NF 2011, NF 2012

## Slide 23: CAE mode-conversion to kinetic Alfvén waves (KAW) predicted to transfer core NBI power to mid-r electrons
GAE/CAEs cause large ce through stochastic orbits (N. Gorelenkov, NF 2010)
CAEs also couple to KAW - Poynting flux redistributes fast ion energy near mid-radius, E|| resistively dissipates energy to thermal electrons
  PCAEKAW ~ 0.4 MW from QL estimate + experimental mode amplitudes
  Pe,NBI ~ 1.7 MW for r <0.3, NBI power deposited on core electrons
wA(R,Z)=wCAE
CAE
(n=8)
KAW
HYM code
E. Belova, PRL 2015
Radial Poynting flux
EBR
~rbeam
Up to 25% of electron heating power transferred to KAW off-axis

## Slide 24: Outline
ST overview
Global MHD Stability
Energy Confinement
Energetic Particles
ST Upgrade Status
Summary

## Slide 25
NSTX and MAST are undergoing major upgrades
~2x higher BT, Ip, PNBI and ~5x pulse length vs. NSTX/MAST
Super-X divertor configuration for FNSF/DEMO divertor solution
Highly tangential 2nd NBI for non-inductive sustainment, profile control
NSTX-U
MAST-U
First test plasma 2017
First test plasma few weeks ago

## Slide 26
New 2nd NBI
1st NBI
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)

## Slide 27: New centerstack (CS) highlights: Jan – Aug 2015
CS crane lift
CS installed
First test plasma
(Ohmic heating only)
Magnetics functional  EFIT reconstructions

## Slide 28
Upgraded STs will provide many opportunities to study toroidal confinement physics in new regimes:
  Low aspect ratio, strong shaping, high b, low collisionality
  Access to strong fast-ion instability drive, high rotation
  Advanced divertors, lithium walls, high-Z PFCs
There are potentially interesting linkages between ST and CT / FRC physics that could be explored further:
  Role of rapid rotation, strong beams, kinetic effects, …
Thank you!
Summary
Notes: Here is the outline of this review to give you an overview of the world ST research.