## Slide 1
The National Spherical Torus Experiment Upgrade (NSTX-U)
xxx, PPPL
For the NSTX-U Team
xxx
March 14, 2015
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
*This work supported by the US DOE Contract No. DE-AC02-09CH11466

## Slide 2
Remember to change the title in the slide master

## Slide 3: Outline
Overview of fusion and plasmas
Fusion plasma confinement in a tokamak
Motivation for studying spherical tokamaks
NSTX Upgrade scientific goals and questions

## Slide 4: Advantages of fusion: safe, sustainable, high energy density, environmentally attractive
Cannot have runaway reaction
  Only small amount of fuel present
  If particles cool, fusion stops
Abundant fuel supply
  D from seawater: HDO, D/H = 1/6400
  T bred from lithium in earth’s crust
High energy density
  1 liter water = 500 liters gasoline
Waste short-lived, low-level
No CO2 production
D: deuterium
T: tritium
n: neutron
a: helium
“D-T” fusion reaction:
High energy gain
≈ 1000 ×

## Slide 5: Fusion requires very high temperatures, but these have already been achieved
Fusion is easiest here at 200 million ᵒC (!!) (350 million ᵒF)
  Minimum fusion “triple-product” (pressure nT and energy confinement time tE) value: 8 atmosphere-seconds
~250 million C
TFTR at PPPL (1990’s)
core
boundary

## Slide 6: At fusion temperatures gas becomes plasma, a “soup” of electrons and positive ions
Water:
0 ᵒC
100 ᵒC
160,000 ᵒC
DT fusion:
200,000,000 ᵒC
At fusion temperatures, particles are so energetic that electrons are stripped from neutral atoms leaving positively charged (+) ions

## Slide 7: Charged particles confined by magnetic fields, but a simple toroidal field gives poor confinement
R
Charged particles spiral around field lines, move freely along field
Bending field into torus creates non-uniform B~1/R
Electrons and ions drift apart vertically  charge separation
Electric field created  particles expelled outward

## Slide 8: Tokamak: Poloidal field from plasma current + toroidal field from magnets create helical field
“Tokamak”: Russian acronym for “toroidal chamber with magnetic coils”
Helical field = B-field covers toroidal surfaces
Allows currents to flow along magnetic field
Short-circuits electric fields that would otherwise expel plasma
Particles tied to surface
Improved confinement

## Slide 9: Tokamaks are not presently steady-state, but in the future will operate without transformer
Conventional Tokamak
Primary transformer coils drive toroidal current in plasma
Must stop when transformer coils reach current/force limits
Inner Poloidal Field Coils
(Primary transformer circuit)
Plasma electric current
(Secondary transformer circuit)
Advanced Tokamak
External: wave and beam current drive
Self-generated: high pressure plasmas make “bootstrap” current
Efficient tokamak power plant will need 70-90% self-generated current

## Slide 10
ITER will be first device to access “burning plasma”, is very large and expensive
Burning plasma: majority of plasma heating power comes from fusion alpha particles from DT reactions
  DT reaction energy split: 1/5 in alphas, 4/5 in neutrons
ITER goal Q = Pfusion / Pext = 10  Pα / Pext= 2
Pα / Pα + ext = 2/3
ITER under construction in Cadarache, France
Toroidal field current: 165 MA
Plasma current: 15 MA
A = 3.1
R = 6.2m
BT = 5.3T
IP = 15MA
6500 tons
80,000 km of Nb3Sn super-conducting strand
Size of ITER driven largely by energy confinement which scales with plasma current, and therefore with size
Can we make smaller devices with better confinement and smaller or cheaper magnets?

## Slide 11: Aspect ratio and elongation are important free parameters
Spherical torus/tokamak (ST) has A = 1.1-2
Conventional tokamak typically A = 3-4
Higher elongation improves stability, confinement
Aspect ratio A = R / a, Elongation k = b / a
a
R
R = major radius, a = minor radius, b = vertical ½ height
a
b

## Slide 12
A ~ 3
k = 1.5-2
bT = 3-10%
A ~ 1.5
k = 2-3
bT = 10-40%
Tokamak
ST
ST can be compact, high beta, and high confinement and favorable average curvature improves stability
Toroidal beta bT = p / (BT02/2m0)
bT [%] º bN IP / (aBT0)
Plasma spends less time in unstable curvature region
IP ~ ITF (1 + k2) / (2 A2 q*)
Energy confinement time tE ∝ IP
• ST has high IP , achieves it cost effectively
• IP increases performance
$
Higher elongation k and low A
lead to higher IP , bT and tE
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 13
Higher bT enables higher fusion power and compact FNSF for required neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Database from NSTX,
NSTX-U
Pfusion ∝ p 2 V ∝ bT2 BT04 V
$
Physics Knob
Product
High neutron wall loading Wn possible in a compact ST
Wn ∝ Pfusion / A ∝ bT2 BT04 a
(not strongly size dependent)
Wn ~ 1 MW/m2 with R ~ 1 m FNSF feasible!
ST-FNSF
Fusion Nuclear Science Facility (FNSF) could aid technology development
Plasma facing components for exhaust, vacuum vessel and shield, tritium fuel cycle…

## Slide 14: The National Spherical Torus Experiment (NSTX)
Located at the Princeton Plasma Physics Laboratory in Princeton, NJ
Operated from 1999-2010
Major accomplishments:

## Slide 15
NSTX-U will provide new data to support ST-FNSF design, ITER operations, boundary solutions
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
~ 5-10x increase in nTt from NSTX
NSTX-U average plasma pressure ~ tokamaks
NSTX-U mission elements:
Advance ST as candidate for FNSF
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
New center-stack doubles toroidal field, plasma current, 5× pulse-length
Tangential injection provides 3-4× higher current drive at low IP:
  2x higher absorption (4080%) at low IP
  1.5-2x higher current drive efficiency

## Slide 16: NSTX achieved favorable confinement and current drive results; Will trends continue in NSTX-U?
Steady-state operation required for FNSF
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
TRANSP Contours of Non-Inductive Fraction
H98y2 confinement
parameter
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors
NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted?
NSTX observed confinement increase at higher Te!
Will trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2

## Slide 17
Compact ST-FNSF has no/small central solenoid
IP Start-up/Ramp-up Critical Issue for ST-FNSF, NSTX achieved 200kA (~20%) “transformer-less” start-up
Long-term major goal of NSTX-U: generate and sustain a high-performance plasma without using any transformer
TSC code successfully simulated helicity injection IP ~200kA in NSTX
Will NSTX-U achieve 400kA or more as per simulations?
0
1.0 ms
1.6 ms
2.7 ms
1
2
0
1
2
0
1
2
R (m)
R (m)
R (m)
0
-2
1
2
-1
Z (m)
~ 1-2 MA of transformer-free start-up current needed for FNSF  10-20% of total current
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 18: NSTX-U will test ability of advanced divertors to mitigate very high heat-fluxes
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)
NSTX-U has additional coils improved control of snowflake
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX
Additional null-point in “snowflake” divertor expands field, reduces heat flux

## Slide 19: Your more specific slides here

## Slide 20: Conclusions
NSTX-U is advancing the spherical torus as a candidate for a Fusion Nuclear Science Facility

## Slide 21: Opportunities to participate in NSTX-U research

## Slide 22: Back-up slides

## Slide 23: What is fusion?
D: deuterium
T: tritium
n: neutron
a: helium
High energy gain
≈ 1000 ×
E = mc2
“D-T” fusion reaction:

## Slide 24: Advantages of fusion: safe, sustainable, high energy density, environmentally attractive
Cannot have runaway reaction
  Only small amount of fuel present
  If particles cool, fusion stops
Abundant fuel supply
  D from seawater: HDO, D/H = 1/6400
  T bred from lithium in earth’s crust
High energy density
  1 liter water = 500 liters gasoline
Waste short-lived, low-level
No CO2 production

## Slide 25: Fusion requires very high temperatures
Fusion is easiest here at 200 million ᵒC (!!) (350 million ᵒF)
  Requires lowest pressure nT and energy confinement time tE
  Minimum fusion “triple-product” value: 8 atmosphere-seconds
Fusion difficulty
(pressure × confinement)

## Slide 26: Magnetic fusion has already achieved the necessary very high temperatures!
~250 million C
TFTR at PPPL (1990’s)
core
boundary

## Slide 27: Gas becomes plasma at fusion temperatures
Water:
0 ᵒC
100 ᵒC
160,000 ᵒC
DT fusion:
200,000,000 ᵒC

## Slide 28: Plasma is a gas of charged particles: “Soup” of negatively charged electrons, positive ions
At fusion temperatures, particles are so energetic that negatively charged (-) electrons are stripped from neutral atom leaving positively charged (+) ions
One benefit of plasma state: charged particle motion can be manipulated by electric and magnetic fields

## Slide 29: An estimated 99% of matter in the observable universe is in the plasma state
Interstellar medium
Aurora Borealis
Solar wind
Plasma processing (semiconductors)
Neon signs
Lightening
A few examples of plasma

## Slide 30
How do we confine plasma?

## Slide 31: Confinement methods for controlled fusion
Inertial Confinement
Gravitational Confinement
Charged particle
Magnetic field
Magnetic Confinement
Fusion
Gravity
Fuel Pellet
Intense Energy
Beams
Sun

## Slide 32: Magnetic fusion is arguably closest to ultimate goal of electricity generation
Ryan Hamerly (Stanford)
Gravitational confinement fusion requires large device
  Need 7-8% of mass of our sun
  Approximately 10× diameter of Earth
Laser fusion ala NIF at best has Efusion / Eelectrical ~ 5%
  So far, 0.004% efficient
Magnetic fusion in ITER:
  Goal: 500MW fusion power for
  ≤ 600MW electrical input for 400s
  Industrial levels of fusion power
14kJ fusion yield achieved

## Slide 33: How would magnetic fusion make electricity?
Spin turbines, generate electricity
Steam or hot helium
Magnets
(-270 - 100ᵒC)
Heat
Blanket
(350 - 1000ᵒC)
helium and deuterium exhaust
Tritium bred from lithium in blanket
External heating
(10’s of MW)
Plasma
(100 million ᵒC)
a self heating
Neutrons

## Slide 34: Charged particles confined by magnetic fields
Charged particles spiral around magnetic field “arrows”, but move freely along the field
Magnetic fusion goal: make field so particles never touch walls
No magnetic field: Charged particles move freely in all directions

## Slide 35: Example magnetic fields in units of Tesla [ T ]
MRI: 0.5-3 T
National High Magnetic Field Laboratory
World Record: 100 T
Non-destructive - for few milliseconds
ITER: 5.3 T
Earth: ~5 × 10-5 T
Refrigerator magnets
~1-5 × 10-3 T
PPPL’s NSTX-U: 1 T

## Slide 36: Magnetic fusion uses electromagnets
Electromagnet: use electrical current “I” to create magnetic field “B”
“B” is perpendicular to “I”
Circular current “coil” makes strong nearly uniform B at center of coil
  Want low/no resistance coil to reduce power: copper and/or superconductors
I
B
I
I
B

## Slide 37: Fusion: Use multiple coils to create “toroidal” field
Position many coils into donut or “torus” shape
Magnetic field never touches wall (!)
Do charged particles ever touch wall?
× 10-20

## Slide 38: Simple toroidal field  poor confinement
R
Bending field into torus creates non-uniform B
  B ~ 1 / R  factor of 2
Electrons and ions drift apart vertically  charge separation
Electric field created  particles expelled outward toward vessel wall

## Slide 39: Helical magnetic field improves confinement
“Helical” field = B-field covers toroidal surfaces
  B arrows never puncture donut
Allows currents to flow along magnetic field
Short-circuits electric fields that would otherwise expel plasma
Particles tied to surface
Improved confinement
“Tokamak”
“Stellarator”

## Slide 40: Tokamak: Poloidal field from plasma current + toroidal field from magnets create helical field
“Tokamak”: Russian acronym for “toroidal chamber with magnetic coils”

## Slide 41: Conventional tokamak is not steady-state
Primary transformer coils drive toroidal electric current in plasma
Must stop when transformer coils reach current and/or force limit
Inner Poloidal Field Coils
(Primary transformer circuit)
Plasma electric current
(Secondary transformer circuit)

## Slide 42: “Advanced Tokamak” uses external + self-generated current to operate without transformer
External: wave and beam current drive
Self-generated: high pressure plasmas make “bootstrap” current
Efficient tokamak power plant will need 70-90% self-generated current

## Slide 43: Stellarator: Toroidal / helical currents in coils + toroidal field from magnets create helical field
Discrete / modular coils
Helical coils
or

## Slide 44: Tokamaks and stellarators are the leading configurations in magnetic fusion
Stellarator advantages:
  No plasma current drive necessary
  More stable, steady-state
Disadvantages:
  More complex coils and exhaust
  Confinement < tokamaks (so far…)
Superconducting tokamak
Superconducting stellarator
Tokamak advantages:
  Best confinement, closest to “breakeven”
  Simpler planar coils and power/particle exhaust
Disadvantages:
  Must drive multi-mega-ampere plasma current
  More prone to rapid loss of plasma = “disruption”
KSTAR (South Korea)
W7-X (Germany) – 1st plasma in late 2015

## Slide 45
ITER will be first device to access “burning plasma”
Burning plasma: majority of plasma heating power comes from fusion alpha particles from DT reactions
  DT reaction energy split: 1/5 in alphas, 4/5 in neutrons
ITER goal Q = Pfusion / Pexternal heating = 10
Q = 10  Palpha / Pexternal = 2
Palpha / Palpha + external = 2 / 3 > 50%
ITER under construction in Cadarache, France
A=3.1, R=6.2m, BT=5.3T, IP=15MA

## Slide 46: ITER magnets will be largest ever built
18 toroidal field magnets
12 Tesla at coil
Weight: 6500 tons
80,000 km of Nb3Sn superconducting strand in total length
Toroidal field current
165 million amps
Plasma current:
15 million amps
15 amps
(1800W)

## Slide 47: Size of ITER driven largely by plasma confinement
Energy confinement scales with plasma current
Large plasma current requires large toroidal field and/or plasma size for plasma to remain stable
Current and confinement both scale with size
Can we make smaller devices with better confinement and smaller or cheaper magnets?
Such questions motivate exploring alternatives…

## Slide 48
How might we possibly improve the conventional tokamak?

## Slide 49: Aspect ratio is important free parameter
Spherical torus/tokamak (ST) has A = 1.1-2
Conventional tokamak typically A = 3-4
Aspect ratio A = R / a
a
R
R = major radius a = minor radius

## Slide 50: STs have higher natural elongation
Higher elongation improves stability, confinement
Elongation k = b / a
b = vertical ½ height a = minor radius
a
b

## Slide 51
A ~ 3
k = 1.5-2
bT = 3-10%
A ~ 1.5
k = 2-3
bT = 10-40%
Tokamak
ST
Favorable average curvature improves stability
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Plasma spends less time in unstable curvature region
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 52
ST can be compact, high beta, and high confinement
Higher elongation k and low A lead to higher IP , bT and tE
IP ~ ITF (1 + k2) / (2 A2 q*)
Normalized pressure bT [%] º bN IP / (aBT0)
High κ ∼ 3.0 equilibrium in NSTX
Energy confinement time tE ∝ IP
IP ~ ITF for ST due to low A and high k
• ST has high IP due to high κ and low A
• IP increases tokamak performance
• ST achieves high performance cost effectively
$
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 53
Fusion technology development is major challenge
Fusion Nuclear Science Facility (FNSF) could aid development
Without R&D, fusion components could fail prematurely, requiring long repair/down time.
This would cripple power plant operation
FNSF can help develop reliable fusion components
Such FNSF facilities must be: modest cost, low T, and reliable
Need to develop reliable and qualified nuclear and other components which are unique to fusion:
Divertor, plasma facing components for exhaust
Blanket and Integral First Wall
Vacuum Vessel and Shield
Tritium Fuel Cycle
Remote Maintenance Components
ST-FNSF

## Slide 54
Higher bT enables higher fusion power and compact FNSF for required neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Data base from START, MAST, PEGASUS and NSTX
Pfusion ∝ p 2 x Volume
Pfusion ∝ bT2 BT04 x Vol
$
Physics Knob
Product
Investment
Wn ∝ Pfusion / Area
High neutron wall loading Wn possible in a compact ST
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1 MW/m2 with R ~ 1 m FNSF feasible!

## Slide 55
Design studies show ST potentially attractive as FNSF
Projected to access high neutron wall loading at moderate R, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R, careful design
PPPL ST-FNSF concept

## Slide 56
ST Extends Predictive Capability for ITER and Toroidal Science
  High b physics, rotation, shaping extend stability, transport knowledge
  NBI fast-ions in present STs mimic DT fusion product parameters in ITER  study burning plasma science
  STs can more easily study electron scale turbulence at low collisionality  important for all magnetic fusion
Unique ST properties also support ITER
Burning Plasma Physics - ITER

## Slide 57
What are the goals of
NSTX Upgrade (NSTX-U)?
What key science questions
will NSTX-U address?

## Slide 58: NSTX Upgrade mission elements
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
ITER
Liquid metals/Li
“Snowflake”
ST-FNSF

## Slide 59
NSTX-U will provide new data to support ST-FNSF design, ITER operations, boundary solutions
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
~ 5-10x increase in nTt from NSTX
NSTX-U average plasma pressure ~ tokamaks
Key NSTX-U research topics for FNSF and ITER:
Stability and steady-state control at high b
Confinement scaling (esp. electron transport)
Non-inductive start-up, ramp-up, sustainment
Divertor solutions for mitigating high heat flux
J. Menard, et al., NF (2012)
New center-stack doubles toroidal field, plasma current, 5× pulse-length
Tangential injection provides 3-4× higher current drive at low IP:
  2x higher absorption (4080%) at low IP
  1.5-2x higher current drive efficiency

## Slide 60: NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted by simulations?
Steady-state operation required for ST, tokamak, or stellarator FNSF
TRANSP Contours of Non-Inductive Fraction
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier

## Slide 61
Compact ST-FNSF has no/small central solenoid
IP Start-up/Ramp-up Critical Issue for ST-FNSF
~ 1-2 MA of transformer-free start-up current needed for FNSF  10-20% of total current
Long-term major goal of NSTX-U: generate and sustain a high-performance plasma without using any transformer
  (this will not be easy…)
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 62: NSTX achieved 200kA (~20%) “transformer-less” start-up Will NSTX-U achieve 400kA or more as per simulations?
TSC code (2D) successfully simulated helicity injection IP ~200kA in NSTX
0
1.0 ms
1.6 ms
2.7 ms
1
2
0
1
2
0
1
2
R (m)
R (m)
R (m)
0
-2
1
2
-1
Z (m)
Additional electron heating likely required
Design of heating system is underway…

## Slide 63: NSTX / MAST observed confinement increase at higher Te (!) Will confinement trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors

## Slide 64: All modern tokamaks / STs use a “divertor” to control where power and particles are exhausted
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)

## Slide 65
Tokamak + ST data: power exhaust width varies as 1 / Bpoloidal
Will previous ST trend continue at 2× IP , BP , BT, power?
ST data breaks aspect ratio degeneracy of data set
Wider heat-flux width may offset smaller R  maybe better than tokamak
Issue: If peak heat flux in divertor region exceeds 10 MW/m2  material damage

## Slide 66: NSTX-U will test ability of radiation and advanced divertors to mitigate very high heat-fluxes
NSTX: reduced heat flux 2-4×via radiation (partial detachment)
Additional null-point in divertor expands field, reduces heat flux
Snowflake/X Divertor
Standard Divertor
NSTX-U has additional coils for up-down symmetric snowflake/X, improved control
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX

## Slide 67
How was NSTX-U constructed?

## Slide 68
New center-stack designed to handle increased forces
Identical 36 TF conductors and innovative flex-bus design
Electric Discharge Machining Cuts
Tested for
300k cycles
TF flex-bus
CS casing
TF cooling lines
TF conductor
OH coil
PF coil 1A
PF coil 1B
PF coil 1C
CHI bus
Friction-stir welded TF flag joints
CTD-425 cyanate ester epoxy blend insulation

## Slide 69
Cooling tube soldered with resin-based flux into inner TF conductor
Conductor being wrapped with fiberglass insulation
Insulated conductor being placed into mold
Assembled TF mold ready for Vacuum Pressure Impregnation (VPI) w/ CTD-425
Center-stack fabrication and assembly (1)
Innovative manufacturing techniques developed
Completion of first TF quadrant

## Slide 70: Center-stack fabrication and assembly (2)
4 TF quadrants assembled
Full TF Bundle after VPI
Aquapour + glass layer applied
OH conductor wound over TF

## Slide 71: Completion of transformer winding and VPI

## Slide 72: Same-day delivery to D-Site costs extra

## Slide 73: New Center-Stack installed in NSTX-U (!) Vacuum pump-down achieved in January, 2015

## Slide 74
Relocated 2nd NBI beam line box from
the TFTR test cell into the NSTX-U test cell
Beam Box being lifted over NSTX
Beam Box placed in its final location and aligned
Beam Box being populated with components
TFTR NBI beam box and components successfully tritium decontaminated

## Slide 75
New 2nd NBI
1st NBI
NSTX Upgrade Project nearing completion
Test plasmas expected in April, research plasmas in June

## Slide 76: Magnetic Confinement Fusion Performance

## Slide 77: Particle trajectories in a tokamak

## Slide 78
S.A. Sabbagh PRL(2006)
Record bN and bN / li accessed in NSTX
using resistive wall mode stabilization
J. W. Berkery, PRL (2011)
W. Zhu, PRL (2006)
S.A. Sabbagh at this APS
High bN regime is important for bootstrap current generation.
High bN/li regime important since high fBS regime has low li.
Major mission of NSTX-U is to achieve fully non-inductive operations at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM

## Slide 79
Example: Disruptivity is reduced with strong shaping of the plasma boundary.
NSTX Data Demonstrates a Favorable Operations Window For Reduced Disruptivity in an ST-FNSF
No strong increase in disruptivity as bN increases
Reduction in disruptivity also with:
  Decreasing li (broader current profile)
  Decreasing pressure peaking
S=37
S=20
Upgrades will test and improve these favorable trends in a systematic way
S.P. Gerhardt et al., NF (2013)
ST-FNSF
(S=q95IP/aBT)

## Slide 80
Favorable Confinement Trend with Collisionality and b found
Important implications for future STs and Demo with much lower n*
M. Valovic et al., NF (2011)
Fig. 70. (a) Normalized confinement time as a function of collisionality at mid-radius in NSTX. Blue points are from discharges that used HeGDC+B wall conditioning, while red points are from discharges that used Li. Reprinted with permission from S.M. Kaye et al., Nucl. Fusion 53 063005 (2013). Copyright (2013). Institute of Physics.
(b) Collisionality scan of thermal energy confinement time in MAST. Reprinted with permission from M. Valovic et al., Nucl. Fusion 51 073045 (2011). Copyright (2011) Institute of Physics.
NSTX
Very promising ST scaling to reactor condition, if continues on NSTX-U/MAST-U
NSTX
tE, th µ n*e-0.1 b-0.9 tokamak empirical scaling (ITER98y,2)
tE, th µ n*e-0.8 b-0.0 ST scaling
S.M. Kaye et al., NF (2007) (2013)
MAST
B tE,th [ T s]
~ n*e -0.82
n*e

## Slide 81
Microtearing-driven (MT) transport may explain ST collisionality scaling
Microtearing-driven ce vs. nei using the GYRO code.
W. Guttenfelder, et al., PoP(2012)
MT growth rate decreases with reduced collisionality in qualitative agreement with the NSTX experiment.
Further electron confinement improvement expected due to reduced collisionality.
NSTX-U

## Slide 82
ETGs measured for the first time with high-k scattering
High be or larger re ∝ be0.5 of ST plasma enabled measurement of ETGs.
E. Mazzucato et al., NF (2009)
H.Y. Yuh et al., PoP (2009)
J.L. Peterson, et al., PoP(2011).
ETG Suppression in Reversed Shear
Electron Temperature Gradient Mode (ETG) Excitation with Core Electron Heating
Shear stabilization of ETGs D. R. Smith, et al., PRL (2009)
Density gradient stabilization of ETGs Y. Ren, et al., PRL (2011)
Note: Here we call electron gyro-scale turbulence as ETGs
Calculated ETG ce by GTS code agrees with experiment
S. Ethier et al., IAEA (2010)
ce (m2/sec)
ce (m2/sec)
time (Vth/LTe)
ce (GTS)

## Slide 83
High Confinement Needed for Compact FNSF
High confinement H-mode in the range of FNSF obtained
Y. Ren.
Fusion gain Q depends strongly on “H”, Q µ H 5-7
Higher H enables compact ST-FNSF H = 1.2 – 1.3
Higher H gives more reactor design flexibility and margins.
• Ion energy transport in H-mode ST plasmas near neoclassical level due to high shear flow and favorable curvature.
• Electron energy transport anomalous
S. Gerhardt NF (2014)
FNSF
H-mode confinement in STs H ~ 1 (ITER98y,2) but enhanced pedestal H-mode (EPH) has 50% higher H up to H ~ 2
R. Maingi, PRL (2010)
EPH
H-mode
NSTX
NSTX

## Slide 84
Divertor flux expansion of ~ 50 achieved with
Snow Flake Divertor with large heat flux reduction in NSTX
NSTX-U will investigate novel divertor heat flux mitigation concepts needed for FNSF and Demo.
• Up-and-down symmetric Snow Flake / X-divertors
• Lithium + high-Z metal PFCs
Divertor heat flux (MW/m2)
Snowflake divertor in NSTX
OSP
V. A. Soukhanovskii et al., PoP (2012)

## Slide 85
ST-FNSF has high P/R due to small R
Innovative Heat Flux Mitigation via Divertor Flux Expansion
D. Ryutov, et al., PoP (2007)
P.M. Valanju, et al., PoP (2009).
Kotschenreuther, et al., PoP (2007)
Lower toroidal field of outboard divertor leg of STs facilitates heat flux mitigation by divertor flux expansion solutions
X-Divertor: CREST
Snow-flake
Super-X: MAST-U
Major mission of MAST-U is to investigate up-down symmetric Super-X configuration. NSTX explored Snow-flake / X-divertor.

## Slide 86
H-mode / ELM physics: High Priority Research Goal
Unmitigated ELMs could cause PFC damage in reactors
ST is in strongly shaped ELM regimes
P.B. Snyder et al., PoP (2002).
NSTX, PEGASUS
(Type I)
MAST
(Type I)
Video images of MAST plasmas showing a filamentary ELM structure.
  N. Ben Ayed et al., PPCF (2009).
K.E. Thome et al., EPR (2014)
FNSF
L-H power threshold scaling extended for low A
• NSTX/MAST/PEGASUS accessed H-mode at very low heating power < 1 MW and also in ohmic plasmas
• NSTX-U and MAST-U will provide H-mode access scaling for FNSF

## Slide 87
ELM Stabilization and Mitigation
Through application of lithium and 3-D fields
D.K. Mansfield, et al., JNM (2009)
ELMs stabilized with edge pressure modification with Li in NSTX
R. Maingi, et al., PRL (2009).
ELM mitigation with n=3
3-D fields (ELM Coils) in MAST
Increasing Type I ELM freq. by x 8 (900 Hz) has reduced heat flux
A. Kirk et al., NF (2013)

## Slide 88
NBI heated ST plasmas provide an excellent testbed for a-particle physics
Alfvenic modes readily accessed due to high Va > VAlf
EP parameter space
a-particles couples to Alfven-type mode strongly when Va > VAlf ~ b-0.5 Cs
Va > VAlf in ITER and reactors
In STs, the condition is easily satisfied due to high beta
A prominent instabilities driven by fast particles are global and called toroidal Alfven eigenmodes (TAE).
NSTX-U will also explore Va < VAlf regime giving more flexibility
  M.P. Gryaznevich et al. PPCF (2004)
Stabilization of TAEs at high β in MAST
TAEs significantly modified at high b as VAlf Cs
  E. D. Fredrickson et al., NF (2013)

## Slide 89
“TAE avalanche” shown to cause energetic particle loss
Uncontrolled a-particle loss could cause reactor first wall damage
Time (ms)
(a)
Multi-mode TAE avalanche can cause significant EP losses as in “sea”of TAEs expected in ITER
D.S. Darrow et al., NF (2013).
  E. D. Fredrickson et al., NF (2013)
Progress in simulation of neutron rate drop
due to TAE avalanche
Time (ms)
Neutron rate (a.u.)
Fast ion loss rate (a.u.)
Frequency (kHz)

## Slide 90
Helicity Injection Is an Efficient Method for Current Initiation
Coaxial Helicity Injection (CHI) Concepts Being Developed
CHI developed on HIT and HIT-II and transferred to NSTX
Discharge evolution of 160 kA closed flux current produced by CHI alone in NSTX
R. Raman et al., PRL (2006)

## Slide 91
Current Ramp-Up and Profile Control Crucial for FNSF
Major Research Topics for NSTX-U
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
Near sustained discharges obtained with modest HHFW power
NSTX

## Slide 92
Current Ramp-Up and Profile Control Crucial for FNSF
Major Research Topics for MAST-U and NSTX-U
  M. Turnyanskiy et al., NF (2009)
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
NSTX
Off-axis NBI CD Required for Profile Control Demonstrated in MAST
Off-axis current drive for profile control will be tested in both MAST-U and NSTX-U with major NBI upgrades.
Near sustained discharges obtained with modest HHFW power.

## Slide 93
Helicity Injection Is an Efficient Method for Current Initiation
Local Helicity Injection (LHI) Concepts Being Seveloped
Long-Pulse Startup Demonstrated in PEGASUS with LHI
CHI and LHI startup to be tested at higher current ~ 0.5-1.0 MA in NSTX-U.
  3-6 kA current injector array in plasma SOL
Improving predictive capability for both CHI and LHI
J. O’Bryan, PhD. Thesis, UW Madison 2014

## Slide 94
Merging Start-Up Yielded High Current STs
Rapid ion heating observed from magnetic reconnection
Y. Ono, et al., NF (2003)
Merging-compression start-up in MAST
Ultra high b STs produced by mergings in TS-3 Device
Y. Ono, et al., this APS
CS Induction
A. Sykes et al., NF (2001)

## Slide 95
NSTX has accessed A, bN, k needed for ST-based FNSF
Requires fBS ≥ 50% for plasma sustainment
fBS º IBS / Ip = CBS bp / A0.5 = (CBS/20) A0.5 q* bN µ A-0.5 (1+k2) bN2 / bT
SC-ST
NSTX achieved fBS ~ 50% and fNI ~ 65-70% with beams
NSTX-U expects to achieve fNI ~100% with the more tangential NBI (~ 1.5- 2x higher current drive efficiency)
S.P. Gerhardt et al., NF (2011)

## Slide 96
Operating ST Research Facilities Since 2000
NSTX and MAST: MA-class STs, Smaller STs addressing topical issues
NSTX/LTX
PEGASUS
KTM
GLOBUS-M
SUNIST
VEST
HIT-II
QUEST
HIST
LATE
TST-2
TS3/4
UTST
ETE
NSTX, USA
R0 ~ 0.85 m
MAST, UK
R0 ~ 0.75 m
HIT-II, USA
QUEST/CPD, Japan
VEST, Korea
ETE, Brazil
LATE, Japan
TS3/4, Japan
SUNIST, China
HIST, Japan
UTST, Japan
TST-2, Japan
GLOBUS-M, Russia
LTX/CDX-U, USA
PEGASUS, USA
STs operated since 2000
MAST
ST25(HTS)
ST25, UK
Notes: NSTX and MAST are MA class STs so they are the flag ships of ST research. They are at present undergoing upgrades for 1 T operation. Globus-M is a medium size ST and it is undergoing upgrade to 1 T operation. There a large number of STs in Japan. And the QUEST device is the largest and their flagship device. It aim is to operate steady-state. There are also STs in China, Korean, Kazakhstan, and Brazil. One recent addition is ST25 which is the first all high temperature SC magnet tokamak by Tokamak Energy which is private funded enterprise. You can see quite a range of aspect ratio. The lowest one is PEGASUS with A = 1.15 with extremely slender center post. LTX is a lithium dedicated machine with A = 1.5. I do not have the time to cover the lithium research but there are companion papers at this conference for those interested. NSTX and MAST are 1.32. The ST devices spans quite broad range to make sure we capture necessary low A physics.

## Slide 97
MA-Class ST Research Started in 2000
Complementary Physics Capabilities of NSTX and MAST
NSTX
MAST
A. Sykes, et al., IAEA 2000, NF 2001
M. Ono, et al., IAEA 2000, NF 2001
NSTX
R = 85 cm
A ≥ 1.3
= 1.7 - 3.0
BT = 5.5 kG
Ip ≤ 1.5 MA
Vp ≤ 14 m3
PNBI = 7.4 MW
Similar Capabilities
MAST
R = 80 cm
A ≥ 1.3
= 1.7 – 2.5
BT ~ 5.0 kG
Ip ≤ 1.5 MA
Vp ≤ 10 m3
PNBI = 4.0 MW
Comprehensive diagnostics
Physics integration
Scenario development
Passive Plates
Heilicity Injection
HHFW
1 x 6 RWM Coils
Large divertor volume
Merging/Compression
ECH
2 x 12 ELM coils
Complementary Capabilities