## Slide 1
NSTX-U FY2014 Q4 Report Presentation
Vlad Soukhanovskii (LLNL)
Masa Ono
Jon Menard
For the NSTX-U Team
PPPL and FES
November 25, 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
*This work supported by the US DOE Contract No. DE-AC02-09CH11466

## Slide 2: Agenda
LLNL collaboration on NSTX-U: status and plans
  Vlad Soukhanovskii - 25 minutes
NSTX-U Project and Facility Status
  Masa Ono and Ron Strykowsky - 35 minutes
FESAC, APS highlights, FY15 research prep, FNSF
  Jon Menard - 40 minutes

## Slide 3
LLNL collaboration on NSTX-U:
status and plans
Vlad Soukhanovskii
Principal Investigator
Leader of the LLNL Collaboration on NSTX-U
FES NSTX-U Q4 Review
25 November 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 4: LLNL collaboration directly supports NSTX-U mission elements and highest priority goals of NSTX-U 5 year plan
Advance ST for Fusion Nuclear Science Facility
  Demonstrate 100% non-inductive sustainment at performance that extrapolates to ≥ 1MW/m2 neutron wall loading in FNSF
  Develop and understand non-inductive start-up and ramp-up (overdrive) to project to ST-FNSF with small/no solenoid
Develop solutions for plasma-material interface challenge
  Develop and utilize high-flux-expansion “snowflake” divertor and radiative detachment for mitigating very high heat fluxes
  Begin to assess high-Z PFCs + liquid lithium to develop high-duty-factor integrated PMI solutions for next-steps
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
  Access reduced n* and high-b combined with ability to vary q and rotation to dramatically extend ST physics understanding

## Slide 5: Research elements of LLNL collaboration are funded by FES via LAB 12-03 and ECRP, and by LLNL LDRD
SOL and Divertor physics
  Snowflake divertor
  Radiative (detached) divertor and divertor control
  SOL and divertor transport and radiation, particle balance, fueling, cryo-pumping
Plasma-surface interactions and material migration
  Divertor and wall recycling
  Divertor and wall erosion and sources
  Mixed-material interactions (Li, B, C, O, Mo, W)
Core impurity transport
  Low and high-Z impurity transport and particle balance
    Laser blow-off impurity injector
LAB12-03
LAB12-03
LAB12-03
ECRP
LLNL LDRD

## Slide 6: LLNL collaboration includes on-site (at PPPL) and off-site LLNL staff
Vlad Soukhanovskii, Physicist, Principal Investigator, on-site
Peter Beiersdorfer, Senior Physicist, off-site
Filippo Scotti, Postdoctoral Researcher, on-site
Postdoctoral Researcher - Experiment, TBD, FY2015, on-site
Postdoctoral Researcher - Experiment, TBD, FY2015, on-site
Postdoctoral Researcher - Modeling, TBD, FY2015, on-site
Staff member(s) – Modeling, off-site
Technical staff at LLNL, as needed, on-site and off-site

## Slide 7: 1. Support the NSTX-U high priority goal “Develop and utilize high-flux-expansion snowflake divertor and radiative detachment for mitigating very high heat fluxes”
DIII-D experiments elucidate on geometry and transport properties of the snowflake configuration (2012-2015)
  Oral talks at PSI, EPS, IAEA FEC 2014 conferences (V. A. Soukhanovskii)
  Invited talk at APS DPP 2014 on new UEDGE model developments
  (T. D. Rognlien)
Using multi-fluid edge transport code UEDGE to understand NSTX experiments and make projections to NSTX-U and ST-FNSF
  PSI and IAEA FEC 2014 presentations (E. T. Meier)
On-going work and near-term plans
  Develop snowflake equilibria and discharge scenarios using NSTX-U PF coils and start-up (2014-2015)
  Study snowflake divertor transport, turbulence, radiation and ELM/pedestal properties on NSTX-U (2015-2016, NSTX-U R(16-1))
  Model snowflake divertor transport with UEDGE, XGC and BOUT++ (2014-2017)
ECRP

## Slide 8: Modeling supports snowflake divertor and impurity-seeded radiative divertor as leading heat flux mitigation candidates in NSTX-U
  Upper-lower standard and snowflake radiative divertor
    Supported by NSTX-U divertor coils and compatible with coil current limits
  Radiative snowflake with 3% carbon
    Wide density operational window as low as ne/nG≤0.4
    Peak heat flux reduced up to 50% stronger (cf. standard radiative divertor) at lower ne
  Less impurity seeding (argon or neon) needed for lower peak heat flux
  Multi-fluid code UEDGE
  Bt = 1.0 T, Ip = 2 MA, PSOL = 9 MW
  NSTX-like transport ci,e=2-4 m2/s, D=0.5 m2/s
Standard Snowflake
Total
Rad.
heating

## Slide 9: 1. Support the NSTX-U high priority goal “Develop and utilize high-flux-expansion snowflake divertor and radiative detachment for mitigating very high heat fluxes”
Radiative divertor feedback control for long-pulse optimization (2015)
  Developing spectroscopic diagnostic prototypes
    Divertor low-Z line radiation (upgraded LLNL divertor SPRED)
    High-n deuterium series emission and photorecombination continuum for divertor Te, ne (new imaging spectrometer)
    Impurity radiation front dynamics (new divertor filtered camera)
  HTPD 2012 and 2014 presentations, two RSI papers (V. A. Soukhanovskii)
DIII-D Divertor Thomson Scattering operation and analysis (2012-2015)
  Unique Te<1 eV measurements, detachment front dynamics for model validation
    PSI 2014 oral talk (A. G. McLean)
  New divertor near-infrared spectrometer (2014-2015)
Conceptual design of Divertor Thomson Scattering for NSTX-U
  Two HTPD 2014 presentations, two RSI papers (A. G. McLean, V. A. Soukhanovskii)
On-going work and near-term plans
  Install and commission radiative divertor control diagnostics on NSTX-U
  Initial radiative divertor experiments (2015-2016, NSTX-U R(16-1))
  Finalize design of Divertor Thomson Scattering diagnostic for NSTX-U proposal
ECRP

## Slide 10: 2. Support the NSTX-U high priority goal “Begin to assess high-Z PFCs and liquid lithium to develop high-duty-factor integrated PMI solutions for next-steps”
Analysis of lithium and carbon erosion in NSTX shows temperature-enhanced lithium sputtering and weak reduction of divertor carbon sputtering with lithium coatings
  PSI 2014 presentation (F. Scotti)
New and upgraded spectroscopic diagnostics to enable recycling, low/high Z impurity erosion flux and divertor profile measurements in NSTX-U (2014-2015)
  Molybdenum erosion diagnostic moved from Alcator C-Mod to tests on LTX
On-going work and near-term plans
  Support cryo-pump physics design experiments (2015)
  Assess role of oxygen in lithium coating pumping and effect on recycling, low and high-Z fluxes (2015-2016, R(16-2))
  Collaborate with UIUC on MAPP probe PSI support (2015-2016)
  Develop modeling capability of lithium coatings and vapor shielding on high-Z substrates using UEDGE, REDEP/WBC, CRETIN (2014-2017)
LAB12-03

## Slide 11: 3. Support the NSTX-U high priority goal “Access reduced n* and high-b combined with ability to vary q and rotation to dramatically extend ST physics understanding”
Lithium and carbon accumulation analysis in NSTX shows complex interplay of neoclassical transport, natural or triggered ELMs and divertor sources
  F. Scotti, Princeton University PhD thesis
  APS DPP 2014 presentation (F. Scotti)
Develop and install three extreme ultraviolet spectrometers for impurity studies (2014-2015)
  Spectrometers delivered to PPPL on 17 November 2014
Develop and install Laser Blow-Off Impurity Injector (2015)
  Supported in part by LLNL LDRD for edge impurity transport measurements and code validation on NSTX-U
  Conceptual design review planned for 01/2015
On-going work and near-term plans
  Provide routine plasma impurity monitoring (2014-2017)
  Perform impurity transport experiments using LBO (2015-2016)
  Assess high-Z impurity transport before and after high-Z PFCs are installed
LAB12-03
LLNL LDRD

## Slide 12: Three XUV spectrometers will provide continuous spectral coverage from 65 to 450 A for low and high-Z line emission measurements
Described in
  J. K. Lepson, J. Phys. B: At. Mol. Opt. Phys. 43, 144018 (2010)
  J. Clementson, RSI 81, 10E326 (2010)
  J. K. Lepson, RSI 83, 10D520 (2012)
Two NSTX spectrometers
  XEUS, 5 to 65 Å region, 2400 gr/mm grating
  LoWEUS, 250 to 450 Å region, 1200 l/mm grating
New MonaLisa (Metal Monitor and Lithium Spectrometer Assembly) spectrometer, 65 to 250 Å
  0.5 m, 1200 l/mm grating
  Princeton Instruments PIXIS XO 100B CCD detector
Delivered to PPPL on 17 November 2014
MonaLisa spectrometer layout
LLNL XUV spectrometer placement on NSTX-U at Bay E midplane

## Slide 13: Backup slides

## Slide 14: Electron pressure balance in the SOL through the transition to detachment at DIII-D (A. G. Mclean, PSI 2014)
The transition to detachment has been well characterized in DIII-D using standard diagnostics and supplemented with divertor Thomson scattering in 2D
Low temperature capability of upgraded divertor Thomson allows precise determination where conditions exist for low temperature processes (e.g., 3-body recombination, molecular assisted dissociation/recombination)
Plasma conditions in the divertor at detachment onset are weakly correlated to conditions upstream
A rapid transition occurs incrementally from the target to the X-point and above as n/nGW is increased
A.G. McLean, PSI-21 Kanazawa, Japan, May 2014

## Slide 15: New CIDTEC camera will be used for measurements of Li, B coatings, oxygen emission, and high-Z erosion
Used by LLNL at Alcator C-Mod for Mo I measurements
  Described in A. James, Plasma Phys. Control. Fusion 55, 125010 (2013)
Radiation-hardened intensified camera CIDTEC I3710DX9 from Thermo Schientific
  30 Hz, VGA resolution, UV-capable
  Photonis XX1450UV image intensifier
  Schott IG-154 imaging bundle
Presently being setup for NSTX-U
  Will be used for Li, B, O, Mo and W emission measurements where line emission is weak
  Image splitter enables
    simultaneous measurements of neutral and singly-ionized species for gross vs net erosion analysis
    Line ratio measurements for Te, etc
    Relative impurity measurements (e.g., Li to C, B to C etc)
B II
Mo I + VB + Plank
CIDTEC camera setup in the lab and examples of Alcator C-Mod images.

## Slide 16: Developing the Snowflake Divertor Physics Basis For High-power Density Tokamaks at DIII-D
SF divertor configurations compatible with high H-mode confinement and high pressure pedestal
Snowflake geometry may offer multiple benefits for inter-ELM and ELM heat flux mitigation
  Geometry enables divertor inter-ELM heat flux spreading over larger plasma-wetted area, multiple strike points
  Broader parallel heat fluxes may imply increased radial transport
  ELM divertor peak target temperature and heat flux reduction, especially in radiative snowflake configurations

## Slide 17: Large Region of Low Bp Around Second-order Null in Snowflake Divertor is Predicted to Modify Power Exhaust
Geometry properties
Criterion: dXX ≤ a (lq /a)1/3
  Higher edge magnetic shear
  Larger plasma wetted-area Awet (fexp)
  Larger parallel connection length L||
  Larger effective divertor volume Vdiv
Transport properties
Criterion: dXX ≤ D*~a (a bpm / R)1/3
  High convection zone with radius D*
  Power sharing over four strike points
  Enhanced radial transport (larger lq)
“Laboratory for divertor physics”
dSF ≤ a (lq /a)1/3 dSF≤D*
Snowflake
Standard
Low Bp contour: 0.1 Bp/Bpmid

## Slide 18: qpeak Reduction in Snowflake Divertor Partly Due to Increased Awet and L||
Flux expansion increased ~20%
  Depends on configuration, can be up to X3
L|| increased by 20-60% over SOL width
Divertor heat flux reduced ~30%
Parallel heat flux reduced ~20%
SOL width
Standard Snowflake
Strike
point
18

## Slide 19: Heat and Particle Fluxes Shared Among Strike Points in Snowflake Divertor
qSP3 / qSP1 < 0.5
PSP3 / PSP1 < 0.3
Sharing fraction maximized at low dXX
GSP3
qSP3
qSP1
Standard Snowflake
19

## Slide 20: Broader q|| Profiles in Snowflake Divertor May Imply Increased Radial Transport
Fit q|| profile with Gaussian (S) and Exp. (lSOL) functions (Eich PRL 107 (2011) 215001)
Increased lq may imply increased transport
  Increased radial spreading due to L||
  SOL transport affected by null-region mixing
  Enhanced dissipation may also play role
lq = 2.40 mm
lq = 3.20 mm
Standard Snowflake
Parallel heat flux (MW/m2)

## Slide 21: Divertor Radiation More Broadly Distributed in Snowflake for Radiative Divertor, qpeak Reduced by x5
Standard Snowflake
Standard Snowflake
Detached radiative divertor produced by D2 injection with intrinsic carbon radiation
In radiative snowflake nearly complete power detachment at PSOL~3 MW
PSOL = 3-4 MW
Divertor heat flux (MW/m2)

## Slide 22
NSTX-U Project / Facility Status
Masa Ono and Ron Strykowsky
for the NSTX-U Team
NSTX-U FY 2014 Q4 Review Meeting
November 25, 2014
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Tsukuba U
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
NFRI
KAIST
POSTECH
SNU
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
NSTX-U
Supported by

## Slide 23
Upgrade Project Status
Preparation toward Operation
Research Operation Schedule
NSTX-U Organization
Summary
Outline

## Slide 24
New Center-Stack Installed In NSTX-U Vacuum pump-down is planned for December
First NBI access port duct installed last week. Smaller flanges being installed

## Slide 25
NSTX Upgrade Project Is 95% Complete
Recent aerial view of NSTX-U Test Cell (Oct. 27, 2014)
CS Casing
HHFW System
1st NBI
2nd NBI
NSTX-U

## Slide 26
New Digital System Provides Comprehensive Coil Protection
Protects NSTX-U machine against electromagnetic loads
Computes forces and stresses in real-time based on reduced models of the full mechanical structure
Redundant systems
System #1 is undergoing final integrated testing, will be used during rectifier dummy-load testing in December, providing real world experience before plasma ops.
System #2 is 90% complete and it will be ready to support CD-4 and beyond.
Full commissioning system will be a key part of early operations
Coil and Plasma Current Measurements
Realtime Acquisition #1
Realtime Acquisition #2
Stand Alone Digital Coil Protection Computer
Digital Coil Protection & Plasma Control Computer
Level-1 Fault Interface
Power Supply Suppress and Bypass
Rectifier Hardware Controls
System #1
System #2
Notes: A bunch of sensors give conditioned current inputs
Output is Go/NoGo… Fault/No Fault

## Slide 27
December
December - January
November - December

## Slide 28
Neutron calibration was performed safely with a stronger neutron source inside the NSTX-U vacuum chamber
The neutron calibration was performed with two major radii with a neutron source mounted on a model train car on a set of circular tracks inside the NSTX-U vacuum chamber.
Dr. Kunihiro Ogawa from the LHD group (NIFS, Japan) observed the calibration, in anticipation of a similar calibration that is to be done on LHD a few months from now.

## Slide 29
The NSTX-U Activity Certification Committee (ACC) reviews continue, and is comprised of representatives from PPPL Engineering, Research, Safety, and the DOE PSO is currently reviewing technical and safety systems for NSTX-U
A PPPL Internal QA Audit of NSTX-U Start-Up has been performed, and has resulted in a punch list of critical Start-Up and Test Procedures for both CD-4 and subsequent physics operations.
A Readiness for Operations Review (Dec. 9 -11) is being arranged through the University, and is prerequisite for our safety certificate prescribing allowable operating parameters. Committee members from LANL, GA, JLAB, MIT, ORNL, CCFE & UW will be here for this review.
Approvals for Operations

## Slide 30
PF1 Field Changes
  FCPC has been configured.
  Connections/labeling in the test cell still required.
MG#1 Weld Repairs
  Maintenance procedures in progress with plans to spin up the set in December.
Field Coil Power Conversion (FCPC) Commissioning
  AC primary Power Systems and new rectifier firing generators ready to support Ops
  The new PLC-based fault relaying system to replace electromagnetic relays is complete and tested. Individual rectifiers are being prepared for open circuit testing.
  The Digital Coil Protection System (DCPS) has been installed, and is undergoing pre-operational testing.
  The Power System Real Time Control (PSRTC) is being tested in conjunction with the rectifier firing generators. DCPS and PSRTC will be ready to support FCPC Dummy Load testing in December.
Preparations for Operations

## Slide 31
Neutral Beam Injection #2
  Pre-operational testing in progress.
  NBI#2 will be ready to pump-down in December.
  Helium Refrigerator compressors have been started and clean-up of process gas in progress.
  Expect to start ion source pre-operational testing (PTP-11) in December to complete the NB! #2 CD-4 in Jan/Feb.
Neutral Beam Injection #1
  After CD-4, will begin to re-commission NBI#1, although will attempt to make parallel progress whenever possible.
Test Cell Mods
  A design for a new North Door shield wall has been completed. Installation in Dec/Jan.
Neutral beam injection (NBI) system should be available for CD-4 and research operations

## Slide 32: Considerable Effort Being Dedicated to Plasma Control Commissioning
Critical magnetic diagnostics
  Final in-vessel sensor installation and repairs completed.
  Presently recommissioning the magnetic integrators.
  New plasma current rogowski processing electronics nearing completion.
  Excellent new magnetic diagnostics on the CS expertly installed.
Making rapid progress in control software development.
  New 64 core plasma control computer to be delivered in a few weeks, with plans to purchase a backup computer in January.
    Supports all plasma control + DCPS System #2.
  Upgrades to realtime data link successfully tested.
    Presently testing new power supply control software.
  Have written new gas delivery system control software, to be tested in December.
  Beginning a “scrub” of remaining plasma control software to remove legacy dependencies.
  Hired a replacement realtime software developer to provide expanded capability and redundancy in this critical area.

## Slide 33
HHFW System for Electron Heating and Current Ramp-up
Improved Antennas were installed on NSTX-U
New Compliant Antenna Feeds
Will allow HHFW antenna feedthroughs to tolerate 2 MA disruptions
Additional ground installed
Prototype compliant feeds tested to 46 kV in the RF test-stand. Benefit of back-plate grounding for arc prevention found.
Antennas were re-installed with the new feeds and back-plate grounding
• Transmission lines are in the process of being installed & tuned.
Remaining tasks:
• RF power supplies to be re-energized in March 2015 time frame to be ready for research operation in May 2015.

## Slide 34: NSTX-U diagnostics to be installed during first year All center stack sensors mounted & ex-vessel terminations in progress
MHD/Magnetics/Reconstruction
  Magnetics for equilibrium reconstruction
  Halo current detectors
  High-n and high-frequency Mirnov arrays
  Locked-mode detectors
  RWM sensors
Profile Diagnostics
  MPTS (42 ch, 60 Hz)
  T-CHERS: Ti(R), V(r), nC(R), nLi(R), (51 ch)
  P-CHERS: V(r) (71 ch)
  MSE-CIF (18 ch)
  MSE-LIF (20 ch)
  ME-SXR (40 ch)
  Midplane tangential bolometer array (16 ch)
Turbulence/Modes Diagnostics
  Poloidal FIR high-k scattering (installed in 2016)
  Beam Emission Spectroscopy (48 ch)
  Microwave Reflectometer,
  Microwave Interferometer
  Ultra-soft x-ray arrays – multi-color
Energetic Particle Diagnostics
  Fast Ion D profile measurement (perp + tang)
  Solid-State neutral particle analyzer
  Fast lost-ion probe (energy/pitch angle resolving)
  Neutron measurements
Edge Divertor Physics
  Gas-puff Imaging (500kHz)
  Langmuir probe array
  Edge Rotation Diagnostics (Ti, V, Vpol)
  1-D CCD H cameras (divertor, midplane)
  2-D divertor fast visible camera
  Metal foil divertor bolometer
  AXUV-based Divertor Bolometer
  IR cameras (30Hz) (3)
  Fast IR camera (two color)
  Tile temperature thermocouple array
  Divertor fast eroding thermocouple
  Dust detector
  Edge Deposition Monitors
  Scrape-off layer reflectometer
  Edge neutral pressure gauges
  Material Analysis and Particle Probe
  Divertor VUV Spectrometer
Plasma Monitoring
  FIReTIP interferometer
  Fast visible cameras
  Visible bremsstrahlung radiometer
  Visible and UV survey spectrometers
  VUV transmission grating spectrometer
  Visible filterscopes (hydrogen & impurity lines)
  Wall coupon analysis
New capability, Enhanced capability

## Slide 35: Considerable Success In Diagnostic Installation Before Vessel Closure With the Support of the Upgrade Project
Neutron detector installation & calibration (with in-vessel train track) completed.
Fiber installation and in-vessel alignments for MPTS Upgrade complete.
MAPP checked for interferences with outboard divertor at sample insertion point and probe drive stand secured to NTC floor.
Tile on CS machined to provide reflecting surface for interferometer/polarimeter.
New shutters installed for “Synthetic Aperture Microwave Imaging” (SAMI) and MSE-LIF diagnostics.
Toroidal CHERS diagnostic recalibrated following window replacement.
Sample coupons placed on vacuum vessel walls and quartz deposition monitors installed.
All flanges required for pumpdown identified and installation in progress.
All major profile diagnostics (MSE, MSE-LIF, CHERS, P-CHERS, MPTS, FIDA, T-FIDA) achieved spatial calibrations before pump-down.

## Slide 36: Operations Team Continuing to Make Progress in Boundary Physics Operations to Prepare the Facility for Research
Massive Gas Injection | Installation procedures for MGI valves have been released. Critical valve components delivered to PPPL (from U. Washington), and support brackets fabricated. Will be installed in parallel with the inner-PF bus work.
Fuelling and Density Control | All gas valves will be under PCS control Allowing SGI to be used for density feedback Divertor injectors for radiation control
Boronization | New engineer with extensive experience in hazardous gas handling completed design for trimethyl borane system Components have been ordered with goal of availability of system for start of research operations
Lithium Evaporators (LITERs) | Fume hood installation and other upgrades complete for laboratory for LITER filling and maintenance Lithium handling procedures being updated – engineer responsible for boronization system involved
Granule Injectors for NSTX | New injector expected to be available for plasma operations – new postdoc responsible for system Lithium granules to be manufactured by UIUC

## Slide 37
Commissioning
Ip<=1.0 MA, BT<=0.5
Breakdown and current ramp scenarios
EFIT & rtEFIT Reconstructions
Shape & position control
Reliable H-mode
Diagnostic operations
DCPS under plasma operations
Boronizaton +He GDC for PFCs
Short Vent to Install New Diagnostics (no manned entry!) only if needed.
Data Acquisition & Diagnostics Commissioning
Ex-Vessel Diagnostic Installations
Gas Delivery System Final Checks
Magnetics Debugging
Beamline #1 Final Checks
Calibrations:
Magnetic
MSE
CHERS
Neutrons
Boronization / GDC
Activities between CD4 and Research Run
Important to optimize them to start the timely research run!
We will try to move the short vent before CD-4.
We will also perform MPTS Rayleigh Raman before CD-4 if possible.
We will try to minimize the commisioning time to move on to the research run as quickly as possible.

## Slide 38
Aquapour + CS casing installation issues caused a CD-4 delay of ~ 3-4 weeks
~ 2 month period allocated between CD-4 and research plasma operations  CD-4 in mid-March, research ops in mid-May
Plan: ~12-14 run weeks (assumes 1 maintenance week / month)
If machine is running well at end of FY15, may run into early FY16
  Provide additional data for APS 2015 and IAEA synopses for 2016
Research Plasma Operation
12-14 Run Weeks
Nov. 2014
Dec. 2014
Jan. 2015
Feb. 2015
Mar. 2015
Apr. 2015
May 2015
Jun. 2015
Sep. 2015
Jul. 2015
Aug 2015
Bakeout
ISTP / Comm
CD4
Nominal NSTX-U run schedule for FY2015

## Slide 39
NSTX-U Organization Chart for FY2015

## Slide 40
• NSTX Upgrade Project is 95% complete and it has entered the final phase. The vacuum pump-down is planned for December. The coil bus installation is starting and expect to last to early February. ISTP is starting at the end of February and CD-4 early March.
• Digital Coil Protection System software implementation is progressing well. Hardware implementation is complete and it is being prepare to support the rectifier commissioning.
• Research operation schedule / commissioning – Presently planning to start research plasma operation in May 2014. Working toward minimizing the research prep time after CD-4.
HHFW system preparation is underway. In-vessel antenna and RF probe installations were complete. The ex-vessel work is ~ 50% complete.
Diagnostic Enhancements / Commissioning are progressing well. All of the planned diagnostics should be available during the first year of plasma operations.
Boundary Physics Enhancement / Preparation is going well (lithium and boronization).
NSTX-U Organization is formulated.
Summary of Preparation toward NSTX-U Operation

## Slide 41: Backup slides

## Slide 42
42

## Slide 45: NSTX-U facility enhancements proposed for 5 year plan support FESAC Tiers/Priorities
Improved particle control tools
  Control D inventory, rapidly trigger ELMs to expel impurities
  Low n* to understand ST confinement to support FNSF, validation
Disruption avoidance, mitigation
  Massive gas injection, detect halos, disruptions, control vf, RWM, ELM
ST start-up and ramp-up tools
  ECH to raise start-up plasma Te to enable FW + NBI + BS IP ramp-up
  Test EBW-CD start-up, sustainment
  Start-up/ramp-up critical for ST-FNSF
Begin transition to high-Z PFCs, assess flowing liquid metals
  Plus divertor Thomson, spectroscopy
Midplane + off-midplane non-axisymmetric control coils (NCC)
Extended low-f MHD sensor set
1MW
28 GHz
gyrotron
Divertor cryo-pump
Upward Li evaporator
Li granule injector (LGI)
High-Z tiles
Actively-supplied, capillary-restrained, gas-cooled LM-PFC
(Transients, PMI)
(FNSF, Predictive)
(Transients, Predictive)
(FNSF)
(PMI, FNSF)

## Slide 46
NSTX-U FY2014 Q4 - Program Highlights
Jon Menard
For the NSTX-U Team
PPPL and FES
November 25, 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
*This work supported by the US DOE Contract No. DE-AC02-09CH11466

## Slide 47: Outline
FESAC strategic plan and NSTX-U
APS-DPP 2014 highlights
FY15 research organization preparation
ST-FNSF LDRD/IAEA/TOFE conclusions/highlights

## Slide 48: NSTX Upgrade mission elements
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
ITER
Liquid metals/Li
“Snowflake”
ST-FNSF

## Slide 49: NSTX-U team-members proposed many innovative initiatives to FESAC SPP aligned with NSTX-U missions
Menard, NSTX-­U: ST research to accelerate fusion development
Majeski, LTX: Exploring the advantages of liquid lithium walls
Fonck, Initiatives in non-­solenoidal startup and edge stability dynamics at near-­unity aspect ratio in the PEGASUS experiment
Raman, Simplifying the ST & AT concepts (CT injection fueling/momentum + EBW)
Maingi, A liquid‐metal plasma-­facing-­component initiative
Jaworski, Liquid metal plasma-­material interaction science and component development toward integrated demonstration
Allain, Establishing the surface science and engineering of liquid-­metal plasma-­facing components
Podestá, Development of tools for understanding, predicting and controlling fast­ion‐driven instabilities in burning plasmas
Sabbagh, Critical need for disruption prediction, avoidance, mitigation in tokamaks
Crocker / Guttenfelder, Validating electromagnetic turbulence and transport effects for burning plasmas
FNSF
Burning plasmas, discovery science
PMI

## Slide 50: NSTX-U missions aligned with FESAC SPP report
“The primary mission of the NSTX-U subprogram element is to evaluate the potential of the low-aspect ratio tokamak, or spherical torus, to achieve the sustained high performance required for a FNSF.”
“Innovative plasma-material-interaction (PMI) solutions are another important element of this program”
“ITER-relevant research on NSTX-U includes energetic particle behavior and high-beta disruption control”
“NSTX-U should primarily focus on resolving the technical issues underpinning the FNSF-ST design.”
  “Key issues: non-solenoidal startup, sustainment of the plasma current, and scaling of confinement with collisionality.”
  LTX, Pegasus: important support for PMI and current initiation
Quotes from the report:

## Slide 51: FESAC SPP Report Priorities:
Tier 1
  Control of deleterious transient events: This Initiative combines experimental, theoretical, and simulation research to understand highly damaging transients and minimize their occurrence in ITER-scale systems.
  Taming the plasma-material interface: This Initiative combines experimental, theoretical, and simulation research to understand and address the plasma-materials interaction (PMI) challenges associated with long-pulse burning plasma operation.
Tier 2
  Experimentally validated integrated predictive capabilities: This Initiative develops an integrated “whole-device” predictive capability, and will rely on data from existing and planned facilities for validation.
  A fusion nuclear science subprogram and facility: This Initiative will take an integrated approach to address the key scientific and technological issues for harnessing fusion power.
Tier 1 Initiatives are higher priority than Tier 2 Initiatives. Within a tier, the priorities are equal.
In concert with above Initiatives, Discovery Plasma Science will advance the frontiers of plasma knowledge to ensure continued U.S. leadership.

## Slide 52: Outline
FESAC strategic plan report
APS-DPP 2014 highlights from review/invited talks
  Talk topics are well aligned with FESAC-SP Tier topics
FY15 research organization preparation
ST-FNSF LDRD/IAEA/TOFE conclusions/highlights

## Slide 53: FR-1: “Recent Progress on Spherical Torus Research and Implications for Fusion Energy Development Path” – M. Ono

## Slide 54: GI1.00003: “Broadening of the divertor heat flux footprint with increasing number of ELM filaments in NSTX” – J.-W. Ahn

## Slide 55: GI1.00003: “Broadening of the divertor heat flux footprint with increasing number of ELM filaments in NSTX” – J.-W. Ahn

## Slide 56: TI1.00001: “Simulation of 3D effects on partially detached divertor conditions in NSTX and Alcator C-Mod” – J. Lore
16 10/30/2014
Connection Length

## Slide 57: TI1.00003: “Drift Kinetic Effects on 3D Plasma Response in High-b Tokamak Resonant Field Amplification Experiments” – Z.R. Wang

## Slide 58: VI2.00002: “Unification of Kinetic Resistive Wall Mode Stabilization Physics in Tokamaks” – S.A. Sabbagh

## Slide 59: YI1.00006: “Energy Channeling & Coupling of NBI-driven Compressional Alfven Eigenmodes to Kinetic Alfven Waves in NSTX” – E. Belova

## Slide 60: YI1.00006: “Energy Channeling & Coupling of NBI-driven Compressional Alfven Eigenmodes to Kinetic Alfven Waves in NSTX” – E. Belova

## Slide 61: Outline
FESAC strategic plan report
APS-DPP 2014 highlights
FY15 research organization preparation
ST-FNSF LDRD/IAEA/TOFE conclusions/highlights

## Slide 62: Update on increasing University engagement in the NSTX-U program
Increasing engagement was FY2014 “Notable Outcome”
Previously developed ideas to enhance participation:
  Expand Early Career Research (ECR) awards to University Scientists
    No support within DoE Office of Science to extend this beyond tenure-track
  Support students with coordinated senior projects and targeted run-time
    Will consider once NSTX-U resumes routine/full operation (late FY15)
  Implementing enhanced collaboration tools (remote control rooms)
    Will engage NSTX-U Science Groups to determine optimal tools (during FY15)
  Implement “NSTX-U Innovative Research Award (NIRA)” with funding targeting primarily university researchers
    No FES funding available, consider funding from NSTX-U post-Upgrade
  Consider direct financial support for start-up and initial salary for tenure-track professor positions (Same answer as previous question)
  More strongly engage University Principal Investigators and researchers in the management of the NSTX-U scientific program
    Implementing this for FY2015 run

## Slide 63: NSTX-U research program will be (re-)organized along 3 “Science Groups” starting with FY15 run
Each TSG will have a leader, deputy, theory rep, and at least 1 university rep to enhance university participation

## Slide 64: Motivations for restructuring science program
TSGs provide expertise in broad range of topics, but program would benefit from better coordination between TSGs
  SG leader responsibility: Coordinate TSG physics research plans, experimental/shot plans, diagnostic coverage & usage
Experiments that engage more than one TSG will receive increased priority for run-time
  Example: experiment on 3D fields generating data for: plasma response, turbulence, energetic particle loss
Efficient shot usage especially important during first run year (many systems need to be re-commissioned)
Incorporate much wider set University researchers/PIs in planning + coordination of research program (FES/PPPL goal)
NEW: Task-force for long-pulse particle control  cross-cutting goal supporting entire research program

## Slide 65: Upcoming research planning/advisory activities
Pre-forum meeting #1 – Early / mid Dec (~1 day)
  Review experiments needed to support restart, physics-ops
    Draft machine/experimental proposal (XMP/XP) list – goals, authors
    Action: SG/TSGs to solicit people to commit to writing these proposals
Pre-forum meeting #2 – Last week of Jan (1.5-2 days)
  Goal: Provide up-to-date operations status to aid scheduling
  Day 1: Diagnostics/operations readiness meeting
    Status updates and projections for all systems needed for research ops
  Day 1.5-2: Update from SG/TSGs on XMP/XP solicitations
Research Forum – Feb 24-27th, 2015 at PPPL
  Plenary session, TSG break-outs, SG sessions, team joint session, summary (also safety session and team photo)
NSTX-U PAC-36 – Sept/Oct 2015 (end of/after FY15 run)

## Slide 66: Research Forum Overview
Science groups will nominally follow priorities/detailed plans developed for 5 year plan (until they are obsolete…)
Abbreviated eXperimental Proposals (XPs) (developed in Dec-Jan) will be presented at the forum
  Motivation, goal, shot plan, # of run days, diagnostics, analysis…
Prioritization carried out at forum using abbreviated XPs
~70-90% of prioritization completed by end of forum
  Highest priority research in research milestones / task forces
  Proposals that address milestones will receive the most run time
  If abbreviated proposal idea is “priority 1”, the author is asked to develop full proposal for operational + program review/approval
Expect ~1/3 of all XPs for year to be approved, ready at start of physics campaign (April 2015), then roll forward
  Typically schedule XPs ~1-2 months in advance

## Slide 67
First run year priorities support mission and 5YP goals
FY2015 Milestones / Task Forces:
Characterize effects of NBI injection angle on fast-ion distribution and NBI-CD profile
Develop physics + operational tools for high-performance discharges (k, d, b, EF/RWM)
Develop snowflake configuration, study edge and divertor properties
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
R15-1
R15-2
R15-3
IR15-1
Quantify impact of broadened J(r) and p(r) on tokamak confinement and stability
Advance ST for FNSF
  Demonstrate full non-inductive sustainment at FNSF-relevant performance levels
  Advance non-inductive start-up and ramp-up (overdrive) for ST-FNSF with small/no solenoid
Develop solutions for PMI challenge
  Develop / utilize high-flux-expansion and radiative detachment to mitigate high heat flux
  Begin to assess high-Z PFCs + liquid Li to develop high-duty-factor integrated PMI solution
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
  Access reduced n* + high-b + varied q and rotation to dramatically extend ST understanding
JRT-15
Mission Elements and 5YP 5 Highest Priorities
NOTE: IR15-1 accelerates snowflake part of R16-1 by 1 year
Long-pulse main-ion and impurity control
Particle Control Task Force (PC-TF)

## Slide 68: Outline
FESAC strategic plan report
APS-DPP 2014 highlights
FY15 research organization preparation
ST-FNSF LDRD/IAEA/TOFE conclusions/highlights

## Slide 69: PF coil set identified that supports combined Super-X + snowflake divertor for range of equilibria
2nd X-point/snowflake increases SOL line-length
Breeding in CS ends important for maximizing TBR
PF coil set supports wide range of li: 0.4 – 0.8
  Elongation and squareness change with li variation
  Fixed strike-point R, controllable B-field angle of incidence (0.5-5˚)
Divertor coils in TF coil ends for equilibrium, high d
Increased strike-point radius reduces B, q||
Strike-point PFCs also shielded by blankets
TF coil
All equilibrium PF coils outside vacuum vessel
PF coil
Blanket
Vessel
Components:

## Slide 70: 0.5 MeV NNBI favorable for heating and current drive (CD) for R=1.7m ST-FNSF
NBCD increases for Einj ≤ 0.5 MeV but saturates for Einj = 0.75 – 1MeV
Fixed target parameters in DD:
  IP = 7.5MA, bN = 4.5, li = 0.5
  ne / nGreenwald = 0.75, H98y,2 = 1.5
  A=1.75, R=1.7m, BT = 3T, k = 2.8
  Te=5.8keV, Ti=7.4keV
Optimal tangency radii:
1.7m ≤ Rtan ≤ 2.4m
Control q(0), qmin
Shine-thru limit
Maximum efficiency: Rtan=2.3-2.4m
0.50

## Slide 71
R=1.7m configuration with long-leg divertor
Cu/SC PF coils housed in VV lower shell structure
SC PF coils pairs located in common cryostat
TF leads
Vertical maintenance
Design features
Cu/SC PF coils housed in VV upper lid
VV outer shell w/ shield material
Angled DCLL concentric lines to external header
Ports for TBM, MTM, NBI
Blankets
TF coils

## Slide 72: Two sizes (R=1.7m, 1m) assessed for shielding, TBR
Parameter:
Major Radius 1.68m 1.0m
Minor Radius 0.95m 0.6m
Fusion Power 162MW 62MW
Wall loading (avg) 1MW/m2 1MW/m2
TF coils 12 10
TBM ports 4 4
MTM ports 1 1
NBI ports 4 3
Plant Lifetime ~20 years
Availability 10-50%
30% avg
6 Full Power Years
(FPY)
Neutron source distribution

## Slide 73: Peak Damage at OB FW and Insulator of Cu Magnets
Peak dpa at OB midplane = 15.5 dpa / FPY
3-D Neutronics Model of Entire Torus
Dose to MgO insulator = 6x109 Gy @ 6 FPY < 1011 Gy limit
Dose to MgO insulator = 2x108 Gy @ 6 FPY < 1011 Gy limit
Peak He production at OB midplane = 174 appm/FPY
He/dpa ratio = 11.2
Center Stack
OB Blanket
R=1.7m configuration

## Slide 74: TBR contributions by blanket region
Inner Blanket Segment = 0.81
Outer Blanket Segment = 0.15
Total TBR ~ 1.03 with no penetrations or ports
(heterogenous outboard blanket)
0.0004
0.0004
0.034
0.034
Breeding at CS ends important:
DTBR = +0.07
R=1.7m configuration

## Slide 75: Impact of TBM, MTM, NBI ports on TBR
No ports or penetrations,
homogeneous breeding zones:
TBR = 1.03
Add 4 Test Blanket
Modules (TBMs)
TBR = 1.02 (DTBR = -0.01)
TBM
LiPb,
cooling channel,
FCI
1 Materials Test Module (MTM)
TBR = 1.01 (DTBR = -0.02)
Ferritic Steel
MTM
4 TBM + 1 MTM + 4 NBI
TBR = 0.97
Approx. DTBR per port:
TBM: -0.25%
MTM: -2.0%
NBI: -0.75%

## Slide 76: Options to increase TBR > 1
Add to PF coil shield a thin breeding blanket (DTBR ~ +3%)
Smaller opening to divertor to reduce neutron leakage
Uniform OB blanket (1m thick everywhere; no thinning)
Reduce cooling channels and FCIs within blanket (need thermal analysis to confirm)
Thicker IB VV with breeding
Potential for TBR > 1 at R=1.7m
PF Coils

## Slide 77: R0 = 1m ST-FNSF achieves TBR = 0.88
TBM
NBI
Distribution of T production
MTM
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 78: Summary
FESAC strategic plan aligned with NSTX-U missions
  FNSF, PMI, ITER/predictive capability
NSTX-U researchers scientifically productive in FY14
  Led analysis for JRT-2014 / plasma response to 3D fields (reported at Q3)
  40 publications + 13 submitted (as of early September) for FY14
  IAEA: 4 orals on NSTX/ST-FNSF, 2 on DIII-D, 1 on C-Mod
  APS-DPP: 6 Invited NSTX/ST-review talks
NSTX-U organizational re-structuring complete, preparing for Research Forum, FY15 campaign
PPPL-led ST-FNSF LDRD completed
  IAEA/TOFE invited talks, identified mission vs. size tradeoff (TBR vs. R)

## Slide 79
Backup slides

## Slide 80: 10 year goal: Integrate high-performance core + metal walls
2015-2019
NSTX-U 5 year goal: Establish ST-FNSF physics/scenarios
Lower A or higher A?
Standard, snowflake, Super-X (MAST-U)?
Inform choice of
FNSF configuration:
Non-inductive start-up, ramp-up
Confinement vs. b , collisionality
Sustain high b with advanced control
Mitigate high heat fluxes
Test high-Z divertor, Li vapor shielding
Establish ST physics / scenarios:
High-Z acceptable? or need high-Z + Li?
Assess for both divertor and first-wall
Inform choice of FNSF / DEMO
plasma facing materials:
2020-2024
Convert all PFCs from C to high-Z
Static  flowing Li divertor module(s), full toroidal flowing Li divertor, high Twall
5s  10-20s for PFC/LM equilibration
Assess ST with high-Z, high-Z + Li
High-performance + metal walls
Plan presented at FESAC:

## Slide 81: NSTX-U facility enhancements proposed for 5 year plan support FESAC Tiers/Priorities
Improved particle control tools
  Control D inventory, rapidly trigger ELMs to expel impurities
  Low n* to understand ST confinement to support FNSF, validation
Disruption avoidance, mitigation
  Massive gas injection, detect halos, disruptions, control vf, RWM, ELM
ST start-up and ramp-up tools
  ECH to raise start-up plasma Te to enable FW + NBI + BS IP ramp-up
  Test EBW-CD start-up, sustainment
  Start-up/ramp-up critical for ST-FNSF
Begin transition to high-Z PFCs, assess flowing liquid metals
  Plus divertor Thomson, spectroscopy
Midplane + off-midplane non-axisymmetric control coils (NCC)
Extended low-f MHD sensor set
1MW
28 GHz
gyrotron
Divertor cryo-pump
Upward Li evaporator
Li granule injector (LGI)
High-Z tiles
Actively-supplied, capillary-restrained, gas-cooled LM-PFC
(Transients, PMI)
(FNSF, Predictive)
(Transients, Predictive)
(FNSF)
(PMI, FNSF)

## Slide 82: NSTX-U will continue to contribute strongly to model validation, and support development of integrated models
MHD: Kinetic MHD for RWM stability, plasma response, momentum transport from 3D fields (MISK, IPEC, POCA, VALEN, PENT, MARS-K, M3D-C1, R-DCON…)
Transport: High-b/electromagnetic effects on electron transport from micro-tearing, Alfvenic instabilities (GYRO, GTS, GTC, …, HYM, ORBIT)
Boundary: Edge kinetic neoclassical & turbulent transport (GENE, GYRO, GS2, XGC), SOL turbulence (SOLT), snowflake/detachment: neutrals, impurities (UEDGE, SOLPS, BOUT++, EIRENE, DEGAS2, DIVIMP)
Fast-ions: Gyro-center and full orbit following (ORBIT, SPIRAL), linear and non-linear Alfven instability, fast-ion transport (NOVA-K, M3D-K, HYM)
RF: Heating, edge power loss (AORSA, TORIC, SPIRAL), RF/fast-ion interactions (hybrid FOW CQL3D), ECH/EBW heating & CD (GENRAY)
Scenarios: 2D/3D helicity injection physics (TSC, NIMROD), time-dependent ramp-up/sustainment modeling (TSC/TRANSP/NUBEAM)

## Slide 83
FY2015-16 research milestones target exploitation of new capabilities, exploration of new regimes
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
FY2016
FY2015
20
18
20
16
Characterize effects of NBI injection angle on fast-ion distribution and NBI-CD profile
Develop physics+operational tools for high-performance discharges (k, d, b, EF/RWM)
Develop snowflake configuration, study edge and divertor properties
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
R15-1
R15-2
R15-3
IR15-1
Quantify impact of broadened J(r) and p(r) on tokamak confinement and stability
Assess disruption mitigation, initial tests of real-time warning and prediction techniques
Develop high-non-inductive fraction NBI H-modes for ramp-up & sustainment
Assess heat-flux mitigation and PFC response using advanced divertor configurations + radiation at high q||-div
Assess fast-wave SOL losses and core thermal / fast ion interactions at increased BT, IP
R16-1
R16-2
R16-3
Assess confinement and local transport and turbulence at low n* with full range of BT, IP, and NBI power
IR16-1
Expt. Run Weeks:
Incremental (full ops)
Transport and Turbulence
Macroscopic Stability
Waves+Energetic Particles
Solenoid-free Start-up/ramp-up
Adv. Scenarios and Control
ITER Needs + Cross-cutting
Boundary
Physics
Materials & PFCs
Joint Research Target (JRT)
Lead JRT on disruption physics
Support JRT on profile effects on stability

## Slide 84: NSTX-U has long-term goal to assess compatibility of high tE and b + 100% non-inductive with metallic PFCs
Cryo +
full lower
outboard high-Z divertor
Lower
OBD
high-Z row of tiles
C
BN
Li
High-Z
Cryo + U+L OBD
high-Z rows of tiles
Nominal 2014-18 5 year plan steps for implementation of cryo-pump + high-Z PFCs + LLD
2015
2016
2017
2018-19
High-Z tile row
Bakeable cryo-baffle for liquid Li
5 year plan base budget case
Flowing Li module
All
high-Z FW + divertors
+ flowing LLD module
Cryo + high-Z FW and OBD
+ liquid Li divertor (LLD)
2021
2022-23
Cryo-pump
High-Z
tile row
High-Z
tile row
High-Z / Li implementation could be accelerated pending results and additional resources

## Slide 85: Up/down-symmetric Super-X/snowflake projected to maintain peak divertor heat flux below material limits
lq = 0.8mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment projected
to reduce peak q to < 2MW/m2
Upstream
Te
[eV]
Max.
q
[MW/m2]
Divertor
Target
Conducted
Radiation
lq ≈ 1.2mm (J. Canik IEEE 2013)
Peak q < 10MW/m2

## Slide 86: Free-boundary TRANSP/NUBEAM used to compute profiles for 100% non-inductive plasmas with QDT ~2
Neoclassical cion
ne / nGreenwald = 0.7
H98,y2 = 1.4
IP = 8.9MA, BT = 2.9T
fNICD = 100%, fBS = 65%
PNNBI = 80MW (0.5MeV)
Pfus = 200MW (50-50 DT)
  2.6% alpha bad orbit loss
QDT = 2.5
bN = 5.5, Wtot = 58MJ
  Wfast / Wtot = 14%
Maintain qmin > 2
q(0) / qmin controllable via Rtan and density

## Slide 87: ST-FNSF shielding and TBR analyzed with sophisticated 3-D neutronics codes
CAD coupled with MCNP using UW DAGMC code
Fully accurate representation of entire torus
No approximation/simplification involved at any step:
  Internals of two OB DCLL blanket segments modeled in great detail, including:
    FW, side, top/bottom, and back walls, cooling channels, SiC FCI
  2 cm wide assembly gaps between toroidal sectors
  2 cm thick W vertical stabilizing shell between OB blanket segments
  Ports and FS walls for test blanket / materials test modules (TBM/MTM) and NNBI
TBM
LiPb,
cooling channel,
FCI
Heterogeneous OB Blanket Model,
including FW, side/back/top/bottom walls, cooling channels, and SiC FCI
NBI

## Slide 88: Mapping of dpa and FW/blanket lifetime (R=1.7 m Device)
dpa / FPY
Peak =
15.5 dpa / FPY
FW/blanket could operate for 6 FPY
if allowable damage limit is 95 dpa
R=1.7m configuration
 Peak EOL Fluence = 11 MWy/m2

## Slide 89: Summary of ST-FNSF TBR vs. device size
R=1.7m: TBR ≥ 1
R=1.0m: TBR < 1 (≈ 0.9)
TBM
NBI
MTM
TBM
MTM
NBI
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 90: FNSF center-stack can build upon NSTX-U design and incorporate NSTX stability results
Like NSTX-U, use TF wedge segments (but brazed/pressed-fit together)
  Coolant paths: gun-drilled holes or grooves in side of wedges + welded tube
Bitter-plate divertor PF magnets in ends of TF achieve high triangularity
  NSTX data: High d > 0.55 and shaping S  q95IP/aBT > 25 minimizes disruptivity
  Neutronics: MgO insulation can withstand lifetime (6 FPY) radiation dose

## Slide 91
Glidcop plates
Insulator
Bitter coil insert for divertor coils in ends of TF

## Slide 92: MgO insulation appears to have good radiation resistance for divertor PF coils

## Slide 93: PF coil currents and current densities
1
2
3
4
5
6
7
8
bN = 5
li = 0.58

## Slide 94
VV lid / PF cryostat enclosure
Full blanket assembly
TF center-stack
Upper TF horizontal legs
Upper dome structure located on test cell shield plug
TF power supplies
JT-60SA NNBI
R=1.7m ST-FNS facility layout
using an extended ITER building

## Slide 95: FNSF Summary: R = 1m and 1.7m STs with Γn = 1MW/m2 and QDT = 1-2 assessed for FNS mission
Ex-vessel PF coil set identified to support range of equilibria and Super-X/snowflake divertor to mitigate high heat flux
0.5MeV NNBI optimal for heating & current drive for R=1.7m
Vertical maintenance approach, NBI & test-cell layouts identified
Shielding adequate for MgO insulated inboard Cu PF coils
  Outboard PF coils (behind outboard blankets) can be superconducting
Calculated full 3D TBR; TBR reduction from TBM, MTM, NBI
Threshold major radius for TBR ~ 1 is R0 ≥ 1.7m
R=1m TBR = 0.88  0.4-0.55kg of T/FPY  $12-55M/FPY
R=1m device will have lower electricity and capital cost  future work could assess size/cost trade-offs in more detail