## Slide 1: NSTX-U Program FY2016 Q3 Report
Jon Menard, Masa Ono (PPPL)
For the NSTX-U Team
PPPL and FES
July 28, 2016

## Slide 2: Outline
Recent research highlights (since Q2)
Progress toward milestones
Future milestone discussion

## Slide 3: Outline
Recent research highlights
  Charge exchange diagnostic results
  MHD
  Energetic Particles
  Boundary Physics

## Slide 4: New CHERS analysis developed for operation with second NSTX-U beam
Active
View
NB1
NB2
NSTX-U
Background
View
Charge Exchange Recombination Spectroscopy (CHERS) measures ion temperature, velocity, and impurity density
“Standard” CHERS analysis uses background view to isolate intrinsic emission present in active view
NB2 emission compromises the CHERS background view and the standard CHERS analysis
Analysis using a single modulated NB1 source developed
  Adequate S/N for profile measurements of Ti, Vt, Nc
  Lower time resolution
  Larger error bars than with multiple NB1 sources
Extraction of signal from one modulated NB source from steady source demonstrated
  Allows CHERS measurement when NB2 sources are operating
  Would allow a continuous MSE measurement with a modulated source for CHERS
FY17 upgrade to CHERS will
substantially improve S/N

## Slide 5: Real-Time Velocity (RTV) system achieved all design goals, routinely taking data
System based on active charge-exchange spectroscopy on NB1 line
Monitor C VI, n=8-7 line @ 5291nm
RTV views interleaved with CHERS views at mid-plane (active & background views)
  4 views available: R=112, 125, 132, 140cm
Acquisition and analysis software improved after first data from NSTX-U plasmas
  Demonstrated RT analysis for vf, possibly Ti (!) at sampling rate up to 5kHz
  Developed post-discharge analysis tools
    vf from real time analysis available right after shot
    Quick analysis (vf, Ti) available ~1 minute after shot
    Full analysis (CHERS-like: vf, Ti, nC) available ~5 minutes after shot
Implemented & tested data transfer to PCS
Data now routinely available to develop & test vf control algorithm(s) in PCS
[M. Podestà, RSI 83 033503 (2012)]

## Slide 6: Real-time analysis provides accurate data for rotation feedback (and more)
post-discharge
real-time
RTV @ R~125cm
Good agreement with main CHERS system
Good match for both vf and Ti between real-time and post-discharge analysis
First RTV data from NSTX-U confirm achievement of design goals
System is ready to support development & testing of vf control on NSTX-U
Additional physics insight can be gathered from post-discharge analysis
  E.g. effects of RMPs, MHD, ELMs, pellets/granules on vf, Ti, nC
  Complements high spatial resolution of CHERS with sub-millisecond time resolution at 4 radii
[M. Podestà, PPCF (submitted 2016)]

## Slide 7: Outline
Recent research highlights
  Charge exchange diagnostic results
  MHD
  Energetic Particles
  Boundary Physics

## Slide 8: MHD, sawteeth can compete in vf redistribution; different time scales, high fsamp enable separation
Complex scenario
  MHD n=1,2 modes act on ~10ms time scale
  Sawteeth act on ~1ms time scale
High fsamp of RTV allows to differentiate time scales
Complements high spatial resolution CHERS profiles

## Slide 9: Reduced kinetic RWM model in DECAF results in a calculation of gtw vs. time for each discharge
Favorable characteristics
  Stability contours CHANGE for each time point (last time point shown left frame)
  Possible to compute growth rate prediction in real time
Initial tests on NSTX RWM database
  86% of RWM shots are predicted unstable
gtw contours vs. ν and wf
Increasing time
ideal
Ideal + kinetic
unstable
stable
Normalized growth rate vs. time
gtw
139514
disruption
predicted instability
Bounce/transit resonances
Precession resonances
<n> = 1 kHz
Kinetic component δWK
  Gaussian forms used to reproduce precession and bounce/transit resonances
  Height, width, position of peak depend on collisionality

## Slide 10: MARS-F and new developed resistive DCON predict unstable tearing mode consistent with NSTX-U observation
Unstable n=1 tearing mode is observed in L mode NSTX-U discharge (204718).
Resistive DCON and MARS-F predict unstable n=1 tearing modes at q>2 singular surfaces.
Diagonal terms of matrix solved by DCON (outer region) is positive at q=3 and 4 surfaces
(q=2) | -4.29
(q=3) | 10.0
(q=4) | 3.18
 | -4.29
 | 10.0
 | 3.18
MARS-F finds unstable tearing mode at zero rotation, growth rate
m=2
3
4
Even parity
Odd parity
(Tearing)
NSTX-U experiment observes n=1 unstable mode which drives n=2, 3 modes later
Unstable n=1 mode
n=2,3 modes driven by n=1 mode

## Slide 11: Multiple compass scans confirm the optimum L-mode EFC phase and amplitude in the flattop
Higher density
Different OH pre-charge (8 kA vs. 20 kA)

## Slide 12: Static EFC scan early in time  different EFC phase
Static EFC scan early in the discharge shows different optimum correction phase
Flattop phase of 15° is counter-productive early on
Phase asymmetry visible in density, neutrons, and core rotation
Search for the time-evolving error field source is ongoing
  Tilted TF, vessel currents?

## Slide 13: Outline
Recent research highlights
  Charge exchange diagnostic results
  MHD
  Energetic Particles
  Boundary Physics

## Slide 14
Beam Ions are Reasonably Well Confined at High Injection Energy, but Some Discrepancy at Low Injection Energy
March 31, 2016, Einj=65keV, 1MW
June 28, 2016, Einj=85keV, 2MW
Source | Rise (Exp/TRANSP) | Decay (Exp/TRANSP)
1B (Rtan 60cm) | 0.55 | 0.88
1C (Rtan 50cm) | 0.60 | 0.88
2A (Rtan 130cm) | 0.58 | 0.88
2C (Rtan 110cm) | 0.58 | 0.72
Source | Rise (Exp/TRANSP) | Decay (Exp/TRANSP)
1B (Rtan 60cm) | 0.80 | 1.04
1C (Rtan 50cm) | 1.08 | 1.05
2A (Rtan 130cm) | 1.02 | 1.06
2C (Rtan 110cm) | 0.86 | 0.98
At Einj=65keV, the rise is smaller and decay is faster than predicted.
At Einj=85keV, the agreement is much better  Beam ions are reasonably well confined.
The machine is cleaner so that the TRANSP assumption that Zeff=1.5 is better or
The voltage is higher so that the reported power is more accurate or
Beam species at high voltage is more reliable

## Slide 15: Off-axis beams suppress counter-propating Global Alfvén Eigenmodes (GAE)
GAE activity, excited by one or two BL#1 sources can be suppressed by adding one BL#2 source, either 2a, 2b or 2c.
Valuable tool for study of possible GAE-induced electron energy transport.
Addition of source 2a
Addition of source 2b
Addition of source 2c

## Slide 16: Counter-propagating TAE seen with off-axis Neutral Beam Injection (source 2a)
Counter-propagating TAE have been predicted for hollow fast-ion profiles.
Preliminary analysis suggests profile isn’t hollow.
Up and down frequency chirps can be used to measure linear growth rate of mode for comparison to theory.

## Slide 17: Outline
Recent research highlights
  Charge exchange diagnostic results
  MHD
  Energetic Particles
  Boundary Physics

## Slide 18: Granule Injector Commissioned on NSTX-U
Granule sizes :
900mm, 700mm, 500mm, 300mm
Injection Species : Li, B4C, C
Injection Velocity : 50 – 150 m/sec
Granule to Granule Injection Frequency : 50 – 500 Hz
Particle drop rates are controlled by a piezoelectric disk.
Granules driven into the plasma by a pneumatic rotary impeller
NSTX-U Granule Injector

## Slide 19: Calculated multi-species injection profiles on NSTX-U
Utilizing different materials and injection velocities tailors the ablation rate and mass deposition location
 | Lithium | Boron Carbide | Carbon (Vitreous)
Density | .534 g/cm 3 | 2.52 g/cm 3 | 2.09 – 2.23 g/cm 3
Mass in a 1mm sphere (mg) | 0.279 | 1.319 | 1.131
Number of atoms/molecules | 2.426E+19 | 1.438E+19 | 5.670E+19
Sublimation Energy (eV/atom) | 1.65 | 5.3 (B) | 7.5
Sublimation Energy Per Granule (J) | 6.415 | 61.070 | 68.154
First Ionization Energy (eV) | 5.3917 | 8.2980 (B) | 11.2603

## Slide 20: MAPP update
Full remote operation (EPICS and LabView® Interface) now possible for in between plasma discharges measurements
XPS, ISS, DRS
measurements
Flush with LD tiles at bay J
(boronization, lithiumization, D+ plasma exposures)
Sequence of operation

## Slide 21: Effect of boronization on PFCs in NSTX-U
Boron oxidation due to plasma exposure measured with MAPP via X-ray Photoelectron Spectroscopy (XPS)
1. ATJ graphite
2. ATJ post boronization
3. ATJ post boronization post plasma exposure
Days after boronization
D+ fluence increasing
Low oxygen % High % of B in metallic state
High oxygen % Low % of B in metallic state
XPS data obtained at the end of each plasmas operations day

## Slide 22: Outline
Recent research highlights
Progress toward milestones
Future milestone discussion

## Slide 23: Progress toward Milestones (I)
R16-1: Assess H-mode energy confinement, pedestal, and SOL characteristics with higher BT, IP and NBI heating power
  All key diagnostics took data, except MSE – was waiting for 90kV on NB1A – got to 90keV on 1A in last 2 weeks.
  Checking data consistency via TRANSP
  Need robust / longer-pulse higher current H-mode scenarios
R16-2: Assess effects of NBI parameters on fast ion distribution function and neutral beam driven current profile
  Neutron, FIDA, ssNPA functional (but no MSE data in FY16)
  Started studies of fast ion confinement vs. Rtan and effect of NB#2 on *AE modes, NBI source scans in L-modes

## Slide 24: Progress toward Milestones (II)
R16-3: Develop physics and operational tools for high-performance discharges.
  Developed shape & vertical control, new inboard gap control, EFC, HFS & LFS fueling, automated shutdown
    Early EF identified, important impact on ops, source not yet understood
  Future: commission n=1 DEFC, RWM control, test LGI
Notable Outcome: Perform experimental research …at magnetic field, IP, pulse length beyond that achieved in NSTX….
  NSTX-U pulse lengths (>2s) exceeded NSTX (< 1.8s) at field (0.65T) exceeding maximum NSTX field (0.55T)
  Achieved IP ~ 1MA – did not exceed max NSTX IP = 1.3MA, will require early EFC + improved early H-mode scenarios
    Not having PF1AU coil could make achieving high current more difficult

## Slide 25: Progress toward Milestones (III)
The JRT overlaps with a Notable Outcome:
  JRT: Conduct research to detect and minimize the consequences of disruptions in present and future tokamaks
  Notable Outcome: Conduct NSTX-U experiments and data analysis to support the FES joint research target ….
Made good progress on this Notable:
  Automatic shutdown algorithms developed
  Detecting disruptions in real-time via the IP error, vertical motion, and (soon) the n=1 locked mode signature.
  DECAF code progressing toward real-time application
  MGI using an electromagnetic valve similar to ITER design
    2 MGI valves installed on the machine, fully commissioned, but could not be tested into plasma due to PF1AU fault

## Slide 26: NSTX-U Experiments Are Using a Significantly Expanded Plasma Shutdown Scheme
SS=0:
Ramp-Up & Flat-Top
SS=4: Insufficient IP
SS=3:
IOH Loss of Control
SS=2:
Fast IP Rampdown
SS=1:
Slow IP Rampdown
NSTX PCS: No means of detecting a disruption, or ramping down the plasma current based on events.
NSTX-U PCS: State machine orchestrates the shutdown.
Disruption Imminent
Disruption Imminent
“SS” = “Shutdown State”

## Slide 27: Example of automated ramp-down now used in routine operations
Plasma control system detects loss of control
  OH solenoid near maximum current
  Vertical oscillations exceed threshold
  Abs( Ip - Ip request ) too large
Feedback control switches to new “states” that attempt to gently end the discharge
IP
IP Request
(including asynchronous transition to rampdown)
  ZP(dZP/dt)
  ZP(dZP/dt) threshold
Normal
Fast IP Rampdown
Insufficient IP
  ZP from EFIT
“State”

## Slide 28: Mid-Plane & Divertor MGI Valves ready to support Plasma Operations
The Pre-operational Test Procedure (PTP) for both MGI valves were completed
Valve power supplies operated at 1kV during PTP
Both valves were calibrated in Nitrogen, Helium and Neon at the full operating pressure
During these tests 400Torr.L of neon was injected into the NSTX-U vessel, this is about twice the amount of neon injection planned for the first MGI experiments to be conducted on NSTX-U

## Slide 29: Outline
Recent research highlights
Progress toward milestones
Future milestone discussion

## Slide 30: Additional discussion points
PF5 usage for MSE-LIF (for next Monday)
Notable outcomes for FY17
PF1AU recovery plans / long-term strategy

## Slide 31: Summary
Many nice physics results from NSTX-U (CHERS, MHD, EP, …) despite limited run time
Research milestones partially completed, but need to revisit and complete milestones requiring higher IP
  Propose that most research milestones shift by ~1 fiscal year
Will prioritize diagnostics and XPs to maximize contributions to FY17 JRT

## Slide 32: Backup

## Slide 33: NSTX-U has matched NSTX highest flat-top pressures for plasma currents up to 0.9MA
Next-step goal: IP  1.1 – 1.3MA
Plasma Current [MA]
Volume Average Pressure [kPa]
NSTX-U, Boronized
NSTX, Lithium
NSTX, Mixed
NSTX, Boronized

## Slide 34: Substantial Progress in Developing L- and H-Mode Scenarios
H-Mode Development
L-Mode Development
“Best” Shots From
January
February
March
April
First H-Mode
NSTX Longest Shot

## Slide 35: Shape and Vertical Position Control Are In Good Position to Support the Future Experiments
rtEFIT/ISOFLUX control established for the plasma radius, vertical position, X-points.
  NSTX didn’t routinely do closed loop X-point control.
  Now multi-threaded rtEFIT with greater capabilities
New vertical control sensors & algorithms -> matching the NSTX elongation for the same li, but at higher A.
Internal Inductance
Elongation
NSTX-U, Boronized
NSTX, Lithium
NSTX, Mixed
NSTX, Boronized

## Slide 36: Mode locking and associated fast dynamic clearly observed on RTV data
L-mode
PNB~1.1MW
Mode grows after t~0.33s, then locks over 10ms
First, fast response observed outside mid-radius
  Then propagates to the core
CHERS provides full profiles pre/post locking (inset)

## Slide 37: Essential step for DECAF analysis of general tokamak data: Identification of rotating MHD (e.g. NTMs)
  Apply FFT to determine mode frequency, bandwidth evolution
  Determine bifurcation, mode locking
n = 1 mode frequency vs. time
(new code)
Magnetic spectrogram of rotating MHD in NSTX-U
Odd-n magnetic signal
Even-n magnetic signal
J. Riquezes (U. Michigan – SULI student)
1 = Mode present
-1 = Mode locked
0 = No mode
DECAF mode status
NSTX-U
204202

## Slide 38: Neutral Gas Shielding (NGS) Model benchmarked on DIII-D
600 mm
600 mm
h : Cloud Shielding Parameter
fB : Field directed heating anisotropy
DH: Sublimation Energy
TS : Granule Surface Temperature
Ablation Rate of the injected granule :
Adapted from Parks et al. Nucl. Fusion 34 (1994) & Kocsis et al. PPCF 41 (1999)
Solid Granule
Neutral Ablatant Cloud
Ionized Material
magnetic field
600 mm
600 mm
Li granule injected into DIII-D