| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Dependence of edge plasma on lithium dose at high doses |
| OP-XP-1113 | Revision: | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: R. Maingi | Date |
| ATI – ET Group Leader: V. Soukhanovskii | Date |
| RLM - Run Coordinator: S. Sabbagh | Date |
| Responsible Division: Experimental Research Operations |
| RESTRICTIONS or MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Dependence of edge plasma on lithium dose | No. OP-XP-1113 |
| --- | --- |
| AUTHORS: R. Maingi, D. Boyle, S. Kaye, C. Skinner | DATE: June 13, 2011 |

# 1.	Overview of planned experiment

The goal of this experiment is document the dependence of the ELM-free H-mode characteristics on the lithium ‘dose’ between discharges. Specifically the recycling, edge profiles (particularly ne, Pe, and Ptot), edge stability, and Zeff will documented over a range of high doses > 300 mg, as part of NSTX’s contribution to the FY11 JRT on pedestal structure.

# 2.	Theoretical/ empirical justification

The controlled introduction of lithium in 2008 provided substantial insight into lithium effects, as well as a number of refereed journal articles.  References ELMy discharges in a boronized vessesl were obtained with  6.5 min of HeGDC between discharges. Lithium was then introduced in a controlled manner, resulting in growing periods of ELM quiescence [Mansfield, JNM 2009], slowly improving edge confinement [Canik, PoP 2011], and edge stability [Boyle, PPCF 2011 submitted]. Fig. 1 shows the evolution of several parameters during this scan as a function of the pre-discharge lithium dose. Note that the divertor Da, confinement enhancement factor H97L, and profile peaking factors all varied with the lithium dose. However there were very few discharges obtained in the fully ELM-free regime with high lithium dose > 300mg. These are needed to determine if the trends observed in Fig. 1 are continuous as they appear to be. As a specific example, we would like to determine if the shift of the edge ne profile from the separatrix varies monotonically with the lithium dose at high dose rates; the answer has implications to general edge stability regimes dominated by kink/peeling modes, as NSTX appears to be [Maingi, PRL 2009].

# 3.	Experimental run plan (1/2 day)

1. Start with a low triangularity 4 MW ELMy reference discharge, e.g. 129019, if time permits (2)

2. Add 300 mg of lithium and document, with constant fueling and NBI if possible (3)

3. Repeat step 2 with 450 mg of lithium; probably will need to increase HFS gas and drop NBI power in this step or in previous step, to 2-3 MW (5)

4. Repeat step 3 with 600 mg of lithium (4)

5. Decision point: either use 850mg or 1200mg of lithium, or both if time permits (4-8)

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

Up to 4 MW NBI, no rf, no CHI. Nominally plan for 2-3 MW NBI.

# 5.	Planned analysis

EFIT, TRANSP, and pedestal profile/stability analysis.

# 6.	Planned publication of results

Results allowing, this will be published at the next APS meeting, and as part of the final FY2011 JRT report.

PHYSICS OPERATIONS REQUEST

| TITLE: Dependence of edge plasma on lithium dose | No. OP-XP-1113 |
| --- | --- |
| AUTHORS: R. Maingi, D. Boyle, S. Kaye, C. Skinner | DATE: June 9, 2011 |

Brief description of the most important operational plasma conditions required: Medium delta discharge that produces ELMy H-mode before lithium is added, i.e. 129019. When high lithium does is added, it becomes ELM-free, as in 129038.

Previous shot(s) which can be repeated: Previous shot(s) which can be modified: 129019, 129038, 129041

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): 4.5 kG Flattop start/stop (s): IP (MA): 0.8 MA Flattop start/stop (s): Configuration: Limiter / DN / LSN / USN: LSN drsep=-5mm Equilibrium Control: Outer gap / Isoflux (rtEFIT) / Strike-point control (rtEFIT) Outer gap (m): 8-11 cm Inner gap (m): 2-4 cm Z position (m): Elongation: 1.8-2 Triangularity (U/L): 0.5-0.6 OSP radius (m): Gas Species: D Injector(s): NBI Species: D Voltage (kV) A: 90 B: 90 C: 70-90 Duration (s): ICRF Power (MW): Phase between straps (°): Duration (s): CHI: Off / On Bank capacitance (mF): LITERs: Off / On Total deposition rate (mg/min): LLD: Temperature (°C): unheated EFC coils: Off/On Configuration: Odd / Even / Other

DIAGNOSTIC CHECKLIST

| TITLE: Dependence of edge plasma on lithium dose | No. OP-XP-1113 |
| --- | --- |
| AUTHORS: R. Maingi, D. Boyle, S. Kaye, C. Skinner | DATE: June 13, 2011 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Beam Emission Spectroscopy |  |  |
| Bolometer – divertor |  | √ |
| Bolometer – midplane array | √ |  |
| CHERS – poloidal | √ |  |
| CHERS – toroidal | √ |  |
| Divertor L-alpha array | √ |  |
| Divertor visible camera |  | √ |
| Dust detector |  |  |
| Edge deposition monitors |  | √ |
| Edge neutral density diag. |  |  |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic |  |  |
| Fast cameras – divertor/LLD |  | √ |
| Fast ion D_alpha - poloidal |  |  |
| Fast ion D_alpha - toroidal |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging – divertor |  | √ |
| Gas puff imaging – midplane |  | √ |
| H camera - 1D |  | √ |
| High-k scattering |  |  |
| Infrared camera – standard |  | √ |
| Infrared camera – 2-color |  | √ |
| Infrared camera – wide-angle |  | √ |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – LLD |  | √ |
| Langmuir probes – bias tile |  |  |
| Langmuir probes – RF ant. |  |  |
| Magnetics – B coils | √ |  |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes |  | √ |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents |  |  |
| Magnetics – RWM sensors |  | √ |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MAPP |  |  |
| Mirnov coils – high f. |  | √ |
| Mirnov coils – poloidal array |  | √ |
| Mirnov coils – toroidal array |  | √ |
| Mirnov coils – 3-axis proto. |  |  |
| MSE-CIF |  | √ |
| MSE-LIF |  |  |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron detectors |  |  |
| Plasma TV |  | √ |
| Reflectometer – 65GHz |  | √ |
| Reflectometer – correlation |  | √ |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  | √ |
| Reflectometer – SOL |  |  |
| RF edge probes |  |  |
| Spectrometer – divertor |  |  |
| Spectrometer – SPRED |  | √ |
| Spectrometer – VIPS |  |  |
| Spectrometer – LOWEUS |  | √ |
| Spectrometer – XEUS |  |  |
| SWIFT – 2D flow |  |  |
| TAE Antenna |  |  |
| Thomson scattering | √ |  |
| USXR – pol. arrays |  | √ |
| USXR – multi-energy |  | √ |
| USXR – TG spectr. |  |  |
| Visible bremsstrahlung det. |  | √ |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray tang. pinhole camera |  |  |

# Text boxes

(a)

(b)

(c)

(d)

(e)

Figure 1: Evolution of plasma parameters as a function of pre-discharge lithium ‘dose’: (a) Lower divertor Da baseline value at t=0.4 sec, (b) energy confinement relative to ITER97-L scaling, (c) ne profile peaking factor, (d) Te profile peaking factor, and (e) Pe profile peaking factor. Panels (b)-(e) were computed at the time of peak WMHD. [Maingi, PRL 2011 submitted]