## Slide 1: UCLA & MAST collaborating to implement Doppler Backscattering on MAST for M9 campaign
DBS measures plasma flow (yielding Er) and intermediate-k turbulence near cutoff
Working with Dr. Jon Hillesheim at MAST
Q-band and V-band systems shipped to MAST in April 2013
  16 channels, 30 – 75 GHz; cutoffs @1 – 7 x 1013 cm-3 in O-mode
  can be configured for DBS or reflectometry
Systems bench tested & installed June 2013
Initial DBS data looks promising
  TAEs observed via DBS (bottom) & Reflectometry
ki+kdn=ks
scattered
radiation
incident
radiation
dn
cutoff
dE
ddf/dt
TAEs
42.5 GHz backscattered microwave spectra:
E = Aexp(if)