## Slide 1: Error Fields (Myers, Gerhardt, Park, and Menard)
NSTX-U error field considerations
  The PF5 coils may have changed shape  could produce n=2 EF
  New current feeds for OH and divertor coils  different (smaller?) EFs
  New J/K cap for NB2  non-axisymmetric EFs during current ramp?
  Unanticipated EF sources are possible (or even probable)
Error Field PTP: Coil shape measurements in the test cell
  Assess PF3/4/5 coil shapes with a ruler and plumb bob
  Measure coil-to-vessel and coil-to-coil positions at multiple toroidal locations
Error Field XMP: Vessel-generated EFs in AC vacuum shots
  The new J/K cap is likely to carry non-axisymmetric induced currents during the current ramp  the importance of this effect is unknown
  Swing the OH + PF3/4/5 during vacuum shots to quantify the axisymmetry of the induced vessel currents

## Slide 2: Error Fields (Myers, Gerhardt, Park, and Menard)
Error Field XP #1: Low β, low density locked mode studies
  n=1 compass scans (multiple phases and amplitudes)
  Should run early in the campaign (the RWM sensors are required)
  Disruptions as the primary diagnostic (rotation available?)
Error Field XP #2: High β n=1,2,3 compass scans
  Intra-shot modulation and/or “spiral” n=1,2 scans during long pulse operation
  Rotation and disruption as diagnostics
  Flip the n=3 polarity to optimize and compare to the NSTX n=3 settings
Error Field XP #3: Optimization of PID Dynamic EF Correction
  Tune amplitudes, phases, and gains of the PID DEFC algorithm
  Requires the real time RWM controller to be operational
  Utilize low pass filter to isolate the effect of DEFC from fast RWM control