## Slide 1
XP1517: Neoclassical toroidal viscosity at reduced collisionality (independent coil control)
S. A. Sabbagh, J.W. Berkery, J.M Bialek
Y.S. Park, (et al…)
Department of Applied Physics, Columbia University, New York, NY
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
NSTX-U Macrostability TSG Meeting
June 30th, 2015
PPPL
V1.1
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Columbia U. Group 2015 Macrostability TSG XPs (Short Summary)
XPs (related XPs assigned numbers for “2011 run”)
  RWM stabilization dependence on neutral beam deposition angle (~XP1149) (Berkery)
  RWM stabilization physics at reduced collisionality (~XP1148) (Berkery)
  RWM state space active control physics (independent coil control) (~XP1145) (Sabbagh)
  RWM control physics with partial control coil coverage (JT-60SA) (~XP1147) (Y-S Park)
  RWM PID control optimization based on theory and experiment (~XP1111) (Sabbagh)
  RWM state space active control at low plasma rotation (~XP1146) (Y-S Park)
  Neoclassical toroidal viscosity - reduced n (independent coil control) (~XP1150) (Sabbagh)
  NTV steady-state rotation at reduced torque (HHFW) (~XP1062) (Sabbagh)
  Multi-mode error field correction using the RWMSC (to follow initial EFC XP)
  NTM Entrainment in NSTX-U (Y.S. Park)
Piggyback XPs
  Disruption PAM characterization, measurements, and criteria (Sabbagh, for DPAM WG)
NOTE: - some shot plans already scoped out in web submissions (not repeated here)
- run day requests mostly assume leveraging “2nd NBI XP”, “Ip/Bt scaling XP”

## Slide 3: XP1517: Neoclassical toroidal viscosity at reduced collisionality (independent coil control)
Motivation
  Experimentally, the dependence of neoclassical toroidal viscosity (NTV) at low collisionality needs further study
  Understanding important for NSTX-U Vf control, other tokamaks, future devices
Goals / Approach
  Examine the dependence of NTV on ion collisionality
    expected to increase with decreasing ni from present experiments, and theory
  Determine if superbanana plateau increase of NTV depends on ni
  Operate with pre-programmed n = 2, 3 applied fields for Vf feedback control testing at reduced ni
Addresses
  NSTX Milestones R(15-3), closed-loop rotation control with 3D fields
  ITPA joint experiment MDC-21
NTV strength varies with plasma collisionality n, dB2, rotation
K.C. Shaing, M.S. Chu, C.T. Hsu, et al., PPCF 54 (2012) 124033
plasma rotation
Ti5/2
K.C. Shaing, et al.,
PPCF 51 (2009) 035004
NTV force in “1/n” collisionality regime
1/aspect ratio (compare to KSTAR)
ni* ~ 1
NSTX
NSTX-U
“offset” rotation

## Slide 4: Measured NTV torque density profiles quantitatively compare well to computed TNTV – NTVTOK code interfaced to NSTX-U
Scale factor ((dL/dt)/TNTV) = 1.7 and 0.6 (for cases shown above) – O(1) agreement
Comparison to full Shaing, et al. theory with NTVTOK code (applicable for all collisionality (as shown above) is possible to compute between shots for NSTX-U
Comparisons will also be made to other NTV codes (e.g. by J-K. Park, et al.)
Experimental
-dL/dt
yN
NSTX
NTVTOK code
n = 2 coil configuration
S.A. Sabbagh, et al., IAEA FEC 2014, paper EX/1-4
n = 3 coil configuration
Experimental
-dL/dt
NTVTOK
yN
NSTX
x0.6
x1.7

## Slide 5: NTV experiment at reduced n is a key step for closed-loop Vf feedback using 3D fields in NSTX-U
Expect stronger NTV torque at higher Ti (-dwf/dt ~ Ti5/2 wf)
  Initially shown in NSTX
  Shown in our recent KSTAR XPs
Present XP
  Operate with larger change in ni
  Attempt to reach quasi-steady-state wf for each ni
  Use braking fields envisioned for Vf FB
S.A. Sabbagh, et al, NF 50 (2010) 025020
S.A. Sabbagh, et al., IAEA FEC 2014, paper EX/1-4
I. Goumiri (PU), S.A. Sabbagh (Columbia U.), D.A. Gates (PPPL)
Y.S. Park, et al, IAEA FEC 2014, paper EX/P8-05

## Slide 6: XP1517:NTV at reduced collisionality (independent coil control) – basic shot scans / run time allocation
Primary scans (usual 3D applied field “steps” ~ 150 ms duration)
  Vary collisionality using usual BT, Ip variation at constant q (4 shots)
  Vary collisionality at fixed, different q (2 more values) (8 shots)
Additional scan components
  Vary applied field spectrum (n = 2, n = 3, n = 2+3 configurations) (data points will come during shots above)
  Vary collisionality in superbanana plateau regime (operate at low wE) (data points will come from end of shots above)
Additional details / options
  Add intervals with n = 1 field correction to determine effect on NTV
  May vary NBI mix in some shots (source 1 NBI vs source 2 NBI) (add 2 shots)
    Primary NBI expected to be from source 1, but will use source 2 NBI (depends on success of CHERS data availability with NBI source 2)
  For example: 1 shot can generate data for (i) n = 2, (ii) n = 3, (iii) n = 3 (n=1 EFC), (iv) superbanana plateau operation at low rotation
Run time
  0.5 priority 1 run days allocated for XP1517 (~14 shots?)
  Will have at least one primary collisionality scan, and the n = 2 and 3 configurations from NTV set-up shots in “uber” Ip, BT scaling XP (~ 6 shots)
  Will have NBI 1,2; n=2,3 fields from NTV shots in “uber” NBI XP (~ 8 shots)

## Slide 7: XP1517:NTV at reduced collisionality (independent coil control) – Diagnostics, etc.
Required diagnostics / capabilities
  RWM coils generating n = 3 and n = 2 configurations
  CHERS toroidal rotation measurement
  Thomson scattering
  MSE
  Toroidal Mirnov array / between-shots spectrogram with toroidal mode number analysis
Desired diagnostics / capabilities
  RWM sensors
  n = 1 field correction (slow n = 1 feedback)
  Real-time rotation measurement
  USXR / ME-SXR
  Fast camera