## Slide 1
XP1518: RWM PID control optimization based on theory and experiment
S. A. Sabbagh, J.W. Berkery, J.M Bialek
Y.S. Park, (et al…)
Department of Applied Physics, Columbia University, New York, NY
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
NSTX-U Macrostability TSG Meeting
June 30th, 2015
PPPL
V1.0
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Columbia U. Group 2015 Macrostability TSG XPs (Short Summary)
XPs (related XPs assigned numbers for “2011 run”)
  RWM stabilization dependence on neutral beam deposition angle (~XP1149) (Berkery)
  RWM stabilization physics at reduced collisionality (~XP1148) (Berkery)
  RWM state space active control physics (independent coil control) (~XP1145) (Sabbagh)
  RWM control physics with partial control coil coverage (JT-60SA) (~XP1147) (Y-S Park)
  RWM PID control optimization based on theory and experiment (~XP1111) (Sabbagh)
  RWM state space active control at low plasma rotation (~XP1146) (Y-S Park)
  Neoclassical toroidal viscosity - reduced n (independent coil control) (~XP1150) (Sabbagh)
  NTV steady-state rotation at reduced torque (HHFW) (~XP1062) (Sabbagh)
  Multi-mode error field correction using the RWMSC (to follow initial EFC XP)
  NTM Entrainment in NSTX-U (Y.S. Park)
Piggyback XPs
  Disruption PAM characterization, measurements, and criteria (Sabbagh, for DPAM WG)
NOTE: - some shot plans already scoped out in web submissions (not repeated here)
- run day requests mostly assume leveraging “2nd NBI XP”, “Ip/Bt scaling XP”

## Slide 3: XP1518: RWM PID control optimization based on theory and experiment
Motivation
  Experiments using n = 1 RWM control in 2010, and subsequent analysis using the VALEN code show that some settings for control using dual BR and Bp sensor feedback were optimal, others could have been improved
  Active RWM PID control settings need to be re-optimized for NSTX-U
  Support general NSTX-U experiments by optimizing RWM PID control
Goals / Approach
  Optimize n = 1 RWM PID control focusing on scans of key parameters
    Vary Bp feedback phase, BR feedback gain – which differ in the most in the analysis from the experimental settings
    Bp sensor gain will also be examined in this experiment (never scanned with r/t AC compensation).
    Perform on high performance target plasmas (fiducial; low li; snowflake)
Addresses
  General support for NSTX-U high beta experiments, R(15-3)
  ITPA joint experiment MDC-17

## Slide 4: RWM Br sensor n = 1 feedback phase variation shows superior settings when combined w/Bp sensors; good agreement w/theory
VALEN calculation of Br+Bp feedback follows XP
  stable plasma (negative “s”)
  Now examining plasma response model variation
    impact of “s”, and diff. rotation (“a”) on results
Dt (s)
Radial field n = 1 (G)
Favorable (experimental) Bp feedback settings, varied BR settings
  Positive/negative feedback produced at theoretically expected phase values
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum EF + RFA
VALEN calculation of NSTX Br + Bp control
n = 1 BR + Bp feedback
(Bp gain = 1, BR gain = 1.5)
NSTX Experiments: Bp + BR feedback
Feedback on

## Slide 5: XP1518: RWM PID control optimization based on theory and experiment – basic shot scans / run time allocation
Primary scans (number of data points/shot will depend on high beta steady-state duration)
  Vary Bp sensor feedback phase, no Br feedback (4 shots) – (at 4 phases/shot)
    Extra shot added here in case gain increase needed
  Vary Bp sensor feedback gain, no Br feedback (2 shots)
  Vary Br sensor feedback gain, with “best” Bp feedback settings (2 shots)
    Br sensor feedback phase of 180 degrees
  Vary Br sensor feedback phase, with “best” Bp feedback settings (2 shots)
  Vary Bp sensor feedback phase to check with “best” Br feedback (4 shots)
Additional details/scans
  Add an interval of pre-programmed n = 1 field to determine that feedback is being effective – change gain if needed on early shots (no extra shots needed)
  Use fiducial, or generally high performance low li target plasma
  May wish to redo all/part of these scans on significantly different NSTX-U plasma conditions (e.g. standard DND vs. snowflake)
Run time
  0.5 priority run days allocated for XP1518 (~14 shots?)

## Slide 6: XP1518: RWM PID control optimization based on theory and experiment – Diagnostics, etc.
Required diagnostics / capabilities
  RWM Bp and Br sensors
  RWM n = 1 PID feedback using Bp and Br sensors
  RWM coils generating n = 3 or n = 2 applied field configurations
  CHERS toroidal rotation measurement
  Thomson scattering
  MSE
  Toroidal Mirnov array / between-shots spectrogram with toroidal mode number analysis
Desired diagnostics / capabilities
  Real-time rotation measurement
  USXR and ME-SXR
  Fast camera