| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: RF Amplification of EHOs in Lithium-pumped ELM-Free Plasmas |
| XP-???? | Revision: 0 | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: R.J. Goldston | Date July 27, 2010 |
| ATI – ET Group Leader: | Date |
| RLM - Run Coordinator: E. Fredrickson | Date |
| Responsible Division: Experimental Research Operations |
| RESTRICTIONS or MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: RF Amplification of EHOs in Lithium-pumped ELM-Free Plasmas | No. |
| --- | --- |
| AUTHORS: R. Goldston, R. Bell, J. Hosea, E. Fredrickson, S. Gerhardt, R. Maingi, K. Tritz, J.R. Wilson | DATE: July 27, 2010 |

# 1.	Overview of planned experiment

NSTX experiences impurity accumulation in ELM-free H-mode plasmas induced by lithium evaporation. Indeed deuterium is apparently effectively pumped, and the steady density rise in the later half of a relatively quiescent lithiated pulse is due to the accumulation of non-fuel components. Both C-Mod and DIII-D have regimes without ELMS, the EDA and QH mode respectively. In both cases fluctuations in the plasma edge are believed to arrest impurity influx and density rise, in the case of DIII-D these are Edge Harmonic Oscillations, and in the case of C-MOD they are Quasi-Coherent Modes. On NSTX we have observed clear signatures of EHO’s in lithiated discharges at about 800 kA and 4 MW of beam power. We propose to explore the possibility of amplifying these modes by driving them with audio-modulated HHFW power. (There is a mini-proposal at C-Mod, independent of this one, to drive the much higher frequency QCMs by the same means.)

# 2.	Theoretical/ empirical justification

In DIII-D QH modes, the EHO is observed with n’s in the range of a few, each rotating in the toroidal direction with n*f, where f is the rotation frequency. On NSTX we have observed modes with n = 4 – 6 (blue to magenta on the figure above) on the Mirnov coils rotating at about 4, 5 and 6 kHz. The measured plasma rotation at the furthest out measured point of 144cm is above 1 kHz. The ultra-soft X-ray system observes modes at these same frequencies. We have carefully examined the scan from XP 1043, with lithium evaporation, and the EHO’s are reproducible in ELM-free shots at plasma current around 800 kA, with beam power in the range of 4 MW, such as 138239, but weaker at higher and lower power, and at higher current. It is important to avoid low-n MHD for these modes to be observed. There is no claim here that these EHO’s are controlling impurity influx, but it is possible that if they were enhanced they would do so.

If it were possible to exert external control over the amplitude of such oscillations through coupling to RF, it would be very favorable for ITER and other devices – for example if such modes could be used to reduce the edge pressure gradient and mitigate ELMs. The alternative of direct inductive coupling, e.g., by coupling power from the SPAs to the RF straps, while possible, would be more cumbersome, so it behooves us to test this simpler approach first.

# 3.	Experimental run plan

I  Establish conditions similar to 138239:

- Establish the presence of EHOs both on the Mirnov and soft X-ray systems

- Measure impurity accumulation

3 shots

II  Add Amplitude-Modulated HHFW Power

- Determine level of power and pulse length that can be reliably obtained. Don't need to push to the highest power levels, which would make this unreliable.
3 shots

- Establish level of amplitude modulation that can be obtained at observed frequency of strongest EHO ~ 4 kHz.
3 shots

- Sweep frequency of amplitude modulation from 0.5 – 7.5 kHz, and determine where maximum amplification occurs.
3 shots

III Maximize effect

- Select optimum point for EHO amplification, if some is observed, and maximize modulated RF power. By looking at the swept results may decide to have some sweeping still in this case. Interleave with shots with same RF power but no amplitude modulation.
6 shots

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

- Lithium evaporation, 4 MW of NBI power, 800 kA, LSN

- Best if this happens soon after HHFW experiments have established reasonably healthy operations

- Need Mirnov array, soft-x-rays, rotation, and impurity accumulation measurements

# 5.	Planned analysis

Will examine impurity accumulation as a function of EHO strength. Will use results to motivate theoretical analysis of coupling of HHFW power to EHO’s. If the result is that there is no change in the amplitude of the EHO’s, then will need to consider inductive drive. It would be valuable also to observe any change on the divertor heat flux. It could go up due to reduced radiative power, or go down (in the most favorable case) due to increased edge oscillation.

# 6.	Planned publication of results

If successful, would merit a PRL.

PHYSICS OPERATIONS REQUEST

| TITLE: RF Amplification of EHOs in Lithium-pumped ELM-Free Plasmas | No. XP-???? |
| --- | --- |
| AUTHORS: R. Goldston et al. | DATE: July 27, 2010 |

Brief description of the most important operational plasma conditions required: Need conditions similar to those for shot 138239 (shape of the standard high-triangularity morning reference shot). Stable operation at 4.5 kG, 0.8 MA with 4MW NBI (2 MW Src. A, 1 MW Srcs. B & C). ELM-free, lithiated H-mode.

Previous shot(s) which can be repeated: 138239 Previous shot(s) which can be modified:

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): as 138239 Flattop start/stop (s): as for shot 138239 IP (MA): 0.8MA Flattop start/stop (s): as for shot 138239 Configuration: LSN - see 138239 for parameters below Equilibrium Control: Isoflux (rtEFIT) Outer gap (m): Inner gap (m): Z position (m): Elongation: Triangularity (U/L): OSP radius (m): Gas Species: D Injector(s): NBI Species: D Voltage (kV) A: ~ 90 B: ~ 65 C: 65 Duration (s): 1.2 ICRF As high modulated power as possible, 0.6 – 0.9 sec CHI: Off Bank capacitance (mF): LITERs: Total deposition rate (mg/min): See 138239 LLD: Temperature (°C): See 138239 EFC coils: as for 138239 Configuration: Odd

DIAGNOSTIC CHECKLIST

| TITLE: RF Amplification of EHOs in Lithium-pumped ELM-Free Plasmas | No. XP-???? |
| --- | --- |
| AUTHORS: R. Goldston et al. | DATE: July 27, 2010 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Beam Emission Spectroscopy |  |  |
| Bolometer – divertor |  | x |
| Bolometer – midplane array | x |  |
| CHERS – poloidal |  | X |
| CHERS – toroidal | X |  |
| Dust detector |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  |  |
| Edge pressure gauges |  |  |
| Edge rotation diagnostic | X |  |
| Fast cameras – divertor/LLD |  | x |
| Fast ion D_alpha - FIDA |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes |  | x |
| FIReTIP |  | x |
| Gas puff imaging – divertor |  |  |
| Gas puff imaging – midplane |  |  |
| H camera - 1D |  | x |
| High-k scattering |  |  |
| Infrared cameras | x |  |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor | x |  |
| Langmuir probes – LLD | X |  |
| Langmuir probes – bias tile | X |  |
| Langmuir probes – RF ant. | X |  |
| Magnetics – B coils | √ |  |
| Magnetics – Diamagnetism | x |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes | x |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents |  |  |
| Magnetics – RWM sensors | x |  |
| Mirnov coils – high f. |  | x |
| Mirnov coils – poloidal array |  |  |
| Mirnov coils – toroidal array | X |  |
| Mirnov coils – 3-axis proto. |  |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE |  | x |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron detectors | X |  |
| Plasma TV | x |  |
| Reflectometer – 65GHz |  |  |
| Reflectometer – correlation |  |  |
| Reflectometer – FM/CW |  |  |
| Reflectometer – fixed f |  |  |
| Reflectometer – SOL | X |  |
| RF edge probes | X |  |
| Spectrometer – divertor | X |  |
| Spectrometer – SPRED | x |  |
| Spectrometer – VIPS | x |  |
| Spectrometer – LOWEUS |  | x |
| Spectrometer – XEUS |  | x |
| SWIFT – 2D flow |  |  |
| Thermocouples LLD | X |  |
| Thomson scattering | X |  |
| Ultrasoft X-ray – pol. arrays | X |  |
| Ultrasoft X-rays – bicolor | x |  |
| Ultrasoft X-rays – TG spectr. | x |  |
| Visible bremsstrahlung det. | x |  |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray tang. pinhole camera |  |  |