## Slide 1
MS TSG Pre-Forum Meeting
Comments on R11-2
Stefan Gerhardt
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Some Background
NSTX typically scans A and k simultaneously.
No inner gap control (at present).
Calculations (using experimental profiles) show a reduced ideal no-wall limit when A and k are increased.
Have never done a dedicated experiment to test the experiment beta limit vs. (high) k and A.
From TRANSP database of high-performance discharges
CHEASE fixed boundary + DCON

## Slide 3: We need to robustly sustain bN=4.5-5 at high A and k
Simulations for 1.0 T, 1.0 MA, k=2.7, A=1.65, 12 MW
  Need bN=4.5-5, at H98=1.1, for fully non-inductive operation.
Scenarios with lower current and more NBCD will likely need A~1.8, k~2.9-3.0 for more off-axis CD.

## Slide 4: Ideal Stability May Further Limit the Operating Space
qmin to low
Internally unstable
Pressure
peaking
too large
Wall Stabilized Regime
Pressure
peaking
too large
qmin to low
Internally unstable
Important future task: re-run with some additional fast ion diffusion to reduce the central NBCD and pressure peaking.
Also would be nice to inmprove the resolution in [H98,fGW] space.
Preliminary!

## Slide 5: What kind of shape changes are possible?
Inner gap scan at fixed outer gap.
Simultaneously increases A and k.
Maintains (nearly) constant distance to the plates and BP RWM sensors.
Increase the outer gap for k=3, A=1.75
Aspect ratio scan at fixed k.
Inner and outer gaps change at fixed plasma height
k scan at fixed aspect ration.
Plasma height changes with fixed inner and outer gaps.
All scans at 700 kA to avoid hitting PF-1A coil current limit!

## Slide 6: Possible (Likely?) ASC Contributions to R11-2
Milestone has a component related to n=0 stability and control.
Improve the vertical controller (SPG).
  Produce a better realtime estimate of dZ/dt.
  Optimize the derivative gain.
    Proportional controller is the ISOFLUX algorithm.
  If necessary, test use of RWM coils for vertical control.
Test more advanced shape control algorithms (EK).
  Use a fully populated “M-Matrix”
  Use it to develop better inner- and bottom- gap control.
Performance impact of k and A (SPG).
  Scan A at fixed k, and k at fixed A.
  Use reduced input power to avoid disruptions.
  Test confinement (and current drive) changes due to shape modifications.
Loss of vertical control when li>0.6

## Slide 7: XP Idea #1: The impact of elongation and aspect ratio on the ideal stability of ST plasmas
NSTX has a large database of stability results with A<1.55 and k<~2.4.
  High-performance NSTX upgrade scenarios will run at larger values of both these parameters.
It is hard to scan these parameters independently in NSTX…
  Will be even harder in NSTX-U.
  This run is the last chance for these types of scans.
Relevant Milestone Text: The maximum sustainable normalized beta will be determined versus aspect ratio (up to A=1.7) and elongation (up to 3) and compared to ideal stability theory using codes such as DCON and PEST.
Propose to do three types of scans (with fast RWM control off?):
  Scan #1: Mixed k & A scan at fixed outer gap (12 shots).
    Use RFA analysis to look for passive instability.
  Scan #2: A scan at fixed kappa (10 shots).
    Test the disruptive bN limit (use the bN controller to ramp to a disrupting in a controlled way).
  Scan #3: Kappa scan at fixed A (10 shots).
    Test the disruptive bN limit (use the bN controller to ramp to a disrupting in a controlled way).
Goals:
  Determine if, within the achievable range of A and k, there is a measurable change in global stability.
    Compare to ideal stability theory.
  Collect data validating the b-limit assumptions for NSTX Upgrade.

## Slide 8: XP Idea #2:MHD Stability at Very High Toroidal-b and Normalized Current
ST reactor designs typically assume very high toroidal b.
  PPPL Pilot: 30-39%, ARIES-ST: 50%, Culham 59%
It may be time to revisit discharge scenarios with very high bT.
  We have made many improvements in control & discharge development since these were last tried in 2005.
    Reduced PCS latency, RWM control, Li PFC conditioning, stronger shaping, better control during the IP ramp.
  We have many new and important diagnostics since 2005.
    MSE, RWM sensors, better USXR systems.
  We may have trouble making these shots again.
    Higher aspect ratio of NSTX-U will lower ideal stability limits.
Propose to revisit discharges in the bT~40% regime.
  Characterize the limiting instabilities.
    What is the maximum stable bT at low q* during the phase when qmin>~1.1 (i.e. before kink/tearing starts).
    Can we modify this limit via the profiles? Allow li to peak up to improve confinement and stability?
  Determine to what extent recent operations improvements facilitate this regime.
  Study disruption precursors.
    Are disruptions detectable in advance?