## Slide 1
Theory Improvements
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC
J.W. Berkery
Department of Applied Physics, Columbia University, New York, NY, USA
Rochester, New York
March 15, 2012

## Slide 2: Kinetic terms in the RWM dispersion relation enable stabilization; theory consistent with experimental results
Dissipation (Im(δWK)) and restoring force (Re(δWK)) from kinetic term enables stabilization of the RWM:
[B. Hu et al., Phys. Plasmas 12, 057301 (2005)]
Precession Drift
Bounce
~ Plasma Rotation:
Collisionality
Theory Development
Collisionality model improvements
Anisotropy of energetic particles
Further rotation effects (inc. poloidal)
Eigenfunction modifications
Neoclassical orbit modification? (with G. Kagan)
gtw contours vs. ν and wf
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]
Precession drift
resonance stabilization
Bounce/transit
resonance stabilization
Marginal stability
instability
(experiment)

## Slide 3: NSTX-U will have lower collisionality and second, off-axis neutral beam
[J. Menard et al., submitted to Nucl. Fusion (2011)]

## Slide 4: EPs have a generally stabilizing effect that is independent of rotation; Anisotropic distribution impacts stability
Addition of simple anisotropy model
(χ0 = 0.75, δχ = 0.25)
reduces stabilizing effect, consistent with quantitative comparison to NSTX
ωφ/ωφexp (marginally stable)
γτw
unstable
stable
[J.W. Berkery et al., Phys. Plasmas 17, 082504 (2010)]
[N. Gorelenkov et al., Nucl. Fusion 45, 226 (2015)]
Anisotropy effects fluid terms, mostly through ballooning term.
Also effects kinetic term, through pitch angle dependence of distribution function.

## Slide 5: Reduced collisionality (ν) is stabilizing for RWMs, but only near kinetic resonances
140132 @ 0.704
NSTX-tested kinetic RWM stability theory: 2 competing effects at lower ν
  Stabilizing collisional dissipation reduced (expected from early theory)
  Stabilizing resonant kinetic effects enhanced (contrasts early RWM theory)
RWM growth rate (γτw)
unstable
[J. Berkery et al., Phys. Rev. Lett. 106, 075004 (2011)]
MISK currently uses an energy-dependent collisionality, MARS-K uses a constant.
Possible improvements:
Particle, momentum, and energy conserving Krook operator for like-particle collisions (suggested by G. Hammett):
Lorentz operator with pitch angle dependence:

## Slide 6: Further exploration of the effect of plasma rotation
[J. Menard, APS 2010 and 2011]
[J. Menard et al., Nucl. Fusion 50, 045008 (2010)]
[N. Aiba et al., Phys. Plasmas 18, 022503 (2011)]
Effect on equilibrium
Including poloidal rotation
Eigenfunction modification (next slide)

## Slide 7: The RWM eigenfunction may be modified by several factors
Kinetic dissipation
Plasma rotation
The importance of eigenfunction modification and Alfven resonances at rational surfaces will come out of code benchmarking.
[J. Menard and Y.Q. Liu, APS 2011]

## Slide 8: How can we approximate eigenfunction modification in MISK with an iterative approach?
We take the eigenfunction from the PEST marginally-stable eigenfunction: γ -> 0, δI -> 0, δWF = -δWV (at the marginal wall position).
We can calculate a fluid growth rate with that fixed eigenfunction, the true wall position, and the assumption that the inertial term is still negligible.
We can calculate a kinetic growth rate and mode rotation frequency by including kinetic effects and anisotropy corrections, but still assuming a fixed eigenfunction and negligible inertial term.
We can even iterate for corrected γ and ωr, and solve for multiple roots. [J. Berkery et al., Phys. Plasmas 18, 072501 (2011)]
Keeping the eigenfunction fixed, we could additionally try to include the inertial term (which actually involves multiple roots as well):
Now, if the eigenfunction is allowed to change, how do we solve for a new one?

## Slide 9: Rotation and kinetic damping may also affect the ideal no-wall stability limit
[J. Menard and Y.Q. Liu, EPS 2012]
[I. Chapman et al., Plasma Phys. Control. Fusion 53 125002 (2011)]

## Slide 10: Finite Larmor Radius Effects

## Slide 11: Finite Orbit Width Kinetic damping of RWMs
For typical MAST case, simple beam distribution
Orbit widths can be very important for fast ions
Use guiding-centre following code to capture this physics
RWM passively stable in ITER Advanced Scenario due to kinetic damping
Only capture these effects by including orbit widths
Sensitive to rotation, so should not be relied upon!
HAGIS code

## Slide 12: Finite Orbit Width
Ian Chapman email:
“I need to talk to YQ and Jon Graves who probably have insight from the algebraic formulation with FOW included that they’re working on.”

## Slide 13: xxx