## Slide 1: XICS design scoping considerations
T&T TSG, Core SG meeting
July 12, 2016

## Slide 2: MIT plans to install XICS for FY17 operation Need to prioritize desired XICS capabilities for NSTX-U
Desired measurement range in minor radii
Desired spatial and temporal resolution desired (< 500 Hz due to detector limits)
Desired measurement accuracy of each plasma quantity
  ion temperature profile
  toroidal rotation profile
  impurity transport (Ar w/ other impurities possible)
  poloidal rotation profile
  radial electric field profile
  electron temperature (from line ratios)
  measurement of in/out asymmetry
Prioritization of measured quantities

## Slide 3: Estimated parameter maximums
ne: 2.51020 m-3 (nGW @ 2 MA)
Te: 3.5 keV (H-mode), 10 keV (reversed shear RF discharges)
Ti: 3.5 keV (H-mode)
Vtor: 400 km/s

## Slide 4: Toroidal rotation up to ~360 km/s measured in NSTX
ne
Te
VTor
nd
6nc
Ti
Zeff

## Slide 5: High current NSTX-U projections
BT=1.0 T, IP=1.7-2 MA, PNBI=10-15 MW (6 beam sources)
  [Fig. 20, Gerhardt NF 52, 083020 (2012)]