## Slide 1: Recent Progress in Understanding Electron Thermal Transport in NSTX and NSTX-U
Y. Ren1
E. Belova1, W. Guttenfelder1, N. Gorelenkov1, S.M. Kaye1, E. Mazzucato1, W.X. Wang1, K. Tritz2, R.E. Bell1, B.P. LeBlanc1, C.W. Domier3,
D.R. Smith4, H. Yuh5, K.C. Lee6, and the NSTX Team
1. PPPL 2. JHU 3. UC-Davis 4. UW-Madison
5. Nova Photonics 6. NFRI
18th International Congress on Plasma Physics
June 27th-July 1st, 2016, Kaohsiung, Taiwan

## Slide 2: Outline
Introduction
Recent results on electron thermal transport in NSTX
  Micro-tearing turbulence in NSTX high-beta and high-collisionality H-mode plasmas
  ETG turbulence in NSTX L and H-mode plasmas
  Fast-ion-driven Alfven eigenmodes in the core region of NSTX high-power H-mode plasmas
NSTX-U Plans for electron thermal transport
Summary

## Slide 3: Spherical Tokamaks Have Some Significant Advantages over Conventional Tokamak
The low aspect ratio of spherical tokamaks leads to improved ¯ limit than conventional tokamaks
  More compact and lower-cost future devices, e.g. Fusion Nuclear Science Facility (FNSF) and power plant
The effective shaping and/or strong ExB shear from low aspect ratio lead to reduced ion-scale turbulence
  Neoclassical ion thermal transport and different confinement scaling for H-mode plasmas

## Slide 4: NSTX Thermal Confinement Has Strong Collisionality Scaling in H-mode Plasmas
Ion transport is neoclassical, consistent with strong flow shear and strong shaping
The confinement scaling is determined by electron thermal transport
NSTX
MAST
Valovič et al.,Nucl. Fusion, 2011
ITER
Doyle et al., Nucl.Fusion 2007
Kaye et al., Nucl. Fusion, 2007
Neoclassical transport by GTC-NEO

## Slide 5: Multiple Mechanisms Should be Responsible for Anomalous Electron Thermal Transport
Different mechanisms needed to account for the always anomalous electron thermal transport
  Different radial regions
    Core flat region (small gradient drive)
    Core gradient region (large gradient drive)
    Edge region (steepest gradient, connection to SOL, e.g. H-mode pedestal)
  Different parametric regimes
    Large/small plasma beta/collisionality, magnetic shear, ExB shear, etc.
Core flat region
Core gradient region
Edge region
r
T

## Slide 6: Multiple Mechanisms Should be Responsible for Anomalous Electron Thermal Transport
Different mechanisms needed to account for the always anomalous electron thermal transport
  Different radial regions
    Core flat region (small gradient drive)
    Core gradient region (large gradient drive)
    Edge region (steepest gradient, connection to SOL, e.g. H-mode pedestal)
  Different parametric regimes
    Large/small plasma beta/collisionality, magnetic shear, ExB shear, etc.
Evidence exists for gradient driven electrostatic and electromagnetic ballooning drift instabilities:
  Low-k (ion-scale): ITG/TEM/KBM/microtearing modes
  High-k (electron-scale): ETG modes
  Turbulent ExB drift and magnetic flutter effects
Fast ion driven Alfvenic eigenmodes found relevant
  GAE and/or CAE modes
  Alfvenic eigenmode induced electron drift orbit stochasticity
Core flat region
Core gradient region
Edge region
r
T

## Slide 7
Micro-tearing turbulence in high-collisionality and high-beta H-mode plasmas
Core flat region
Core gradient region
r
T

## Slide 8: First Successful Nonlinear Microtearing Simulations for NSTX
dBr (Gauss)
BT0=3.5 kG
Movies at http://www.pppl.gov/~wgutten/
W. Guttenfelder et al., PRL (2011)
~98% of transport due to magnetic “flutter” contribution
wisland(n) > drrat(n), island overlap  perturbed field line trajectories are stochastic*
ce,EM =1.25 rscs2/a close to collisionless Rechester-Rosenbluth** (lmfp=12 m, Lc2.5 m)
*E. Wang et al., PoP (2011).
**A.B. Rechester & M.N. Rosenbluth, PRL (1978)

## Slide 9: Micro-tearing Mode Predictions are Consistent with NSTX H-mode Plasmas
As transport drops, a/LTe will increase (for fixed heat flux), at some point ETG (TEM/KBM?) should become important
This transition likely to determine limit of “favorable” n* scaling
Non-linear transport
A representative NSTX H-mode
Using micro-tearing-based RLW electron thermal diffusivity model
Good agreement seen when micro-tearing linearly important
W. Guttenfelder et al., PRL (2011)
Kaye et al., NF (2015)

## Slide 10
ETG turbulence in NSTX L and H-mode plasmas
Core flat region
Core gradient region
r
T

## Slide 11: A High-k Microwave Scattering System was Used to Measure Electron-scale Turbulence in NSTX
Probe beam
Scattered light
Spherical mirror
kp
ks
Probe beam
θs
ki
D.R. Smith, PhD thesis, 2009
High-k turbulence measurement |  |  | 
 | r/a | Measured quantity | Spatial & temporal resolution
280 GHz microwave scattering system | ~0.2-1 from core to edge | Density fluctuation | 3 ≤ k┴ρs ≤ 12 R ~ ±2 cm f~ 5 MHz

## Slide 12: First Identification of ETG Turbulence in NSTX RF-heated L-mode Plasmas
The measured high-k turbulence is shown to be driven by electron temperature
  In RF-heated helium L-mode plasma (1.2 MW, 5.5 kG, 700 kA)
  Fluctuation propagates in the electron diamagnetic direction
  Clear reduction in turbulence spectral power at lower electron temperature gradient
Electron direction
Mazzucato et al., PRL 2008, NF 2009

## Slide 13: ETG Turbulence can Produce Experimentally Relevant Electron Thermal Transport
Significant ETG-induced contributions to anomalous Âe confirmed with global gyrokinetic code GTS
Strong energy coupling to electron version of GAM (very high-ω ZF)
W.X. Wang et al., PoP (2015)

## Slide 14: Large ELM Event Induces Density Profile Steepening in the Core Region
After the ELM event:
  Large density gradient developed in the high-k measurement region.
  Electron temperature gradient also increases
  Electron density has only a moderate decrease
  Electron temperature remains essentially constant
No large MHD mode appears before and right after the ELM event
High-k measurement region
ELM event
Shot=140620

## Slide 15: Reduced ETG Turbulence Intensity and Electron Thermal Transport is Observed with Density Profile Steepening
Significant decrease in spectral power in electron-scale observed for
Electron thermal diffusivity is decreased by a factor of ~2 after the ELM event
See Y. Ren et al., PRL 2011, PoP 2012
Density gradient stabilization of high-k turbulence further confirmed in J. Ruiz-Ruiz et al., PoP 2015
High-k region

## Slide 16: Nonlinear ETG Simulations Reproduce Observed Dependence of Electron Transport on Density Gradient
Experimental Qe is found to decrease after the ELM event with large density gradient
The same trend is found from nonlinear ETG simulations, but does not agree quantitatively
Nonlinear GYRO ETG simulations with: local general equilibrium, kinetic ions and electrons, collisions, electromagnetic, flow and flow shear
experiment
simulations

## Slide 17: Predicted Qe is Sensitive to Electron Temperature Gradient
Before ELM, a 20-30% increase in a/LTe is able to match the experimental Qe
After ELM, increasing a/LTe by 40% after still cannot match experimental Qe

## Slide 18
Fast-ion-driven Alfven eigenmodes in the core region of NSTX high-power H-mode plasmas
Core flat region
Core gradient region
T

## Slide 19: Core Te Flattening in High-power NBI H-mode Plasmas is Observed to be Correlated with *AE Activities
Core Te flattening correlated with NBI power
  No simultaneous increase in central Te
Almost a factor of 10 increase in core Âe (r/a~0.2)
  Âe calculated with TRANSP power balance analysis
D. Stutman et al., PRL (2009)
CAEs/

## Slide 20: Core Te Flattening in High-power NBI H-mode Plasmas is Observed to be Correlated with *AE Activities
Core Te flattening correlated with NBI power
  No simultaneous increase in central Te
Almost a factor of 10 increase in core Âe (r/a~0.2)
  Âe calculated with TRANSP power balance analysis
  Consistent with stochastic electron thermal transport induced by Alfvenic eigenmode (GAE and/ CAE)

## Slide 21: Core Te Flattening in High-power NBI H-mode Plasmas is Observed to be Correlated with *AE Activities
Core Te flattening correlated with NBI power
  No simultaneous increase in central Te
Almost a factor of 10 increase in core Âe (r/a~0.2)
  Âe calculated with TRANSP power balance analysis
  Consistent with stochastic electron thermal transport induced by Alfvenic eigenmode (GAE and/ CAE)
Coupling of CAEs with KAWs, an alternative explanation
E. Belova et al., PRL (2015)

## Slide 22: Decrease in *AE Activity Measured by BES Corresponds with Peaking of Central Electron Temperature
Te remains peaked even with large single mode (bulk *AE still largely suppressed)
  Consistent with both mechanisms

## Slide 23: Improved Capabilities of NSTX-U will Strongly Support the Study of Electron Thermal Transport
Doubled BT, IP and NBI-heating power
  3-6 times lower in ne*; flow/q profile control
More details presented by J. Menard on Monday

## Slide 24: Improved Capabilities of NSTX-U will Strongly Support the Study of Electron Thermal Transport
Doubled BT, IP and NBI-heating power
  3-6 times lower in ne*; flow/q profile control
A new FIR high-kθ scattering system being designed at UC-Davis
  To be installed for FY17 run campaign

## Slide 25: Improved Diagnostics on NSTX-U will Strongly Support the Study of Electron Thermal Transport
Micro-tearing turbulence gyrokinetic simulation
Doubled BT, IP and NBI-heating power
  3-6 times lower in ne*; flow/q profile control
A new FIR high-kθ scattering system being designed at UC-Davis
  To be installed for FY17 run campaign
A DBS/CPS system will be installed for FY17 run campaign
  Measure ion-scale turbulence
  Able to measure magnetic fluctuations (CPS)
48 BES channels are now available on NSTX-U
  16 more than NSTX

## Slide 26: NSTX-U T&T Research Plan Aims to Identify Operational Regimes of Instabilities Responsible for Electron Thermal Transport
Near-term plan
  Identify dominant modes in lower ne* H-mode plasmas of NSTX-U
  Characterize low/high-k turbulence and electron thermal transport in isolated regimes of micro-instabilities guided by GK simulations
  BES/reflectometry for CAE/GAE measurements with a range of BT, Ip, ne* and PNBI, coupled with ORBIT code
  Cold pulse propagation (Laser Blow-off and ME-SXR) for profile stiffness
  Couple with turbulence diagnostics, GK simulations and experimental tools
Long term plan
  Identify operational regimes of ETG, microtearing, AE (CAE/GAE) and ITG/TEM/KBM using the full set of turbulence diagnostics
  Expand turbulence and electron thermal transport parametric dependence, e.g. on , ½*, Ti/Te and Zeff
  Study electron thermal transport and turbulence in long pulse and fully non-inductive scenario
  Develop physics-based reduced models for electron thermal transport

## Slide 27: Summary
NSTX has made significant progress towards understanding anomalous electron thermal transport
  First nonlinear gyrokinetic simulation of microtearing turbulence to produce experimental confinement scaling and transport in NSTX H-mode plasmas
  ETG turbulence driving electron thermal transport in L and H-mode plasmas, supported by linear and nonlinear gyrokinetic simulations
  *AE-induced core Te flattening, consistent with electron stochastic transport from ORBIT simulations and the coupling between CAEs and KAWs
Electron thermal transport will be the key part of the transport and turbulence research plan for NSTX-U
  Ip ~2 MA, BT ~1 T, 2nd NBI (~12 MW), a suite of turbulence diagnostics, e.g. new high-k scattering system and DBS/CPS

## Slide 28
Backup slides

## Slide 29: Beam Emission Spectroscopy (BES) Diagnostic Provides the Capability of Measuring Internal *AE Mode Structure
32 detection channels for NSTX and to be upgraded to 48 channels for NSTX-U
56 sightlines in radial and poloidal arrays spanning core to SOL
2 MHz sampling
k┴ri ≤ 1.5 & 2-3 cm spot size
Field-aligned optics with high throughput (etendue = 2.3 mm2-ster)
neutral beam Da emission
density
fluctuation
C ≈ 1/2
D.R. Smith et al., Rev. Sci. Instrum (2010)

## Slide 30: Threshold Gradients for ETG modes are much Higher after the ELM
Before ELM, ETG is largely unstable
After ELM, ETG is largely stable
Stability analysis performed with GS2 code (Kotschenreuther et al., 1995)

## Slide 31: Increase in ETG Threshold Gradient is due to Large Density Gradient
Stability analysis performed with GS2 code (Kotschenreuther et al., 1995)
Before ELM, ETG is largely unstable
After ELM, ETG is largely stable
Manually decreasing R/Lne brings down critical gradient as expected from linear theory (e.g. Jenko et al, 2001)

## Slide 32: ETG Turbulence Stabilization by Reversed Magnetic Shear is Responsible for ITB Formation
k┴re  0.1-0.2
HHFW only with beam blips
Yuh et al., NF 2009 and PRL 2011

## Slide 33: ETG Turbulence Stabilization by Reversed Magnetic Shear is Responsible for ITB Formation
HHFW only with beam blips
Yuh et al., NF 2009 and PRL 2011
k┴re  0.1-0.2

## Slide 34: ETG Turbulence Stabilization by Reversed Magnetic Shear is Responsible for ITB Formation
HHFW only with beam blips
Minimal ExB shearing rate due to cold ions with low toroidal rotation
Magnetic shear alone suppresses electron turbulence
Yuh et al., NF 2009 and PRL 2011
k┴re  0.1-0.2

## Slide 35: Predicted Qe is Sensitive to Electron Temperature Gradient
Before ELM, a 20-30% increase in a/LTe is able to match the experimental Qe
After ELM, increasing a/LTe by 40% after still cannot match experimental Qe

## Slide 36: Trapped Electron Mode (TEM) Destabilized by Large Density Gradient may Contribute to Transport
Before ELM, a 20-30% increase in a/LTe is able to match the experimental Qe
After ELM, increasing a/LTe by 40% after still cannot match experimental Qe
Large TEM-induced transport (~30 MW) is predicted after ELM without EB shear stabilization
Using experimental EB shear almost completely suppresses transport
 does not require much residual transport to match experimental Qe
~30 MW