| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: Ohmic H-Modes |
| OP-XP-1039 | Revision: 1 | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: S. Kubota | Date |
| ATI – ET Group Leader: | Date |
| RLM - Run Coordinator: | Date |
| Responsible Division: Experimental Research Operations |
| RESTRICTIONS or MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: Ohmic H-Modes | No. OP-XP-1039 |
| --- | --- |
| AUTHORS: S. Kubota, K.C. Lee, R. Maingi, S.J. Zweben, R.J. Maqueda, R.E. Bell, B.P. LeBlanc, S.M. Kaye, T.S. Hahm | DATE: July 27, 2010 |

# 1.	Overview of planned experiment

This experiment revisits Ohmic H-modes (similar to XP-506) with new and upgraded turbulence diagnostics.  The purpose is to study turbulence in the L-mode phase, H-mode phase, and at the L-H transition, with the goal of correlating both local (edge) and non-local (core) turbulence behavior with the ETB formation.  Comparisons will be made with existing L-H transition theories, including K.C. Lee’s gyrocenter shift theory.

# 2.	Theoretical/ empirical justification

Ohmic H-modes offer a good template for studying the L-H transition: 1) peaked density profiles provide good targets for the reflectometers, 2) there are no fast-ion driven fluctuations to complicate turbulence measurements, and 3) we avoid complicating physics due to external momentum input and hot fueling.  In addition, several upgraded and new turbulence diagnostics are available for 2010.

# 3.	Experimental run plan

(1)  Re-establish Ohmic H-mode shot similar to 129693 with GPI gas puff on.  Adjust fueling gas puff to reach target edge electron density of 1.5x1013 cm-3.  Use slight Ip rampdown if necessary for reproducible L-H transition.   (4 shots)

(2)  Set target conditions and take data.   (6 shots)

Settings for the poloidal correlation reflectometer will be adjusted.

- Reflection layer ~ETB radius.		(2 shots)

- Reflection layer outside ETB radius.		(2 shots)

- Reflection layer inside ETB radius.		(2 shots)

(3)  Switch from LSN to DND configuration.  Establish stable target with appropriate density and reproducible L-H transition, as in (1).  Poloidal correlation reflectometer set to best position from (2).     (2-6 shots)

(4)  If time permits, take data at the two other poloidal correlation reflectometer settings from (2).           (4 shots)

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

A well conditioned chamber with low recycling is necessary.  The lead diagnostics are the reflectometers (FMCW, correlation, and fixed-frequency) and GPI.  Other required diagnostics are the ERD, MPTS, CHERS (passive), FIReTIP and the divertor calibrated Da camera.  Additional requested diagnostics are BES, high-k, USXR, edge probes, and ME-SXR (available Aug-Sept?).

A constant BT/Ip scan in an L-mode target, either Ohmic or low power NBI (below AE triggering threshold) will help to frame the results of this XP.  These conditions may be achieved in S.J. Zweben’s XP proposal or XP-1038.

Reflectometry is a radar diagnostic that is strongly affected by the shape (curvature and asymmetry) of the reflecting layer.  An XMP with combined scans of the magnetic axis vertical position and  are required for definitive quantitative estimates of turbulence properties from this XP.

# 5.	Planned analysis

EFIT, LRDFIT, TRANSP, edge and core gyro-kinetic codes.  Analysis of reflectometry data will require the use of 1D and 2D UCLA full-wave codes.  Analysis of passive CHERS measurements and estimates of the edge neutral density from calibrated Da measurements are also necessary.

# 6.	Planned publication of results

This XP combines several new and unique diagnostic capabilities for  looking at turbulence, which should yield several publications: PRL, PPCF, PoP, RSI.

PHYSICS OPERATIONS REQUEST

| TITLE: Ohmic H-Modes | No. OP-XP-1039 |
| --- | --- |
| AUTHORS: S. Kubota, K.C. Lee, R. Maingi, S.J. Zweben, R.J. Maqueda, R.E. Bell, B.P. LeBlanc, S.M. Kaye, T.S. Hahm | DATE: |

(use additional sheets and attach waveform diagrams if necessary)

Brief description of the most important operational plasma conditions required:

Previous shot(s) which can be repeated: Previous shot(s) which can be modified:

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): 53 Flattop start/stop (s): 0.0/0.6 IP (MA): 0.9 Flattop start/stop (s): 0.2/0.6 Configuration: DN / LSN Equilibrium Control: Outer gap / Isoflux (rtEFIT) / Strike-point control (rtEFIT) Outer gap (m): Inner gap (m): Z position (m): 0.0 Elongation: Triangularity (U/L): OSP radius (m): Gas Species: Injector(s): NBI Species: D Voltage (kV) A: B: C: Duration (s): ICRF Power (MW): Phase between straps (°): Duration (s): CHI: Off / On Bank capacitance (mF): LITERs: Off / On Total deposition rate (mg/min): LLD: Temperature (°C): EFC coils: Off/On Configuration: Odd / Even / Other (attach detailed sheet)

DIAGNOSTIC CHECKLIST

| TITLE: Ohmic H-Modes | No. OP-XP-1039 |
| --- | --- |
| AUTHORS: S. Kubota, K.C. Lee, R. Maingi, S.J. Zweben, R.J. Maqueda, R.E. Bell, B.P. LeBlanc, S.M. Kaye, T.S. Hahm | DATE: |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Beam Emission Spectroscopy |  | √ |
| Bolometer – divertor |  |  |
| Bolometer – midplane array |  |  |
| CHERS – poloidal | √ |  |
| CHERS – toroidal | √ |  |
| Dust detector |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  |  |
| Edge pressure gauges |  |  |
| Edge rotation diagnostic | √ |  |
| Fast cameras – divertor/LLD |  |  |
| Fast ion D_alpha - FIDA |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes |  |  |
| FIReTIP | √ |  |
| Gas puff imaging – divertor |  |  |
| Gas puff imaging – midplane | √ |  |
| H camera - 1D | √ |  |
| High-k scattering |  | √ |
| Infrared cameras |  |  |
| Interferometer - 1 mm |  |  |
| Langmuir probes – divertor |  |  |
| Langmuir probes – LLD |  |  |
| Langmuir probes – bias tile |  |  |
| Langmuir probes – RF ant. |  |  |
| Magnetics – B coils | √ |  |
| Magnetics – Diamagnetism |  |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes |  |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents |  |  |
| Magnetics – RWM sensors |  |  |
| Mirnov coils – high f. | √ |  |
| Mirnov coils – poloidal array | √ |  |
| Mirnov coils – toroidal array | √ |  |
| Mirnov coils – 3-axis proto. |  |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE |  |  |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron detectors |  |  |
| Plasma TV |  |  |
| Reflectometer – Q-Band | √ |  |
| Reflectometer – correlation | √ |  |
| Reflectometer – FM/CW | √ |  |
| Reflectometer – V-Band | √ |  |
| Reflectometer – SOL | √ |  |
| RF edge probes |  |  |
| Spectrometer – divertor |  |  |
| Spectrometer – SPRED |  |  |
| Spectrometer – VIPS |  |  |
| Spectrometer – LOWEUS |  |  |
| Spectrometer – XEUS |  |  |
| SWIFT – 2D flow |  |  |
| Thomson scattering |  |  |
| Ultrasoft X-ray – pol. arrays |  | √ |
| Ultrasoft X-rays – bicolor |  |  |
| Ultrasoft X-rays – TG spectr. |  |  |
| Visible bremsstrahlung det. |  |  |
| X-ray crystal spectrom. - H |  |  |
| X-ray crystal spectrom. - V |  |  |
| X-ray tang. pinhole camera |  |  |