## Slide 1: Controlled Snowflake Studies
P. Vail, E. Kolemen

## Slide 2
We request multiple days with a few shots each
  This will allow fixing code and updating control in between tests
Independent control for lower and upper SFD (two different days)
  Control of snowflake radius, angle, and combined control (radius + angle).
  Snowflake centroid control PF1AL, PF1CL, and PF2L (+upper coils)
  Show we can achieve the SFD-, SFD+, SFD with varying parameters with minimal coil perturbation
Combined upper and lower SFD using PF coils.
  Checking out the 4 X-points are calculated consistently.
Solving issues related to integration of upper and lower SFD control with the full shape control
  Inner gap control coupling, drsep and vertical control coupling
XP1508: Controlled Snowflake Studies

## Slide 3: Snowflake control system
Block diagram of NSTX-U snowflake control system.
First implemented at the DIII-D tokamak.
Kolemen et al., JNM 2015.

## Slide 4: Snowflake locator
Need one-step algorithm for approximating location of two x-points
Local expansion of the flux function in the Grad-Shafranov equation to third-order*
*Based upon Ryutov et al. Plasma Physics and Controlled Fusion (2010).

## Slide 5: Calculate the expansion coefficients
Magnetic Field at 3 points
Six unknown coefficients
Six equations
Control parameters: radius, angle, centroid.

## Slide 6: Snowflake controller
Control coils
Snowflake parameters
Need to find control matrix M

## Slide 7: Snowflake control simulation
Using TokSys toolbox developed by General Atomics.
Set of MATLAB functions and scripts for tokamak modeling (including plasma control).
Grad-Shafranov solver for plasma equilibria + additional tools.
Wrote scripts for calculating snowflake location and control Jacobian.
Can run various simulations from different initial equilibria.

## Slide 8: Snowflake Control Simulation - initial equilibrium
The starting point for snowflake control simulation for NSTX-U is an equilibrium with an upper and lower snowflake divertor designed using the TokSys toolbox from General Atomics.

## Slide 9: Initial equilibrium - PF coil currents

## Slide 10
Phase 1: Independent control for upper and lower SFD.
  Control of snowflake radius, angle, and combined control (radius + angle).
  Achieved and controlled upper and lower SFD using PF coils.
  Majority of development work thus far performed for lower SFD using PF1AL, PF1CL, and PF2L coils for control.
  Further development needed for snowflake centroid control.
Phase 2: Integrated control of upper and lower SFD.
Snowflake Control - Development Plan

## Slide 11: Snowflake Radius Control
Scenario: Scan the snowflake radius from ~12 cm to ~3 cm at a constant angle in the snowflake minus configuration.

## Slide 12: Snowflake Radius Control

## Slide 13: Snowflake Radius Control - coil currents with theta control engaged

## Slide 14: Snowflake Radius Control

## Slide 15: Snowflake Radius Control - Perfect Snowflake
Scenario: Scan the snowflake radius from ~12 cm to ~0 cm (perfect snowflake).

## Slide 16: Snowflake Radius Control - Perfect Snowflake

## Slide 17: Snowflake Radius Control to Perfect Snowflake

## Slide 18: Snowflake Angle Control
Scenario: Scan from a snowflake minus (theta ~ 120°) to a snowflake plus (theta ~ 30°) configuration at constant x-point separation (rho).

## Slide 19: Snowflake Angle Control

## Slide 20: Snowflake Angle Control - coil currents with rho control engaged

## Slide 21: Snowflake Angle Control

## Slide 22: Snowflake Control - Upper Divertor
Similar control simulation has been performed for upper SFD.
Change Radius
Change Radius
Change Angle
Change Angle

## Slide 23: Snowflake Control - Upper Divertor

## Slide 24
Relay Feedback and X-point Height Control
Egemen Kolemen
S. Gerhardt and D. A. Gates
2010 Results Review
Nov/30/2010
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 25: 2009 Run: Experimental System ID (Open Loop)
System Id: Identify the effect of the actuator on the boundary shape.
Reaction Curve Method
From Step Response obtain:
  Time delay, rise time
  and size of change gives
  the control tuning parameters.
P
Time

## Slide 26: 2009 Run: Experimental System ID (Open Loop)
System Id: Identify the effect of the actuator on the boundary shape.
Reaction Curve Method
Problem:
  Many shots needed
  Need the actuator in open loop.
  Not precise
P
System Id results from 2009 run

## Slide 27
Advantages:
  Only a single experiment is needed.
  Closed loop:
    More stable
    Enable system ID for actuators that can’t be open loop (for example: vertical control)
Control
Output
Process
Output
The closed-loop plant response period (Pu) & amplitude (A) are used for PID controller tuning.
Experimental System ID: Closed Loop Auto-tune with Relay Feedback


## Slide 28: Experimental System ID: Closed Loop Auto-tune with Relay Feedback
Advantages:
  Only a single experiment is needed.
  Closed loop:
    More stable
    Enable system ID for actuators that can’t be open loop (for example: vertical control)
Control
Output
h
Pu
A
The closed-loop plant response period (Pu) & amplitude (A) are used for PID controller tuning.
Process
Output


## Slide 29
Tuned via Relay-Feedback.
Achieved RMS <1 cm X-point height error and <2 cm SP.
Scenario used for LLD experiments.
Successful Developed Combined X-point Height / SP Control
Evolution of Plasma Boundary: X-point height roughly constant as OSP ramps

## Slide 30
The main issue will be inner gap (Coupling with other controls needed)
Then, move to other shape parameters
If time Permits Start Working on the
Full Multiple-Input-Multiple-Output (MIMO) Control
-Inner Gap
-Lower Inner Strike Point
-Vertical Position
-Squareness
Upper X-point Height …

## Slide 31: Implementation of the MIMO Control
We will compare the toksys MIMO control design to previous year method based on PID tuning based on three parameters (Kolemen, NF 2010)
In this method, we use K, the DC gain (obtained from ISOLVER), L the delay in the system (known parameter), T the rise time of flux response to the voltage input. The only unknown here is the T which is a function of the Tcoil and Tplasma. Tcoil is known (Inductance/Res.), Tplasma (wall penetration time) can be guessed based on previous experiments.
IPF2 versus Rosp location via ISOLVER
simulations. DC Gain (ΔRosp/ΔIPF2)
Can be obtained via these simulations.
Sample Tuning based on the
K (DC gain), T (Rise time), L (Delay)

## Slide 32: X-Point R, Z Control: Time required ~Two ½ Days
Use PF1/2 coils
Should be able to determine gains with 4-6 shots on one day to measure system response and 5-10 shots to demonstrate gains
Practical limits on RX and ZX range will require about 8 shots each to determine
Tuning the other shape controls:
  Start Initial Design of the full shape control
  Attention to vertical stability and inner gap