## Slide 1
1: ASC “Theory and Computation” Prep
2: NSTX-U Five Year Plan Discussion
SPG
NSTX
Supported by
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
NFRI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin

## Slide 2: Goals of NSTX Advanced Scenario and Control TSG are Complicated and Divisions with other TSGs Sometimes a Bit Arbitrary
Study, implement, optimize axisymmetric control techniques.
  Kinetic and magnetic profiles.
  Boundary and divertor magnetic geometry control.
  Vertical position control.
Combine various tools developed in other TSGs into integrated scenarios.
  For instance, ELM pacing XPs targeting density control were in ASC.
  Impurity control for scenario development in FY-10.
High non-inductive fraction under NB heating has been in ASC.
  Typically coupled with optimization to high-k.
  NBCD is ASC, but details of fast ion transport & redistribution are WEP
  However
    RF CD and low-current 100% NI scenarios with HHFW H&CD have historically been in WEP TSG.
    Maximization of bN part of ASC, but more in MS.
Discharge development for the NSTX team (sometimes).

## Slide 3: Two Overarching Theory/Modeling Needs
1: Need advanced control algorithms for boundary shape, divertor geometry, kinetic and magnetic profiles, and divertor heat fluxes.
  Should include actuator saturation.
2: In order to tune those control algorithms, need fast, benchmarked models for how sources of particles, momentum, heat and current modify the kinetic and magnetic profiles and free-boundary equilibrium.

## Slide 4: Need #1: Models for Scenario Development
NBCD with *AE modes
  In the absence of low-f MHD, the neutral beam drive current can apparently be explained using classical physics alone.
  At higher values of bfast, *AE modes can lead to redistribution/modification of the fast ion distribution.
  Theory is needed for when these modes will turn on, and what their effect on the pressure & current profile will be.
  Need measurements of fast ion distribution (FIDA, neutrons, ssNPA, fusion product detector) and NBCD profile.
Prediction of the thermal transport
  The bootstrap current depends sensitively on the gradients in the thermal profiles. NBCD depends on Te/ne.
  Conversely, the transport, and hence thermal profiles, can be a strong function of the current profile shape.
  It is critical to have a model for the thermal transport and its response to heating and current drive actuators.
  Include both core & pedestal (and the joining region), including fast-ion MHD leading to transport.
Need accurate, benchmarked models for HHFW and EBW H&CD within integrated codes such as TRANSP.

## Slide 5: Need #2: Realtime Control
Need a reliable algorithm for the individual and combined control of the current and rotation profiles, along with bN.
  The theory of that algorithm should help us to understand to what extent these quantities can be independently controlled given the coupled actuators Vloop, Pinj, JNBCD, TNB and TNTV.
More generally, need the ability to test the actual control algorithms in simulations with high degrees of physics fidelity, i.e. flight simulator mode.
  Could in principle be accomplished by connecting PCS to PTRANSP, CORSICA, or TSC.
Need the ability to predict the future equilibrium and stability properties of the plasma.
  Faster than realtime look-ahead of the evolution of the equilibrium
    (Very) reduced transport models.
  Stability assessments of those future states (n=0, n=1, ELM?). Future coil currents and boundary shape.
  Control intervention based on the predictions.

## Slide 6: 5-year Plan Prep

## Slide 7: Propose Four Interrelated Thrusts in the 5-Year Plan
High-Performance Discharge Development
Axisymmetric Control
Scenario Optimization For Next-Step STs
Off-Normal Event Detection and Handling

## Slide 8: Thrust #1: High Performance Discharge Optimization
100% non-inductive scenarios (ASC).
  Begin at ~0.7 T, Ip=600-700 kA.
  Increase the non-inductive current level/duration as the allowed toroidal field increases.
High Current (~2 MA) scenarios (ASC,BP).
  Start at ~1400 kA, BT=0.7 T.
  Increase the current level as the allowed toroidal field increases and the heat flux mitigation strategies are developed.
  Optimize startup for reduced density
    Ramp-rate, fuelling scheme, H-mode timing.
  Increased current contingent on:
    Timing of high-current and high-field operation.
    Timing on the TF conductor upgrade.
    Progress on heat flux mitigation
    Event handling and disruption avoidance.
Couple non-inductive startup to high-performance steady state (ASC, WEP, SFSU).
  NBCD ramp-up studies, including effect of *AE.
  Boundary and profile control during ramp-up.
HHFW & EBW Integration (ASC, WEP)

## Slide 9: Thrust 2: Axisymmetric Control Development Elements
Improved vertical position control (ASC):
  Better vertical motion detection
  Additional coils in the vertical control loop (biased or bi-polar PF-2?)
MIMO Boundary Control (ASC):
  Off-diagonal elements of the M-matrix.
  Better inner-gap control, more generic shape controllers.
Snowflake Divertor Control (ASC, BP):
  Multiple X-point finding.
  New control matrix for divertor parameters.
  Develop better general understanding of SFD controllability.
Profile control (ASC, MS, T&T):
  Parameterize the effect of different NB tangency on the q-profile.
  J or P profile control using Pinj, Vloop (and outer gap?) as actuators.
  Rotation profile control using Pinj, TNTV as actuators.
  Compatibility with each other and with bN control

## Slide 10: Thrust 2: Axisymmetric Control Development Elements
Divertor power control (ASC, BP).
  Radiative divertor control.
    BP needs to provide realtime diagnostics and quantify the actuator response (gas puffing impact).
    Need plan for new gas injectors in upper & lower divertors.
  Heat-flux based magnetic balance control.
    BP needs to provide the realtime heat flux.
Density control (ASC, BP).
  Need either realtime MPTS or an interferometer
    MPTS more generically useful, but interferometer much faster.
  Use SGI as an actuator.
    Other fuelling sources can be used as they are developed.

## Slide 11: Thrust 3: Scenario Optimization For Next-Step Devices
Optimal q-profile and rotation profiles (ASC, MS, T&T).
  Rotation profile impacts thermal transport, RWM and tearing stability.
  q-profile impacts thermal transport, kink/tearing stability.
  Effects may not be complementary:
    Elevated qmin might be bad for transport, good for tearing.
    Reversed shear and ITBs are good for transport, bad for stability.
  Utilize feedback control to stay in these optiman states.
    Or feedforward control if feedback is not so hot.
Conditions for classical NBCD (ASC, WEP).
  Test NBCD vs. classical predictions as a function of bfast, q-profile, Vfast/VA.
  Determine the degree to which next-step devices can operate in a regime with classical NBCD.
Validation of integrated models (ASC, WEP, T&T).
  T&T TSG to be working on reduced models for thermal transport.
  WEP TSG to be working fast ion transport from *AE modes.
  Test the integrated predictions against the measured discharge evolution.
  If reasonable, begin projection to FNSF.

## Slide 12: Thrust 4: Off-Normal Event Detection and Response
Disruption detection (ASC, MS).
  Use realtime diagnostics to predict imminent disruptions.
  Start with RWM sensors, and then add more as necessary.
    Neutrons, MPTS.
  Consider realtime RFA measurements?
PSRTC and/or PCS will be used to detect approaches to current/force/I2t limits (ASC).
Develop off-normal event handling infrastructure (ASC).
  Process data from both the coil limits and disruption detection.
  Start with Ip rampdowns based on imminent limit/disruption.
  Develop more sophisticated responses.
    Rampdown in the presence of a large n=1 mode may need to be different?
    Modification of coil current requests based on approach to current limits?