## Slide 1: Initial error field correction studies in the National Spherical Torus Experiment Upgrade
Clayton E. Myers1, S. P. Gerhardt1, J. E. Menard1, N. M. Ferraro1, J.-K. Park1, R. E. Bell1, B. P. LeBlanc1, M. Podestà1, and S. A. Sabbagh2
APS-DPP 2016
San Jose, California
November 1, 2016
1Princeton Plasma Physics Laboratory, 2Columbia University

## Slide 2: Error field correction is key to achieving high performance
Error field correction (EFC) objectives:
  Probe the plasma response to applied 3D fields
  Near-term empirical EFC prescription
  Error field source identification
EFC sensors and actuators in NSTX-U:
  Four sets of 3D magnetic field sensors with 12 toroidal locations each (BP/BR, Upper/Lower)
  Six midplane EFC coils to apply n=1,2,3 fields simultaneously  new capability for NSTX-U

## Slide 3: Candidate error field sources in NSTX-U
Candidate error field sources:
  Non-circularity of the main vertical field coil (PF5)
  Non-axisymmetry of vessel eddy currents
  Tilt of the TF coil from the vertical
  Tilt of the OH coil from the vertical
  Time-dependent OH×TF interaction [see right]
Error field identification techniques:
  Plasma-like vacuum shots
  Feed-forward EFC coil currents
  Compass scans (n = 1)
Menard et al. Nucl. Fusion 2010

## Slide 4: OH×TF interaction definitively ruled out
In NSTX, time-dependent OH×TF error field due to OH lead geometry
Designed out of NSTX-U with coaxial OH lead assembly [Menard NF 2012]
Compare plasma-like vacuum shots:
  In NSTX, OH×TF error field visible in dBR as IOH swings negative
  In NSTX-U, no such OH×TF error field is measured

## Slide 5: Seek initial n = 1 EFC with PF5-proportional 3D fields
Apply n = 1 fields at fixed phase
Set amplitude proportional to the main vertical field (PF5)
Locking events visible in the density and in dBP

## Slide 6: Seek initial n = 1 EFC with PF5-proportional 3D fields
Apply n = 1 fields at fixed phase
Set amplitude proportional to the main vertical field (PF5)
Locking events visible in the density and in dBP

## Slide 7: Feed-forward phase scan: f = 135°
Apply n = 1 fields at fixed phase
Set amplitude proportional to the main vertical field (PF5)
Locking events visible in the density and in dBP
Applied field phase scan:
  Optimum phase = 135°

## Slide 8: Feed-forward amplitude scan: IEFC = 600 A
Apply n = 1 fields at fixed phase
Set amplitude proportional to the main vertical field (PF5)
Locking events visible in the density and in dBP
Applied field phase scan:
  Optimum phase = 135°
Applied field amplitude scan:
  Optimum amplitude = 600 A
  Proportional to PF5

## Slide 9: Long-pulse L-mode scenario established after implementing PF5-proportional EFC
Quickly established a robust 1 MW beam-heated L-mode scenario
Ip = 800 kA with flat density evolution and quiescent dBP
The discharge terminates at ~1.7 sec due IOH limit

## Slide 10: Refine optimum EFC with an n = 1 compass scan
Compass scan steps:
Select n = 1 phase
Ramp n = 1 amplitude until the discharge terminates

## Slide 11: Refine optimum EFC with an n = 1 compass scan
Compass scan steps:
Select n = 1 phase
Ramp n = 1 amplitude until the discharge terminates

## Slide 12: Refine optimum EFC with an n = 1 compass scan
Compass scan steps:
Select n = 1 phase
Ramp n = 1 amplitude until the discharge terminates
Repeat at multiple phases

## Slide 13: The optimum phase shifts from 135° to 80°
Optimum EFC:
f = 80° (prev. 135°)
IEFC = 550 A (prev. 600 A)
Compass scan steps:
Select n = 1 phase
Ramp n = 1 amplitude until the discharge terminates
Repeat at multiple phases
Fit circle to locking points
The optimum EFC is located at the center of the circle

## Slide 14: Additional compass scans confirm the optimum EFC
Higher density
Same optimum EFC
Rotation dominates the density scaling?
Different OH flux state
Same optimum EFC
Eliminates the OH as a major error field source
Original compass scan
Optimum amplitude: 550 A
Optimum phase: 80°

## Slide 15: High performance H-modes achieved after implementing compass-scan-optimized EFC
Minimal core MHD
H98y,2 ≥ 1
βN/βno-wall ≥ 1

## Slide 16: A different EFC phase is required early in time
A static applied n = 1 phase scan early in time shows a different optimum EFC phase
The optimum flattop phase of 80° is counter-productive early
The phase asymmetry is visible in the density and core rotation
Continue to search for the time-evolving error field source

## Slide 17: Optimized EFC enables long-pulse L-modes and high-performance H-modes in NSTX-U
Summary:
  Identified flattop EFC settings that enable long-pulse L-modes and high-performance H-modes
  Eliminated two candidate error field sources:
    OH×TF interaction
    Tilt of the OH coil from the vertical
  Identified an asymmetry in the optimum early time EFC with respect to the optimum flattop EFC
More analysis and metrology are ongoing:
  Multiple error field sources are in play (PF5 + ??)
  Suspect a static tilt of the TF bundle is contributing
  Time-dependent plasma response?