## Slide 1: Recent Progress in Understanding Electron Thermal Transport in NSTX and NSTX-U
Y. Ren1, E. Belova1, W. Guttenfelder1, N. Gorelenkov1, S.M. Kaye1,
E. Mazzucato1, W.X. Wang1, K. Tritz2, R.E. Bell1, B.P. LeBlanc1,
C.W. Domier3, D.R. Smith4, H. Yuh5, K.C. Lee6, and the NSTX-U Team
1. PPPL 2. JHU 3. UC-Davis 4. UW-Madison 5. Nova Photonics
6. NFRI
58th Annual Meeting of the APS Division of Plasma Physics, San Jose, California, October 31st - November 4th, 2016

## Slide 2: Outline
Introduction
Recent results on electron thermal transport in NSTX
  Micro-tearing turbulence in NSTX high-beta and high-collisionality H-mode plasmas
  ETG turbulence in NSTX L and H-mode plasmas
  Fast-ion-driven Alfven eigenmodes in the core region of NSTX high-power H-mode plasmas
NSTX-U Plans for electron thermal transport
Summary

## Slide 3: Spherical Tokamaks Have Some Significant Advantages over Conventional Tokamak
The low aspect ratio of spherical tokamaks leads to improved ¯ limit than conventional tokamaks
  More compact and lower-cost future devices, e.g. Fusion Nuclear Science Facility (FNSF) and power plant
The effective shaping and/or strong ExB shear from low aspect ratio lead to reduced ion-scale turbulence
  Neoclassical ion thermal transport and different confinement scaling for H-mode plasmas

## Slide 4: NSTX Thermal Confinement Has Strong Collisionality Scaling in H-mode Plasmas
Ion transport is neoclassical, consistent with strong flow shear and strong shaping
The confinement scaling is determined by electron thermal transport
NSTX
MAST
Valovič et al.,Nucl. Fusion, 2013
ITER
Doyle et al., Nucl.Fusion 2007
Kaye et al., Nucl. Fusion, 2007
Neoclassical transport by GTC-NEO

## Slide 5: Multiple Mechanisms should be Responsible for Anomalous Electron Thermal Transport
Different mechanisms needed to account for the always anomalous electron thermal transport
  Different radial regions
    Core flat region (small gradient drive)
    Core gradient region (large gradient drive)
    Edge region (steepest gradient, connection to SOL, e.g. H-mode pedestal)
  Different parametric regimes
    Large/small plasma beta/collisionality, magnetic shear, ExB shear, etc.
Evidence exists for gradient driven electrostatic and electromagnetic ballooning drift instabilities:
  Low-k (ion-scale): ITG/TEM/KBM/microtearing modes
  High-k (electron-scale): ETG modes
  Turbulent ExB drift and magnetic flutter effects
Fast ion driven Alfvenic eigenmodes found relevant
  GAE and/or CAE modes
  Alfvenic eigenmode induced electron drift orbit stochasticity
Core flat region
Core gradient region
Edge region
r
T

## Slide 6
First nonlinear gyrokinetic simulation of micro-tearing turbulence in high-collisionality and high-beta H-mode plasmas
Core flat region
Core gradient region
r
T

## Slide 7: Microtearing Modes are Found to be Unstable in Many High n* H-mode Discharges
Microtearing dominates over r/a=0.5-0.8, kqrs<1 (n5-70)
Real frequencies in electron diamagnetic direction, w  w*e = (kqrs)(a/Ln+a/LTe)(cs/a)
ETG mostly stable due to larger Zeff3, (R/LTe)crit,ETG~(1+ZeffTe/Ti)
electron diamagnetic
direction
Real frequencies
Growth rates
Eigenfunctions in “ballooning” space
Linear GYRO simulations [Candy & Waltz, Phys. Rev. Lett. (2003); https://fusion.gat.com/theory/Gyro] using local general equilibrium, kinetic ions (D+C) and electrons, collisions, fully electromagnetic
BT=0.35 T, Ip=700 kA, PNBI=4 MW

## Slide 8: First Successful Nonlinear Microtearing Simulations for NSTX
dBr (Gauss)
BT0=3.5 kG
Movies at http://www.pppl.gov/~wgutten/
W. Guttenfelder et al., PRL (2011)
~98% of transport due to magnetic “flutter” contribution
wisland(n) > drrat(n), island overlap  perturbed field line trajectories are stochastic*
ce,EM =1.25 rscs2/a close to collisionless Rechester-Rosenbluth** (lmfp=12 m, Lc2.5 m)
*E. Wang et al., PoP (2011).
**A.B. Rechester & M.N. Rosenbluth, PRL (1978)

## Slide 9: Near Linear Scaling of Transport with ne Consistent with Experimental Scaling
As transport drops, a/LTe will increase (for fixed heat flux), at some point ETG (TEM/KBM?) should become important
This transition likely to determine limit of “favorable” n* scaling
Non-linear transport
NSTX experimental scaling
(Kaye et al., 2007)
WitE ~ n*-0.95

## Slide 10
ETG turbulence in NSTX L and H-mode plasmas
Core flat region
Core gradient region
r
T

## Slide 11: A High-k Microwave Scattering System was Used to Measure Electron-scale Turbulence in NSTX
Probe beam
Scattered light
Spherical mirror
kp
ks
Probe beam
θs
ki
D.R. Smith, PhD thesis, 2009
High-k turbulence measurement |  |  | 
 | r/a | Measured quantity | Spatial & temporal resolution
280 GHz microwave scattering system | ~0.2-1 from core to edge | Density fluctuation | 3 ≤ k┴ρs ≤ 12 R ~ ±2 cm f~ 5 MHz

## Slide 12: First Identification of ETG Turbulence in NSTX RF-heated L-mode Plasmas
The measured high-k turbulence is shown to be driven by electron temperature gradient (Mazzucato et al., PRL 2008, NF 2009).
  In RF-heated helium L-mode plasma (1.2 MW, 5.5 kG, 700 kA)
  Fluctuation propagates in the electron diamagnetic direction
  Clear reduction in turbulence spectral power at lower electron temperature gradient
Electron direction
W.X. Wang et al., PoP (2015)

## Slide 13: ETG Turbulence can Produce Experimentally Relevant Electron thermal Transport
Significant ETG-induced contributions to anomalous Âe confirmed with global gyrokinetic code GTS
Strong energy coupling to electron version of GAM (very high-ω ZF)

## Slide 14: Large ELM Event induces Density Profile Steepening in the Core Region
After the ELM event:
  Large density gradient developed in the high-k measurement region.
  Electron temperature gradient also increases
  Electron density has only a moderate decrease
  Electron temperature remains essentially constant
No large MHD mode appears before and right after the ELM event
High-k measurement region
ELM event
Shot=140620

## Slide 15: Reduced ETG Turbulence Intensity and Electron Thermal Transport is Observed with Density Profile Steepening
Significant decrease in spectral power in electron-scale observed for
Electron thermal diffusivity is decreased by a factor of ~2 after the ELM event
See Y. Ren et al., PRL 2011, PoP 2012
Density gradient stabilization of high-k turbulence further confirmed in J. Ruiz-Ruiz et al., PoP 2015
High-k region

## Slide 16: Nonlinear ETG Simulations Reproduce Observed Dependence of Electron Transport on Density Gradient
Experimental Qe is found to decrease after the ELM event with large density gradient
The same trend is found from nonlinear ETG simulations, but does not agree quantitatively
Nonlinear GYRO ETG simulations with: local general equilibrium, kinetic ions and electrons, collisions, electromagnetic, flow and flow shear
experiment
simulations

## Slide 17: Trapped Electron Mode (TEM) Destabilized by Large Density Gradient may Contribute to Transport
Before ELM, a 20-30% increase in a/LTe is able to match the experimental Qe
After ELM, increasing a/LTe by 40% after still cannot match experimental Qe
Large TEM-induced transport (~30 MW) is predicted after ELM without EB shear stabilization
Using experimental EB shear almost completely suppresses transport
 does not require much residual transport to match experimental Qe
~30 MW

## Slide 18: ETG Turbulence Stabilization by Reversed Magnetic Shear is Responsible for ITB Formation
HHFW only with beam blips
Minimal ExB shearing rate due to cold ions with low toroidal rotation
Magnetic shear alone suppresses electron turbulence
Yuh et al., NF 2009 and PRL 2011
k┴re  0.1-0.2

## Slide 19
Fast-ion-driven Alfven eigenmodes in the core region of NSTX high-power H-mode plasmas
Core flat region
Core gradient region
T

## Slide 20: Core Te Flattening in High-power NBI H-mode plasmas is Observed to be Correlated with *AE Activities
Core Te flattening correlated with NBI power
  No simultaneous increase in central Te
Almost a factor of 10 increase in core Âe (r/a~0.2)
  Âe calculated with TRANSP power balance analysis
  Calculated neutron rate with classical fast particle slowing-down in good agreement with measured neutron rate
Increased *AE (GAE/CAE) activity observed from edge Mirnov measurement
D. Stutman et al., PRL (2009)

## Slide 21: ORBIT Guiding Center Code is Used to Simulate GAE Effects on Electron Thermal Transport
(~3-6)

## Slide 22: Decrease in *AE Activity Measured by BES Corresponds with Peaking of Central Electron Temperature

## Slide 23: Study of Electron Thermal Transport will Benefit from Two New Capabilities of NSTX-U
q and flow profile control from larger tangency radius RTAN of 2nd NBI
  2x higher CD efficiency
100% non-inductive CD

## Slide 24: Improved Diagnostics on NSTX-U will Strongly Support the Study of Electron Thermal Transport
A new FIR high-kθ scattering system being designed at UC-Davis
  To be installed for FY17 run campaign

## Slide 25: Improved Diagnostics on NSTX-U will Strongly Support the Study of Electron Thermal Transport
A new FIR high-kθ scattering system being designed at UC-Davis
  To be installed for FY17 run campaign
A DBS/CPS system will be installed for FY17 run campaign
  Measure ion-scale turbulence
  Able to measure magnetic fluctuations (CPS)
48 BES channels are now available on NSTX-U
  16 more than NSTX
Micro-tearing turbulence gyrokinetic simulation

## Slide 26: Summary
NSTX has made significant progress towards understanding anomalous electron thermal transport
  First nonlinear gyrokinetic simulation of microtearing turbulence to produce experimental confinement scaling and transport in NSTX H-mode plasmas
  ETG turbulence driving electron thermal transport in L and H-mode plasmas, supported by linear and nonlinear gyrokinetic simulations
  *AE-induced core Te flattening, consistent with electron stochastic transport from ORBIT simulations; Alternative mechanism of coupling CAE to KAW also presented
Electron thermal transport will be the key part of the transport and turbulence research plan for NSTX-U
  Ip ~2 MA, BT ~1 T, 2nd NBI (~12 MW), a suite of turbulence diagnostics, e.g. new high-k scattering system and DBS/CPS