## Slide 1: Impact of physics and technology innovations on compact tokamak fusion pilot plants
Jonathan Menard (PPPL)
T. Brown, S. Gerhardt, R. Maingi, R. Majeski, Y. Zhai,
L. El-Guebaly (UW Madison), and the NSTX-U team
58th Annual Meeting of the APS Division of Plasma Physics
San Jose, California
October 31 - November 4, 2016

## Slide 2: Possible missions for fusion next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak - DTT
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe

## Slide 3: Possible missions for fusion next-steps
Integrate high-performance, steady-state, exhaust
  Divertor test-tokamak - DTT
Fusion-relevant neutron wall loading
  Gn ~ 1-2MW/m2, fluence: ≥ 6MW-yr/m2
Tritium self-sufficiency
  Tritium breeding ratio TBR ≥ 1
Electrical self-sufficiency
  Qeng = Pelectric / Pconsumed ~ 1
Large net electricity generation
  Qeng >> 1, Pelectric = 0.5-1 GWe
This talk: assess possible innovations to achieve these missions in a single and more compact tokamak device

## Slide 4: Outline
Scalings for electricity gain
Scalings for DT fusion gain
Possible innovations for higher gain
Example low-A pilot plant concept
Summary

## Slide 5: Electricity gain Qeng determined primarily by engineering efficiencies and fusion gain
  Parameter Assumptions:
    Mn = 1.1, Ppump = 0.03×Pth
    Psub + Pcontrol = 0.04×Pth
    haux = 0.3
    hCD = ICDR0ne/PCD  0.3×1020A/W/m2
For more details see J. Menard, et al., Nucl. Fusion 51 (2011) 103014
th  thermal power conversion efficiency
aux  injected power wall plug efficiency
Q  Pfus / Paux = fusion power / auxiliary power
Qeng 
Electricity produced
Electricity consumed
=
Qeng = hth haux Q ×

## Slide 6: Fusion gain QDT  H25 from low  high gain
Fix current, field, density, geometry, auxiliary power, aP = 0.7:
QDT ≤1  QDT  Q*DT  H2 QDT >>1  QDT  Q*DT2.5  H5

## Slide 7: Stability limits and other operating constraints
n = 0 stability limit: elongation k ≤ kmax(li, e, bP, wall)
n > 0 stability limits:
  Pressure: bN  bT aBT0 / IP [%mT/MA] < bN-max(e, k, d, profiles)
  Current: q*  pa2BT0(1+k2)/m0R0IP > 2
Density limit: ne < nGreenwald = 1020m-3 IP [MA] / pa[m]2
Steady-state: IPlasma = Ibootstrap (BS) + Iexternal current drive (CD)
  fBS = CBS e1/2 bP bP bT  bN2 G(k) G(k)  k or (1+k2)/2 ~ k2
  Fraction of external current drive = fCD = 1 - fBS

## Slide 8: Gain vs. physics and engineering constraints
For steady-state, current limit is weaker constraint than high fBS  no q* dependence  relevant variables are bN / fBS and fgw:
Choose electrostatic gyro-Bohm Petty-08 with no b degradation (JET, DIII-D, NSTX)
Optimize: confinement, current drive vs density aspect ratio
C. Petty, et al., Phys. Plasmas 15 (2008) 080501

## Slide 9: Potential Innovation Areas for Compact Pilot
Aspect Ratio – Reduced A  higher bN and k
Magnet Technology – HTS for higher BT, Jwinding-pack
Confinement – Optimize edge transport barrier
Current Drive – Negative NBI, new RF techniques
Divertors – Long-leg, liquid metals
Blankets – Liquid metal, high efficiency

## Slide 10: Potential Innovation Areas for Compact Pilot
Optimize this
combination first
Assess R0 = 3m  smallest size for Qeng > 1, high fluence
Aspect Ratio
Magnet Technology
Confinement
Current Drive
Divertors
Blankets

## Slide 11: Optimization Approach
Fix plasma major radius, heating power (PNNBI=50MW)
  R0 = 3m – smallest size for Qeng > 1 + high fluence ~ 6MWy/m2
Vary aspect ratio from A = 1.6 to 4
Include blanket/shield model to achieve TBR~1 for all A
Apply magnet (see backup) and plasma constraints
  HTS strain: 0.3%, bN(e) n=1 no-wall, k(e): 0.95×limit, fGW = 0.8
  Vary HTS current density, peak field
  Also scan inboard shielding thickness
Compute QDT, Qeng, and required H98 (unconstrained)

## Slide 12: Aspect ratio dependence of limits: k(e), bN(e)
NSTX data (+ST-FNSF models) at low-A, DIII-D, ARIES-AT for high A
  k  1.9 for A  
Profile-optimized no-wall stability limit at fBS ≈ 50% (Menard PoP 2004)
  bN  3.1 for A  
e = A-1
Pilot study uses 1.0 × bN values here:
bN
Pilot study uses 0.95 × k values here:
e = A-1
k
J. Menard, et al., Nucl. Fusion 56 (2016) 106023
H. Zohm, et al., Nucl. Fusion 53 (2013) 073019

## Slide 13: Rotation profile control may provide stable operation near and above n=1 no-wall limit
NSTX, DIII-D show resonant damping can stabilize resistive wall mode (RWM)
Use neutral beams, rotation damping from 3D fields, other actuators to control rotation for RWM stability
Reduced drift-kinetic MHD
RWM stability map
gtwall
133776, t=0.861 s
precession resonance
bounce / circulating resonance
NSTX
Expt. rotation for RWM-stable plasma
YI2.00005 - J. Berkery (Columbia University)
BI2.00005 - I. Goumiri (Princeton University)
S. Sabbagh (Columbia University) – APS-DPP 2014

## Slide 14: HTS cables using REBCO tapes achieving high winding pack current density at high BT
Base cable: 50 tapes YBCO Tapes with 38 mm substrate (Van Der Laan, HTS4Fusion, 2015)
Higher Jcable HTS cable concepts under development:
Base Conductor
He Gas Cooled
8kA, JWP ~ 160MA/m2
Conductor on Round Core Cables (CORC)
JWP ~ 70MA/m2 at 19T
7 mm
SS conductor jacket for strength
7 mm
Copper
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable

## Slide 15: At lower A, high TF winding-pack current density enables access to maximum allowed BT at coil
12T: ITER-like TF coil limit
(Nb3Sn, 11.8T)
19T: Present CORC HTS limit
Chart: Max BT at TF coil [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 18.3214 | 18.7622 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19
80 | 16.433 | 17.1602 | 17.7576 | 18.1294 | 18.4409 | 18.7044 | 18.9935 | 18.9996 | 18.9999 | 19 | 19 | 19
40 | 11.266 | 13.8912 | 16.0357 | 16.4935 | 16.8683 | 17.1797 | 17.6277 | 18.277 | 18.8214 | 19 | 19 | 19
30 | 8.4495 | 10.4184 | 12.1777 | 13.3057 | 14.277 | 15.1135 | 16.3799 | 17.2829 | 17.8659 | 18.3192 | 18.9755 | 19
20 | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12.2231 | 13.3857 | 14.3299 | 15.7496 | 16.7393
20 (12T) | 5.633 | 6.9456 | 8.1185 | 8.8704 | 9.518 | 10.0757 | 10.9199 | 12 | 12 | 12 | 12 | 12
Coil structure sized to maintain ≤ 0.3% strain on winding pack
Effective inboard tungsten carbide (WC) neutron shield thickness = 60cm
JWP [MA/m2]
(12T)

## Slide 16: High current density HTS cable motivates consideration of lower-A tokamak pilot plants
ITER-like TF constraints:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW, Pnet < -90MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
  Small Pnet at A=2.2-3.5
JWP ≥ 70MA/m2,Bmax ≤ 19T
  Pfusion ~500-600MW
  Pnet = 80-100MW at A=1.9-2.3
A ~ 2 attractive at high JWP
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
JWP [MA/m2]
(12T)

## Slide 17: R=3m Pilot Plants require elevated H values
H98y2 = 1.5-1.8
HPetty-08 = 1.25-1.4
Effective inboard WC n-shield thickness = 60cm
JWP [MA/m2]

## Slide 18: Increased edge rotation shear, wider and higher pedestal can increase normalized confinement ~1.5×
NSTX: Enhanced Pedestal H-mode
Higher edge vf shear (+Li)  H98=1.3-1.8
H981.5-1.8
2× wider,
2-3× higher pedestal
(BCM: Bursty chirping mode)
S. Gerhardt, et al., Nucl. Fusion 54 (2014) 083021
T. Osborne, et al., Nucl. Fusion 55 (2015) 063018
Li injection phases
Da
H98
Prad [MW]
Peped [kPa]
Lithium injection on DIII-D
Pewidth [cm]
#159643
Time [ms]
EPH
H

## Slide 19: Li (solid and liquid) PFCs can increase confinement
H98y2 increased from 0.8  1.4
NSTX (wider  higher pedestals)
D.P. Boyle, et al., J. Nucl. Mater. 438 (2013) S979
H98~1
2-4x improvement over ITER98P(y,2)
J.C. Schmitt, et al., Phys. Plasmas 22 (2015) 056112
LTX (flatter  higher T profiles)

## Slide 20: High-efficiency current drive options exist but need additional R&D and demonstration (1)
ARC (MIT)
Inboard Launch Lower Hybrid
hCD ~ 3.6×1019 A/W/m2
HFS LHCD needs expt test
Helicon wave ray paths
Z [m]
R [m]
LH wave ray path
B. Sorbom, et al., Fus. Eng. Design, 100, (2015) 378
R. Prater, et al., Nucl. Fusion 54 (2014) 083024
FNSF-AT (GA)
Helicon Wave
hCD ~ 2.1×1019 A/W/m2
Helicon tests: DIII-D, KSTAR
Low-field side
40-80MW 1.2GHz
High-field side
25MW 8GHz
Current drive (CD) efficiency target
for Pilot Plant:
hCD  ne ICD R / P
At least 2×1019 A/W/m2
Prefer > 3×1019 A/W/m2 to keep fBS ≤ ~80%

## Slide 21: High-efficiency current drive options exist but need additional R&D and demonstration (2)
Negative Neutral Beam Injection (NNBI)
hCD ~ 3.5×1019 A/W/m2
Test on JT-60SA, leverage ITER NNBI
NNBI
RTAN = 3.6m
NNBI
RTAN = 3.9m
NNBI
RTAN = 3.0m
NNBI
RTAN = 3.3m
L. El-Guebaly, et al., Energies, 9 (2016) 632
Mid-plane tangential
50MW 0.5MeV
Electron Bernstein Wave (EBW)
hCD ~ 3×1019 A/W/m2
Ongoing / future tests: QUEST / NSTX-U, MAST-U
HTS ST-FNSF/Pilot
NSTX-U simulations at 28GHz scaled to R=3m, Te=13keV, 110GHz
G. Taylor, et al., EPJ Web of Conferences 87, 02013 (2015)

## Slide 22: Despite ITER’s beam ions being “too light”, Ron was impressed by the scale of ITER NBI
Ron Davidson inside mock-up of TFTR vacuum vessel
Plasma neutralization (≈80% efficient), laser photo-detachment (≈95% efficient) could improve haux from 30  40-50%

## Slide 23: Potential Innovation Areas for Compact Pilot
Aspect Ratio
Magnet Technology
Confinement
Current Drive
Divertors
Blankets

## Slide 24: Long-leg / Super-X aids heat flux reduction
A=2 HTS TF FNSF/Pilot
lq ~ 1mm, assume S ≈ lq (closed divertor)
T. Eich, et al., Nucl. Fusion 53 (2013) 093031
(Partial) detachment reduces peak q by further factor of 2-4
frad=0.8, fobd=0.8, Ndiv = 2

## Slide 25: Another option: use fast-flowing Liquid Metal (LM) divertor for high heat-flux mitigation
Long-leg / Super-X divertor
9 MW/m2
21 MW/m2
Shorter leg LM divertor
Geometry also compatible with
“vapor box” concepts (Ono / Goldston)

## Slide 26: Advanced divertors under active development
MAST-U will test range of divertors:
  Conventional, snowflake (not shown)
  Long-leg “Super-X” with variable flaring
EAST testing flowing liquid Li limiter:
EAST results will inform possible NSTX-U LM divertor
E. Havlickova, et al., Plasma Phys. Control. Fusion 56 (2014) 075008
J.S. Hu, et al., Nucl. Fusion 56 (2016) 046011

## Slide 27: Example: A=2, R0 = 3m HTS-TF Pilot Plant
Cryostat volume ~ 1/3 of ITER
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%
H98 = 1.75, HPetty-08 = 1.3
fgw = 0.80, fBS = 0.76
Startup IP (OH)~2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW
ENBI=0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence: 7MWy/m2
J. Menard, et al., Nucl. Fusion 56 (2016) 106023

## Slide 28: Low-A HTS design with Li flow on divertor and inboard surfaces
Double null liquid metal divertor system
Li flows from upper divertor down the inboard wall, exiting just after the lower inboard divertor.
Separate Li cooling of lower divertor
LM thickness = 5-10 mm, flow speed ~5-10 m/s
T. Brown, et al., submitted to Nuclear Fusion

## Slide 29: Benefits of shorter-leg liquid metal divertor:
No top PF coil or separate cryo-stat  simplified maintenance
1
2
3
4
5
6
7
8
Significantly reduce outboard PF coil current, force, structure
If liquid lithium, wall pumping could help increase H-factor

## Slide 30: Liquid metal blankets offer potential for high thermal efficiency, modular design
Dual-coolant Lead-Lithium (DCLL) blankets, 20 vertical sectors: hth = 30-45% (55% SiC/SiC)
HTS ST-FNSF/Pilot
ARC (MIT)
Jointed TF
FLiBe liquid immersion blanket, single component/removable: hth = 40-50%
FLiBe:
600-900ºC
PbLi
450-750ºC
SiC / PbLi
1000ºC
L. El-Guebaly, et al., Energies, 9 (2016) 632

## Slide 31: Summary: Compact fusion Pilot Plants possible with improved technology and physics operating regimes
Rare Earth BCO (REBCO) HTS TF magnet development
Lower A to improve stability – informed by NSTX-U/MAST-U
Pedestal confinement control via optimized velocity-shear, width
  Li wall pumping to provide pedestal width control, flatter T profiles
More efficient bulk current drive to facilitate steady-state
Long-leg / Super-X for heat-flux mitigation for narrow SOL
Liquid metals to exhaust heat, particles, eroded materials
  Simplify PF coil layout and vertical maintenance strategy
High-temp, efficiency modular or pool liquid-metal blankets

## Slide 32
Backup slides

## Slide 33: A = 1.8-2.3 maximizes TF magnet utilization, and TF will be significant fraction of core cost
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
JWP = 70MA/m2
A=4 utilization ~1/3-1/2 of maximum at low A
Optimal range

## Slide 34: A ≥ 3 maximizes blanket volume utilization
JWP = 70MA/m2
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:

## Slide 35: ST-FNSF may need solenoidless current start-up method Coaxial Helicity Injection (CHI) effective for current initiation
NSTX: 150-200kA closed flux current
NSTX-U: CHI projects to 300-400kA
2
2
2
R (m)
R (m)
0
Z (m)
1.0 ms 1.6 ms 2.7 ms
R (m)
0
0
2
0
-2
TSC axisymmetric
simulation of CHI startup
CHI developed on HIT, HIT-II
Transferred to NSTX / NSTX-U
R. Raman et al., PRL 2006

## Slide 36: NIMROD simulations of CHI at high Lundquist number  plasmoid-mediated reconnection assists in flux closure
Sweet Parker (S-P) reconnection in the injector region at low Lundquist number
Plasmoids seen in NSTX CHI
Plasmoids potentially important for extrapolating CHI to FNSF
NIMROD Simulations
F. Ebrahimi, et al., PRL (2015), NF (2016)
Plasmoids
NIMROD simulation
Experiment

## Slide 37: HFS Injection at low TF Provides Non-Solenoidal Sustainment at High IN
HFS LHI development campaign provides unique operation space
  Low ITF ~ 0.6 Ip
  accessible
Enables high bt access1
  Aided by anomalous ion heating
Kinetic constraints on magnetic equilibrium fits2
  Ptot(0)
  Edge location defined by Te profiles
1 M.W. Bongard, et al. NP10.52 Poster Wed morning
2 G.M. Bodner, et al. NP10.54, Poster Wed. morning
Ti
ne(1019 m-3)
Te (eV)
150
50
0
Te (eV)
0
0.8
Rmaj (m)
0.4
100
0
0.8
Rmaj (m)
0.4
1.5
ne (1019 m-3)
1.0
0.5
0.0
IN = 15
120
80
40
0
Ip (kA)
60
30
0
ITF (kA)
Time (ms)
18
22
26
Notes: As it turns out, HFS injection at low toroidal field provides a unique operating space for non-solenoidal sustainment at High normalized current.
You heard previously that Plasma Material Interactions in our HFS injection campaign limited the magnitude of toroidal field we could apply.
When we pushed this space to its limits, ultimately here a toroidal field current only 60% our plasma current (shown here on the second trace), we were able to access and sustain plasmas in an operating space with very high normalized currents, at times with values 10-15.
Coupled with high densities and temperatures, shown here on the bottom right versus major radius, this enables access to very high beta toroidal values. A key feature I don’t have time to go into detail on, and that we’re still actively investigating, is the role of anomalous ion heating due to reconnection in the edge during LHI. I’m showing here the electron temperature profile in red, which interestingly shows a sharp gradient region in the edge. Regarding the ion temperatures, at this time point we measure the core ion temperature to be ~1.5 times the core electron temperature. This provides a significant contribution to the total plasma pressure.
Now, in order to accurately calculate toroidal beta, we’ve done kinetically-constrained magnetic equilibrium fits using the Thomson profiles. Specifically, we’ve constrained the total core pressure as measured by Thomson and our ion temperature diagnostic, and we’ve constrained the edge location as defined by the electron temperature profiles.

## Slide 38: LHI-Produced Plasmas at low Bt Provide High bt
bT for sustained, low-ℓi, high-k, LHI-driven plasmas
Sample magnetic reconstruction at t = 24.5 ms, using kinetic constraints
1 M.W. Bongard, et al. NP10.52 Poster Wed morning
120
100
80
40
20
0
bt (%)
60
10
5
0
IN
15
Notes: TO SAY:
I’m showing a sample magnetic reconstruction here on the left hand side which uses these kinetic constraints, here for a plasma current of 0.1 MA and toroidal field of 25 mT.
These plasmas are highly elongated, and have an extremely low li. For this case, we obtain a toroidal beta of 95%.
On the right hand side I’m showing a Troyon plot, a scatter plot of toroidal beta versus normalized plasma current. Operating spaces of several other tokamaks are shown as shaded regions, and updated Pegasus discharges are highlight as individual points. I should mention that the filled-in symbols represent beta-values obtained directly from kinetically-constrained equilibrium reconstructions. The empty symbols are magnetics-only reconstructions that have been calibrated based on the constrained results.
We note that some of the highest beta values come directly from kinetically-constrained equilibria.
I should also point out, too, that all of these discharges used zero Ohmic drive. Every Pegasus plasma on this plot was produced using solely Local Helicity Injection.
TO DO:
- Get list / have list on hand of caveats from Ray’s IAEA talk…

## Slide 39: Engineering constraints
Magnet constraints
  Maximum stress in TF magnet structure = 0.66 GPa
  HTS tape/cable strain limit 0.3% (equivalent to 0.4 GPa)
  Winding pack current density (CORC 2015) 70 MA/m2
  OH at small R  higher solenoid flux swing for higher A
Shielding / blankets
  HTS fluence limit: 3.5-5 x 1022 n/m2
  Shield:10x n-shielding factor per 15-16cm WC for HTS TF
  Include inboard & outboard breeder thickness for TBR ~ 1
    “Effective shield thickness” includes shield + DCLL blanket
Electrical system efficiency assumptions:
  30% wall plug efficiency for H&CD - typical of NNBI
  ≥ 45% thermal conversion efficiency - typical of DCLL
    Also include pumping, controls, other sub-systems - see Pilot Plant NF 2011 paper

## Slide 40: Simplified TF magnet design equations
From J. Schwartz, Journal of Fusion Energy, Vol. 11, No. 1, 1992

## Slide 41: HTS performance vs. field and fast neutron fluence

## Slide 42: Increased TF winding-pack current density can increase BT in plasma 2-3× at low A
JWP [MA/m2]
(12T)
Chart: BT at geometric center [T]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
160 | 2.1314 | 2.8724 | 3.5298 | 3.927 | 4.2687 | 4.5627 | 5.0076 | 5.6937 | 6.3054 | 6.802 | 7.5484 | 8.0687
70 | 1.9117 | 2.6272 | 3.299 | 3.7471 | 4.1431 | 4.4917 | 5.0059 | 5.6935 | 6.3054 | 6.802 | 7.5484 | 8.0687
40 | 1.3106 | 2.1267 | 2.9791 | 3.4089 | 3.7897 | 4.1256 | 4.6459 | 5.477 | 6.2462 | 6.802 | 7.5484 | 8.0687
30 | 0.98296 | 1.595 | 2.2623 | 2.7501 | 3.2076 | 3.6294 | 4.317 | 5.1791 | 5.929 | 6.5583 | 7.5387 | 8.0687
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.6629 | 4.4422 | 5.1301 | 6.2571 | 7.1086
20 | 0.6553 | 1.0634 | 1.5082 | 1.8334 | 2.1384 | 2.4196 | 2.878 | 3.596 | 3.9824 | 4.296 | 4.7674 | 5.096
2× increase
3× increase
1.2× increase

## Slide 43: High current density HTS toroidal field coils could enable access to high fusion power in R~3m device
ITER-like TF constraints:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
JWP ≥ 70MA/m2,Bmax ≤ 19T
  Pfusion ~500-600MW
Chart: Pfusion [MW]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | 246.0028 | 432.7379 | 583.3162 | 607.5533 | 606.7621 | 589.7419 | 571.4392 | 537.6294 | 500.4852 | 453.345 | 358.4489 | 278.381
0.4 | 174.8919 | 332.4576 | 482.5278 | 533.6621 | 558.8914 | 564.7819 | 570.7858 | 537.5829 | 500.4765 | 453.3423 | 358.4484 | 278.3808
0.5 | 51.1869 | 172.9943 | 358.5903 | 407.2527 | 434.1847 | 444.1135 | 462.48 | 481.3769 | 487.0152 | 453.345 | 358.4489 | 278.381
0.6 | 19.8048 | 68.1159 | 153.2279 | 212.6847 | 264.1296 | 304.1657 | 373.389 | 409.141 | 418.1467 | 406.719 | 357.0235 | 278.381
0.7 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 139.6142 | 171.0165 | 189.3741 | 197.5059 | 184.0685
20 | 5.343 | 17.8599 | 40.6874 | 57.346 | 72.1979 | 83.986 | 104.837 | 131.5217 | 119.8912 | 105.974 | 79.8077 | 59.401
JWP [MA/m2]
(12T)

## Slide 44
A=2, R0 = 3m device TF inboard leg
0.167 m2 winding area
Current per coil: 6 MA
Winding Cd: 35.9 MA/m2

## Slide 45: CAD Geometry of OB Blanket with Ports
Stabilizing
Shells
MTM
TBM
4 NBIs
Detailed Blanket Internals

## Slide 46: Model blanket and shield thickness vs. A

## Slide 47: Neutronics analysis for HTS TF shielding

## Slide 48: Need inboard breeding for TBR > 1 at A=2
10cm IB blanket sufficient for TBR > 1.04
Outboard TBR ~ 0.92
TBR
Required TBR = 1.04
(4% margin)
IB blanket thickness [cm]

## Slide 49: HTS TF lifetime is very strong function of inboard shielding thickness
Inboard shield + blanket equivalent to 60cm WC 
3FPY  6-7MWy/m2  fulfill FNSF requirement

## Slide 50: Detailed breeding calculations completed for A=2
Step 1- Infinite media of LiPb
Step 2- LiPb confined to OB FW/blanket
Step 3- Assembly gaps added
Step 4- Homogeneous mixture of blanket in upper and lower ends of OB blanket
Step 5- FW material added
Step 6- Side, back, and front walls added
Step 7- Cooling channels added
Step 8- SiC FCI added
Step 9- Stabilizing shells added
Step 10- MTM only inserted (TBR relative to Step #9)
Step 11- 4 TBMs only inserted (TBR relative to Step #9)
Step 12- 4 NBIs only inserted (TBR relative to Step #9)
Step 13- all MTM, 4 TBMs, and 4 NBIs inserted
Step 14 – include inboard breeding blanket

## Slide 51: Outboard / inboard blanket vertical maintenance
Outboard blanket removed
Inboard blanket removed after outboard blanket sectors removed

## Slide 52
Long-leg / deep-V slot divertor
PF coils outside TF
Increase strike-point radius ~2× to reduce q|| and peak heat flux
Divertor PFCs in region of reduced neutron flux
Narrow divertor aperture for increased TBR
More space for breeding at top and bottom of device

## Slide 53: Pilot Plant study exploring liquid metal divertor design similar to flowing water curtain systems
Ferritic steel backing plate
Shield block
LM containment structure
LM injector system can be assembled in a single or double unit

## Slide 54: Comparison of long vs. shorter-leg divertor Pilots:
Long-leg/Super-X divertor
Liquid Metal divertor
Simplify vertical maintenance
Reduce outboard PF currents  can use LTS PF coils

## Slide 55: Lower Li containment system
One of ten 100 mm ID Li inboard drain lines
Li flows over inboard surface to a continuous trough that feeds ten Li drain lines.
Base Li return trough

## Slide 56: Local details of Li divertor / inboard FW
Li and inboard component piping
Li drain plenum
Upper Li feed
Lower divertor
Inboard DCLL blanket
Inboard shield
Li flow on girdle shell